## Slide 1: Recent Trends in NOX in the Great Lakes Region

## Slide 2: Policy Concerns in the Great Lakes Region
Michigan specifically requested ORD (in 2024) investigate inconsistencies between model predictions of O3 and ambient data over time at monitors currently exceeding the O3 NAAQS on the eastern shore of Lake Michigan
  In early 2025 Wisconsin brought similar concerns to EPA
  These concerns are not unique; many areas are having similar issues where models (CMAQ and CAMx) project O3 levels well below the NAAQS while monitored levels remain above the NAAQS
  This suggests the problem is with a ubiquitous emissions sector, most likely mobile (onroad and nonroad)
  EPA’s emission models for onroad and nonroad predict large year-to-year decreases in emissions while measurements suggest NOX has not decreased in recent years
  Modest onroad emission reductions related to technology implementation and fleet turnover may be offset by increased vehicle miles traveled or increased emissions related to intermodal activity driven by changing consumer habits

## Slide 3: Background
O3 in the region is often highest in the late spring/early summer and due to a combination of regional O3 and local production in the Chicago area amplified by shallow mixing over Lake Michigan
O3 formation largely NOX limited (especially the regional component) meaning NOX emissions most important for appropriately representing the change in O3 due to changing emissions over time

## Slide 4: Trends in NOX emissions
Annual state total emissions shown for 2 different modeling platforms that include a baseline and multiple projected future years
The new 2022 baseline is compared to the projected 2023 year (from 2016 baseline) as one way to evaluate projected emissions used in modeled attainment test demonstrations
Comparison of 2022 with 2023 for onroad suggests projections from 2016 overly optimistic; when aggregated over the entire central or eastern U.S. these “over-controls” will likely result in unrealistically low regional O3 and in some places (like the Chicago area) also impact local O3 formation
The NONROAD emissions are based on activity information included in the last official release of the model over a decade ago and was not updated with 2022 information for the 2022 modeling platform
  For this sector the 2022 baseline does not provide a point of evaluation because it is essentially the same as the projected emissions from 2016
  MOVES2014 includes the NONROAD2008 model; NONROAD not expected to be updated in MOVES5
Differences in other sectors like EGUs and area (nonpoint) important in some areas

## Slide 11: Satellite (TROPOMI) data
TROPOMI NO2 and HCHO column data shown as May and June average by year (2019 to 2024) based on OFFL product from RSIG
  This data is shown as multi-year average and as the anomaly for each year compared to the multi-year average
Site specific NO2 column for each month and year (2019 to 2024) shown for CASTNET monitors and for the O’Hare airport location
Systematic decreases in NO2 column are not obvious in the Great Lakes region between 2019 and 2024
Year specific differences in NO2 and HCHO column seem related to specific emissions events and meteorology

## Slide 12
Monthly average NO2 column density from TROPOMI extracted for a subset of CASTNET sites
Somewhat surprising pattern differences between upwind CASTNET sites (Bondville, Stockton, Perkinstown) and downwind site (Hoxeyville)

## Slide 13
NO2 column TROPOMI product May

## Slide 14
NO2 column TROPOMI product June

## Slide 15
HCHO column TROPOMI product May

## Slide 16
HCHO column TROPOMI product June

## Slide 17
Surface level monthly average MDA8 O3 measurements for month of May

## Slide 18
Surface level monthly average MDA8 O3 measurements for month of June

## Slide 19
NO2 column HCHO column Surface MDA8 O3
Sometimes regional monthly anomalies in HCHO line up spatially with surface MDA8 O3 anomalies
Difficult to evaluate these relationships in the upper plains due to paucity of O3 measurements

## Slide 20
NO2 column HCHO column Surface MDA8 O3
Sometimes regional monthly anomalies in HCHO do not line up spatially with surface MDA8 O3 anomalies
Longer range transport from Ozarks more important during these years?

## Slide 21: What can trends in ambient measurements tell us about NO2 projections?
Daytime NO2 measurements at U.S. monitors log-transformed and regressed over time to calculate the linear change in NO2 per year
  Averages based on M-F, 11AM – 4 PM, May – August
National aggregate of all monitors suggests 2-3% per year over the past decade following a period of more steep decline of 6-7% per year between 2004 and 2013

## Slide 22: What can trends in ambient measurements tell us about NO2 projections?
Examined trends in surface NO2 in-situ measurements near different types of mobile sources: intermodal hubs, areas expected to have unusually large EV penetration into the market resulting in an “upper bounds” of onroad change over time, and other areas likely more typical of vehicle types and activity
  Monitors near intermodal facilities had a 3% decrease in NO2 per year
  Monitor near an area of high EV penetration had a 10% decrease in NO2 per year
  Monitor in SE Atlanta shows steady NO2 increases over time (near airport)
Modeled onroad decreases in the Great Lakes region 8-10% based on EPA projections
  Nonroad 3-6% annual decreases in the Great Lakes region
  EGUs 7-14% annual decreases in the Great Lakes region

## Slide 23
Near-road NOx (42603) trend, log scale, ppb
Site is located in the heart of a national logistics and intermodal transit hub
Observed decrease of 3% per year
Map below

## Slide 24
Near-road NOx (42603) trend, log scale, ppb
Site is located adjacent to a national logistics and intermodal transit hub
2020 decrease is likely due to COVID-related activity changes
Observed decrease of 7% per year is likely biased by the anomalous 2020 data point, and r2 value is relatively small
With the removal of the 2020 data pint, the trend at this site would be more similar to that shown above

## Slide 25
Near-road NOx (42603) trend, log scale, ppb
Site is located in the heart of Silicon Valley known to have among the largest penetration of EV registrations in the country
Observed decrease of 10% per year with a high degree of confidence
Map below

## Slide 26
A few near-road monitors in the midwest/Great Lakes
Rate of change at these sites is 5 to 8% per year

## Slide 27: Comparing monitored trends with model projections
Showing the same model projections by sector but this time log transformed to calculate a linear regression consistent with the trend in ambient data
Model projected reductions in onroad and EGUs much larger than indicated by ambient data

## Slide 30
Cropland landcoverage
Average NO2 column density from TROPOMI
How well is this sector being characterized in the baseline modeling and how well is it being projected into the future? New methods for soil NO/HONO emissions may help here (J Bash)

## Slide 31
Monthly average NO2 column density from TROPOMI extracted for O’Hare airport and Global 1 intermodal facility in Chicago
No obvious decrease in NO2 over time

## Slide 32: Other regional sources
Looked at Konza Prairie and see spring (April in particular) prescribed burning showing up for NO2 column density
Large source of NO2 (and O3) during the early spring
Likely a little too early in the spring to consistently impact high O3 in the Great Lakes region
Using the baseline in the future year probably reasonable for grassland burning in eastern Kansas.

## Slide 33: Extra slides

## Slide 34: Bonus slides for Southwest region

## Slide 37
Ozone production rates are very sensitive to NOx concentrations below ~3 -4 ppb for most relevant VOC abundances

## Slide 38
Assuming NOy measured at Bondville for the very selective hours is aged (no NOx remaining), the relationship of ozone to NOy points to a pretty reasonable ozone production efficiency
Since NOy trends are not generally decreasing at this site, it may be reasonable to think that the source is not yet well controlled.

## Slide 42
Long term record of surface NO2 measurements in the Chicago area clearly show a decrease over time but that decrease is less obvious over the past decade (red box)