## Slide 1: AC-VC Atmospheric Composition Virtual Constellation Whitepaper: “Monitoring Surface PM2.5: An International Constellation Approach to Enhancing the Role of Satellite Observations” B. Veihelmann, ESA, AC-VC Co-Chair S. Kondragunta, NOAA, AC-VC Topical Lead

## Slide 2: Purpose
Room for improvement
Collaborative constellation approach
Not covered by other inter-agency coordinating groups
AC-VC gathered experts on
  aerosol observations
  air quality modelling
Whitepaper with actionable recommendations
Objective: Strengthen the role of satellite missions with aerosol observation capabilities in monitoring particulate pollution of air

## Slide 3: White Paper
Title: “Monitoring Surface PM2.5: An International Constellation Approach to Enhancing the Role of Satellite Observations”
Authors: 46 from academia and space agencies, led by S. Kondragunta (NOAA) and B. Veihelmann (ESA)
Executive Summary (1/2 page)
Recommendations (1 page)
Detailed discussion: status, needs, best practices
  Satellite sensors that bring PM information
  Satellite products and consistency
  Approaches to constrain particulate pollution levels
  Validation
References
Appendices

## Slide 4: White Paper Recommendations
Exploit NRT information from meteorological imagers
Exploit information from multi-angle polarimetric imagers
Exploit vertical information from spectrometers
Develop synergetic aerosol retrievals from multiple sensors
Enhance consistency of aerosol products ( AEROSAT)
Enhance radiometric consistency of space-borne sensors ( GSICS)
Develop fast forward operators for assimilation of satellite observations
Improve consistency of aerosol representation in models and satellite products
Improve uncertainty estimates in satellite aerosol products,
Develop schemes for assimilation of Level-1 satellite data
Improve aerosol models and Level-2 assimilation schemes ( AEROCOM)
Develop data processing tools incl. machine learning
Create ground-based validation supersites with comprehensive sets of sensors
Enhance ground-based observation infrastructure including low-cost PM sensors
Facilitate data access
Satellite Products
Interface with Model
Validation

## Slide 5: Way Forward: Roadmap for the implementation of the white paper
Use cases (proposed by AC-VC leadership)
  Integrating Satellite Derived PM2.5 into EPA’s AirNow System
  Copernicus Atmospheric Monitoring System use of satellite aerosol products
  Enhancing Air Quality Decision-making Activity in Indian Megacities through Assimilation of NASA Earth Observations and Development of a Decision Support System
  Monitoring, Forecasting Air Quality and Building Capacity in Asia through NASA-USAID Partnership

## Slide 6
GeoXO Atmospheric Composition Capabilities
Presented by Shobha Kondragunta
Disclaimer: The scientific results and conclusions, as well as any views or opinions expressed
herein, are those of the author(s) and do not necessarily reflect those of NOAA or
the Department of Commerce.
Joanna Joiner
Instrument Scientist
Shobha Kondragunta
Product Scientist
Greg Frost
User Scientist

## Slide 7
Notes: Geo-ring for air quality concept originated originally under CEOS atmospheric composition virtual constellation discussion. A white paper was written in 2011 with all space agencies agreeing that identical instruments (spectrometers) should be flown on geostationary satellites to capture changing global diurnal air quality. NOAA/NESDIS was part of this study and contributed to the white paper. It is a very good thing that NOAA is onboard with its GeoXO ACX instrument as an operational follow-on to TEMPO as both Sentinel-4 and GEMS have operational follow-ons.

## Slide 8: NOAA’s Legacy of Geostationary Operational Environmental Satellites
1975
1980
1994
2006
2016
2032

## Slide 9: Atmospheric Composition: A Multi-Instrument Synergy
OMI NO2 over TEMPO field of regard
Vis/IR Imager (GXI)
Fire detection
Fire radiative power
Aerosol type
Aerosol optical depth
Aerosol concentration
IR Sounder (GXS)
Ozone
Carbon monoxide
Carbon dioxide
Ammonia
CO total column, CrIS on NOAA-20, 14 Sep 2020
UV/Vis Spectrometer (ACX)
(TEMPO analog)
Ozone
Nitrogen dioxide
Sulfur dioxide
Formaldehyde
Aerosol layer height
UV AI
UV aerosol optical depth
IR Sounding
Vis/Near-IR Imagery
Atmos. Composition
Joint ABI/VIIRS Flood Product used to help response in Nicaragua
Day/Night Imagery
Lightning Mapping
Ocean Color

## Slide 10: GeoXO ACX Instrument
Attribute |  | What |  | Why
Coverage |  | CONUS, southern Canada, northern Mexico, Caribbean |  | Hourly inputs to national air quality, hazard and fire forecasting capabilities and warnings.
Spatial Resolution |  | 8x3 km2 @ nadir |  | Resolve sources, including cities, highway corridors, airports, oil/gas fields, large point sources like fires and power plants.
Temporal Resolution |  | 60 min |  | Capture diurnal variations in pollution emissions, photochemistry, and exposure. Detect episodic events like wildfires and volcanoes. Select for cloud-free conditions. Increase geographic coverage compared with LEO or surface observations.
Spectral Coverage / Resolution |  | UV: 300-500 nm Vis: 540-740 nm Both @ 0.6 nm |  | UV: ozone, nitrogen dioxide, formaldehyde, sulfur dioxide, absorption aerosol optical depth. Vis: cloud/aerosol layer height, PBL ozone, vegetation.
Analysis by Zigang Wei (IMSG at NOAA)
Notes: GeoXO ACX attributes are similar to NASA’s TEMPO instrument. GEMS which is already in orbit does not have the second visible detector to do boundary layer ozone and aerosol layer height using oxygen absorption. NOAA is working with GEMS data and adapting some of its algorithms to run on GEMS radiances in preparation for TEMPO and ACX. The diurnal variations of NO2 over Seoul, New York, and Los Angeles shows the complexity of understanding air quality issues as these are region specific and source specific.

## Slide 11
Pursue the exploitation of the near-real time (NRT) information on Particulate Matter (PM) from meteorological imagers.
Pursue the use of aerosol height information from hyperspectral imagers for constraining surface PM. Pursue the development of related fast forward operators.
Top 1 and 3 recommendations
Notes: CEOS atmospheric composition virtual constellation just completed writing a 100-page white paper on monitoring fine particulate matter from satellites. The top 2 recommendations of the white paper are use met imagers to derive information and work with spectrometers like GEMS, TEMPO, and ACX to derive aerosol layer height. NOAA has begun investing in the development of aerosol layer height product that will be discussed in the next few slides.

## Slide 12: Preparing for GeoXO ACX and TEMPO using GEMS Data
GEMS provides eight hourly observations per day. Three-day animation of aerosol layer height is shown on the left
TROPOMI provides one observation per day. Daily images of TROPOMI shows lack of spatial coverage as well as diurnal changes
Analysis by Pubu Ciren (IMSG at NOAA)
S5P TROPOMI ALH

## Slide 13
UV Aerosol Index (March 4, 2022)
0245 UTC 0345 UTC 0445 UTC 0545 UTC
TROPOMI
TROPOMI
TROPOMI
Analysis by Pubu Ciren (IMSG at NOAA)

## Slide 14
GEO
GEO sampled as LEO
Number of Days
GEO imager observations provide better estimates of fine particulate pollution (PM2.5) and the resulting exposure of harmful levels of pollution compared to LEO or surface observations.
Zhang et al., Nowcasting applications of geostationary satellite hourly surface PM2.5 data, Weather and Forecasting, 2022
Value of Geostationary Satellite Observations of Air Quality
Example: 2020 Gigafire event
On a daily basis, about 40% more people would be informed about harmful air quality using GEO observations compared with LEO data.
On an hourly basis, 10 times as many people would be informed about air pollution using GEO observations compared with surface-based data.
Notes: Using NOAA’s operational geostationary satellite estimates of hourly surface fine particulate matter concentrations, we also investigated to see how many days in a year do we have air quality standard violated? When we did this study using geo vs. leo, we quickly found that the information content from geo is so much more than leo due to density of observations. Again, most of the air quality standard violations are in the west because that is where most of the fire activity is. In the east, due to pollution control strategies, we no longer see air quality standard violations.

## Slide 15
Zhang et al., Nowcasting applications of geostationary satellite hourly surface PM2.5 data, Weather and Forecasting, 2022
Value of Geostationary Satellite Observations of Air Quality
Notes: This slide and next slide show why having geostationary satellite data are beneficial. NOAA has been flying an imager for several decades and now we have an advanced baseline imager with onboard calibration that can provide good aerosol retrievals. For air quality applications, we converted the aerosol optical depth to surface fine particulate matter concentrations to conduct some scientific studies. This map shows what time of the day pollution peaks. Indeed, consistent with our understanding of planetary boundary layer dynamics, sources, and chemistry pollution peaks either in the late evening or early morning associated with rush hour traffic. Whereas in the west where wildfires dominate fine particulate pollution, it peaks during the day because fires have strong diurnal variation and peak during the day.

## Slide 16
Advisors:
Andrew Heidinger
Dan Lindsey
Mitch Goldberg
Walter Wolf
Monika Kopacz
Kathryn Mozer
Barry Lefer
Support:
Victoria Breeze
Shiv Das
2ACX Product Scientist
3ACX User Scientist
1ACX Instrument Scientist
‡Starting May 2024
ACX Science Team Members | 
Susan Anenberg | Laura Judd
Jerome Barre | Shobha Kondragunta2
Trevor Beck | Istvan Laszlo
Patricia Castellanos | Randall Martin
David Edwards | Brian McDonald
Lawrence Flynn | R. Bradley Pierce
Gregory Frost3 | Ivanka Stajner
Gonzalo Gonzalez Abad | James Szykman
Katherine Hawley | Omar Torres
Barron Henderson | Luke Valin
Daven Henze | Jun Wang
Joanna Joiner1 |