## Slide 1: “NEXUS” Multi-Pollutant Analysis Tool Development: Status Update
HEID/AQAD Briefing
March 23, 2021
Carey Jang & Beth Landis
Data Viewer Module
Data Input Module
Data Query Module
“NEXUS 1.5” available on OAQPS’s Shared Drive at: “G:\SHARE\NEXUS\NEXUS 1.5\”
or at EPA’s new FTP site: ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/

## Slide 2: Overview
Feedback from OAQPS/SMT Briefing
NEXUS Updates
  Metrics (Toxics)
  2017 Data
  Proximity Based Module (Multi-pollutant)
National Sector Approach – NEXUS Application
Examples for Regions
  Chicago
  Pittsburgh
  Houston
Next Steps / Issues for Discussion
2

## Slide 3: Feedback from OAQPS & SMT Briefing
National level screening capabilities for sectors in addition to current “area” orientation of tool
Improve the national screening metrics for air toxics to reduce possible ‘false-negatives’
Codify “proximity-based“ EJ screening analysis for sources/sectors across criteria and toxic pollutants
Provide information that can help prioritize SPPD rules
Incorporate Economic information?
3

## Slide 4: Need to Improve Air Toxics Metrics
MP Team engaged with Air Toxics Team to improve upon current national screening metrics for air toxics
Current risk metrics were based on county-level population weighted averages (not appropriately accounting for local nature of risks) so false negatives could influence the areas ranking
ATAG provided input on improving these metrics
  New metrics now reflect more local risk (census-tracts) and expressed in “X in a million”
  Update use of percentiles based on risk value
4

## Slide 5: NEXUS 1.7 (Under Development)
Near-term Priorities for 2021 NEXUS development:
Upgrade NEXUS (modules/metrics/EJ ) for beta release
  Revise air toxic (AT) metrics based on AT team’s suggestions
  Include EJ/demographic index & Tribal areas
2017 emissions data update (including GHG & Sector mapping)
(Note: used to support “Sector Prioritization” work)
2017 fused AQ (PM2.5, O3, AT) & risk data update (with need to discuss air toxics risk effort at DD and/or office level)
Draft design for new “Proximity-based risk & EJ analysis” module (census “block group”-level)
Ongoing
Planned
5

## Slide 6: New “Proximity-based Risk & EJ Analysis Module”
Allow to set a flexible “Radius of Impact” for selected source/facility
Source: American Synthesis Rubber Co., KY Sector group: Polymers and Resins Production
[ x Display national map for Sector group
Create Table
Create Plot
Proximity-based Source/Sector Multi-Pollutant Risk & EJ Analysis
Source/Sector Analysis
Spatial Analysis
1
50km
Radius of Impact
Add “Tribal” for listing tribal areas (All & individual)
6

## Slide 7: Screening Proximity Analysis in NEXUS: Tabular Data Summary
Facility: American Synthesis Rubber Co., Louisville, KY Sector Group: Polymers and Resins Production Top Risk Drivers: ETO, Formaldehyde |  |  |  |  | Selected Options: Radius of Impact: 10km Number of CBSAs: 25 (top MP risk ranking) Air Toxics Risk threshold: 10 (“x”-in-a million) |  |  | 
 | Within Radius of Facility | County Avg. | State Avg. | EPA Region Avg. |  | Nation Avg. | Sector Group (within radius) National avg. | Sector Group (within radius) Top 25 CBSAs
Population total | x,xxx | xx,xxx | xxx,xxx | xxx,xxx |  | 317,xxx,xxx | xxx,xxx | xxx,xxx
PM2.5 risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Ozone risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Air Toxics risk: Cancer risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Cancer risk value (“x”-in-a million)) | x.x | x.x | x.x | x.x |  | x.x | x.x | x.x
Cancer risk value above selected threshold (population %tile) | x% | x% | x% | x% |  | x% | x% | x%
Non-cancer risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Non-cancer risk (Hazard Index) | x.x | x.x | x.x | x.x |  | x.x | x.x | x.x
Climate risks: Flood (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Sea level rise (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Fire (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Disease (%tile) | x% | x% | x% | x% |  | x% | x% | x%
EJ/Demographics: Minority group (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Low-income group (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Demographic Index (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Linguistic Isolation (%tile) | x% | x% | x% | x% |  | x% |  | x%
7

## Slide 8
Screening Proximity Analysis in NEXUS: Example Chart
Within Radius County avg. State avg. EPA region avg. Nation avg. Sector Group avg.
of Facility (Within Radius)
Facility: American Synthesis Rubber Co., Louisville, KY
Sector Group: Polymers and Resins Production
Nation
avg. (%tile)
Climate Risks
Air Quality
PM2.5 risk
O3 risk
Air Toxics risk
Cancer risk
Non-Cancer risk
Flood
Fire
Sea Level Rise
Heat
Disease
Climate Risks
EJ Indicators
Population
Minority
Income
Education
Language
Flood
Fire
Sea Level Rise
Heat
Disease
(%tile
8

## Slide 9: Proximity Analysis Module: Spatial Analysis (census “block group”-level)
Proximity-based Source/Sector Multi-Pollutant Risk & EJ Analysis
Spatial Analysis
EJ
Indicators
Climate
Risk
Minority
Fire
Source/Sector Analysis
Climate Risks
Air Quality
PM2.5 risk
O3 risk
Air Toxics risk
Cancer risk
Non-Cancer risk
Flood
Fire
Sea Level Rise
Heat
Disease
Climate Risks
EJ Indicators
Population
Minority
Income
Education
Language
Flood
Fire
Sea Level Rise
Heat
Disease
9

## Slide 10: Sector Emissions Prioritization Analysis over Major CBSAs using NEXUS
Products: Two Output Tables
  Table-1: Top “x” (x=20 in this case) “Facility” emissions (NOx, SO2, VOCs, Primary PM2.5, PM & metal HAPs, Gas & VOC HAPs) table for “x” (x=50) CBSAs with top ranked MP risk
  Table-2 (Summary): Total “Sector group” emissions summed up together over all top 50 CBSAs (Facilities combined into ~60 “Sector group” based on “Sector definition” spreadsheet created by Marc H. and SPPD) based on 2017 emissions data
10

## Slide 11: Step #1 : CBSAs w/ Top-Ranked MP Risks
Method: Identify CBSAs with top MP risk ranking: Major CBSAs are selected.
11
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
1 | EPA Region 5 | IL-IN-WI | Chicago-Joliet-Naperville, IL-IN-WI | 1
2 | EPA Region 3 | PA | Pittsburgh, PA | 1
3 | EPA Region 6 | TX | Houston-Sugar Land-Baytown, TX | 1
4 | EPA Region 9 | CA | Los Angeles-Long Beach-Santa Ana, CA | 2
5 | EPA Region 6 | TX | Dallas-Fort Worth-Arlington, TX | 2
6 | EPA Region 4 | GA | Atlanta-Sandy Springs-Marietta, GA | 3
7 | EPA Region 4 | FL | Tampa-St. Petersburg-Clearwater, FL | 3
8 | EPA Region 4 | AL | Birmingham-Hoover, AL | 3
9 | EPA Region 9 | AZ | Phoenix-Mesa-Glendale, AZ | 3
10 | EPA Region 9 | CA | Fresno, CA | 3
11 | EPA Region 2 | NY-NJ-PA | New York-Northern New Jersey-Long Island, NY-NJ-PA | 3
12 | EPA Region 5 | OH | Cleveland-Elyria-Mentor, OH | 3
13 | EPA Region 9 | CA | Sacramento--Arden-Arcade--Roseville, CA | 4
14 | EPA Region 9 | NV | Las Vegas-Paradise, NV | 4
15 | EPA Region 4 | NC-SC | Charlotte-Gastonia-Rock Hill, NC-SC | 5
16 | EPA Region 9 | CA | San Diego-Carlsbad-San Marcos, CA | 5
17 | EPA Region 5 | MI | Detroit-Warren-Livonia, MI | 5
18 | EPA Regions 5 & 7 | MO-IL | St. Louis, MO-IL | 5
19 | EPA Region 5 | MI | Grand Rapids-Wyoming, MI | 6
20 | EPA Region 4 | TN | Nashville-Davidson--Murfreesboro--Franklin, TN | 6
21 | EPA Region 9 | CA | Bakersfield-Delano, CA | 6
22 | EPA Regions 2 & 3 | PA-NJ-DE-MD | Philadelphia-Camden-Wilmington, PA-NJ-DE-MD | 6
23 | EPA Region 9 | CA | Riverside-San Bernardino-Ontario, CA | 6
24 | EPA Region 4 | FL | Miami-Fort Lauderdale-Pompano Beach, FL | 6
25 | EPA Region 6 | LA | Baton Rouge, LA | 7
26 | EPA Region 6 | TX | El Paso, TX | 7
27 | EPA Region 10 | WA | Seattle-Tacoma-Bellevue, WA | 7
28 | EPA Region 4 & 5 | KY-IN | Louisville-Jefferson County, KY-IN | 7
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
29 | EPA Region 8 | CO | Denver-Aurora-Broomfield, CO | 8
30 | EPA Region 3 | PA | Reading, PA | 8
31 | EPA Region 9 | CA | Visalia-Porterville, CA | 8
32 | EPA Region 1 | CT | Bridgeport-Stamford-Norwalk, CT | 8
33 | EPA Region 4 & 6 | TN-MS-AR | Memphis, TN-MS-AR | 8
34 | EPA Regions 2 & 3 | PA-NJ | Allentown-Bethlehem-Easton, PA-NJ | 9
35 | EPA Region 6 | LA | New Orleans-Metairie-Kenner, LA | 9
36 | EPA Region 4 | NC | Greensboro-High Point, NC | 10
37 | EPA Region 4 | AL | Mobile, AL | 10
38 | EPA Region 4 | TN-GA | Chattanooga, TN-GA | 11
39 | EPA Region 4 | TN | Knoxville, TN | 11
40 | EPA Region 3 | DC-VA-MD-WV | Washington-Arlington-Alexandria, DC-VA-MD-WV | 11
41 | EPA Region 6 | OK | Tulsa, OK | 11
42 | EPA Region 9 | AZ | Tucson, AZ | 11
43 | EPA Region 4 | SC | Charleston-North Charleston-Summerville, SC | 12
44 | EPA Region 4 | SC | Greenville-Mauldin-Easley, SC | 12
45 | EPA Region 3 | WV | Charleston, WV | 13
46 | EPA Region 4 | SC | Spartanburg, SC | 13
47 | EPA Region 4 | NC | Winston-Salem, NC | 13
48 | EPA Region 4 | FL | Lakeland-Winter Haven, FL | 13
49 | EPA Region 5 | OH | Akron, OH | 13
50 | EPA Region 6 | TX | Beaumont-Port Arthur, TX | 14
51 | EPA Region 5 | MI | Lansing-East Lansing, MI | 14
52 | EPA Region 4 | FL | Orlando-Kissimmee-Sanford, FL | 14
53 | EPA Region 10 | OR | Eugene-Springfield, OR | 14
54 | EPA Region 9 | NV | Reno-Sparks, NV | 14
55 | EPA Regions 4 & 5 | OH-KY-IN | Cincinnati-Middletown, OH-KY-IN | 14
56 | EPA Region 3 | PA | Lancaster, PA | 14

## Slide 12: Step #2 : Create Top Facilities “Table-1” (for each CBSA)
CBSA Name: Chicago-Joliet-Naperville, IL-IN-WI. Population: 9452622 |  |  |  |  |  |  | 
Facility Info | NOx (TON) | Facility Info | SO2 (TON) | Facility Info | Gas_ VOC_ HAPs (LB) | Facility Info | CO2e (TON)
Facility name: ArcelorMittal Burns Harbor LLC County/City/State: Porter/Burns Harbor/IN EIS_ID: 7376511 Sector Group: Coke Ovens NAICS code: 331110 NAICS description: Iron and Steel Mills and Ferroalloy Manufacturing | 9001 | Facility name: ArcelorMittal Burns Harbor LLC County/City/State: Porter/Burns Harbor/IN EIS_ID: 7376511 Sector Group: Coke Ovens NAICS code: 331110 NAICS description: Iron and Steel Mills and Ferroalloy Manufacturing | 12959 | Facility name: Chicago OHare International Airport County/City/State: Cook/Chicago/IL EIS_ID: 2681611 Sector Group: Air Transportation NAICS code: 488119 NAICS description: Other Airport Operations | 930152 | Facility name: ArcelorMittal USA LLC County/City/State: Lake/East Chicago/IN EIS_ID: 3986611 Sector Group: Iron and Steel Production NAICS code: 331110 NAICS description: Iron and Steel Mills and Ferroalloy Manufacturing | 12849804
Facility name: Northern Indiana Public Service Company LLC - RM Schahfer Generating Station County/City/State: Jasper/Wheatfield/IN EIS_ID: 7957011 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 4925 | Facility name: US STEEL GARY WORKS County/City/State: Lake/Gary/IN EIS_ID: 8192011 Sector Group: Petroleum Refining NAICS code: 324199 NAICS description: All Other Petroleum and Coal Products Manufacturing | 5681 | Facility name: ARCELORMITTAL USA LLC County/City/State: Lake/East Chicago/IN EIS_ID: 3986511 Sector Group: Iron and Steel Production NAICS code: 331110 NAICS description: Iron and Steel Mills and Ferroalloy Manufacturing | 502521 | Facility name: ArcelorMittal Burns Harbor LLC County/City/State: Porter/Burns Harbor/IN EIS_ID: 7376511 Sector Group: Coke Ovens NAICS code: 331110 NAICS description: Iron and Steel Mills and Ferroalloy Manufacturing | 11170969
Facility name: Chicago OHare International Airport County/City/State: Cook/Chicago/IL EIS_ID: 2681611 Sector Group: Air Transportation NAICS code: 488119 NAICS description: Other Airport Operations | 3797 | Facility name: ARCELORMITTAL USA LLC County/City/State: Lake/East Chicago/IN EIS_ID: 3986511 Sector Group: Iron and Steel Production NAICS code: 331110 NAICS description: Iron and Steel Mills and Ferroalloy Manufacturing | 3030 | Facility name: BP Products North America Inc Whiting R County/City/State: Lake/Whiting/IN EIS_ID: 7247711 Sector Group: Petroleum Refining NAICS code: 32411 NAICS description: Petroleum Refineries | 337592 | Facility name: US STEEL GARY WORKS County/City/State: Lake/Gary/IN EIS_ID: 8192011 Sector Group: Petroleum Refining NAICS code: 324199 NAICS description: All Other Petroleum and Coal Products Manufacturing | 10261468
Method: Output a table with “Top 20 facility emissions” (NOx, SO2, VOCs, primary PM2.5, HAPs, CO2e, etc.) for each CBSA (total 50 sub-tables)
12

## Slide 13: Step #3 : Create “Table-2” (Sector Group Summary)
“Sector group” emissions combined for all 50 CBSAs (based on top 20 facility emissions in each CBSA); Total Population: 134,940,816 |  |  |  |  |  |  |  | 
Sector Group | SO2 (TON) | NOx (TON) | PM2.5 (TON) | Gas_VOC_HAPs (LB) | Heavy_Metal_HAPs (LB) | CO2e (TON) | SO2 Score (freq. & rank) | 
Electric Utilities | 276526 | 195865 | 25828 | 6432707 | 127030 | 485754073 | 2014 | 
Petroleum Refining | 52943 | 40169 | 12438 | 10295621 | 99736 | 95097998 | 574 | 
Coke Ovens | 22405 | 15473 | 5158 | 1787622 | 29716 | 14570119 | 132 | 
Pesticides and Agricultural Chemical Manufacturing | 17644 | 5861 | 1292 | 1627958 | 1788 | 18233480 | 153 | 
Inorganic Chemical Manufacturing | 14522 | 7273 | 1405 | 1073205 | 48966 | 5231826 | 190 | 
Mineral Processing | 13714 | 12628 | 1659 | 886251 | 33740 | 8364046 | 256 | 
Iron and Steel Production | 10679 | 13345 | 5691 | 858984 | 110757 | 33030868 | 375 | 
Cement Manufacturing | 10566 | 44083 | 5007 | 1472498 | 25010 | 27859268 | 444 | 
Air Transportation | 8127 | 63035 | 2685 | 10417526 | 122777 | 18485627 | 1380 | 
Pulp and Paper Industry | 7413 | 9791 | 2779 | 7227413 | 23704 | 10517197 | 251 | 
Organic Chemical Manufacturing | 6240 | 38070 | 6254 | 10280694 | 20059 | 82521408 | 299 | 
Landfills | 2952 | 9872 | 2356 | 2799470 | 1880 | 28651639 | 563 | 
Consumer Products (Cleaning, Photographic, etc.) | 2815 | 1980 | 486 | 1363144 | 1724 | 1389978 | 66 | 
Oil and Gas Production and Distribution | 2717 | 28271 | 2259 | 4467061 | 1804 | 12342771 | 466 | 
Food Products Manufacturing | 2705 | 6197 | 3085 | 4110212 | 2496 | 3408089 | 327 | 
Non-Ferrous Metals Production | 2694 | 3511 | 1695 | 3663067 | 91643 | 2165692 | 212 | 
Glass Manufacturing | 2355 | 5832 | 953 | 92289 | 9990 | 1174855 | 210 | 
Clay Products Manufacturing | 1349 | 685 | 602 | 650323 | 1631 | 200293 | 311 | 
Waste Incineration | 1024 | 11872 | 483 | 679918 | 1801 | 9825913 | 189 | 
Method: Output summary “Table-2” w/ all top 20 facility emissions combined into “Sector group” for all top ranked 50 CBSAs (Note: Facilities are grouped into ~60 sectors based on “Sector definition” spreadsheet created by Marc H. & SPPD) based on 2017 data
13

## Slide 14: SO2 & NOx: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Chart: Total SO2 & NOx emissions (tpy) from top Sector groups
| Electric Utilities | Petroleum Refining | Coke Ovens | Pesticides and Agricultural Chemical Manufacturing | Inorganic Chemical Manufacturing | Mineral Processing | Iron and Steel Production | Cement Manufacturing | Air Transportation | Pulp and Paper Industry | Organic Chemical Manufacturing | Landfills | Consumer Products (Cleaning, Photographic, etc.) | Oil and Gas Production and Distribution | Food Products Manufacturing | Non-Ferrous Metals Production | Glass Manufacturing | Clay Products Manufacturing | Waste Incineration | Asphalt Products Manufacturing | Mining Activities
SO2 | 276526.3062 | 52943.1734 | 22404.8065 | 17644.0804 | 14521.6033 | 13714.4318 | 10678.7031 | 10566.429 | 8126.8388 | 7412.9793 | 6239.8283 | 2952.1673 | 2814.5235 | 2716.7565 | 2704.9001 | 2693.8076 | 2354.6044 | 1348.7497 | 1024.3245 | 917.4123 | 860.1116
NOx | 195864.5328 | 40168.8675 | 15472.6338 | 5861.2174 | 7272.8804 | 12628.2753 | 13345.4622 | 44083.4072 | 63034.7835 | 9790.7401 | 38070.4692 | 9872.4188 | 1980.2363 | 28271.167 | 6197.3419 | 3510.7028 | 5832.2555 | 684.7521 | 11871.941 | 1211.0917 | 3246.8551
over
14

## Slide 15: SO2 & NOx: Sector Group “Score” (Score = Frequency & Rank)
Chart: 
| Electric Utilities | Petroleum Refining | Coke Ovens | Pesticides and Agricultural Chemical Manufacturing | Inorganic Chemical Manufacturing | Mineral Processing | Iron and Steel Production | Cement Manufacturing | Air Transportation | Pulp and Paper Industry | Organic Chemical Manufacturing | Landfills | Consumer Products (Cleaning, Photographic, etc.) | Oil and Gas Production and Distribution | Food Products Manufacturing | Non-Ferrous Metals Production | Glass Manufacturing | Clay Products Manufacturing | Waste Incineration | Asphalt Products Manufacturing | Mining Activities
SO2 | 2014 | 574 | 132 | 153 | 190 | 256 | 375 | 444 | 1380 | 251 | 299 | 563 | 66 | 466 | 327 | 212 | 210 | 311 | 189 | 389 | 120
NOx | 2463 | 492 | 100 | 102 | 97 | 263 | 287 | 547 | 1163 | 237 | 397 | 208 | 73 | 806 | 283 | 172 | 183 | 53 | 242 | 17 | 131
SO2 & NOx: Score of Top Sector Groups
15

## Slide 16: Primary PM2.5: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Chart: 
| Electric Utilities | Petroleum Refining | Organic Chemical Manufacturing | Iron and Steel Production | Coke Ovens | Cement Manufacturing | Food Products Manufacturing | Pulp and Paper Industry | Air Transportation | Landfills | Oil and Gas Production and Distribution | Mining Activities | Non-Ferrous Metals Production | Mineral Processing | Polymers and Resins Production | Iron and Steel Foundries | Inorganic Chemical Manufacturing | Pesticides and Agricultural Chemical Manufacturing | Glass Manufacturing | Asphalt Products Manufacturing | Government (non-Defense)
PM2.5 (TON) | 25827.9863 | 12437.633 | 6254.3809 | 5690.8713 | 5158.3213 | 5007.4356 | 3084.5061 | 2778.9607 | 2684.9839 | 2356.4402 | 2258.6926 | 2089.5651 | 1695.4921 | 1659.0549 | 1505.6629 | 1480.2527 | 1404.6369 | 1292.0852 | 953.2937 | 928.9664 | 856.4677
over
Primary PM2.5 emissions (ton/yr) from top Sector groups
16

## Slide 17: Primary PM2.5 : Sector Group “Score” (Score = Frequency & Rank)
Chart: 
| Electric Utilities | Petroleum Refining | Organic Chemical Manufacturing | Iron and Steel Production | Coke Ovens | Cement Manufacturing | Food Products Manufacturing | Pulp and Paper Industry | Air Transportation | Landfills | Oil and Gas Production and Distribution | Mining Activities | Non-Ferrous Metals Production | Mineral Processing | Polymers and Resins Production | Iron and Steel Foundries | Inorganic Chemical Manufacturing | Pesticides and Agricultural Chemical Manufacturing | Glass Manufacturing | Asphalt Products Manufacturing | Government (non-Defense)
PM2.5 top20 score | 2539 | 617 | 364 | 345 | 138 | 480 | 479 | 326 | 716 | 362 | 356 | 234 | 324 | 228 | 164 | 229 | 120 | 129 | 186 | 143 | 62
Primary PM2.5: Score of Top Sector Groups
17

## Slide 18: Gas & VOC HAPs: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Chart: 
| Air Transportation | Petroleum Refining | Organic Chemical Manufacturing | Pulp and Paper Industry | Polymers and Resins Production | Plastic and Metal Parts Manufacturing | Electric Utilities | Oil and Gas Production and Distribution | Food Products Manufacturing | Non-Ferrous Metals Production | Landfills | Transportation Equipment Auto and Light Duty Truck | Wholesale and Retail Trade | Coke Ovens | Transportation Equipment Ship/Boat Building & Repair | Pesticides and Agricultural Chemical Manufacturing | Cement Manufacturing | Consumer Products (Cleaning, Photographic, etc.) | Metal Fabrication | Inorganic Chemical Manufacturing | Petroleum Products Distribution
Gas_VOC_HAPs (LB) | 10417526.399 | 10295620.989 | 10280694.057 | 7227413.2437 | 7153760.6784 | 6573090.6333 | 6432706.8109 | 4467061.335 | 4110211.5326 | 3663066.9479 | 2799469.9445 | 2602184.4014 | 2136286.2907 | 1787622.2229 | 1769261.2721 | 1627958.0555 | 1472497.6393 | 1363143.832 | 1239126.7811 | 1073204.5379 | 1057320.5515
Gas & VOC HAPs emissions (lb/yr) from top Sector groups
18

## Slide 19: Gas & VOC HAPs: Sector Group “Score” (Score = Frequency & Rank)
Chart: 
| Air Transportation | Petroleum Refining | Organic Chemical Manufacturing | Pulp and Paper Industry | Polymers and Resins Production | Plastic and Metal Parts Manufacturing | Electric Utilities | Oil and Gas Production and Distribution | Food Products Manufacturing | Non-Ferrous Metals Production | Landfills | Transportation Equipment Auto and Light Duty Truck | Wholesale and Retail Trade | Coke Ovens | Transportation Equipment Ship/Boat Building & Repair | Pesticides and Agricultural Chemical Manufacturing | Cement Manufacturing | Consumer Products (Cleaning, Photographic, etc.) | Metal Fabrication | Inorganic Chemical Manufacturing | Petroleum Products Distribution
Gas_VOC_HAPs top20 score | 1422 | 544 | 655 | 372 | 449 | 570 | 1058 | 530 | 261 | 377 | 440 | 266 | 179 | 102 | 183 | 154 | 256 | 181 | 175 | 80 | 121
Gas & VOC HAPs: Score of Top Sector Groups
19

## Slide 20: Heavy Metal HAPs: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Heavy HAPs emissions (lb/yr) from top Sector groups
Chart: 
| Electric Utilities | Air Transportation | Iron and Steel Production | Petroleum Refining | Non-Ferrous Metals Production | Inorganic Chemical Manufacturing | Transportation Equipment Auto and Light Duty Truck | Mineral Processing | Coke Ovens | Metal Fabrication | Cement Manufacturing | Pulp and Paper Industry | Iron and Steel Foundries | Organic Chemical Manufacturing | Glass Manufacturing | Transportation Equipment Ship/Boat Building & Repair | Business Activities | Transportation Equipment Aerospace Industry | Waste Treatment and Disposal | Building Products Manufacturing | Plastic and Metal Parts Manufacturing
Heavy_Metal_HAPs (LB) | 127029.7646 | 122776.7046 | 110756.807 | 99736.2364 | 91643.1076 | 48966.3979 | 36095.3706 | 33740.1057 | 29716.3211 | 26233.0074 | 25009.7078 | 23704.0343 | 23233.7697 | 20059.4486 | 9990.1173 | 7759.171 | 7100.5414 | 6357.3919 | 5996.8864 | 5187.5464 | 4799.6812
20

## Slide 21: Heavy Metal HAPs: Sector Group “Score” (Score = Frequency & Rank)
Heavy Metal HAPs: Score of Top Sector Groups
Chart: 
| Electric Utilities | Air Transportation | Iron and Steel Production | Petroleum Refining | Non-Ferrous Metals Production | Inorganic Chemical Manufacturing | Transportation Equipment Auto and Light Duty Truck | Mineral Processing | Coke Ovens | Metal Fabrication | Cement Manufacturing | Pulp and Paper Industry | Iron and Steel Foundries | Organic Chemical Manufacturing | Glass Manufacturing | Transportation Equipment Ship/Boat Building & Repair | Business Activities | Transportation Equipment Aerospace Industry | Waste Treatment and Disposal | Building Products Manufacturing | Plastic and Metal Parts Manufacturing
Heavy_Metal_HAPs top20 score | 1169 | 3286 | 520 | 404 | 1113 | 163 | 169 | 139 | 33 | 391 | 328 | 202 | 241 | 225 | 118 | 83 | 108 | 88 | 79 | 44 | 86
21

## Slide 22: CO2e: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Chart: CO2e emissions (ton/yr) from top Sector groups
| Electric Utilities | Petroleum Refining | Organic Chemical Manufacturing | Iron and Steel Production | Landfills | Cement Manufacturing | Air Transportation | Pesticides and Agricultural Chemical Manufacturing | Coke Ovens | Oil and Gas Production and Distribution | Pulp and Paper Industry | Waste Incineration | Mineral Processing | Inorganic Chemical Manufacturing | Construction and Related Industries | Polymers and Resins Production | Business Activities | Food Products Manufacturing | Mining Activities | Non-Ferrous Metals Production | Waste Treatment and Disposal
CO2e (TON) | 485754073.3999 | 95097997.6137 | 82521408.4743 | 33030867.612 | 28651639.0371 | 27859267.6207 | 18485626.9882 | 18233480.213 | 14570119.2452 | 12342770.6501 | 10517197.2191 | 9825912.883 | 8364045.7709 | 5231826.336 | 5161734.6426 | 4612128.3752 | 3506487.8326 | 3408089.4849 | 2184543.3443 | 2165692.0817 | 1901478.423
over
22

## Slide 23: CO2e: Sector Group “Score” (Score = Frequency & Rank)
CO2e: Score of Top Sector Groups
23
Chart: 
| Electric Utilities | Petroleum Refining | Organic Chemical Manufacturing | Iron and Steel Production | Landfills | Cement Manufacturing | Air Transportation | Pesticides and Agricultural Chemical Manufacturing | Coke Ovens | Oil and Gas Production and Distribution | Pulp and Paper Industry | Waste Incineration | Mineral Processing | Inorganic Chemical Manufacturing | Construction and Related Industries | Polymers and Resins Production | Business Activities | Food Products Manufacturing | Mining Activities | Non-Ferrous Metals Production | Waste Treatment and Disposal
 | 3264 | 493 | 601 | 272 | 1132 | 595 | 672 | 118 | 87 | 291 | 215 | 136 | 219 | 32 | 119 | 150 | 118 | 327 | 34 | 269 | 99

## Slide 24: Examples for Regional Engagement: Highest MP Risk Areas
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
1 | EPA Region 5 | IL-IN-WI | Chicago-Joliet-Naperville, IL-IN-WI | 1
2 | EPA Region 3 | PA | Pittsburgh, PA | 1
3 | EPA Region 6 | TX | Houston-Sugar Land-Baytown, TX | 1
4 | EPA Region 9 | CA | Los Angeles-Long Beach-Santa Ana, CA | 2
5 | EPA Region 6 | TX | Dallas-Fort Worth-Arlington, TX | 2
6 | EPA Region 4 | GA | Atlanta-Sandy Springs-Marietta, GA | 3
7 | EPA Region 4 | FL | Tampa-St. Petersburg-Clearwater, FL | 3
8 | EPA Region 4 | AL | Birmingham-Hoover, AL | 3
9 | EPA Region 9 | AZ | Phoenix-Mesa-Glendale, AZ | 3
10 | EPA Region 9 | CA | Fresno, CA | 3
11 | EPA Region 2 | NY-NJ-PA | New York-Northern New Jersey-Long Island, NY-NJ-PA | 3
12 | EPA Region 5 | OH | Cleveland-Elyria-Mentor, OH | 3
13 | EPA Region 9 | CA | Sacramento--Arden-Arcade--Roseville, CA | 4
14 | EPA Region 9 | NV | Las Vegas-Paradise, NV | 4
15 | EPA Region 4 | NC-SC | Charlotte-Gastonia-Rock Hill, NC-SC | 5
16 | EPA Region 9 | CA | San Diego-Carlsbad-San Marcos, CA | 5
17 | EPA Region 5 | MI | Detroit-Warren-Livonia, MI | 5
18 | EPA Regions 5 & 7 | MO-IL | St. Louis, MO-IL | 5
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
19 | EPA Region 5 | MI | Grand Rapids-Wyoming, MI | 6
20 | EPA Region 4 | TN | Nashville-Davidson--Murfreesboro--Franklin, TN | 6
21 | EPA Region 9 | CA | Bakersfield-Delano, CA | 6
22 | EPA Regions 2 & 3 | PA-NJ-DE-MD | Philadelphia-Camden-Wilmington, PA-NJ-DE-MD | 6
23 | EPA Region 9 | CA | Riverside-San Bernardino-Ontario, CA | 6
24 | EPA Region 4 | FL | Miami-Fort Lauderdale-Pompano Beach, FL | 6
25 | EPA Region 6 | LA | Baton Rouge, LA | 7
26 | EPA Region 6 | TX | El Paso, TX | 7
27 | EPA Region 10 | WA | Seattle-Tacoma-Bellevue, WA | 7
28 | EPA Region 4 & 5 | KY-IN | Louisville-Jefferson County, KY-IN | 7
29 | EPA Region 8 | CO | Denver-Aurora-Broomfield, CO | 8
30 | EPA Region 3 | PA | Reading, PA | 8
31 | EPA Region 9 | CA | Visalia-Porterville, CA | 8
32 | EPA Region 1 | CT | Bridgeport-Stamford-Norwalk, CT | 8
33 | EPA Region 4 & 6 | TN-MS-AR | Memphis, TN-MS-AR | 8
34 | EPA Regions 2 & 3 | PA-NJ | Allentown-Bethlehem-Easton, PA-NJ | 9
35 | EPA Region 6 | LA | New Orleans-Metairie-Kenner, LA | 9
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. OAQPS could provide area profile packets to Regions to discuss nature of MP issues and possible avenues to address or conduct more refined analyses.
The information above was generated in NEXUS & exported into Excel where rankings were applied.
These CBSAs include at least one county that meets ALL the following criteria:
PM Mortality Number Percentile >= 90
O3 Mortality Number Percentile >= 90
Cancer Risk Rate Max Percentile >= 90 (max census tract-level in a county)
24

## Slide 25: Example 1 - Chicago CBSA
25
Generated in NEXUS

## Slide 26: Example 1 - Chicago CBSA – Top Emission Sources
26
Generated in NEXUS

## Slide 27: Example 1 - Chicago CBSA – US Steel Gary Works
Demographic Index
People of Color Population
Low Income
National Percentiles
27
Generated in NEXUS
Generated in EJSCREEN
Generated in EJSCREEN
Generated in EJSCREEN

## Slide 28: Example 2 - Pittsburgh CBSA
28
Generated in NEXUS

## Slide 29: Example 2 - Pittsburgh CBSA – Top Emission Sources
EGUs
29
Generated in NEXUS

## Slide 30: Example 2 - Pittsburgh CBSA – Dominated by EGUs
30
Generated in NEXUS

## Slide 31: Example 3 - Houston CBSA
31
Generated in NEXUS

## Slide 32: Example 3 - Houston CBSA – Top Emission Sources
32
Generated in NEXUS

## Slide 33: Example 3 - Houston CBSA – Baytown
National Percentiles
Baytown Refinery (Petroleum)
Baytown Olefins Plant (Chemical Plant)
Demographic Index
People of Color Population
Low Income
33
Generated in NEXUS
Generated in EJSCREEN
Generated in EJSCREEN
Generated in EJSCREEN

## Slide 34: Next Steps / Issues for Discussion
Next Steps
  Follow up with additional EJ discussions/connection with EJSCREEN
  Updating existing data to 2017
    Emissions, O3/PM2.5/Toxics concentration, O3 and PM2.5 risk
  Add new information
    Tribal areas, Advance areas, GHG emissions, monitoring data
  Develop proximity analysis module for MP risk, EJ & climate
  Meeting with economics group
Issues for Discussion
  2017 Air Toxics Risk Data
  OAQPS review/prioritization of analytical tools
  Funding mechanism
34

## Slide 35: Questions?
35

## Slide 36: Appendix A
Consideration of Climate Indicators
36

## Slide 37: Climate Vulnerability
“Vulnerability is the susceptibility to the adverse effects of climate change, including both climate variability and extremes. Vulnerability measures the intersection of exposure, sensitivity to harm, and capacity to adapt to change. “ - NRDC Report; Turner et al 2003
1. What populations are particularly vulnerable to the projected effects of climate change?
2. Where is climate change vulnerability likely to increase baseline susceptibility to air pollution?
3. How might these vulnerabilities intersect with vulnerabilities relevant for EJ issues?
How can we identify/consider compounding vulnerabilities in communities likely to simultaneously experience air pollution, Environmental Justice, and climate issues?
37

## Slide 38: Data Driven Screening Tools
Data driven EJ screening tools either exist (i.e., EJ Screen/OEJ) or are in development (i.e., NEXUS, C. Jang/AQMG)
  Biden EO specifies “the development of a Climate and Environmental Justice Screening Tool, building off EPA’s EJSCREEN, to identify disadvantaged communities, support the Justice40 Initiative, and inform equitable decision making across the federal government”
OAQPS can assist in the effort to enhance these tools to reflect climate vulnerability thereby allowing for development of strategies and programs seeking to protect public and environmental health in areas with elevated risk for climate change impacts by identifying compounding vulnerabilities across the Climate-EJ space
  Addition of policy-relevant data layers / new indices
  Enhanced proximity analysis capabilities
Geographically explicit screening tools also help connect across scales, e.g., characterizing impacts of national climate strategies at the local/community level
NEXUS Tool
(slide from C. Jang)
EJ Screen (OEJ)
38

## Slide 39: Elements of Climate Vulnerability
Components of climate vulnerability include environmental, physical, social, and economic factors (United Nations 2004 Report)
We can begin to characterize environmental and physical vulnerability with existing data sets and modeling tools
Many components contributing to underlying vulnerability are not explicitly tied to specific areas or environmental factors, but rather are intrinsic to broader socio-economic systems (e.g. food security, income and education, etc)
Opportunities for collaboration with HEID, ORD, OAP, and other partners with expertise in identifying and incorporating these elements of climate vulnerability
Potential overlap with EJ vulnerabilities
Mainali and Pricope 2017
39

## Slide 40: Geospatial Components of Climate Vulnerability
Geographic/Demographic Indicators
Low-lying/coastal
High elevation
Dense Urban
Extremely rural
Environmental Indicators*
Wildfire smoke prevalence
Precipitation (high and low)
Temperature stress (hot and cold)
Changes in meteorology (T, Precip, etc)
* These types of layers can be difficult to quantify directly without additional tools, e.g. meteorological or air quality models
Image credit: Associated Press
References: IPCC, NCA4
Image credit: cdc.gov
40

## Slide 41
Floodplain
Projected Change in Precipitation by 2050
Addition of Policy-Relevant Data Layers / Indices
EnviroAtlas
NASA/NEX project
Combined Climate Indicators
41

## Slide 42
Addition of Policy-Relevant Data Layers / Indices
Figure courtesy of J. Kelly
Combined Climate Indicators
42

## Slide 43
Addition of Policy-Relevant Data Layers / Indices
Figure courtesy of J. Kelly
Combined Climate Indicators
43

## Slide 44: Appendix B
New Air Toxics Metrics
44

## Slide 45: NEXUS Updates: New Air Toxics Metrics
Risk:
□ Cancer Risk (max tract-level risk in the county): (default checked)
o Top risk Percentile (higher than x%) 90 (Note: default checked)
o Risk value (x-in-1 million) ? (Note: use 90 %tile risk value)
□ Non-cancer Hazard (max tract-level HI in the county):
o Top risk Percentile (higher than x%) 90 (default if above box checked)
o Hazard Index (HI) ? (Note: use 90 %tile value, find a reasonable range)
(Note: Add up all “HI” in “NATA_2014_Tract_HIs_FINAL” file.
“HI” > 1 means likely adverse non-cancer hazard; <1 means unlikely
Current
New
Cancer Risk (max tract-level risk in the county):
□ PM & Metal HAPs
Pollutant: All
○ Top risk percentile (higher > %) 90
○ Risk value (x-in-1 million) ?
□ Gas & VOC HAPs
Pollutant: All
○ Top risk Percentile (higher > %) 90
○ Risk value (x-in-1 million) ?
[ ] Advanced Options:
45

## Slide 46: Appendix C
Continuation of Slide 12
46

## Slide 47: CBSA Name: Chicago-Joliet-Naperville, IL-IN-WI. Population: 9452622
Facility name: US STEEL GARY WORKS County/City/State: Lake/Gary/IN EIS_ID: 8192011 Sector Group: Petroleum Refining NAICS code: 324199 NAICS description: All Other Petroleum and Coal Products Manufacturing | 3089 | Facility name: ArcelorMittal USA LLC County/City/State: Lake/East Chicago/IN EIS_ID: 3986611 Sector Group: Iron and Steel Production NAICS code: 331110 NAICS description: Iron and Steel Mills and Ferroalloy Manufacturing | 2274 | Facility name: Ford Motor Co County/City/State: Cook/Chicago/IL EIS_ID: 7317011 Sector Group: Transportation Equipment Auto and Light Duty Truck NAICS code: 336111 NAICS description: Automobile Manufacturing | 297409 | Facility name: WISCONSIN ELECTRIC POWER COMPANY D/B/A WE ENERGIES-PLEASANT PRAIRIE POWER PLANT County/City/State: Kenosha/Pleasant Prairie/WI EIS_ID: 7509411 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 6703669.7
Facility name: ARCELORMITTAL USA LLC County/City/State: Lake/East Chicago/IN EIS_ID: 3986511 Sector Group: Iron and Steel Production NAICS code: 331110 NAICS description: Iron and Steel Mills and Ferroalloy Manufacturing | 2868 | Facility name: Northern Indiana Public Service Company LLC - RM Schahfer Generating Station County/City/State: Jasper/Wheatfield/IN EIS_ID: 7957011 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 1706 | Facility name: Ingredion Inc County/City/State: Cook/Bedford Park/IL EIS_ID: 946411 Sector Group: Food Products Manufacturing NAICS code: 311221 NAICS description: Wet Corn Milling | 225917 | Facility name: Northern Indiana Public Service Company LLC - RM Schahfer Generating Station County/City/State: Jasper/Wheatfield/IN EIS_ID: 7957011 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 6492832.9
Facility name: WISCONSIN ELECTRIC POWER COMPANY D/B/A WE ENERGIES-PLEASANT PRAIRIE POWER PLANT County/City/State: Kenosha/Pleasant Prairie/WI EIS_ID: 7509411 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 2128 | Facility name: BP Products North America Inc Whiting R County/City/State: Lake/Whiting/IN EIS_ID: 7247711 Sector Group: Petroleum Refining NAICS code: 32411 NAICS description: Petroleum Refineries | 1619 | Facility name: ArcelorMittal Burns Harbor LLC County/City/State: Porter/Burns Harbor/IN EIS_ID: 7376511 Sector Group: Coke Ovens NAICS code: 331110 NAICS description: Iron and Steel Mills and Ferroalloy Manufacturing | 214217 | Facility name: Dynegy Kendall Energy LLC County/City/State: Kendall/Minooka/IL EIS_ID: 9692211 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 2943248.8
Facility name: BP Products North America Inc Whiting R County/City/State: Lake/Whiting/IN EIS_ID: 7247711 Sector Group: Petroleum Refining NAICS code: 32411 NAICS description: Petroleum Refineries | 1440 | Facility name: Exxon Mobil Oil Corp County/City/State: Will/Channahon/IL EIS_ID: 7360711 Sector Group: Petroleum Refining NAICS code: 324110 NAICS description: Petroleum Refineries | 1570 | Facility name: Exxon Mobil Oil Corp County/City/State: Will/Channahon/IL EIS_ID: 7360711 Sector Group: Petroleum Refining NAICS code: 324110 NAICS description: Petroleum Refineries | 163903 | Facility name: Exxon Mobil Oil Corp County/City/State: Will/Channahon/IL EIS_ID: 7360711 Sector Group: Petroleum Refining NAICS code: 324110 NAICS description: Petroleum Refineries | 2663474.1
Facility name: Northern Indiana Public Service Company LLC - Bailly Generating Station County/City/State: Porter/Chesterton/IN EIS_ID: 7376611 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 1169 | Facility name: Ingredion Inc County/City/State: Cook/Bedford Park/IL EIS_ID: 946411 Sector Group: Food Products Manufacturing NAICS code: 311221 NAICS description: Wet Corn Milling | 1463 | Facility name: Dart Container Corp of Illinois County/City/State: Kane/North Aurora/IL EIS_ID: 2603711 Sector Group: Foam Manufacturing NAICS code: 326140 NAICS description: Polystyrene Foam Product Manufacturing | 134077 | Facility name: Waukegan Electric Generating Station County/City/State: Lake/Waukegan/IL EIS_ID: 7792311 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 2228899.2
Facility name: Exxon Mobil Oil Corp County/City/State: Will/Channahon/IL EIS_ID: 7360711 Sector Group: Petroleum Refining NAICS code: 324110 NAICS description: Petroleum Refineries | 1160 | Facility name: Waukegan Electric Generating Station County/City/State: Lake/Waukegan/IL EIS_ID: 7792311 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 931 | Facility name: Equistar Chemicals LP County/City/State: Grundy/Morris/IL EIS_ID: 8209311 Sector Group: Consumer Products (Cleaning, Photographic, etc.) NAICS code: 325998 NAICS description: All Other Miscellaneous Chemical Product and Preparation Manufacturing | 132087 | Facility name: Northern Indiana Public Service Company LLC - Bailly Generating Station County/City/State: Porter/Chesterton/IN EIS_ID: 7376611 Sector Group: Electric Utilities NAICS code: 221112 NAICS description: Fossil Fuel Electric Power Generation | 2120968.6
47

## Slide 48: Appendix D
Continuation of Slide 13
48

## Slide 49
Asphalt Products Manufacturing | 917 | 1211 | 929 | 479267 | 2470 | 359866 | 389
Mining Activities | 860 | 3247 | 2090 | 478466 | 3527 | 2184543 | 120
Waste Treatment and Disposal | 640 | 2452 | 579 | 663971 | 5997 | 1901478 | 235
Construction and Related Industries | 580 | 2640 | 303 | 192543 | 3476 | 5161735 | 85
Polymers and Resins Production | 504 | 6810 | 1506 | 7153761 | 2487 | 4612128 | 104
Commercial Sterilization | 434 | 2222 | 305 | 155006 | 1090 | 1260938 | 115
Business Activities | 382 | 5055 | 627 | 761149 | 7101 | 3506488 | 99
Fibrous Minerals Production | 295 | 332 | 856 | 356831 | 1963 | 426975 | 58
Metal Fabrication | 293 | 1715 | 596 | 1239127 | 26233 | 757296 | 50
Wholesale and Retail Trade | 179 | 1305 | 531 | 2136286 | 4275 | 475685 | 52
Textiles and Apparel Manufacturing | 149 | 359 | 190 | 335731 | 300 | 74258 | 30
Iron and Steel Foundries | 143 | 578 | 1480 | 211778 | 23234 | 553631 | 82
Government (non-Defense) | 90 | 1927 | 856 | 232383 | 3357 | 662687 | 70
Building Products Manufacturing | 80 | 747 | 449 | 349973 | 5188 | 455439 | 11
Transportation Equipment Aerospace Industry | 45 | 735 | 106 | 671151 | 6357 | 214916 | 1
Agriculture and Forest Products (Not Specified) | 44 | 55 | 55 | 8973 | 48 | 177 | 25
“Sector group” emissions combined for all 50 CBSAs (based on top 20 facility emissions in each CBSA); Total Population: 134,940,816 |  |  |  |  |  |  |  | 
Sector Group | SO2 (TON) | NOx (TON) | PM2.5 (TON) | Gas_VOC_HAPs (LB) | Heavy_Metal_HAPs (LB) | CO2e (TON) | SO2 Score (freq. & rank) | 
49