## Slide 1: “NEXUS” Multi-Pollutant Analysis Tool Development: Status Update
HEID/AQAD Briefing
April 12, 2021
Carey Jang & Beth Landis
Data Viewer Module
Data Input Module
Data Query Module
“NEXUS 1.5” available on OAQPS’s Shared Drive at: “G:\SHARE\NEXUS\NEXUS 1.5\”
or at EPA’s new FTP site: ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/

## Slide 2: Overview
Feedback from OAQPS/SMT Briefing
NEXUS Updates
  Metrics (Toxics)
  2017 Data
Ranking of Highest Risk Areas
Examples: NEXUS use for MP & EJ purposes within areas
  Region 5 – Chicago
  Region 6 – Houston
  Region 3 - Pittsburgh
  NAA – Atlanta
  Advance Area – Louisville
Developing a Multi-pollutant Proximity Based Module
Next Steps / Issues for Discussion
2

## Slide 3: Feedback from OAQPS & SMT Briefing
Improve the national screening metrics for air toxics to reduce possible ‘false-negatives’
Augment current “area” orientation of tool to provide national and area-specific screening capabilities for sectors in multi-pollutant context
Within high-risk areas, provide multi-pollutant proximity-based screening capabilities for sources/sectors so accounts for both criteria and toxic pollutants
Incorporate Economic information?
3

## Slide 4: NEXUS 1.7 (Under Development)
Near-term Priorities for 2021 NEXUS development:
Upgrade NEXUS (metrics/EJ indicators) for EPA beta testing
  Revising national air toxic (AT) metrics based on AT team’s suggestions
  Include EJ/demographic index from EJSCREEN & Tribal areas
2017 emissions data update (including GHG & Sector mapping)
2017 AQ concentrations (PM2.5, O3, AT) & risk data update (note: separate discussion on air toxics risk effort with SMT)
Draft design for new Multi-pollutant based “Proximity analysis” module for EJ and related considerations (at census tract and block level)
Ongoing
Planned
4

## Slide 5: Need to Improve Air Toxics Metrics
MP Team engaged with Air Toxics Team to improve upon current national screening metrics for air toxics
Current risk metrics were based on county-level population weighted averages (not appropriately accounting for local nature of risks) so false negatives could influence the areas ranking
ATAG provided input on improving these metrics
  New metrics now reflect more local risk estimates (at census-tract level) and expressed in “X in a million”
  Update use of percentiles based on risk value
5

## Slide 6: NEXUS Updates: New Air Toxics Metrics
Current
Updated
6

## Slide 7: Regional Engagement: Highest MP Risk Areas
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
1 | EPA Region 5 | IL-IN-WI | Chicago-Joliet-Naperville, IL-IN-WI | 1
2 | EPA Region 3 | PA | Pittsburgh, PA | 1
3 | EPA Region 6 | TX | Houston-Sugar Land-Baytown, TX | 1
4 | EPA Region 9 | CA | Los Angeles-Long Beach-Santa Ana, CA | 2
5 | EPA Region 6 | TX | Dallas-Fort Worth-Arlington, TX | 2
6 | EPA Region 4 | GA | Atlanta-Sandy Springs-Marietta, GA | 3
7 | EPA Region 4 | FL | Tampa-St. Petersburg-Clearwater, FL | 3
8 | EPA Region 4 | AL | Birmingham-Hoover, AL | 3
9 | EPA Region 9 | AZ | Phoenix-Mesa-Glendale, AZ | 3
10 | EPA Region 9 | CA | Fresno, CA | 3
11 | EPA Region 2 | NY-NJ-PA | New York-Northern New Jersey-Long Island, NY-NJ-PA | 3
12 | EPA Region 5 | OH | Cleveland-Elyria-Mentor, OH | 3
13 | EPA Region 9 | CA | Sacramento--Arden-Arcade--Roseville, CA | 4
14 | EPA Region 9 | NV | Las Vegas-Paradise, NV | 4
15 | EPA Region 4 | NC-SC | Charlotte-Gastonia-Rock Hill, NC-SC | 5
16 | EPA Region 9 | CA | San Diego-Carlsbad-San Marcos, CA | 5
17 | EPA Region 5 | MI | Detroit-Warren-Livonia, MI | 5
18 | EPA Regions 5 & 7 | MO-IL | St. Louis, MO-IL | 5
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
19 | EPA Region 5 | MI | Grand Rapids-Wyoming, MI | 6
20 | EPA Region 4 | TN | Nashville-Davidson--Murfreesboro--Franklin, TN | 6
21 | EPA Region 9 | CA | Bakersfield-Delano, CA | 6
22 | EPA Regions 2 & 3 | PA-NJ-DE-MD | Philadelphia-Camden-Wilmington, PA-NJ-DE-MD | 6
23 | EPA Region 9 | CA | Riverside-San Bernardino-Ontario, CA | 6
24 | EPA Region 4 | FL | Miami-Fort Lauderdale-Pompano Beach, FL | 6
25 | EPA Region 6 | LA | Baton Rouge, LA | 7
26 | EPA Region 6 | TX | El Paso, TX | 7
27 | EPA Region 10 | WA | Seattle-Tacoma-Bellevue, WA | 7
28 | EPA Region 4 & 5 | KY-IN | Louisville-Jefferson County, KY-IN | 7
29 | EPA Region 8 | CO | Denver-Aurora-Broomfield, CO | 8
30 | EPA Region 3 | PA | Reading, PA | 8
31 | EPA Region 9 | CA | Visalia-Porterville, CA | 8
32 | EPA Region 1 | CT | Bridgeport-Stamford-Norwalk, CT | 8
33 | EPA Region 4 & 6 | TN-MS-AR | Memphis, TN-MS-AR | 8
34 | EPA Regions 2 & 3 | PA-NJ | Allentown-Bethlehem-Easton, PA-NJ | 9
35 | EPA Region 6 | LA | New Orleans-Metairie-Kenner, LA | 9
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. OAQPS could provide area profile packets to Regions to discuss nature of MP issues and possible avenues to address or conduct more refined analyses.
The information above was generated in NEXUS & exported into Excel where rankings were applied.
These CBSAs include at least one county that meets ALL the following criteria:
PM Mortality Number Percentile >= 90
O3 Mortality Number Percentile >= 90
Cancer Risk Rate Max Percentile >= 90 (max census tract-level in a county)
7

## Slide 8: Region 5 Example—Chicago CBSA
8
Generated in NEXUS

## Slide 9: Chicago CBSA: Top Emission Sources
9
Generated in NEXUS

## Slide 10: Chicago CBSA: US Steel Gary Works & EJ Screening
Demographic Index
People of Color Population
Low Income
National Percentiles
10
Generated in NEXUS
Generated in EJSCREEN
Generated in EJSCREEN
Generated in EJSCREEN

## Slide 11: Region 6 Example – Houston CBSA
11
Generated in NEXUS

## Slide 12: Houston CBSA: Top Emission Sources
12
Generated in NEXUS

## Slide 13: Houston CBSA: Baytown Chemical Plant & Refinery
National Percentiles
Baytown Refinery (Petroleum)
Baytown Olefins Plant (Chemical Plant)
Demographic Index
People of Color Population
Low Income
13
Generated in NEXUS
Generated in EJSCREEN
Generated in EJSCREEN
Generated in EJSCREEN

## Slide 14: Region 3 Example - Pittsburgh CBSA
14
Generated in NEXUS

## Slide 15: Pittsburgh CBSA: Top Emission Sources
EGUs
15
Generated in NEXUS

## Slide 16: Pittsburgh CBSA: Dominated by EGUs
16
Generated in NEXUS

## Slide 17: Pittsburgh CBSA: EJ Concerns
National Percentiles
Demographic Index
People of Color Population
Low Income
Generated in EJSCREEN
Generated in EJSCREEN
Generated in EJSCREEN
Generated in NEXUS
No major sources in the downtown area where EJ indicators are highest. Could transport play a role??
17

## Slide 18: Pittsburgh CBSA: EJ Concerns
Lincoln Park community top 95-100% for demographic index, people of color & low income. Could they be impacted by transport? Predominate winds from NW/W/SW. There are facilities upwind…
Generated in EJSCREEN
Generated in NEXUS
Generated in MRCC’s Application Tools Environment (cli-MATE)
Generated in EJSCREEN
18

## Slide 19: Pittsburgh CBSA: Potential Impacts to Lincoln Park Community
Lincoln Park
Backtrajectory passes right over W.H. Sammis Plant (EGU) in Ohio..
Generated in NOAA’s HYSPLIT
Generated in NEXUS
19

## Slide 20: Pittsburgh CBSA: W.H. Sammis Plant EGU
Sammis Plant (EGU) is a top NOx & VOC emitter for the area. Could it lead to higher concentrations of O3 downwind in the Lincoln Park Community?
20

## Slide 21: NAA Example - Atlanta
The maps above were generated for the Atlanta CBSA (2014 O3 NAA), using the data query module. The top 10 Gas & VOC HAPS emission sources are plotted.
21

## Slide 22: NAA Example - Atlanta
NEXUS can be used to identify top emission sources. Information above was generated in Data Query for the Atlanta CBSA. This can help identify the potential co-benefits of controls.
22

## Slide 23: ADVANCE Example - Louisville
The map above was generated for the Louisville/Jefferson County - Elizabethtown - Madison, KY-IN CBSA (2014 O3 NAA), using the data query module. The top 10 Gas & VOC HAPS emission sources are identified.
23

## Slide 24: ADVANCE Example - Louisville
2 of the top 4 NOx emission sources outside Jefferson County, KY (Jefferson County, IN & Tremble, KY)
24

## Slide 25: ADVANCE Example - Louisville
Top 2 VOC emission sources are in Nelson County, KY
25

## Slide 26: ADVANCE Example - Louisville
2 of the top 4 gas & VOC HAPs emission sources in Indiana (Harrison & Clark County)
26

## Slide 27: MP Proximity Analysis Example – Developing Capabilities
EJSCREEN Low Income Population
AK Steel
US Steel
NEXUS is used to quickly identify top emitters of NOx, SO2, PM2.5, and heavy-metal HAPs near elevated demographic index and has developing proximity capability
EJSCREEN Demographic Index
AK Steel
US Steel
27

## Slide 28: MP Proximity Analysis Example – Developing Capabilities
28

## Slide 29: “Zoom-out” of Selected Facility to Sector Group at National Level
Display all facilities within same Sector Group
Provide color scale for MP risk value (e.g., red w/ high MP risk)
Allow to “zoom-in” to individual facilities to conduct proximity analysis (i.e., back to “proximity module”)
29

## Slide 30: Next Steps / Issues for Discussion
Next Steps
  Updating existing data to 2017
    Emissions, O3/PM2.5/Toxics concentration, O3 and PM2.5 risk
  Add new information
    Tribal areas, Advance areas, GHG emissions, monitoring data
  Develop MP proximity analysis module for areas
    MP risk in context of EJ (and can incorporate climate considerations)
  Follow up with additional EJ discussions/connection with EJSCREEN?
  Meeting with economics group
Issues for Discussion
  2017 Air Toxics Risk Data (to be topic of AT-DAT meeting with ATC)
  OAQPS review/prioritization of analytical tools
  Funding mechanism
30

## Slide 31: Questions?
31

## Slide 32: Appendix A
Example Proximity Analysis Table
32

## Slide 33: Screening Proximity Analysis in NEXUS: Tabular Data Summary
Facility: American Synthesis Rubber Co., Louisville, KY Sector Group: Polymers and Resins Production Top Risk Drivers: ETO, Formaldehyde (examples) |  |  |  |  | Selected Options: Radius of Impact: 10km Number of CBSAs: 25 (top MP risk ranking) Air Toxics Risk threshold: 10 (“x”-in-a million) |  |  | 
 | Within Radius of Facility | County Avg. | State Avg. | EPA Region Avg. |  | Nation Avg. | Sector Group (within radius) National avg. | Sector Group (within radius) Top 25 CBSAs
Population total | x,xxx | xx,xxx | xxx,xxx | xxx,xxx |  | 317,xxx,xxx | xxx,xxx | xxx,xxx
PM2.5 risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Ozone risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Air Toxics risk: Cancer risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Cancer risk value (“x”-in-a million)) | x.x | x.x | x.x | x.x |  | x.x | x.x | x.x
Cancer risk value above selected threshold (population %tile) | x% | x% | x% | x% |  | x% | x% | x%
Non-cancer risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Non-cancer risk (Hazard Index) | x.x | x.x | x.x | x.x |  | x.x | x.x | x.x
Climate risks: Flood (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Sea level rise (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Fire (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Disease (%tile) | x% | x% | x% | x% |  | x% | x% | x%
EJ/Demographics: Minority group (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Low-income group (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Demographic Index (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Linguistic Isolation (%tile) | x% | x% | x% | x% |  | x% |  | x%
33

## Slide 34: Appendix B
NEXUS Sector Ranking within Highest Risk Areas
34

## Slide 35: MP Ranking: CBSAs w/ Top-Ranked MP Risks
Method: Identify CBSAs with top MP risk ranking: Major CBSAs are selected.
35
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
1 | EPA Region 5 | IL-IN-WI | Chicago-Joliet-Naperville, IL-IN-WI | 1
2 | EPA Region 3 | PA | Pittsburgh, PA | 1
3 | EPA Region 6 | TX | Houston-Sugar Land-Baytown, TX | 1
4 | EPA Region 9 | CA | Los Angeles-Long Beach-Santa Ana, CA | 2
5 | EPA Region 6 | TX | Dallas-Fort Worth-Arlington, TX | 2
6 | EPA Region 4 | GA | Atlanta-Sandy Springs-Marietta, GA | 3
7 | EPA Region 4 | FL | Tampa-St. Petersburg-Clearwater, FL | 3
8 | EPA Region 4 | AL | Birmingham-Hoover, AL | 3
9 | EPA Region 9 | AZ | Phoenix-Mesa-Glendale, AZ | 3
10 | EPA Region 9 | CA | Fresno, CA | 3
11 | EPA Region 2 | NY-NJ-PA | New York-Northern New Jersey-Long Island, NY-NJ-PA | 3
12 | EPA Region 5 | OH | Cleveland-Elyria-Mentor, OH | 3
13 | EPA Region 9 | CA | Sacramento--Arden-Arcade--Roseville, CA | 4
14 | EPA Region 9 | NV | Las Vegas-Paradise, NV | 4
15 | EPA Region 4 | NC-SC | Charlotte-Gastonia-Rock Hill, NC-SC | 5
16 | EPA Region 9 | CA | San Diego-Carlsbad-San Marcos, CA | 5
17 | EPA Region 5 | MI | Detroit-Warren-Livonia, MI | 5
18 | EPA Regions 5 & 7 | MO-IL | St. Louis, MO-IL | 5
19 | EPA Region 5 | MI | Grand Rapids-Wyoming, MI | 6
20 | EPA Region 4 | TN | Nashville-Davidson--Murfreesboro--Franklin, TN | 6
21 | EPA Region 9 | CA | Bakersfield-Delano, CA | 6
22 | EPA Regions 2 & 3 | PA-NJ-DE-MD | Philadelphia-Camden-Wilmington, PA-NJ-DE-MD | 6
23 | EPA Region 9 | CA | Riverside-San Bernardino-Ontario, CA | 6
24 | EPA Region 4 | FL | Miami-Fort Lauderdale-Pompano Beach, FL | 6
25 | EPA Region 6 | LA | Baton Rouge, LA | 7
26 | EPA Region 6 | TX | El Paso, TX | 7
27 | EPA Region 10 | WA | Seattle-Tacoma-Bellevue, WA | 7
28 | EPA Region 4 & 5 | KY-IN | Louisville-Jefferson County, KY-IN | 7
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
29 | EPA Region 8 | CO | Denver-Aurora-Broomfield, CO | 8
30 | EPA Region 3 | PA | Reading, PA | 8
31 | EPA Region 9 | CA | Visalia-Porterville, CA | 8
32 | EPA Region 1 | CT | Bridgeport-Stamford-Norwalk, CT | 8
33 | EPA Region 4 & 6 | TN-MS-AR | Memphis, TN-MS-AR | 8
34 | EPA Regions 2 & 3 | PA-NJ | Allentown-Bethlehem-Easton, PA-NJ | 9
35 | EPA Region 6 | LA | New Orleans-Metairie-Kenner, LA | 9
36 | EPA Region 4 | NC | Greensboro-High Point, NC | 10
37 | EPA Region 4 | AL | Mobile, AL | 10
38 | EPA Region 4 | TN-GA | Chattanooga, TN-GA | 11
39 | EPA Region 4 | TN | Knoxville, TN | 11
40 | EPA Region 3 | DC-VA-MD-WV | Washington-Arlington-Alexandria, DC-VA-MD-WV | 11
41 | EPA Region 6 | OK | Tulsa, OK | 11
42 | EPA Region 9 | AZ | Tucson, AZ | 11
43 | EPA Region 4 | SC | Charleston-North Charleston-Summerville, SC | 12
44 | EPA Region 4 | SC | Greenville-Mauldin-Easley, SC | 12
45 | EPA Region 3 | WV | Charleston, WV | 13
46 | EPA Region 4 | SC | Spartanburg, SC | 13
47 | EPA Region 4 | NC | Winston-Salem, NC | 13
48 | EPA Region 4 | FL | Lakeland-Winter Haven, FL | 13
49 | EPA Region 5 | OH | Akron, OH | 13
50 | EPA Region 6 | TX | Beaumont-Port Arthur, TX | 14
51 | EPA Region 5 | MI | Lansing-East Lansing, MI | 14
52 | EPA Region 4 | FL | Orlando-Kissimmee-Sanford, FL | 14
53 | EPA Region 10 | OR | Eugene-Springfield, OR | 14
54 | EPA Region 9 | NV | Reno-Sparks, NV | 14
55 | EPA Regions 4 & 5 | OH-KY-IN | Cincinnati-Middletown, OH-KY-IN | 14
56 | EPA Region 3 | PA | Lancaster, PA | 14

## Slide 36: Sectors Most Prevalent in Highest Risk Areas
“Sector group” emissions combined for all 50 Highest Risk Ranked CBSAs Total Population: 134,940,816 |  |  |  |  |  |  |  | 
Sector Group | SO2 (TON) | NOx (TON) | PM2.5 (TON) | Gas_VOC_HAPs (LB) | Heavy_Metal_HAPs (LB) | CO2e (TON) | SO2 Score (freq. & rank) | 
Electric Utilities | 276526 | 195865 | 25828 | 6432707 | 127030 | 485754073 | 2014 | 
Petroleum Refining | 52943 | 40169 | 12438 | 10295621 | 99736 | 95097998 | 574 | 
Coke Ovens | 22405 | 15473 | 5158 | 1787622 | 29716 | 14570119 | 132 | 
Pesticides and Agricultural Chemical Manufacturing | 17644 | 5861 | 1292 | 1627958 | 1788 | 18233480 | 153 | 
Inorganic Chemical Manufacturing | 14522 | 7273 | 1405 | 1073205 | 48966 | 5231826 | 190 | 
Mineral Processing | 13714 | 12628 | 1659 | 886251 | 33740 | 8364046 | 256 | 
Iron and Steel Production | 10679 | 13345 | 5691 | 858984 | 110757 | 33030868 | 375 | 
Cement Manufacturing | 10566 | 44083 | 5007 | 1472498 | 25010 | 27859268 | 444 | 
Air Transportation | 8127 | 63035 | 2685 | 10417526 | 122777 | 18485627 | 1380 | 
Pulp and Paper Industry | 7413 | 9791 | 2779 | 7227413 | 23704 | 10517197 | 251 | 
Organic Chemical Manufacturing | 6240 | 38070 | 6254 | 10280694 | 20059 | 82521408 | 299 | 
Landfills | 2952 | 9872 | 2356 | 2799470 | 1880 | 28651639 | 563 | 
Consumer Products (Cleaning, Photographic, etc.) | 2815 | 1980 | 486 | 1363144 | 1724 | 1389978 | 66 | 
Oil and Gas Production and Distribution | 2717 | 28271 | 2259 | 4467061 | 1804 | 12342771 | 466 | 
Food Products Manufacturing | 2705 | 6197 | 3085 | 4110212 | 2496 | 3408089 | 327 | 
Non-Ferrous Metals Production | 2694 | 3511 | 1695 | 3663067 | 91643 | 2165692 | 212 | 
Glass Manufacturing | 2355 | 5832 | 953 | 92289 | 9990 | 1174855 | 210 | 
Clay Products Manufacturing | 1349 | 685 | 602 | 650323 | 1631 | 200293 | 311 | 
Waste Incineration | 1024 | 11872 | 483 | 679918 | 1801 | 9825913 | 189 | 
Method: Highest emitting sectors within top ranked 50 CBSAs (Note: Facilities are grouped based on “Sector definition” spreadsheet created by Marc H. & SPPD)*
36
*Appendix contains graphics with sector ranking by pollutants

## Slide 37: SO2 & NOx: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Chart: Total SO2 & NOx emissions (tpy) from top Sector groups
| Electric Utilities | Petroleum Refining | Coke Ovens | Pesticides and Agricultural Chemical Manufacturing | Inorganic Chemical Manufacturing | Mineral Processing | Iron and Steel Production | Cement Manufacturing | Air Transportation | Pulp and Paper Industry | Organic Chemical Manufacturing | Landfills | Consumer Products (Cleaning, Photographic, etc.) | Oil and Gas Production and Distribution | Food Products Manufacturing | Non-Ferrous Metals Production | Glass Manufacturing | Clay Products Manufacturing | Waste Incineration | Asphalt Products Manufacturing | Mining Activities
SO2 | 276526.3062 | 52943.1734 | 22404.8065 | 17644.0804 | 14521.6033 | 13714.4318 | 10678.7031 | 10566.429 | 8126.8388 | 7412.9793 | 6239.8283 | 2952.1673 | 2814.5235 | 2716.7565 | 2704.9001 | 2693.8076 | 2354.6044 | 1348.7497 | 1024.3245 | 917.4123 | 860.1116
NOx | 195864.5328 | 40168.8675 | 15472.6338 | 5861.2174 | 7272.8804 | 12628.2753 | 13345.4622 | 44083.4072 | 63034.7835 | 9790.7401 | 38070.4692 | 9872.4188 | 1980.2363 | 28271.167 | 6197.3419 | 3510.7028 | 5832.2555 | 684.7521 | 11871.941 | 1211.0917 | 3246.8551
over
37

## Slide 38: Primary PM2.5: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Chart: 
| Electric Utilities | Petroleum Refining | Organic Chemical Manufacturing | Iron and Steel Production | Coke Ovens | Cement Manufacturing | Food Products Manufacturing | Pulp and Paper Industry | Air Transportation | Landfills | Oil and Gas Production and Distribution | Mining Activities | Non-Ferrous Metals Production | Mineral Processing | Polymers and Resins Production | Iron and Steel Foundries | Inorganic Chemical Manufacturing | Pesticides and Agricultural Chemical Manufacturing | Glass Manufacturing | Asphalt Products Manufacturing | Government (non-Defense)
PM2.5 (TON) | 25827.9863 | 12437.633 | 6254.3809 | 5690.8713 | 5158.3213 | 5007.4356 | 3084.5061 | 2778.9607 | 2684.9839 | 2356.4402 | 2258.6926 | 2089.5651 | 1695.4921 | 1659.0549 | 1505.6629 | 1480.2527 | 1404.6369 | 1292.0852 | 953.2937 | 928.9664 | 856.4677
over
Primary PM2.5 emissions (ton/yr) from top Sector groups
38

## Slide 39: Gas & VOC HAPs: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Chart: 
| Air Transportation | Petroleum Refining | Organic Chemical Manufacturing | Pulp and Paper Industry | Polymers and Resins Production | Plastic and Metal Parts Manufacturing | Electric Utilities | Oil and Gas Production and Distribution | Food Products Manufacturing | Non-Ferrous Metals Production | Landfills | Transportation Equipment Auto and Light Duty Truck | Wholesale and Retail Trade | Coke Ovens | Transportation Equipment Ship/Boat Building & Repair | Pesticides and Agricultural Chemical Manufacturing | Cement Manufacturing | Consumer Products (Cleaning, Photographic, etc.) | Metal Fabrication | Inorganic Chemical Manufacturing | Petroleum Products Distribution
Gas_VOC_HAPs (LB) | 10417526.399 | 10295620.989 | 10280694.057 | 7227413.2437 | 7153760.6784 | 6573090.6333 | 6432706.8109 | 4467061.335 | 4110211.5326 | 3663066.9479 | 2799469.9445 | 2602184.4014 | 2136286.2907 | 1787622.2229 | 1769261.2721 | 1627958.0555 | 1472497.6393 | 1363143.832 | 1239126.7811 | 1073204.5379 | 1057320.5515
Gas & VOC HAPs emissions (lb/yr) from top Sector groups
39

## Slide 40: Heavy Metal HAPs: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Heavy HAPs emissions (lb/yr) from top Sector groups
Chart: 
| Electric Utilities | Air Transportation | Iron and Steel Production | Petroleum Refining | Non-Ferrous Metals Production | Inorganic Chemical Manufacturing | Transportation Equipment Auto and Light Duty Truck | Mineral Processing | Coke Ovens | Metal Fabrication | Cement Manufacturing | Pulp and Paper Industry | Iron and Steel Foundries | Organic Chemical Manufacturing | Glass Manufacturing | Transportation Equipment Ship/Boat Building & Repair | Business Activities | Transportation Equipment Aerospace Industry | Waste Treatment and Disposal | Building Products Manufacturing | Plastic and Metal Parts Manufacturing
Heavy_Metal_HAPs (LB) | 127029.7646 | 122776.7046 | 110756.807 | 99736.2364 | 91643.1076 | 48966.3979 | 36095.3706 | 33740.1057 | 29716.3211 | 26233.0074 | 25009.7078 | 23704.0343 | 23233.7697 | 20059.4486 | 9990.1173 | 7759.171 | 7100.5414 | 6357.3919 | 5996.8864 | 5187.5464 | 4799.6812
40

## Slide 41: CO2e: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Chart: CO2e emissions (ton/yr) from top Sector groups
| Electric Utilities | Petroleum Refining | Organic Chemical Manufacturing | Iron and Steel Production | Landfills | Cement Manufacturing | Air Transportation | Pesticides and Agricultural Chemical Manufacturing | Coke Ovens | Oil and Gas Production and Distribution | Pulp and Paper Industry | Waste Incineration | Mineral Processing | Inorganic Chemical Manufacturing | Construction and Related Industries | Polymers and Resins Production | Business Activities | Food Products Manufacturing | Mining Activities | Non-Ferrous Metals Production | Waste Treatment and Disposal
CO2e (TON) | 485754073.3999 | 95097997.6137 | 82521408.4743 | 33030867.612 | 28651639.0371 | 27859267.6207 | 18485626.9882 | 18233480.213 | 14570119.2452 | 12342770.6501 | 10517197.2191 | 9825912.883 | 8364045.7709 | 5231826.336 | 5161734.6426 | 4612128.3752 | 3506487.8326 | 3408089.4849 | 2184543.3443 | 2165692.0817 | 1901478.423
over
41