## Slide 1: “NEXUS 2.3”: Quick Tutorial
Download “NEXUS” tool: The “NEXUS 2.3” package (“NEXUS 2.3 Setup.exe” & “NEXUS 2.3 Data.exe”: run both “*.exe” files to install) can be downloaded at EPA’s new FTP site:
https://gaftp.epa.gov/aqmg/cjang/NEXUS/MP_Team/NEXUS 2.3/*
Note: Require software installation privilege or “Power Broker” (limited elevated privilege) to install “NEXUS tool” at EPA’s PC; Check “This PC\Documents\My NEXUS files\data\* (\tool\*, \result\*)” to see if NEXUS program & input dataset are installed successfully
1

## Slide 2: NEXUS Tool: On-line User’s Manual
Click “book” icon to launch “User’s manual”
2
Hot link to User’s manual’s “Data Viewer” chapter (same for “Data Input” module & “Data Query” model)

## Slide 3: NEXUS Tool: Data Viewer Module
Select & adjust “Ambient” or “Risk” levels
“Advanced Option”: provide HAPs & species selections
Click “File” to open or save a project
Switch between 3 key modules
NEXUS project file name
3
Select desired ambient data (DV) year (2013-2020)

## Slide 4: Data Viewer: “Apply” New Selections
New selections will appear in “Slider bars” panel and map display
“Apply” new selections
“Check” boxes to add/remove selections
“Slider bars” allow to select & adjust “Ambient” and/or “Risk” threshold levels to display corresponding color map
4

## Slide 5: NEXUS Update: New EJ Metric and Data
5
New EJ/Demographic metric is displayed with “green dash” for counties exceeding selected threshold

## Slide 6: Data Viewer: “Reset” New Selections
6
“Reset” new selections
default configuration
risk-based
risk-based in %tile

## Slide 7: Data Viewer Module: Map Layers menu
7
“Map Layers” menu: Provide (show/hide) map overlaps of various areas, AQ metrics and boundary lines
Click “X” to close “Map Layers” menu

## Slide 8: Data Viewer Module: Configure Base Map & Color
“Base Map” menu: Change boundary lines and background map (e.g., “Google Map”)
Click “color map” to change color & transparency
“Right-click” map to save map image
8

## Slide 9: Data Viewer Module: MP Risk Ranking
“CBSA Risk Ranking”: provide MP risk ranking by CBSA or County
9

## Slide 10: Data Viewer: “Region Selection”
Allow to select “EPA regions”, “States”, or “CBSA”
10

## Slide 11: Data Viewer: Select EPA Region/State/CBSA
Examples:
EPA Region 4
State: NC
Louisville CBSA (KY/IN)
11

## Slide 12: Data Viewer: Major Emission Sources
Click “Display Emission Sources” tab (or right-click) to display emission sources and launch new window
Click any “facility” to link & display source location and emitted pollutants information. Same facility emitting various pollutants can be identified with the same highlighted color.

## Slide 13: Data Viewer: Major Emission Sources
Allow to scroll down to CBSA-level (e.g., Durham CH CBSA ) or County-level
Durham CH CBSA
13
Emissions ranking by “color” of circles from red (higher) to blue (lower)

## Slide 14: NEXUS: “Monitoring Data/Site” Module
Monitor Site/Data
14
Click to select monitor site & pollutant
Click to display
AQ trend at monitor site
Click menu (or right-click) to display “Monitor Sites/Data”
Use different symbol to display each pollutant’s “monitoring sites” e.g., PM2.5 (triangle), O3 (star), etc.
AQ trend

## Slide 15: Two ways navigate to Proximity Analysis Module
Or click any facility, monitor site or a county, and then right-click on map and select “Display Proximity Analysis”.
Click menu (or right-click) to display “Proximity Analysis” module

## Slide 16: Proximity Analysis Module: Overlaying Map
“Set up Threshold” panel (similar to Data Viewer module) allows to identity those geographic areas exceeding the selected thresholds.
The AQ Risk/Concentration and EJ indicators configurations provide metric selections to overlay the MP and/or EJ analysis map.
Check (Uncheck) to show (hide) an overlaying map

## Slide 17: Proximity Analysis Module: Overlaying Map
Click “Reset” button to reset all values to default (or to a specified %tile if all indicators are selected in %tile)
Provide a “toggle” choice to select “Risk %tile” or “Risk value”

## Slide 18: Proximity Analysis Module: Legend Configure
Click nay color tile to to config the legend color & transparency

## Slide 19: Proximity Analysis Module: Set the “Radius of Analysis”
Adjust the analysis radius
Click the “Select Location” and select a census tract, a monitor site or a facility in “Select Location” dialog
(b) Or Double-click a facility or monitoring site or a census tract to select proximity analysis center point

## Slide 20: Proximity Analysis Module: Show Detail information
Click a facility or monitoring site or a census tract to show the detail information

## Slide 21: Proximity Analysis Module: Summary Table/Plot
Summary table
Emissions
Summary plot
Select one or more indicators to plot the summary results for selected point within radius, county/CBSA/State/EPA Region and Nation avg.
Support to output the summary table as excel file (*.xlsx)
Set the radius of analysis and the threshold of air toxics to show the summary results for selected point within radius

## Slide 22: Data Viewer: Top “x” Emission Sources
Durham county, NC
22
Provide selection of Facility or Source Category
Provide selection of Facility & Source Category

## Slide 23: NEXUS Update: “Source Category Emissions”
“Source Category Emissions” module provide five source categories, including “Point”, “Non-Point”, “On-Road”, “Non-Eoad”, and “Wvent” emissions for the selected region, CBSA, or county.
For “Non-Point”, including Resident Wood Combustion emissions.
23

## Slide 24: NEXUS Update: “Sector Emissions Summary”
24
“Sector Emission Summary” function allow to select major CBSAs and provides source and sector emissions summary to support “Sector Prioritization” effort

## Slide 25: NEXUS Update: “Sector Emissions Summary”
25
Summary table
Emissions
Frequency & Rank
Summary plot

## Slide 26: Data Viewer: EPA Region Table Generator
“EPA Region Table Generator” provides attainment status of O3 and PM2.5 and their DVs; also allows to select any EPA region based on data updated to 2020.
26

## Slide 27: Data Viewer: Data Search & Filter
Click “+” to add filters; Click “x” to remove current filter;
Click “Output data…” to output current page records or all records
Show specified records per page.
27

## Slide 28: Data Input Module: Data Preview
Click to view data
Click to run & save project
Select a table to view if there are multiple tables in the selected data source file
Check to use filter to query data
“Transparency” & “Open-Source”:
All NEXUS input/output data files are available under:
“This PC\Documents\My NEXUS files\Data (\Result)”
28
Click to change input data file

## Slide 29: Data Query Module: Overlaying Map
Overlaying Map selection
Region Selection
Data Query qualifier selection
Data Query Configuration
29

## Slide 30: Data Query Module: Configure Data Query
“Data Query Filter” allows to select “qualifiers” for query
“Data Query Preview” displays the selected “qualifiers” at the same time
30

## Slide 31: Data Query Module: Attribute Table
Detachable “Attribute Table”
Filter/search/export functions
31

## Slide 32: Data Query Module: Attribute Table
Click a “record” to link and display its location & info.
32

## Slide 33
End
33