## Slide 1: “NEXUS” Multi-Pollutant Analysis Tool Development: Status and Progress
OAQPS Briefing
February 1, 2021
Carey Jang & Beth Landis
Data Viewer Module
Data Input Module
Data Query Module
“NEXUS 1.5” available on OAQPS’s Shared Drive at: “G:\SHARE\NEXUS\NEXUS 1.5\”
or at EPA’s new FTP site: ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
1

## Slide 2: Overview
Multi-Pollutant Background
NEXUS Tool Development
  Expected Use
  Schedule
Key Modules
Benefits of NEXUS to OAQPS
Examples
Discussion & Next Steps
Live Demo
2

## Slide 3: Multi-Pollutant (MP) Background
3
Support a comprehensive, MP treatment of air quality problems to effectively improve air quality and make the most efficient use of available resources
  Primary Goal - identify & evaluate local control strategies targeting emissions of O3 & PM2.5 and their precursors while at the same time reducing Air Toxics of concern for communities to maximize both health benefits and air quality improvements
MP planning has the potential to reduce the costs and increase benefits associated with air quality management (AQM)
Supports S/L/T air agencies in developing MP, risk-based AQM plans and implementing strategies that reduce air pollution emissions & improve public health
Success has been demonstrated in Detroit and SC; another project is currently underway in Louisville, KY (briefed in May 2020)
Tools needed to analyze MP data are either available currently or being developed in OAQPS (NEXUS)

## Slide 4: NEXUS Tool Development
Motivation: Develop a new multi-pollutant analysis tool to identify and assess areas with high ambient levels and/or health risks associated with PM2.5, O3 and Air Toxics
Phase-1: Develop a GIS-based NEXUS prototype with a user-friendly graphical interface to provide analysis and visualization functions of potential multi-pollutant AQ issues at national level (continental US)
Phase-2: Expand the NEXUS tool to allow users to dial into an EPA region, State, or metropolitan area and provide data query and V/A functions for “AQ and emissions” information over the selected region of interest
4

## Slide 5: Expected Use of NEXUS Tool
The NEXUS tool will allow users to do the following:
  National screening for areas with MP issues: Phase 1 development will provide ability to quickly screen areas across nation that have combination of high air quality and/or risk levels for O3, PM2.5 and Air Toxics.
  Area screening to understand nature of MP problem: Phase 2 development will provide ability to ‘dial-into’ specific areas to determine extent to which common emissions sources are causing the MP issues.
We expect to use this tool to engage with Regions and identify areas that would potentially benefit most from MP approaches to reduce emissions (including current NA areas).
The NEXUS tool will essentially provide a ‘conceptual model’ of MP issues to facilitate engagement with state/local/tribal agencies and community stakeholder groups.
We also believe that it has additional uses across the Office for Air Toxics, Environmental Justice and other programs.
5

## Slide 6: NEXUS Tool : Schedule & Installation
Work Plan | Date
Developed NEXUS tool prototype and Phase-1 functions | April 2020
Developed Phase-2 functions and deliver first working (interim) NEXUS tool | August 2020
Developed a fully functional NEXUS tool and on-line User’s Manual | Dec. 2020
Upgrading NEXUS tool for Beta testing and broader OAQPS and Regional office use | Jan. ~ July 2021
6
Download “NEXUS” tool: The “NEXUS 1.5” package (“NEXUS v1.5 setup.exe” & “NEXUS 1.5 Data.exe”: run both to install) is available at OAQPS’s Shared Drive a:t G:\SHARE\NEXUS\NEXUS 1.5\ or at EPA’s new FTP site: ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
(Note: Require software installation privilege to install “NEXUS tool” on EPA’s PCs)

## Slide 7: NEXUS Tool: Briefing Schedule
Audience | Date
AQAD & HEID – DD & Management Team | Sept. 25, 2020
Air Toxics Team | Nov. 3, 2020
AQPD – DD & Management Team | Dec. 10, 2020
OID – DD & Management Team | Jan. 25, 2021
SPPD – DD & Management Team | Jan 28, 2021
OAQPS – Office Director | Feb 1, 2021
7

## Slide 8: NEXUS Tool: Three Key Modules
Data Viewer module
Data Input module
Data Query module
View and create interactive Map/Data/Chart/Table
Provide flexible selections & mapping of “Ambient” and/or “Risk” levels of PM2.5, O3 and Air Toxics
Provide regional analysis for “EPA region”, “States”, “CBSA”, and “County”
Link and display major emission sources locations & emitted pollutants info.
Allow to update & change input data files
Provide data preview and filter functions
Currently uses 10 publicly available input data files (~4GB)
Quick turnaround to run & save to a new “project” using new input data files
Expand data field selections and flexibility for exploratory/advanced users
Provide overlaying map and summary table for data query results
Current data query based on selected data fields: “Ambient/Risk, Advance area, Socio-demographic (EJ) area, NA Area, Class I area”
8

## Slide 9: NEXUS Tool: Connections to Each Division
AQPD
NAAs
Advance
Class I Areas
OID
Environmental Justice
Tribes
Training
  OAQPS
  Identify areas with common high AQ & risk across O3, PM2.5, and Air Toxics
HEID
MP Areas
BenMAP
Climate
AQAD
Emissions
Modeling
Monitoring
DVs
SPPD
Sector Prioritization
Sources
9

## Slide 10: NEXUS Tool: Examples
How can NEXUS be used to identify highest risk areas across O3, PM2.5, and Air Toxics, the sector(s) contributing and EJ communities impacted?
  Example 1  Region 5  Detroit
How can NEXUS be used to identify how best to address multi-pollutant risks in nonattainment areas?
  Example 2  Region 4  Louisville
How can NEXUS be used to review industrial sources and potential impacts on EJ communities?
  Example 3  Region 4  Birmingham
10

## Slide 11: NEXUS Tool: Example 1 - ID High MP Risk Areas, Contributing Sector(s) & EJ Areas
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics.
Example map above is for Region 5
11

## Slide 12: NEXUS Tool: Highest MP Risk Areas in R5
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. Example table above was generated in Data Query for Region 5. Table Generator Module is planned for future development. Currently, data can be exported to Excel.
12

## Slide 13: NEXUS Tool: R5 Rankings from Data Query Module
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. Information above was generated in Data Query for Region 5 and exported into excel where rankings were applied.
Top CBSAs (using this approach) – Chicago, Detroit, Cleveland, Columbus, Indianapolis, Cincinnati, Milwaukee, Minneapolis, Dayton & Akron
13
STATE | COUNTY | CBSA NAME | PM Mortality Num % | O3 Mortality Num % | Total Risk Num % | Overall Rank | Poverty / Disadvantage | Advance Area Type
IL | Cook County | Chicago-Joliet-Naperville, IL-IN-WI | 99 | 99 | 99 | 1 | Neutral | 
MI | Wayne County | Detroit-Warren-Livonia, MI | 99 | 99 | 99 | 1 | Disadvantaged | 
MI | Oakland County | Detroit-Warren-Livonia, MI | 99 | 99 | 98 | 2 | Advantaged | 
OH | Cuyahoga County | Cleveland-Elyria-Mentor, OH | 99 | 99 | 98 | 2 | Disadvantaged | 
OH | Franklin County | Columbus, OH | 99 | 99 | 98 | 2 | Neutral | 
IN | Marion County | Indianapolis-Carmel, IN | 99 | 98 | 98 | 3 | Disadvantaged | 
OH | Hamilton County | Cincinnati-Middletown, OH-KY-IN | 99 | 98 | 97 | 4 | Disadvantaged | 
WI | Milwaukee County | Milwaukee-Waukesha-West Allis, WI | 99 | 98 | 97 | 4 | Disadvantaged | PM
MN | Hennepin County | Minneapolis-St. Paul-Bloomington, MN-WI | 98 | 98 | 98 | 4 | Advantaged | Both
IL | DuPage County | Chicago-Joliet-Naperville, IL-IN-WI | 98 | 97 | 98 | 5 | Most Advantaged | 
MI | Macomb County | Detroit-Warren-Livonia, MI | 98 | 98 | 97 | 5 | Advantaged | 
OH | Montgomery County | Dayton, OH | 98 | 98 | 95 | 6 | Disadvantaged | 
IN | Lake County | Chicago-Joliet-Naperville, IL-IN-WI | 98 | 97 | 95 | 7 | Neutral | 
OH | Summit County | Akron, OH | 98 | 97 | 95 | 7 | Neutral | 
IL | Lake County | Chicago-Joliet-Naperville, IL-IN-WI | 97 | 96 | 97 | 7 | Advantaged | 

## Slide 14: NEXUS Tool: Detroit CBSA
NEXUS can be used to explore CBSAs with multi-pollutant concerns. This information was generated in Data Viewer for the Detroit CBSA. Two counties (Wayne & Genessee) are outlined in green, showing that they are “disadvantaged or under”. Let’s explore where the major sources are located in the CBSA…
14

## Slide 15: NEXUS Tool: Emissions Sources in Detroit CBSA
Top NOx Emission Sources
W
W
W
W
W
W
W
W
W
W
W
W
W
W
W
W
S
S
S
M
M
M
M
M
Ma
Ma
G = Genessee Co., Ma= Macomb Co., M= Monroe Co., S = St. Clair Co., W = Wayne Co.
G
S
S
S
G
G
G
W
W
W
M
M
M
Ma
Ma
Ma
Top VOC Emission Sources
Top PM2.5 Emission Sources
NEXUS can be used to identify top emission sources. The information above was generated in Data Query for the Detroit CBSA . We can quickly see that the majority of the NOx, VOC & PM2.5 emission sources are located in Wayne County. Let’s explore the Wayne County sources further…
15

## Slide 16: NEXUS Tool: Emissions Sources in Wayne County
NEXUS can be used to identify top emission sources. The information above was generated in Data Query for Wayne County, MI. This can help identify the potential co-benefits of controls. Let’s explore AK Steel and US Steel further...
16

## Slide 17: NEXUS Tool: Steel Mills in Wayne County
AK Steel
US Steel
AK Steel & US Steel were both identified as top emitters for NOx, SO2, PM2.5 and Heavy Metal HAPs, highlighting the potential co-benefits of controls in these steel mills. The above map was generated in NEXUS Data Query. Let’s see the proximity of these steel mills to EJ communities…
17

## Slide 18: NEXUS Tool: EJ Indices in Wayne County
EJSCREEN Demographic Index
EJSCREEN Low Income Population
EJSCREEN Minority Population
AK Steel
US Steel
NEXUS Map
NEXUS can be used to determine EJ communities in areas with MP concerns. NEXUS currently includes a poverty/disadvantage index, and we plan to incorporate additional EJ metrics such as the data inputs below from EJSCREEN. These indices show the close proximity of AK Steel & US Steel to EJ communities.
18

## Slide 19: NEXUS Tool: Example 2 – MP Risk in NAAs
The map above was generated for the Louisville/Jefferson County - Elizabethtown - Madison, KY-IN CBSA (2015 marginal O3 NAA & 2008 Advance Area), using the data query module. The top 10 Gas & VOC HAPS emission sources are identified.
19

## Slide 20: NEXUS Tool: NOx Emission Sources in Louisville CBSA
2 of the top 4 NOx emission sources (EGUs) are outside Jefferson Co., KY (Jefferson Co., IN & Tremble, KY)
20
Indiana Kentucky Electric Corp.
Louisville G&E Co. – Trimble Co.

## Slide 21: NEXUS Tool: VOC Emission Sources in Louisville CBSA
Top 2 VOC emission sources (distilleries) are in Nelson County, KY
21

## Slide 22: NEXUS Tool: Gas & VOC HAPs Emission Sources in Louisville CBSA
2 of the top 4 gas & VOC HAPs emission sources in Indiana (Harrison & Clark County)
22

## Slide 23: NEXUS Tool: Addressing MP Concerns
NEXUS can be used to quickly demonstrate to an area (Louisville) that coordination outside of their local jurisdiction (Jefferson County, KY) is necessary in order to see the reductions needed to come into attainment
Coordination is needed with the state of Kentucky, state of Indiana, EPA R4 & EPA R5
23

## Slide 24: NEXUS Tool: Example 3 – Reviewing an Industrial Source
Drummond’s ABC Coke facility in Tarrant, AL, just outside the Birmingham city limits in Jefferson County, recently paid fines under settlement agreement for emitting 10x more benzene than reporting, along with other violations. We can use NEXUS to take a look at the facility.
24

## Slide 25: NEXUS Tool: Reviewing an Industrial Source near EJ Areas
NEXUS Map
EJSCREEN Demographic Index
EJSCREEN Low Income Population
EJSCREEN Minority Population
Adding EJ metrics, such as those shown below in EJSCREEN, can be used in NEXUS to determine the proximity of industrial sources to EJ communities in areas with MP concerns.
25

## Slide 26: NEXUS Tool: Potential EJ Capability Additions
A source/sector module could allow for Multi-pollutant ‘proximity-based assessment’ for EJ communities
  Define an area around a source/sector and calculate % distribution of demographics (race, ethnicity, etc.)
  Compare % distribution to the state, region, or national level averages
  Expand demographic comparisons to include O3, PM2.5 and Air Toxics risks or other metrics of interest (e.g., emissions density, pop-weighted air quality concentrations, etc.)
Incorporate analysis similar to what is currently used for Risk and Technology Review (RTR) and other actions
  NEXUS could provide a more transparent and accessible way to complete screening analyses and share across the office and programs (criteria and toxics). However, the ability to accurately screen for toxics is limited at this time
26

## Slide 27: NEXUS Tool: Discussion and Next Steps (1)
    Short-term:
    GOAL: Upgrade/improve NEXUS tool to reflect latest data & information and MP team’s feedbacks
    Currently expect FY21 funding to support NEXUS -- perhaps $50k from AQAD
      Update NEXUS data to 2017
        2017 data for O3, PM2.5 & Air Toxics risk/ambient/emissions
        Tribal boundaries & socioeconomic/demographic data for EJ
      Add O3, PM2.5, and Air Toxics monitoring data
      Update metrics/indicators (e.g., risk metrics, EJ indicators)
    Engage across Office to determine how this tool may best inform or be used for OAQPS’s Air Toxics Strategy programs
      Consider addition of screening-level analysis & assessment capabilities (e.g., proximity-based EJ analysis)
27

## Slide 28: NEXUS Tool: Discussion and Next Steps (2)
    Long-term:
    Upgrade and prepare NEXUS for Beta test within OAQPS and with EPA Regions
    Based on Office wide engagements, use updated NEXUS tool with 2017 data to inform Multi-pollutant, Air Toxics, Advance, and EJ efforts as appropriate
    Develop plan for routine updates and maintenance of the NEXUS tool to best support OAR/OAQPS programs and determine appropriate extensions as need and resources provide.
    Collaborate with OID on NEXUS Training Materials
28

## Slide 29
Live Demo
Carey Jang
29

## Slide 30: NEXUS Tool Demo: 2014 NEXUS Case
30
Launching Page
Roadmap for Demo:
(Use example cases)
National View: Use “NEXUS” across pollutants to provide an initial “SCREEN” at the national level by providing an indicator where there may be a common set of sources contributing to Multi-pollutant issues.
Regional View: Dial into a region or area of interest to understand the pollutant/source connections, and potential for more effective and efficient multi-pollutant solution.
2008

## Slide 31: “NEXUS 1.5”: Quick Tutorial
Carey Jang
Download “NEXUS” tool: The “NEXUS 1.5” package (“NEXUS v1.5 setup.exe” & “NEXUS 1.5 Data.exe”: run both to install) is available at OAQPS’s Shared Drive at: G:\SHARE\NEXUS\NEXUS 1.5\
or at EPA’s new FTP site:
ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
(Note: Require software installation privilege to install “NEXUS tool” on EPA’s PC)
31

## Slide 32: NEXUS Tool: On-line User’s Manual
Hot link to User’s manual’s “Data Viewer” chapter (same for “Data Input” & “Data Query”
Click “book” icon to launch “User’s manual”
32

## Slide 33: NEXUS Tool: Data Viewer Module
Select & adjust “Ambient” & “Risk” levels
“Advanced Option”: provide HAPs & species selections
Click “File” to open or save a project
Switch between 3 key modules
Loaded NEXUS project file name
33

## Slide 34: Data Viewer Module: Selections & Map Display
Select & adjust “Ambient” & “Risk” threshold levels for color map display
“Apply” new selections to “Radio button” panel
34

## Slide 35: Data Viewer: “Apply” New Selections
New selections will appear on-the-fly in “radio button” panel and map display
“Apply” new selections
“Check” new selections
35

## Slide 36: Data Viewer Module: Base Map & Color
Click to change color & transparency
“Base Map”: Change boundary lines and background map
“Right-click” map to save image
36

## Slide 37: Data Viewer: “Region Selection”
Allow to select “EPA regions”, “States”, or “CBSA”
37

## Slide 38: Data Viewer: Select EPA Region/State/CBSA
Examples:
EPA Region 4
NC
Louisville CBSA
38

## Slide 39: Data Viewer: Major Emission Sources
Click “Emission Sources” tab to display emission sources (green dots) and launch new window
Click any “facility” to link & display source location and emission information
39

## Slide 40: Data Viewer: Major Emission Sources
Allow to scroll down to county-level (e.g., Wake County, NC)
Wake county, NC
40

## Slide 41: Data Viewer: Top “x” Emission Sources
Durham county, NC
Provide selection of CAPs precursors & HAPs species
41

## Slide 42: Data Viewer: EPA Region Table Generator
“EPA Region Table Generator” is still under development, but a preview of example “EPA Region 4” tables can be provided
42

## Slide 43: Data Viewer: Data Search & Filter
Click “+” to add filters; Click “x” to remove current filter;
Click “Output data…” to output current page records or all records
Show specified records per page.
43

## Slide 44: Data Query Module: Main Page
Region Selection
Data Query qualifier selection
Map Overlaying selection
Detachable “Attribute Table”
11111111
Data Query Configuration
44

## Slide 45: Data Query Module: Configure Data Query
45
“Data Query Filter” allows to select “qualifiers” for query
“Data Query Preview” displays the selected “qualifiers” at the same time

## Slide 46: Data Query Module: Overlaying Map
46
Overlaying Map selection
46

## Slide 47: Data Query Module: Attribute Table
Detachable “Attribute Table”
Filter/link/export functions (to be completed)
47

## Slide 48: Data Query Module: Attribute Table
Click a “record” to link and display its location & info.
48

## Slide 49: Data Input Module: Data Preview
Click to change input data file
Click to view data
Click to run & save project
Select a table to view if there are multiple tables in the selected data source file
Check to use filter to query data
49

## Slide 50: RoadMap for NEXUS Tool Demo (1)
National Screening (2014 Data)
Replicate 2008 NEXUS map with O3/PM2.5 concentrations above NAAQS and NATA risk estimates above selected percentile of top 10%
  What happens to areas at lower O3/PM2.5 NAAQS levels?
  What happens to areas current over O3/PM2.5 NAAQS if change HAP risk percentile?
Provide NEXUS map on risk basis: O3/PM2.5 BenMAP mortality risk based on fused surfaces and NATA risk estimates above selected percentile of top 10% for all pollutants
  What happens to MP areas as one changes percentile to top 20% or others?
  What is relationship between Heavy Metal HAPs risk (top 10%) and PM2.5 risk to identify potential co-pollutant issues?
  What is relationship between Gas/VOC HAPs risk (top 10%) and O3 risk to identify potential co-pollutant issues?
50

## Slide 51: RoadMap for NEXUS Tool Demo (2)
Regional/State/CBSA/County Screening
EPA Region 4 Example
  Areas with MP risk in top 10% across O3, PM2.5 and HAPs
  Louisville CBSA: General view and then dial into “Jefferson County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
51

## Slide 52: RoadMap for NEXUS Tool Demo (3)
Data Query: State/CBSA/County Views
Advance Areas
  Initial view of national level information using the Advance Area definition to show overlay with MP areas
  Region 5 => Minneapolis Example: General view and then dial into “Dakota County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
52

## Slide 53: RoadMap for NEXUS Tool Demo (4)
Data Query: State/CBSA/County Views
Socio-Economic/Demographic (EJ) Areas
  Initial view of national level information using the Poverty/Disadvantaged indicator to show overlay with MP areas
  Region 5 => Detroit Example: General view and then dial into “Wayne County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
53

## Slide 54
End
54

## Slide 55
Data Input Module: Input Files & Attributes
Data Input File Names | Data Format | Data Description | Data Source | Data Period
“2014 O3 & PM2.5 fused Ambient & Risk” | Geodataset | O3/PM2.5 ambient & risk data at county/census tract level | from OAQPS MP team | 2014
“2014 NATA Risk” | Geodataset | Air Toxics ambient & risk data at county/census tract level | from OAQPS MP team | 2014
“O3_DV_2009_2018” | Excel | O3 design values at county level | From EPA public website: https://www.epa.gov/air-trends/air-quality-design-values | 2009 to 2018
“PM_DV_2009_2018” | Excel | PM2.5 design values at county level | From EPA public website: https://www.epa.gov/air-trends/air-quality-design-values | 2009 to 2018
“Advance areas O3_PM” | Geodataset | O3 & PM2.5 Advance Areas | from OAQPS MP team | 2018
“Index of Poverty_ Disadvantage” | Excel | Index of poverty/disadvantage at county level | from Univ. of Michigan website: https://poverty.umich.edu/projects/understanding-communities-of-deep-disadvantage/ | 2017
“NEI_County_CAPs” “NEI_Facility_HAPs_ CAPs” | Geodataset | Major emission sources and facility info. of CAPs & HAPs at county level | From OAQPS public website: ftp://newftp.epa.gov/EPADataCommons/OAR/OAQPS/NEI/NEI_Facility_HAPs_CAPs.zip ftp://newftp.epa.gov/EPADataCommons/OAR/OAQPS/NEI/NEI_County_CAP.zip | 2008, 2011, 2014
“2014 NEI_NATA Emissions” | Access Database (*. accdb) | NATA emissions data from 2014 NEI database, including various source groups | From EPA public website: https://www.epa.gov/national-air-toxics-assessment/2014-nata-assessment-results#emissions | 2014
“Class1_FederalAreas” | Geodataset | Mandatory Class 1 Federal Areas | From Mandatory Class 1 Federal Areas Web Service: https://edg.epa.gov/data/public/OAR/OAQPS/Class1/Class1Areas.zip | —
55