## Slide 1: “NEXUS” Multi-Pollutant Analysis Tool Development: Status and Progress
OAQPS/OID Briefing
January 25, 2021
Carey Jang & Beth Landis
Data Viewer Module
Data Input Module
Data Query Module
“NEXUS 1.5” available on OAQPS’s Shared Drive at: “G:\SHARE\NEXUS\NEXUS 1.5\”
or at EPA’s new FTP site: ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
1

## Slide 2: Overview
Multi-Pollutant Background
NEXUS Tool Development
  Expected Use
  Schedule
Key Modules
Questions NEXUS can Answer & Examples: OID focused
Discussion & Next Steps
Live Demo

## Slide 3: Multi-Pollutant (MP) Background
3
Support a comprehensive, MP treatment of air quality problems to effectively improve air quality and make the most efficient use of available resources
  Primary Goal - identify & evaluate local control strategies targeting emissions of O3 & PM2.5 and their precursors while at the same time reducing air toxics of concern for communities to maximize both health benefits and air quality improvements
MP planning has the potential to reduce the costs and increase benefits associated with AQM
Supports SLT air agencies in developing risk-based MP AQM plans and implementing strategies that reduce air pollution emissions & improve public health
Success has been demonstrated in Detroit and SC & a project is currently underway in Louisville, KY
Tools needed to analyze MP data are either available currently or being developed in OAQPS (NEXUS)

## Slide 4: NEXUS Tool Development
Motivation: Develop a new multi-pollutant analysis tool to identify and assess areas with high ambient levels and/or health risks associated with PM2.5, O3 and air toxics
Phase-1: Develop a GIS-based NEXUS prototype with a user-friendly graphical interface to provide analysis and visualization functions of potential multi-pollutant AQ issues at national level (continental US)
Phase-2: Expand the NEXUS tool to allow users to dial into an EPA region, State, or metropolitan area and provide data query and V/A functions for “AQ and emissions” information over the selected region of interest
4

## Slide 5: Expected Use of NEXUS Tool
The NEXUS tool will allow users to do the following:
  National screening for areas with MP issues: Phase 1 development will provide ability to quickly screen areas across nation that have combination of high air quality and/or risk levels for O3, PM2.5 and air toxics.
  Area screening to understand nature of MP problem: Phase 2 development will provide ability to ‘dial-into’ specific areas to determine extent to which common emissions sources are causing the MP issues.
We expect to use this tool to engage with Regions and identify areas that would potentially benefit most from MP approaches to reduce emissions (including current NA areas).
The NEXUS tool will essentially provide a ‘conceptual model’ of MP issues to facilitate engagement with state/local/tribal agencies and community stakeholder groups.
We also believe that it has additional uses across the Office for air toxics, Environmental Justice and other programs.
5

## Slide 6: NEXUS Tool : Schedule & Installation
Work Plan | Date
Developed NEXUS tool prototype and Phase-1 functions | April 2020
Developed Phase-2 functions and deliver first working (interim) NEXUS tool | August 2020
Developed a fully functional NEXUS tool and on-line User’s Manual | Dec. 2020
Upgrading NEXUS tool for Beta testing and broader OAQPS and Regional office use | Jan. ~ July 2021
6
Download “NEXUS” tool: The “NEXUS 1.5” package (“NEXUS v1.5 setup.exe” & “NEXUS 1.5 Data.exe”: run both to install) is available at OAQPS’s Shared Drive a:t G:\SHARE\NEXUS\NEXUS 1.5\ or at EPA’s new FTP site: ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
(Note: Require software installation privilege to install “NEXUS tool” at EPA’s PCs)

## Slide 7: NEXUS Tool : Briefing Schedule
Audience | Date
AQAD & HEID – DD & Management Team | Sept. 25, 2020
Air Toxics Team | Nov. 3, 2020
AQPD – DD & Management Team | Dec. 10, 2020
OID – DD & Management Team | Jan. 25, 2021
SPPD – DD & Management Team | Jan 27, 2021
OAQPS – Office Director | Feb 1, 2021

## Slide 8: NEXUS Tool: Three Key Modules
Data Viewer Module
Data Input Module
Data Query Module
Setting Pane - users can set up standard values for several kinds of pollutant data for the data viewer
Viewer Pane - shows multi-pollutant data in maps, charts and tables.
Setting Pane – users can define data sources for NEXUS
Preview Pane – preview input files
Upper Pane - the query conditions setting pane
Middle Pane – map
Bottom Pane – attribute table

## Slide 9: NEXUS Tool: DATA VIEWER
Data Viewer module
View and create interactive Map/Data/Chart/Table
Provide flexible selections & mapping of “Ambient” and/or “Risk” levels of PM2.5, O3 and air toxics
Provide regional analysis for “EPA region”, “States”. CBSA”, and “County”
Link and display major emission sources locations & emitted pollutants info.
9

## Slide 10: NEXUS Tool: DATA INPUT
Currently, there are 10 input data files used (publicly available)
Allow users to update/preview/filter Input data files
Run and Save to a new project after loading new input data files
Data Input module
Allow to update & change input data files
Provide data preview and filter functions
Extend to use 10 input data files now (publicly available, ~4 GB)
Quick turnaround to run & save to a new “project” using new input data files
10

## Slide 11
Data Input Module: Input Files & Attributes
Data Input File Names | Data Format | Data Description | Data Source | Data Period
“2014 O3 & PM2.5 fused Ambient & Risk” | Geodataset | O3/PM2.5 ambient & risk data at county/census tract level | from OAQPS MP team | 2014
“2014 NATA Risk” | Geodataset | Air toxics ambient & risk data at county/census tract level | from OAQPS MP team | 2014
“O3_DV_2009_2018” | Excel | O3 design values at county level | From EPA public website: https://www.epa.gov/air-trends/air-quality-design-values | 2009 to 2018
“PM_DV_2009_2018” | Excel | PM2.5 design values at county level | From EPA public website: https://www.epa.gov/air-trends/air-quality-design-values | 2009 to 2018
“Advance areas O3_PM” | Geodataset | O3 & PM2.5 Advance Areas | from OAQPS MP team | 2018
“Index of Poverty_ Disadvantage” | Excel | Index of poverty/disadvantage at county level | from Univ. of Michigan website: https://poverty.umich.edu/projects/understanding-communities-of-deep-disadvantage/ | 2017
“NEI_County_CAPs” “NEI_Facility_HAPs_ CAPs” | Geodataset | Major emission sources and facility info. of CAPs & HAPs at county level | From OAQPS public website: ftp://newftp.epa.gov/EPADataCommons/OAR/OAQPS/NEI/NEI_Facility_HAPs_CAPs.zip ftp://newftp.epa.gov/EPADataCommons/OAR/OAQPS/NEI/NEI_County_CAP.zip | 2008, 2011, 2014
“2014 NEI_NATA Emissions” | Access Database (*. accdb) | NATA emissions data from 2014 NEI database, including various source groups | From EPA public website: https://www.epa.gov/national-air-toxics-assessment/2014-nata-assessment-results#emissions | 2014
“Class1_FederalAreas” | Geodataset | Mandatory Class 1 Federal Areas | From Mandatory Class 1 Federal Areas Web Service: https://edg.epa.gov/data/public/OAR/OAQPS/Class1/Class1Areas.zip | —
11

## Slide 12: NEXUS Tool: DATA QUERY
Data Query module
Expand data field selections and flexibility for exploratory/advanced users
Provide overlaying map and summary table for data query results
Current data query based on selected data fields: “Ambient/Risk, Advance area, Socio-demographic (EJ) area, NA Area, Class I area”
12

## Slide 13: OID Related Examples
How can NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics?
  Example 1  Miami CBSA
How can NEXUS be used to identify the nature of multi-pollutant risks affecting Tribes?
  Example 2  Oklahoma City-Shawnee CBSA
How can NEXUS be used to identify the nature of multi-pollutant risks in areas with EJ concerns?
  Example 3  Memphis CBSA
13

## Slide 14: NEXUS Tool: Example 1 - ID High MP Risk Areas
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. Example map above is for Region 4
14

## Slide 15: NEXUS Tool: Highest MP Risk Areas in R4
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. Example table above was generated in Data Query for Region 4. Table Generator Module is planned for future development. Currently, data can be exported to Excel.
15

## Slide 16: NEXUS Tool: Rankings from Data Query Module
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. Information above was generated in Data Query for Region 4 and exported into excel where rankings were applied.
Top 5 CBSAs (using this approach) – Miami, Tampa, Atlanta, Birmingham, Louisville
16

## Slide 17: NEXUS Tool: Emissions Sources in Miami CBSA
NEXUS can be used to identify top emission sources. Information above was generated in Data Query for the Miami CBSA. This can help identify the potential co-benefits of controls.
17

## Slide 18: NEXUS Tool: Source Details in Miami CBSA
NEXUS can be used to identify top emission sources. Information above was generated in Data Query for the Miami CBSA.
What is this and where is it located?
18

## Slide 19: NEXUS Tool: Example 2—MP Sources in OKC-Shawnee CBSA
Cheyenne & Arapaho Tribes, OK
Iowa Tribe of OK
Citizen Potawatomi Nation, OK
The Chickasaw Nation
The maps above were generated for the Oklahoma City-Shawnee CBSA using the NEXUS data query module & EnviroMapper to demonstrate the benefit of adding a Tribal Boundary layer. The top 10 Gas & VOC HAPS emission sources are plotted in NEXUS.
Kickapoo Tribe of OK

## Slide 20: NEXUS Tool: Emissions Sources in OKC-Shawnee CBSA
NEXUS can be used to identify top emission sources. The information above was generated in Data Query for the Oklahoma City-Shawnee CBSA . This can help identify the potential co-benefits of controls. Let’s explore the Horseshoe Lake Generating Station further…

## Slide 21: NEXUS Tool: Source Details in OKC-Shawnee CBSA
Citizen Potawatomi Nation, OK
Kickapoo Tribe of OK
These maps were generated for the Oklahoma City-Shawnee CBSA using the NEXUS data query module & EnviroMapper to demonstrate the benefit of adding a Tribal Boundary layer. The #1 NOx Source for the CBSA (Horseshoe Lake Generating Station), also a top emitter for SO2 and heavy metal HAPs, is located in very close proximity to two Tribes. There are potential co-benefits of controlling this source that would likely result in benefits to these Tribes.

## Slide 22: NEXUS Tool: Example 3 - MP Risks in EJ Communities
NEXUS can be used to determine EJ communities in areas with multi-pollutant concerns. The information above was generated in Data Query. NEXUS currently includes a poverty/disadvantage index, and we plan to incorporate additional EJ metrics. Let’s explore the Memphis CBSA further…

## Slide 23: NEXUS Tool: Screening with Data Query Module
EJSCREEN Minority Population
EJSCREEN Demographic Index
EJSCREEN Low Income Population
Memphis CBSA using the NEXUS data query module
NEXUS can be used to determine EJ communities in areas with multi-pollutant concerns. NEXUS currently includes a poverty/disadvantage index, and we plan to incorporate additional EJ metrics such as the data inputs above from EJSCREEN.

## Slide 24: NEXUS Tool: Major Emissions Sources in Memphis
NOx
PM2.5
1,4-Dichlorobenzene
Heavy Metal HAPs
Mercury
Arsenic
NEXUS can create bar charts of major emission sources. The bar charts above show the Allen Fossil Plant as a top 2 emitter for PM2.5, NOx, 1,4-Dichlorobenzene, Heavy Metal HAPS, Mercury & Arsenic, demonstrating the potential co-benefits of controls

## Slide 25: NEXUS Tool: EJ Screening in Memphis
EJSCREEN Demographic Index
EJSCREEN Low Income Population
EJSCREEN Minority Population
Adding additional indices to NEXUS would allow us determine when facilities, such as Allen Fossil Plant, are near EJ communities
Map Generated in NEXUS

## Slide 26: Potential Environmental Justice Indices
  Environmental Indicators
    PM2.5
    Ozone
    NATA Cancer Risk
    NATA Respiratory HI
    NATA Diesel PM
    Traffic Proximity
    Lead Paint Indicator
    Superfund Proximity
    RMP Proximity
    Hazardous Waste Proximity
    Wastewater Discharge Indicator
  Demographic Indicators
    Demographic Index
    Minority Population
    Low Income Population
    Linguistically Isolated
    Less Than HS Educated
    Under Age 5
    Over Age 64
  Additional EJ Layers
    Nonattainment area
    Hazardous waste
    EJ Grants
    Water features
    Places
    Schools
    Parks
    Transportation
    EPA Tribal Areas Boundaries
    Prisons
    Public Housing
    Subsidized Housing
    Sites reporting to the EPA
Currently in EJSCREEN…
Additional Ideas:
Walkability, asthma rates, proximity to parks/green spaces, high VMT/day within ¼-½ mile buffer, hospitalizations, proximity to sources & disadvantaged areas
Already in NEXUS -– Would Like to Add to NEXUS

## Slide 27: Potential EJ Capability Additions
A source/sector module could allow for Multi-pollutant ‘proximity-based assessment’ for EJ communities
  Define an area around a source/sector and calculate % distribution of demographics (race, ethnicity, etc.)
  Compare % distribution to the state, region, or national level averages
  Expand demographic comparisons to include O3, PM2.5 and Air Toxic risks or other metrics of interest
Codify initial screen currently used for Risk and Technology Review (RTR) and other actions
  NEXUS could provide a more transparent and accessible way to complete these screening analyses and share across the office and programs (criteria and toxics)

## Slide 28: Discussion and Next Steps (1)
28
    Short-term:
    GOAL: Upgrade/improve NEXUS tool to reflect latest data & information and MP team’s feedbacks
    Currently expect FY21 funding to support NEXUS -- perhaps $50k from AQAD
      Update NEXUS data to 2017
        2017 data for O3, PM2.5 & Air Toxics risk/ambient/emissions
        Tribal boundaries & socioeconomic/demographic data for EJ
      Add O3, PM2.5, and Air Toxics monitoring data
      Update metrics/indicators (e.g., risk metrics, EJ indicators)
    Engage across Office to determine how this tool may best inform or be used for OAQPS’s Air Toxic Strategy programs
      Consider addition of screening-level analysis & assessment capabilities (e.g., proximity-based EJ analysis)

## Slide 29: Discussion and Next Steps (2)
    Long-term:
    Upgrade and prepare NEXUS for Beta test within OAQPS and with EPA Regions
    Based on Office wide engagements, use updated NEXUS tool with 2017 data to inform Multi-pollutant, Air Toxics, Advance, and EJ efforts as appropriate
    Develop plan for routine updates and maintenance of the NEXUS tool to best support OAR/OAQPS programs and determine appropriate extensions as need and resources provide.
    Collaborate with OID on NEXUS Training Materials
29

## Slide 30
Live Demo
Carey Jang
30

## Slide 31: NEXUS Tool Demo: 2014 NEXUS Case
31
Launching Page
Roadmap for Demo:
(Use example cases)
National View: Use “NEXUS” across pollutants to provide an initial “SCREEN” at the national level by providing an indicator where there may be a common set of sources contributing to Multi-pollutant issues.
Regional View: Dial into a region or area of interest to understand the pollutant/source connections, and potential for more effective and efficient multi-pollutant solution.
2008

## Slide 32: “NEXUS 1.5”: Quick Tutorial
Carey Jang
Download “NEXUS” tool: The “NEXUS 1.5” package (“NEXUS v1.5 setup.exe” & “NEXUS 1.5 Data.exe”: run both to install) is available at OAQPS’s Shared Drive at: G:\SHARE\NEXUS\NEXUS 1.5\
or at EPA’s new FTP site:
ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
(Note: Require software installation privilege to install “NEXUS tool” at EPA’s PC)
32

## Slide 33: NEXUS Tool: On-line User’s Manual
Hot link to User’s manual’s “Data Viewer” chapter (same for “Data Input” & “Data Query”
Click “book” icon to launch “User’s manual”
33

## Slide 34: NEXUS Tool: Data Viewer Module
Select & adjust “Ambient” & “Risk” levels
“Advanced Option”: provide HAPs & species selections
Click “File” to open or save a project
Switch between 3 key modules
Loaded NEXUS project file name
34

## Slide 35: Data Viewer Module: Selections & Map Display
Select & adjust “Ambient” & “Risk” threshold levels for color map display
“Apply” new selections to “Radio button” panel
35

## Slide 36: Data Viewer: “Apply” New Selections
New selections will appear on-the-fly in “radio button” panel and map display
“Apply” new selections
“Check” new selections
36

## Slide 37: Data Viewer Module: Base Map & Color
Click to change color & transparency
“Base Map”: Change boundary lines and background map
“Right-click” map to save image
37

## Slide 38: Data Viewer: “Region Selection”
Allow to select “EPA regions”, “States”, or “CBSA”
38

## Slide 39: Data Viewer: Select EPA Region/State/CBSA
Examples:
EPA Region 4
NC
Louisville CBSA
39

## Slide 40: Data Viewer: Major Emission Sources
Click “Emission Sources” tab to display emission sources (green dots) and launch new window
Click any “facility” to link & display source location and emission information
40

## Slide 41: Data Viewer: Major Emission Sources
Allow to scroll down to county-level (e.g., Wake County, NC)
Wake county, NC
41

## Slide 42: Data Viewer: Top “x” Emission Sources
Durham county, NC
Provide selection of CAPs precursors & HAPs species
42

## Slide 43: Data Viewer: EPA Region Table Generator
“EPA Region Table Generator” is still under development, but a preview of example “EPA Region 4” tables can be provided
43

## Slide 44: Data Viewer: Data Search & Filter
Click “+” to add filters; Click “x” to remove current filter;
Click “Output data…” to output current page records or all records
Show specified records per page.
44

## Slide 45: Data Query Module: Main Page
Region Selection
Data Query qualifier selection
Map Overlaying selection
Detachable “Attribute Table”
11111111
Data Query Configuration
45

## Slide 46: Data Query Module: Configure Data Query
46
“Data Query Filter” allows to select “qualifiers” for query
“Data Query Preview” displays the selected “qualifiers” at the same time

## Slide 47: Data Query Module: Overlaying Map
47
Overlaying Map selection
47

## Slide 48: Data Query Module: Attribute Table
Detachable “Attribute Table”
Filter/link/export functions (to be completed)
48

## Slide 49: Data Query Module: Attribute Table
Click a “record” to link and display its location & info.
49

## Slide 50: Data Input Module: Data Preview
Click to change input data file
Click to view data
Click to run & save project
Click to view data
Select a table to view if there are multiple tables in the selected data source file
Check to use filter to query data
50

## Slide 51: RoadMap for NEXUS Tool Demo (1)
National Screening (2014 Data)
Replicate 2008 NEXUS map with O3/PM2.5 concentrations above NAAQS and NATA risk estimates above selected percentile of top 10%
  What happens to areas at lower O3/PM2.5 NAAQS levels?
  What happens to areas current over O3/PM2.5 NAAQS if change HAP risk percentile?
Provide NEXUS map on risk basis: O3/PM2.5 BenMAP mortality risk based on fused surfaces and NATA risk estimates above selected percentile of top 10% for all pollutants
  What happens to MP areas as one changes percentile to top 20% or others?
  What is relationship between Heavy Metal HAPs risk (top 10%) and PM2.5 risk to identify potential co-pollutant issues?
  What is relationship between Gas/VOC HAPs risk (top 10%) and O3 risk to identify potential co-pollutant issues?
51

## Slide 52: RoadMap for NEXUS Tool Demo (2)
Regional/State/CBSA/County Screening
EPA Region 4 Example
  Areas with MP risk in top 10% across O3, PM2.5 and HAPs
  Louisville CBSA: General view and then dial into “Jefferson County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
52

## Slide 53: RoadMap for NEXUS Tool Demo (3)
Data Query: State/CBSA/County Views
Advance Areas
  Initial view of national level information using the Advance Area definition to show overlay with MP areas
  Region 5 => Minneapolis Example: General view and then dial into “Dakota County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
53

## Slide 54: RoadMap for NEXUS Tool Demo (4)
Data Query: State/CBSA/County Views
Socio-Economic/Demographic (EJ) Areas
  Initial view of national level information using the Poverty/Disadvantaged indicator to show overlay with MP areas
  Region 5 => Detroit Example: General view and then dial into “Wayne County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
54

## Slide 55
End
55

## Slide 56
NEXUS Demo: Example Cases
    Data Input module:
    Expand 1->10 inputs data files; Plan to update to 2017 (CDC & NATA)
    Data Query Module:
    Expand fields/flexibility: Exploratory users
    Configure DQ” window: Select Advance Area, EJ, 2017 DVs => Apply map
    Overlay Map & Detachable table summary
    Select “EPA Region 5” => “Advance + EJ”
    Change color transparency & Google Map
    CBSA: Minneapolis-> Major emis. sources
    Facility (Xcel Energy - Black Dog)
    Dakota Co. ->
      “PM2.5 + H.M.HAPs” (Xcel Energy)
      “VOC + NOx + G&V HAPs” (Flint Hills)
    Back to “EPA Region 5” -> EJ: Select “Disadvantage & under”
    CBSA: Detroit -> Wayne Co. ->
      “NOx + SOx” (DTE Elec.)
      “PM2.5 + H.M.HAPs” (AK Steel, US Steel)
    CBSA: Cincinnati -> Butler Co. (AK Steel) (Cincinnati News article)
56
    Main GUI:
    Mimic 2008 MP report; County-based map
    Color/legend setup; Exceed “Ambient or risk” threshold defined in “Center panel”
    Click “county” to show “Data Content”
    Center panel & Left panel
    On-line User’s Manual & PPT Tutorial
    Nation View :
    “Ambient”: PM2.5: 12 -> 10 ug/m3; O3: 70 -> 65 ppb; “Risk”: Air Toxic 10% ->0%-> 20%
    All Risk only: O3:10%, PM:10%, AT: 10%
    Advanced: Heavy-metal HAPs, G&V:10%
      Co-PM risk: PM: 10%, H.M. HAPs: 10%
      Co- PM/NA: 12 ug/m3, H.M HAPs:10%
      Co-O3 risk: O3: 10%, G&V HAPs: 10%
      Co- O3/NA: 70 ppb, G&V HAPs:10%
    Advanced: H-M: Chromium & G-V: HCHO
    EPA Region/State/CBSA View:
    “dial-in” for regional (all risk: 10%)
    EPA Regions: R4/R5/R9 -> States: NC/CA -> CBSA: RDU
    “right-click” -> Major Emis. Sources
    Change color transparency/Google Map
    Major Emission Sources:
    CBSA: Louisville -> Jefferson Co. -> Facility (Louisville G&E)
    SO2/NOx/HAPs, Facility, Data Content;
    Top X Emission Sources: CAPs & HAPs
Notes: 1. Thank Cen/Gao/Luo/Chen; 2. HZ more visits; 3. AP on HZ