## Slide 1: 2022 EPA Regulatory Modeling Platform Air Quality Model Performance: 36US3
EPA/OAQPS/AQAD/AQMG

## Slide 2: Agenda
2022 Modeling Platform Background
Air Quality Model : CMAQ
  Model domain
  Model configurations
36US3 Model Performance Evaluations
  Overall performance
  Hemispheric CMAQ BC
Next Steps

## Slide 3: Goals and Potential Applications of 2022 Modeling Platform
To develop a more contemporary modeling platform including base year data (emissions, met, IC/BCs) and future year emissions projections for potential EPA regulatory analysis
To support state/local/tribal air agencies for SIPs and related implementation efforts, such as modeling for ozone NAAQS SIPs and PM NAAQS implementation

## Slide 5: Timeline for 2022v1 Platform Development

## Slide 6: Status of Meteorological data
2022 meteorological data from Weather Research Forecast (WRF) model have been generated, evaluated and ready for use
Performed multiple sensitivity analyses on WRF setups based on feedback from States/MJOs. Based on those analyses, our standard configuration remains preferred
Data have been uploaded to Amazon Web Services (AWS) for download or use in cloud computing
Meteorological model performance TSD is available on SCRAM
wind speed, temperature, mixing ratio bias by month for 36NOAM domain.

## Slide 7: Hemispheric/Global Modeling to Develop 2022 Boundary Conditions
Model | Simulation | BCON
GEOS-Chem v14.0.1 | 2022 Complete | 36US3 Complete
Hemispheric CMAQ v5.4+ | 2022 Complete | 36US3 Complete
NASA GMAO GEOS-CF | Daily 1-day hindcasts Daily 5-day forecast | 36US3 Complete
Evaluation
  Sondes: NOAA GML and World Ozone and Ultraviolet Radiation Data Centre
  Surface: CASTNET surface data monitors
  Data are available on Amazon Web Services (AWS) for download or use in cloud computing
Notes: A column to CF, GC, CQ, think about sonde evaluations

## Slide 8: CMAQ Configurations : 36US3, 12US1 & 2
CMAQ version 5.4.0.4
STAGE with bi-directional flux on
  Fertilizer NH3 emission control
Lightning NOx (LNOx) inline calculation on
  First time to include LNOx inline for platform
Inline BEIS biogenic emission on
  Regular application for platform
CB6r5_ae7_aq non-volatile POA
Dust off (detailed info in next slide)
ICON/BCON:
  GEOS-CF: CF BC
  GEOS-Chem: GC BC
  H-CMAQ: CQ BC
Objectives:
  Select a BCON for 12US2
  Check emissions

## Slide 9: Wind-blown dust
CQ-BC 36US3 WBD inline is off.
In CMAQv5.4, there is a glitch in the source code, WBD emissions are sensitivity to the land use (NLCD 40 vs MODIS)
In this 2022 CQ run, we used MODIS, CQ-HEMI include WBD inline using MODIS land use

## Slide 10: 2022 CMAQ 36US3 modeling platform high level performance evaluations

## Slide 11: CMAQ 36US3 Model performance: Summary
The CMAQ simulations at 36US3 have similar PM2.5 and O3 performance statistics (surface data) using GEOS-CF, GEOS-Chem, and H-CMAQ BC
Notes: CASTNET is more proper for MPE for 36US3

## Slide 12: CMAQ 36US3 Model performance: O3 season, 8hr_max (May 1 to September 30, 2022)
The CMAQ simulations at 36US3 using GEOS-CF and H-CMAQ BC have slightly better performance statistics (surface data) than the one using GEOS-Chem
Network | NUM_OBS | MEAN_OBS | MEAN_MODEL | Norm_Median_Bias | Median_Bias | Norm_Median_Error | Median_Error | Correlation
CMAQ_2022hc_cb6r5ae7_GEOS_CF_36US3 |  |  |  |  |  |  |  | 
CASTNET | 11463 | 45.51 | 43.93 | -3.46 | -1.58 | 10.6 | 4.83 | 0.65
AQS | 178205 | 44.65 | 44.40 | -0.49 | -0.22 | 11.4 | 5.09 | 0.73
CMAQ_2022hc_cb6r5ae7_GEOS_Chem_36US3 |  |  |  |  |  |  |  | 
CASTNET | 11463 | 45.51 | 42.71 | -6.24 | -2.85 | 12.2 | 5.57 | 0.62
AQS | 178205 | 44.65 | 43.26 | -3.09 | -1.37 | 12.7 | 5.66 | 0.70
CMAQ_2022hc_cb6r5ae7_HEMI_36US3 |  |  |  |  |  |  |  | 
CASTNET | 11463 | 45.51 | 46.44 | 2.60 | 1.19 | 10.2 | 4.67 | 0.66
AQS | 178205 | 44.65 | 46.20 | 3.93 | 1.75 | 11.5 | 5.13 | 0.74
Notes: Try not to say which model has the worse MPE, the states/MJOs can use any BC they prefer to use if the model designs follow the guideline.

## Slide 13: CMAQ 36US3 Model performance: PM2.5 Bias
Overall, the biases are similar among these three 36US3 model runs for PM2.5
CF BC
GC BC
CQ BC
MB (ug/m3)
NMB (%)

## Slide 14: CMAQ 36US3 Model performance: Performance Statistics plots

## Slide 15: CMAQ 36US3 Performance Statistics Plots: PM2.5 Median Bias
Overall, the errors are similar among these three 36US3 model
CF BC
GC BC
CQ BC
AQS
CSN
IMPROVE

## Slide 16: CMAQ 36US3 Performance Statistics Plots: PM2.5 Normalized Mean Bias
Overall, the NMBs are similar among these three 36US3 model runs except spring. In general, CQ BC predicts slightly higher PM2.5 in spring than other two BC runs
CF BC
GC BC
CQ BC
AQS
CSN
IMPROVE

## Slide 17: CMAQ 36US3 Model performance: Annual surface O3 MDA8 Bias
H-CMAQ BC has better performance in west and southwest regions, but overestimates O3_8hrmax in other regions.
CF BC
GC BC
CQ BC
MB (ppb)
NMB (%)

## Slide 18: CMAQ 36US3 Model performance: May – June 2022 surface O3 MDA8 Bias
CF BC
GC BC
CQ BC
MB (ppb)
NMB (%)

## Slide 19: CMAQ 36US3 Model performance: July - August 2022 surface O3 MDA8 Bias
CF BC
GC BC
CQ BC
NMB (%)
MB (ppb)

## Slide 20: CMAQ 36US3 Performance Statistics Plots: O3 MDA8 Median Bias
CF BC
GC BC
CQ BC
In general, CQ BC predicts slightly higher O3_8hrmax than other two BC runs.
AQS
CASTNET

## Slide 21: CMAQ 36US3 Performance Statistics Plots: O3 MDA8 Normalized Mean Bias
CF BC
GC BC
CQ BC
In general, CQ BC predicts slightly higher O3_8hrmax than other two BC runs and has slightly better performance in spring and summer for W and SW regions.
AQS
CASTNET

## Slide 22: CMAQ 36US3 Model performance: O3 vertical profile in mid-troposphere
CQ BC has slightly better O3 (5-95%) between 40000 to 75000 Pa compared to sondes.
CF BC
GC BC
CQ BC

## Slide 23: CMAQ 36US3 Model performance: O3 vertical profile near 12US2 BCON
CQ BC has slightly better agreement of vertical profile of O3 at Trinidad Head, California sonde.
CF BC
GC BC
CQ BC
annual
winter
summer
fall
spring
annual
winter
summer
fall
spring
annual
winter
summer
fall
spring

## Slide 24: EPA’s Next Steps for CMAQ 12US2 Simulations and Evaluations
The initial CMAQ simulation at 36US3 has similar PM2.5 and O3 performance statistics using BC from simulations using GEOS-CF (CF), GEOS-Chem (GC), and HEMI-CMAQ (CQ) BC.
Detailed model performance
  Slightly better ability to capture O3 peaks in CASTNet and AQS monitors in June/July in the Southwest and West regions .
  Less negative annual bias of PM2.5 in IMPROVE sites in the Southwest and N. Rockies regions.
  Slightly better O3 (5-95%) between 40000 to 75000 Pa compared to sondes.
Flexibility
  Hemispheric CMAQ (and GEOS-Chem) runs are conducted by the EPA and we have more control on the model configurations
For EPA platform development, we are moving forward with a single set of BCs for 12km CMAQ and CAMx runs.
If we see different 12km model performance in CMAQ and CAMx then we could do sensitivity studies with differing BCs if necessary.

## Slide 25: 2022 modeling platform high level spatial and temporal trends CQ BC CMAQv5.4.0.4

## Slide 26: CMAQ 36US3 CQ BC Model: PM2.5 Annual Spatial Pattern
36km resolution, so the model cannot fully capture urban gradients or mountain inversions in the West

## Slide 27: CMAQ 36US3 CQ BC Model: PM2.5 Time Series
PM2.5 ug/m3

## Slide 28: CMAQ 36US3 CQ BC Model: PM2.5 Time Series
PM2.5 ug/m3

## Slide 29: CMAQ 36US3 CQ BC Model: MDA8 O3 Seasonal Spatial Pattern
Spatial patterns looks different for seasonal mean vs high days

## Slide 30: CMAQ 36US3 CQ BC Model: MDA8 O3 Time Series
MDA8 O3 ppb

## Slide 31: CMAQ 36US3 CQ BC Model: MDA8 O3 Time Series
MDA8 O3 ppb

## Slide 32: Sensitivity CMAQ and CAMx runs
CMAQ
  M3DRY
  Uni-directional flux
  Nitrate photolysis with full halogen chemistry
  Semivolatile POA
  Semivolatile POA with pcSOA
  Wind-blown dust
CAMx
  Uni-directional flux
  NH3 Rscale = 0
  v7.3 with more detailed SOA

## Slide 33: Next Steps
36US3 data release to AWS: October 2024
  EPIC and Lightning data
12US2 CMAQ and CAMx model runs and MPEs: November 2024
  Configuration sensitivities
12US2 data release to AWS: Nov - Dec 2024
  CMAQ: EPIC and Lightning data
  CAMx: O3 column and photolysis rate data
  ICON and BCON
Technical Support Document v1: January 2025
2022 modeling platform v2

## Slide 34: Any questions? What are States and MJOs’ plans?