## Slide 1
Control of Air Pollution from Stationary Sources
Keith Barnett
Group Leader, Minerals and Manufacturing Group
Sector Policies and Programs Division
July 9, 2019

## Slide 2: SPPD’s Role in Improving Air Quality
EPA works to improve the quality of ambient air by reducing pollution at the source
SPPD develops air emissions regulations – under authority of the Clean Air Act – that limit the pollution a stationary source can emit
The types of sources regulated include:
  Large sources such as refineries, chemical plants, and electric utility boilers
  Small sources such as dry cleaners and autobody refinishers
SPPD rules are Federal and cover all sources in a particular industrial sector regardless of location in U.S.

## Slide 3: SPPD’s Role in Improving Air Quality
The Clean Air Act (CAA) regulates emissions from stationary sources based on type of pollutant:
  Criteria Pollutants: carbon monoxide, lead, nitrogen oxides, ground-level ozone, particulate matter, and sulfur dioxides
  Hazardous Air Pollutants, or Air Toxics: 187 listed and known or suspected to cause cancer, such as xylene, mercury, chromium, benzene, dioxin, asbestos, etc.
Some regulations cover only new sources; others cover new and existing sources
The different types of regulations are governed by separate sections of the CAA

## Slide 4: Types of Regulations
New Source Performance Standards (NSPS)
  Section 111 of the CAA
  Regulates emissions of criteria pollutants
National Emissions Standards for Hazardous Air Pollutants (NESHAP)
  Section 112 of the CAA
  Regulates emissions of air toxics
Commercial and Industrial Solid Waste Incineration Units (CISWI)
  Section 129 of the CAA
  Regulates emissions of some air toxics and some criteria pollutants
Consumer and Commercial Product VOC Rules
  Section 183(e) of the CAA
  Regulates emissions of volatile organic compounds

## Slide 5: NSPS
CAA section 111 governs development of New Source Performance Standards (NSPS)
In most cases, NSPS only apply to new, reconstructed, or modified sources
  “New” means construction commenced after publication date of proposed rule
  “Reconstructed” means, after publication date of proposed rule, an existing facility (source) replaced components to such an extent that capital costs exceeded 50 percent of what it would cost to construct an entirely new facility
  “Modified” means the source was changed so that emissions of a regulated pollutant increased or resulted in emission of air pollutant not previously emitted
NSPS for new and reconstructed sources are typically the same, but there have been exceptions
NSPS limits for modified sources may be different from those for new sources
Most of SPPD’s recent rulemakings have been reviews of existing NSPS (required every 8 years)

## Slide 6: NSPS
NSPS emission limits should be based on best system of emissions reduction (BSER) – formerly best demonstrated technology (BDT)
No specific statutory definition on how to determine BSER
  Cost and economic impacts considered
  Non-air quality health, environmental, and energy impacts considered
  Technology must be adequately demonstrated
First step in BSER development is to identify applicable control technologies or other means of emissions reduction
Once identified, performance of these technologies/means are evaluated to determine achievable emissions levels
BSER selected based on costs and performance
Remember: BSER for a modified (and sometimes reconstructed) source may not be the same as BSER for a new source

## Slide 7: Standards of Performance for Existing Sources
CAA section 111(d) provides statutory basis to apply standards of performance to existing sources
Authority limited to pollutants that do not have ambient air quality standards, or are not on a list to have ambient air quality standards developed, or are not pollutants regulated under CAA section 112 (NESHAP)
The pollutants would be regulated via emissions guidelines through State Implementation Plans (SIPs)
If any state does not develop a plan, a Federal Implementation Plan (FIP) is developed and implemented
In addition to the previous considerations in developing NSPS, remaining useful life of existing sources may be considered
Notes: Note for Rick Vetter: As you are probably aware, the issue of what “are not pollutants regulated under section 112” means is front and center in the existing EGU GHG proposed rule. Our position is that we can regulate non-HAP pollutant emissions from sources even if the source is part of a category of sources subject to a NESHAP. Some in industry argue that any source category regulated under section 112 cannot be regulated under 111(d). The law has ambiguity here and we believe that we have taken a reasonable interpretation on this issue.

## Slide 8: NESHAP: MACT Standards
MACT: Maximum Achievable Control Technology
EPA must regulate all emitted Hazardous Air Pollutants (HAP)
Standards must have minimum stringency levels (MACT floors)
  For existing sources, MACT floors determined by two factors:
    If 30 or more sources, standard based on average performance of best 12 percent of sources from which EPA has emissions data
    Otherwise, standard based on average of top five performers
  For new sources, performance of the best controlled similar source
Control costs cannot be considered in setting MACT floors
Levels more stringent than the floor should always be evaluated (beyond-the-floor); costs can be considered when determining if a beyond-the-floor standard is appropriate

## Slide 9: MACT Standards: RTR
RTR: Residual Risk and Technology Review
CAA requires residual risk review once, 8 years after promulgation
CAA requires technology reviews every 8 years
The residual risk analysis covers all sources subject to the relevant MACT standard and includes:
  Major sources
  Synthetic area sources, if subject to a MACT standard due to “once-in-always-in” policy
  Area sources, if subject to a MACT standard

## Slide 10: NESHAP: GACT Standards
Smaller (area) sources of air toxics emissions may be regulated using generally available control technology (GACT)
GACT is not as clearly defined in the law as MACT
Costs and economic Impacts are considered
Technology review is required every 8 years

## Slide 11: Differences between NESHAP and NSPS
NESHAP NSPS
MACT standards always apply to major sources of HAP; area sources may be MACT or GACT | There is no major/area source differentiation
Apply to new and existing sources | Do not apply to existing sources except in limited circumstances under section 111(d)
MACT standards have a minimum stringency level (floor); cost cannot be considered | Costs are always considered
Regulate 187 hazardous air pollutants (HAP), also called air toxics | Regulate criteria pollutants (particulate matter, carbon monoxide, ground-level ozone, lead, sulfur dioxides, and nitrogen oxides; plus other non-HAP such as total fluorides)
Statutory requirement that all emitted HAP must be regulated | Do not have to regulate all emitted criteria pollutants
GACT standards have no minimum stringency and costs are considered | There is no major/area source differentiation

## Slide 12: Section 129 Standards (CISWI)
CISWI: Commercial and Industrial Solid Waste Incineration Units
CAA section 129 applies to any source burning any solid waste, as defined under the nonhazardous solid waste definitional rule
Section 129 does not apply to sources combusting hazardous solid waste (regulated under section 112)
A source cannot be subject to a section 112 and a section 129 rule at same time
Once any source is subject to section 129, it is exempt from any section 112 rule, regardless of whether or not there is currently a 129 rule in place

## Slide 13: Example of NSPS/NESHAP Rule
The simplified emission regulations for cement kilns are as follows:
NESHAP |  |  | 
If your source is a (an): | And if is located at a: | Your emissions limits are: | And the units of the emissions limit are:
Existing kiln | Major or area source | PM 0.07 D/F 0.2 Mercury 55 THC 24 | lb/ton clinker ng/dscm (TEQ) lb/MM tons clinker ppmvd
Existing kiln | Major source | HCl 3 | ppmvd
New or reconstructed kiln | Major or area source | PM1 0.02 D/F 20.2 Mercury 21 THC 24 | lb/ton clinker ng/dscm (TEQ) lb/MM tons clinker ppmvd
NSPS |  |  | 
New kiln | Major source | HCl 3 | ppmvd
New or reconstructed kiln | Anywhere | PM 0.02 NOx 1.50 SO2 0.40 | lb/ton clinker lb/ton clinker lb/ton clinker

## Slide 14: Section 129 Standards (CISWI)
CAA section 129 rules are a blend of NSPS and MACT
New sources are regulated under NSPS but the emission levels are set in the same manner as new source MACT
Existing sources are regulated under emissions guidelines and SIPs
Emission levels are set similar to existing source MACT
  Key difference: Must set MACT floors based on average of best performing 12 percent of all sources – not just 12 percent for which EPA has data
  Requires emissions be measured (or estimated) for all sources in category
Work practice standards are not allowed
Particulate matter, sulfur dioxides, nitrogen oxides, hydrochloric acid, carbon monoxide, lead, cadmium, mercury, and dioxins/furans must be regulated through numerical emission limits
Opacity regulated as appropriate
EPA can choose to regulate other pollutants but does not have to establish numerical limits

## Slide 15: Section 129 Standards (CISWI)
A section 129 rule new source NSPS is implemented in the same manner as any other NSPS
A section 129 existing source emissions guideline is implemented in the same manner as a section 111(d) Standard of Performance – through SIPs
Residual risk analysis is required once, 8 years after promulgation
Technology review is required every 5 years (more frequent than other programs)

## Slide 16: Consumer and Commercial Product VOC Rules
Reduce air pollution by limiting amounts of volatile organic compounds (VOCs) that may be present in certain commercial products
Includes consumer products such as cleaners, polishes, auto refinishing coatings, aerosols, paints, etc.