## Slide 1: Geospatial Gridding Surrogate Updates for the 2020 Emissions Modeling Platform
April 2023
James Beidler and Alison Eyth

## Slide 2: Spatial Surrogates
Map county emissions to an air quality modeling grid
Processed with Surrogate Tool Using
A modeling grid
Weighting Attributes
Spatial Unit Data (Counties)
The weighting and spatial unit data are “Shapefiles”

## Slide 3: Updated Year-specific Shapes and Weighting Data
The last significant gridding surrogate update coincided with the 2017NEI cycle and platform
New versions of previously used datasets available since the 2017 platform
  2019 NLCD replaces the 2011 NLCD
  2020 ACS/Census release replaces the 2016 release
New datasets for improved sector and SCC-specific approaches
  Livestock surrogates associated with specific animals
  Fugitive dust for unpaved roads
Updated selection of properties from legacy datasets
  Detached, single, and dual unit homes from ACS
National Land Cover Database (NLCD)
  High resolution land cover data
American Community Survey (ACS)
  Census statistics over a five year period related to housing and population
Food and Agriculture Organization (FAO) and National Pollutant Discharge Elimination System (NPDES)
  FAO remote-sensed animal specific rasters and NPDES water permits for AFOs
OpenStreetMap (OSM)
  Crowd-sourced attributes for road and parking surfaces, locations of fueling stations
USGS Mineral Resources Data System (MRDS)
  Locations and types of mines and quarries

## Slide 4: Livestock Surrogates
2010 Animal-specific FAO raster data at ~10 km resolution
  Masked with NLCD agriculture areas to improve spatial resolution for fine scales
NPDES water waste animal feedlot (AFO) permits for states where available
  IA, NC, SC, MN, WI, CA have public datasets with varying coverage by animal type
Animal types: beef cattle, dairy cattle, chicken, swine, sheep, horse, turkey

## Slide 5: NPDES Impact on Livestock Surrogates
NPDES point data improves allocation at 4 km
NC Swine
CA Dairies

## Slide 6: NLCD Surrogates
National Land Cover (NCLD) data were updated to 2019 from 2011
  Land use with percent developed impervious space
  Used to define land area, water, and development related surrogates
  NLCD surrogates commonly used as a gapfiller for other surrogates
  Downscaled to 250 m from 30 m using NN approach

## Slide 7: Available NLCD Surrogates
Open Space (< 20% impervious)
Low Development (20-49% impervious)
Med Development (50-79% impervious)
High Development (80%+ impervious)
Total Agriculture (pasture, hay, row crops)
Forest Land (all tree types)
Recreational Land
All Land
All Water

## Slide 8: OpenStreetMap Surrogates
Crowd-source open geographic database
  Network of nodes, lines, and polygons
  Contains attributes indicating
    Road amenities such as fueling stations
    Surface types of roads and parking areas
Fuel stations, asphalt surfaces, unpaved roads

## Slide 9: OpenStreetMap Surrogates (ctd.)
Unpaved roads are a key source of fugitive dust (PM)
Previous platforms used NLCD Open Space and Low Development surrogate
New surrogate uses lines/roads with unpaved surface types

## Slide 10: American Community Survey Surrogates
2020 release of 5-year data
Data by census block (sub-county) level
Population, housing, primary home heating
Detached homes and single/dual units
  New and can be used for residential wood combustion sources

## Slide 11: Other Aspects of Spatial Surrogates
Spatial surrogates are mapped to inventory data using a gridding cross-reference
  Mappings typically done using source category code (SCC) but can also be done using the state or state and county FIPS code with or without the SCC
  When quality weighting data are available mappings can be specific (ie. Sand and Gravel Quarries SCC to Sand and Gravel Quarry surrogate)
  Many sources have broad mappings (i.e. Automobile surface coating SCCs to NLCD Low + Med + High surrogate)
  Updates were made in 2020 platform for livestock, afdust, rwc, and a couple SCCs in nonpt, nonroad, and solvents
Surrogates may be gap-filled using other surrogates as generalized fallbacks when the weighting spatial data has incomplete coverage
  Example, the Beef Cattle surrogate is gap-filled by the NLCD Agriculture surrogate

## Slide 12: Other Surrogates
Oil and gas surrogates updated with 2020 year-specific data
Onroad surrogates use 2017 HPMS, same as 2017 platform
  Have not been updated with available 2018 data
NTAD rail uses 2014 data
  Updated rail lines available, but no new activity for proper weighting
Split USGS mines into lead and crushed stone types
  Last Mineral Resources Data System (MRDS) update is 2016
Airport areas, port areas, golf courses, extended idle locations are not updated
  Smaller sources, did not check for new shapefiles

## Slide 13: Possible Future Updates
Recreational waters surrogate
  Currently uses all NLCD all water, not necessarily representative of activity
Parking (on/off street)
  Exhaust and evaporative off-network emissions
  Currently uses NLCD all-development
Airport areas
  Used for av-gas refueling, weigh by general aviation activity?
Research other data sources for rail activity

## Slide 14: Appendix A. Updated Cross-reference Entries

## Slide 15: Appendix A. Updated Cross-reference cont.