## Slide 1: Projecting Emissions Inventories for Air Quality Modeling of Future Years
July 29, 2019
Alison Eyth, Jeff Vukovich, Caroline Farkas
EPA Office of Air Quality Planning and Standards
Emission Inventory and Analysis Group

## Slide 2: Future Year Projections Course Outline and Schedule
1:25 Introduction to projections
1:40 Control Strategy Tool overview
2:00 Nonpoint projections
2:20 EGU projections
2:35 Break
2:45 Oil and gas projections
3:05 Airports, Non-EGU point
3:20 Onroad and Nonroad projections
3:45 Commercial marine vessel and rail
4:00 Wrap up and final questions
Notes: Alison: Intro, EGU, Onroad
Caroline: CoST, nonEGU point, Ag, fugitive dust, Aviation
Jeff: O&G, RWC, CMV

## Slide 3: Future Year Projections
Overview
  Projections require inventories and ancillary data
  Strive for consistency in methods when there are multiple future years
Estimate changes between base and future years
  Activity changes
  Rules / technology changes in intervening years
  Facility and unit closures
  Interpolation / extrapolation often difficult
Projection techniques
  Apply factors and/or percent reductions that account for activity change and controls to a set of sources
  Add or replace a sector inventory or portion thereof
  Use a model to compute the future year inventory
Notes: Estimating growth and controls applied to an emissions sector are the typical steps used in future year projections.

## Slide 4: Future Year Projections Overview
Once created, the future year inventory is then processed by SMOKE in a similar way as if it were a base year inventory
Notes: Start with base year inventories; incorporate activity data, growth and control info, and historical data; then create future year inventory

## Slide 5: Why Develop Projected Emission Inventories?
Near-term projections to historic years
  The full NEI is developed every three years (2011, 2014, 2017, 2020 …) but we often need to do air quality modeling for years other than NEI years (e.g., 2016)
  For years in the past, existing data can help inform the projection
Longer-term future projections (e.g., 2023, 2028, 2035)
  We need to evaluate policy options and impacts of changing emissions and use the results in a relative sense
  EPA develops Regulatory Impact Analyses (RIAs) for regulations
    Describe the potential social benefits and social costs
  Interstate transport: The Clean Air Act’s "good neighbor" provision requires EPA and states to address interstate transport of air pollution that affects downwind states' ability to attain and maintain National Ambient Air Quality Standards (NAAQS)
  Other types of analyses: regional haze, etc.
Notes: Future-year projected emission inventories are used in air quality models as one way to evaluate impacts of policy options.

## Slide 6: Developing Projections (1/2)
Future year emission inventories are developed starting with the base-year inventory and modeling platform
  Techniques vary by sector
For non-historic year projections, meteorology is kept the same as base year, so base year-specific fires and biogenic emissions are used in the future years

## Slide 7: Developing Projections (2/2)
Factors to consider for each sector include:
  Confidence in base year inventory data
  Historical data available since base year
  What sources of information are available for each sector
    Databases (e.g. Annual Energy Outlook (AEO))
    Models (e.g. Integrated Planning Model (IPM) for EGUs)
  How can these sources of information be used for estimating emissions? (e.g., to update activity data)
  Spatial and temporal resolution of information
  Federal and state rules that go into effect in the intervening years are considered
  Point sources: consent decrees, planned shutdowns, etc.
Notes: Some emissions sectors require various data sources so that future-year projections can be better estimated.

## Slide 8: Modeling Platforms with Projections
2011v6.3 platform
  https://www.epa.gov/air-emissions-modeling/2011-version-63-platform
  Based on 2011 NEI version 2 with updates (used 5+ years)
  Supported the Final Cross-State Air Pollution Rule (CSAPR) Update with cases 2011ek and 2017ek, and 2017ek_cntl
  Added 2011el and 2023el for a preliminary analysis of ozone transport with respect to the 2015 National Ambient Air Quality Standard (NAAQS) for ozone
    2011en and 2023en provided updates
  Added 2028el for regional haze
2016 Platform
  2016 beta is now a real base year, not a projection
  2016 Beta platform has draft projections but 2016v1 will have final projections
Notes: Summary of future-year projection work done with the year 2011 emissions modeling platform.
Near-term projection work done with the year 2014 and 2016 emissions modeling platforms.

## Slide 9: 2011v6.3 Data on Web Site
https://www.epa.gov/air-emissions-modeling/2011-version-63-platform
Notes: The 2011v6.3 FTP site has inventories, ancillary data and reports for several cases: 2011ek, 2017ek, 2011el, 2028el, 2011en, and 2023en

## Slide 10: Projection Techniques
Inventory projection techniques differ for different modeling platform sectors
  Some done using the Control Strategy Tool (CoST) within the Emissions Modeling Framework (EMF)
  Others are taken as outputs from models
Sparse Matrix Operator Kernel Emissions (SMOKE) modeling system is used to prepare the emissions for air quality models (e.g. CMAQ, CAMx)
Notes: CoST and SMOKE are two tools that can be used to project emissions to a future year.

## Slide 11: Projections overview: Sectors projected based on NEI emissions
Sector(s) | Data sources and techniques used
Agricultural NH3 (ag) | USDA animal population growth estimates, livestock only.
Fugitive dust (afdust) | County-level VMT and population Annual Energy Outlook (AEO)-based projections to paved roads.
Residential Wood Combustion (rwc) | 2015 Wood heaters New Source Performance Standards (NSPS) with growth and appliance change-outs/retirement assumptions.
Class 1&2 CMV + trains (cmv_c1c2, rail) | Locomotive and Marine (RIA-based) rule growth and controls; California data scaled from CARB inventories.
Class 3 CMV (cmv_c3) | Regional-based growth factors + ECA-IMO engine and fuel controls, extending from ports (state), to near-offshore (EEZ) to global; California scaled from CARB data.
Oil and Gas (pt_oilgas, np_oilgas) | AEO production forecast and historical activity. Various NSPS impacts + local information.
Remaining non-EGUs (ptnonipm, nonpt) | AEO production, consumption fuel-based growth. Various NSPS impacts + local information. Numerous additional growth/control/closure information.

## Slide 12: Projections overview: Sectors not projected from NEI base year emissions
Sector(s) | Data sources and techniques used
EGUs (ptegu) | Integrated Planning Model (IPM), Eastern Regional Technical Advisory Committee (ERTAC) EGU model
Onroad mobile (onroad) | MOVES2014b w/ projected activity, fuels, inspection and maintenance, controls, speciation; Include state inputs California magnitude from CARB but temporalized based on SMOKE-MOVES
Nonroad mobile (nonroad) | MOVES2014vb projected inventories (previously NMIM/NONROAD), except for California data provided by CARB
Canada/Mexico (othar, othpt, othon) | Canada: apply projection factors; sometimes adjust based on changes to U.S. inventories Mexico: Future-year inventories projected from 2008 base year inventory plus MOVES-Mexico
Biogenics & Fires (beis, agfire, ptfire) | No projections, same as base year in non-historc projections due to constant meteorology

## Slide 13: Future-year Emissions Modeling Ancillary Data
Most ancillary (i.e., non-inventory) data stays the same in the base and future year modeling
Meteorology is held constant
Spatial surrogates are constant
Temporal profiles are constant for most sectors (except for EGUs)
Speciation profiles are constant for many sources
  Updated in future year for mobile sources
Notes: Meteorological data and spatial surrogates are two examples of data held constant when generating future-year projections.
Temporal and speciation profiles can change in future-year projections but doesn’t occur often and is limited to select sectors.

## Slide 14: Available Tools for Projection of non-EGU Point/Nonpoint Projections
Control Strategy Tool (CoST) – a good organizational and reporting tool
SMOKE – traditional approach; good for simplified projection tasks
Notes: When using CoST, start with base year inventory; compile closure, projection, and control packets; run CoST which outputs a future year inventory. This inventory goes into SMOKE and the outputs of SMOKE go into the air quality model. SMOKE can also do projections, but without the same level of tracability as CoST. This method is more likely used for simple sensitivity analyses. Still, you start with the base year inventory, develop projection and control factors, run SMOKE, and then run the AQM. Next: Jeff

## Slide 15: Questions?
Any questions on the basic concepts of projections?
Notes: Next: Jeff

## Slide 16: Control Strategy Tool (CoST)
Part of the Emissions Modeling Framework (EMF)
  https://cmascenter.org/cost/
  Used to project most NEI non-EGU point and nonpoint inventories
  Exceptions include stand-alone future year inventories (e.g., biodiesel and cellulosic plants, new cement kilns)
Has a hierarchy for how “packets” are applied
Tracks the impact of each packet on the inventory
Used for projections, but also includes algorithms for other analyses like maximum emissions reduction and least-cost
Notes: CoST is part of the EMF and is a valuable tool that allows use to apply growth and controls to generate a resulting future year inventory.

## Slide 17: Control Strategy Tool: Packet Types
CLOSURE
  Facility, unit, stack and/or process-level
  Effective date needed
  July 1 cut-off (apply if before July 1 of target year)
PROJECTION
  Scalars (e.g., 0.3 = 70% reduction, 2.0=100% increase)
  All inventories: geographic (FIPS state / county), pollutant, source classification code (SCC)
  Point only: target a facility/sub-facility / or North American Industry Classification System (NAICS)
CONTROL
  Similar facility/geographic/SCC/pollutant applicability as PROJECTION packets
  Percent reductions (0-100), optional rule effectiveness and rule penetration
  Compliance date optional
  July 1 cut-off
Notes: Packet types include CLOSURE, PROJECTION and CONTROL packets.

## Slide 18: Closure Packet Example
Closures are applied for
a target year (e.g., 2020):
Records with effective
dates up to July 1 of target
year will be applied
region_cd
facility_id
unit_id
rel_point_id
process_id
faclity_name
comment
Closures can be applied at multiple levels:
Region_cd (FIPS) - state & county code
Facility (plant)
Unit (point)
Release point (stack)
Process (segment)
New format: country_cd, tribal_cd, SCC
effective_date
Notes: Note that Plant Closure format uses older terminology of plant/point/stack/segment but Facility closure extended format uses the newer terms: facility/unit/release point process and we are working on updating to this

## Slide 19: Projection Packet Example
Factors
to apply
are here
Projection entries can also be specified at multiple levels
An older / simpler version with only FIPS, SCC, proj_factor,
and POLL also exists

## Slide 20: Control Packet Example
Ending FIPS with 000 applies to entire state
Rule effectiveness and penetration usually 100
APPFLAG of Y means to apply it
REPFLAG of R means replace existing controls, A means add on
Applied if compliance_date is before July 1 of target year
Note: A newer control format supports: country_cd, region_cd, facility_id, unit_id, rel_point_id, process_id, tribal_code, etc.
Notes: Control efficiency is the key attribute, plus the setting of the attributes to specify what is controlled

## Slide 21: Control Strategy Tool: Hierarchy
CLOSURES, PROJECTION, CONTROL packet types applied separately in a run
All packets for each type concatenated and QA’d
Most-specific applicable row (compliance date, application flag) supersedes more general entries
Care needed when there are overlapping consent decrees, comments, broad control programs
  Need to be careful how you build packets
  QA is very important to ensure output from strategy matches intentions – especially where the same sources are impacted by multiple packets
Notes: The hierarchy used in CoST is important for tracking how growth and control information is applied to a base-year inventory to create a future-year inventory.

## Slide 22: CoST Packet Priorities
General <- Specific
Entries in packets that are more specific have higher priority than the more general ones
Notes: Matching hierarchy is used to apply priorities to various growth and control information in packets input into CoST.

## Slide 23: Control Strategies within the Emissions Modeling Framework
Notes: The EMF allows the user to examine control strategies (series of packets).

## Slide 24: Editing a Control Strategy
Type of Analysis
and
Target Year are key parameters

## Slide 25: Select Inventories for Strategy
Select one
or more
inventories
to project

## Slide 26: Select Control Programs to Apply
Select all
relevant
control
programs

## Slide 27: Control Strategy Tool: Outputs
After strategy
is run, Outputs
will appear: a
Detailed result
and Messages
It is important
to review these
outputs
Summaries of
detailed result
are also helpful
After QA, create
a controlled
inventory

## Slide 28: Example Detailed Result (only selected columns shown)
Notes: Note the different types in CM_ABBREV: PTCLOSURE, PROJECTION, controls – known and unknown, then POLL, and attributes of affected point sources; also notice the specified adjustment factors, percent reductions, cost, final emissions, and emission reduction....

## Slide 29: Create Controlled inventory
Once the detailed results are quality assured, create
Controlled inventories by selecting the results of interest and clicking Create to generate the controlled inventories

## Slide 30: Control Strategy Tool: Sectors/ Relative Complexity
Some packets shared over multiple sectors, some packets contain several sources of data/programs
Simple sectors: afdust, ag, rwc, cmv_c1c2, cmv_c3, rail:
  1 projection packet for each sector
Oil & gas nonpoint (np_oilgas):
  3 packets
Remaining nonpoint (nonpt):
  4 packets
Oil & gas point (pt_oilgas):
  8 packets
Non-EGU point, not oil & gas (ptnonipm):
  14 packets
Notes: Some sectors require many different packets to estimate future-year emissions.

## Slide 31: Projections: Quality Assurance
CoST detailed results
  Review carefully to make sure the packets have been applied as you intended
  Use Compare Datasets feature of EMF to review FIPS/SCC combinations in older and newer strategies
  Do multiple levels of comparison depending on nature of the packets used: e.g., state, SCC, NAICS, poll, facility, unit
Use EMF to generate Structured Query Language (SQL)-based QA reports
  By control program
  Geography (e.g., state, county)
  Source classification code (SCC)
  Can limit pollutants in summary
  Option to show “unaffected” sources
Create custom reports and summaries
Filter / sort in CoST then export to CSV

## Slide 32: Questions?
Any questions on the Control Strategy Tool?
Notes: Next: Caroline

## Slide 33: Nonpoint Projections

## Slide 34: Data Sources for Nonpoint Projections
Energy Information Administration/Annual Energy Outlook
  Oil & gas, industrial sources
Data from multiple EPA offices
  Office of Research and Development: animal NH3
  Office of Air Quality Planning and Standards: RICE NESHAPs, regional haze, consent decrees, oil & gas, RWC
  Office of Transportation and Air Quality: portable fuel containers (PFCs), upstream emissions
  Office of Atmospheric Programs: oil & gas
  Office of Enforcement and Compliance Assurance (OECA): consent decrees
Outside agencies
  Federal: animal projections
  State/local/regional: closures, projections, ICI boilers, fuel sulfur
  Contractors: projections and controls for industrial sources including oil & gas, RWC
Collaboration needed to determine “most-appropriate” data for each source category
Notes: Various data sources are used for non-point source future-year projections. One example of a data source is the Annual Energy Outlook (AEO).

## Slide 35: Nonpoint Projections: Ag NH3
Animal-specific livestock only (no fertilizer approach: fertilizer future year = base year)
Based on national population estimates from the USDA and state submitted state- and county-based growth factors
Historical trends comparing number of animals vs production rates, net impact through 2028:
  Slight increases for cows, turkey
  Increases in pork, broilers, layers
  and poultry
Notes: USDA is typically one source of information used project emissions from livestock.

## Slide 36: Nonpoint Projections: Ag NH3 Equations
~
  Projection Factor:
  Example: Beef cows projected to 2023 from 2016
  = 1.04
Notes: Base year and future year activity information can be used to generate a projection factor.

## Slide 37: Ag Control Program
Select a dataset
for the control
program then
view the data…
Notes: Edit control program window for ag projections. Includes strategy name, description, start date, end date, who created it, dataset type, dataset, and version.

## Slide 38: Nonpoint Projections: Ag NH3 (continued)
  For each pollutant and SCC
  * If State or Regional data were available, this calculation would apply the corresponding projection factor based on FIPS and SCC
Ag Projection packet in EMF data viewer
(SCC-specific, but not FIPS or POLL-specific)
Notes: The base year emissions are multiplied by projection factors according to their SCCs.

## Slide 39: Nonpoint Projections: Fugitive Dust
  Impacts paved road dust only; unpaved road dust held constant for future years in 2016 platform
  Function of VMT on roads
  Onroad VMT projected to future year using AEO
  County projection factor equation
    PROJFAC = (Future-year total county VMT)
                (Base-year total county VMT)
  Future emis = PROJFAC * base emis
Notes: Fugitive dust emissions are a function of VMT. Future year VMT estimates are used to project emissions for fugitive dust sector.

## Slide 40: Example Fugitive Dust Packet
Projection
factors
are
specific
to each
county
the same
for each
pollutant
Notes: Spreadsheet showing fugitive dust packet. Columns are FIPS, SCC, PROJFAC, and comment showing source type.

## Slide 41: QA of ag/afdust Projections
Compare base and future year emissions to ensure that factors were properly applied
Create percent and absolute difference maps to make sure that results are as expected
Note: Future year fugitive dust inventories undergo meteorological and transport fraction reductions like the base year ones do

## Slide 42: Regional Grouping for Bar Charts
Source: https://www.ladco.org/wp-content/uploads/Images/MJOs_Feb2019.png
Notes: Map of regional planning organizations: WRAP, CenRAP, MWRPO, MidAtlantic/Northeast, VISTAS. These will be used in charts.

## Slide 43: Changes in ag NH3 emissions 2016-2028
CENRAP LADCO Northeast SESARM WRAP
Orange= 2016ff
Yellow = 2023ff
Green = 2028ff
Difference in tons
Difference in percent
Notes: State level map of agricultural NH3 emissions shows that NC, TX, CA, and IA are highest. NH3 is expected to increase moderately from 2016 to 2023 and 2028. The CENRAP region has more than twice as much ag NH3 emissions as any other regions. Percent change in VOC would look the same as NH3, but not the absolute difference.

## Slide 44: Changes in afdust PM2.5 2016-2028
3,000,000
CENRAP LADCO Northeast SESARM WRAP
Orange= 2016ff
Yellow = 2023ff
Green = 2028ff
Notes: Map of fugitive dust emissions shows that TX, NM, KS and IL have the highest emissions. The CENRAP region more emissions than other areas. Emissions are expected to increase because paved road dust emissions are correlated to VMT increases in later years.

## Slide 45: Nonpoint Projections: Residential Wood Combustion
Growth derived from year 2012 appliance shipments and revenue forecasts (e.g. US Bureau of Economic Analysis)
Updated to include the NSPS for ‘wood heaters’: https://www.epa.gov/residential-wood-heaters/final-2015-new-source-performance-standards-residential-wood-heaters
Net decrease rather than increase in RWC emissions vs business as usual approach in prior platform
Reflect year 2015 rulemaking and minor corrections
Appliance-specific retirement/replacement rates for most sources
“No-change” assumption used in western states: WA, OR, CA
Burn bans not addressed due to their unpredictable episodic nature
Notes: Sometimes it is found best to assume “no-change” in emissions from base to future year (e.g. Western states in the residential wood combustion). However, each new modeling platform requires that assumptions be revisited.

## Slide 46: Packets for RWC projections
Different factors are applied by SCC (i.e., fireplaces, fireplace inserts, wood stoves), emissions held constant in CA, OR, WA

## Slide 47: Changes in RWC Emissions 2016-2028
Notes: Maps and a chart show how residential wood combustion emissions change from 2016 to 2028. States with the most RWC are MN, MI, and WI, followed by NY and PA. The LADCO and Northeast have the most PM2.5 emissions from RWC, but WRAP and CENRAP are close. Emissions are projected to decrease by 2028. Methods for estimating RWC emissions changed in 2014, so the emissions look different in 2014 and 2016 and projections off of 2014 may look different in nature.

## Slide 48: Questions?
Any remaining questions on nonpoint sectors?

## Slide 49: EGU Projection Methods
EPA primarily uses the Integrated Planning Model (IPM)
  The National Electric Energy Data System (NEEDS) database defines the sources used in IPM
  NEEDS is regularly updated to reflect announced retirements and planned controls
    Data sources include EIA Form 860, Emissions Tracking System (ETS) / CAMD Data and stakeholder comments
  IPM has been updated over time to account for new data, including energy supply, demand, and prices, from a variety of sources, including EIA’s Annual Energy Outlook
  IPM output emissions are “dropped in” to replace ptegu emissions that were used in the base year
For the 2023en case, engineering analysis was used
  Incorporated historic 2016 emissions and other known upcoming changes to project to 2023
ERTAC EGU model has been developed by MJOs
  Used by many states and groups for planning purposes

## Slide 50: EGU Projections with IPM
EGUs are identified in the NEI point inventory by filling in the IPM_YN column of the flat file
  Populated from a set of alternate IDs stored in EIS
  Sometimes there are not 1-1 matches between units in the NEI and the NEEDS database used by IPM
IPM reflects impacts of rules in intervening years
  E.g., CSAPR, MATS, BART
IPM v6 produces outputs for these years:
  2021, 2023, 2025, 2030, 2035, 2040, 2045, 2050
  Updated inputs, assumptions, and features
More information on IPM is available here: https://www.epa.gov/airmarkets/clean-air-markets-power-sector-modeling
Notes: Note: ACE is not included in the May, 2019 case but the impacts would be very small even if it were.

## Slide 51: Flat Files Created from IPM Outputs
IPM regional, seasonal outputs are converted to a Flat File format that can be input to SMOKE
  For a specific model output year, parse results to unit-level for each season (Pollutants = NOx, SO2, Hg, CO2)
  SMOKE-ready Flat file is created from parsed file
    Cross reference from National Electric Energy Data System (NEEDS) to NEI units is used to assign NEI-compatible IDs, locations, stack parameters (improved with state review)
    PM emissions are created as a postprocess based on emission factors, fuel, and control information
The base year EGU inventory is fully replaced by the flat file inventory output from IPM
  IPM results not used in air quality modeling for geothermal, nuclear, wind, solar, or hydro

## Slide 52: Future year EGU Processing with IPM
Parsing to
unit-
level
NEI to
Flat file
creation

## Slide 53: Map of 67 IPMv6 Output Regions
https://www.epa.gov/airmarkets/documentation-epa-platform-v6-november-2018-reference-case-chapter-3-power-system
Notes: https://www.epa.gov/sites/production/files/2019-03/documents/chapter_3_0.pdf Figure 3-1

## Slide 54: EGU Temporal Allocation for Future Years
For sources with CEMS that exist in both base and future years, allocate seasonal emissions to base year (2011 or 2016) hourly temporal pattern of CEMS data by pollutant (i.e., NOx, SO2)
  Compute hourly ratio for each hour of season in base year and multiply that by the seasonal total to get the future year hourly emissions
Units not matched to CEMS data (aka “non-CEMS”) are temporalized using fuel- and pollutant-specific regional average profiles to allocate emissions to month, then day, then hour
  Method is also used for new units, units with no base year emissions, units that change fuels from base to future, and units with large predicted increases in emissions

## Slide 55: Temporal profile regions are Consistent with those used in base year

## Slide 56: Example Temporal Plots: base year, unit-specific, regional
Compute fraction
of emissions @ each
hour of the season (winter/summer)
2. Future emissions @
each hour = seasonal
emissions * hourly factor
Seasonal emissions going down in
this example
Regional average profile (red) does not include gaps
CEMS-based profile (green) has service gaps

## Slide 57: Adjust Emissions Below Historic Maximum
When emissions are found to go above the historic maximum, allocate the excess evenly to other hours
Notes: For 2016 platform, historic maximum from 2014-2017 was computed and used. For 2011 platform, years were 2011-2016.

## Slide 58: Use Regional Profile when Cannot Adjust below Historic Maximum
See 2023en emissions modeling TSD for more details

## Slide 59: Regional Profile Applied but Exceeds Historic Maximum in Some Hours
Notes: Sometimes even when we apply a regional profile, it can exceed the historic maximum in some hours.

## Slide 60: Changes in EGU emissions 2016-2028
500,000

## Slide 61: Questions?
Any questions on EGU projections?
Notes: Next: Jeff

## Slide 62: Oil and Gas Projections
Volatile sector; industry changing frequently
Various data sources
  State and county historical data
  Annual Energy Outlook (AEO) tables
Various approaches are available

## Slide 63: Oil and Gas Projections Overview
Data sources
  Annual Energy Outlook (AEO) production forecast data from the Energy Information Administration (EIA) to estimate activity in future years
  State historical production data to capture recent growth
  County historical exploration data from recent years
New Source Performance Standards (NSPS) applications
Includes both point and nonpoint sources
  Point: Production, Pipelines, other supporting activities
  Nonpoint: Production and Exploration
Includes data and comments from states and regional planning organizations on the 2016 emissions platform
Notes: AEO-forecasted and historical oil and gas production data can be use to estimate growth in this sector.

## Slide 64: Applying Growth and Control Factors to Project Emissions
Notes: The flowchart starts with the base year inventory. Projection packets are developed from historic and AEO forecast production data. Control packets are developed based on the projected production data and the impact of NSPS and other control programs. The packets are fed into CoST to create a future year inventory, which is then processed by SMOKE to create AQM-ready emissions.

## Slide 65: Oil and Gas Supply Regions: AEO2018
Notes: Map of oil and gas supply NEMS regions. Consists of west coast, rocky mountains, midcontinent, east, gulf coast, and Southwest (western TX and eastern NM).

## Slide 66: Oil and Gas Supply Regions: AEO2019
Rocky Mountain/Dakota
region in AEO2018 now broken up into 2 regions
Notes: Map of oil and gas supply NEMS regions. Consists of west coast, rocky mountains, midcontinent, east, gulf coast, and Southwest (western TX and eastern NM).

## Slide 67: Oil and Gas Projections: Supply Region-Level Forecasts Method
AEO Tables: Regional production
  Table 60: lower 48 crude oil production
  Table 61: lower 48 natural gas production
AEO Tables: national production
  Table 14: Oil and gas supply
    Coalbed methane production
    Natural gas liquids production
    Offshore production: state-owned sources only
Develop oil/gas/both cross-reference by source classification code (SCC) to apply regional/national factors
Notes: Various tables from the AEO are used to support the development of projected future year emissions for oil and gas sources.

## Slide 68: Oil and Gas Projections: Supply Region-level example used for 2011 platform
Applied this method for 2011v6.3 modeling platform along with state-specific factors supplied from MARAMA
Large regions where only 2-3 states make up the bulk of the production can cause issues with smaller-producing states in the region
Notes: AEO forecasts oil and gas production in various supply regions. Growth can be quite different region to region.

## Slide 69: AEO Supply Region example
Notes: Expected production levels from 2016-12030 is shown in the table for each year and NEMS region - both onshore and offshore in million barrels per day

## Slide 70: AEO Supply Region Example (2)
Notes: Projection factors are derived for teh east and Gulf Coast regions for each year starting with 2016 by dividing the future year by the 2016 production. The East factor for 2028 is 1.629 and the Gulf Coast is 1.2.

## Slide 71: Oil and Gas Projections: Historical State Data + AEO Supply Region Method
Historical state change
X
AEO Supply Region change
Combined factors representing both historical state data and AEO supply region change for each state
Notes: Historic factors from 2011-2016 multiplied by AEO factors from 2016 to the future year to compute a combined factor by state.

## Slide 72: Oil and Gas Projections: Online Historical State Data
Historical state production data publicly available on EIA website used to project sources from a base year to a recent year (e.g. 2016 to 2017 or 2018)
  Natural Gas http://www.eia.gov/dnav/ng/ng_sum_lsum_a_epg0_fgw_mmcf_a.htm
  Crude Oil http://www.eia.gov/dnav/pet/pet_crd_crpdn_adc_mbbl_a.htm
  Coalbed methane https://www.eia.gov/dnav/ng/ng_prod_coalbed_s1_a.htm
Notes: Recent historical oil and gas production data at the state-level can be obtained and use to bridge the gap from base year (e.g. 2014) to a more recent year (e.g. 2016).

## Slide 73: Oil and Gas Projections: Historical State Data Bridge to Supply Region-Level Forecast
Then use AEO Supply Region production forecasts to project from 2017 or 2018 to desired future year
  Some adjustments based on historical trends for “low production” states may be needed
Combine factors to get a state-specific projection factor from base year to desired future year
For nonpoint sources use SCC-oil/gas/both cross-reference to apply state-specific factors
For point sources use a oil/gas/both cross-reference by SCCs and North American Industry Classification System (NAICS) codes to apply state-specific factors
Notes: Recent historical oil and gas production data at the state-level can be obtained and use to bridge the gap from base year (e.g. 2014) to a more recent year (e.g. 2016).

## Slide 74: Oil and Gas Projections: NSPS Controls
New Source Performance Standards applications
  Oil and Gas (VOC)
  Process Heaters (NOX)
  Reciprocal Internal Combustion (IC) Engines (NOX, CO and VOC)
  Natural Gas Turbines (NOX)
Point and nonpoint sources where applicable
Notes: A control efficiency formula is one method that can be used to estimate a reduction of emissions due to NSPS controls.

## Slide 75: Oil and Gas Projections: NSPS Controls
For future-year NSPS controls, we attempted to control only new sources/equipment
  Accounts for growth and retirement of existing sources and the differences between the new and existing source emission rates
Control_Efficiency (%) = 100 * (1- [(Pf-1)*Fn + (1-Ri)t + (1-(1-Ri)t)*Fn]/ Pf)
  Pf = growth rate expressed as ratio (e.g. 1.5=50% cumulative growth)
  t = number of years between base and future years
  Fn = emission factor ratio for new sources
  Ri = retirement rate, expressed as decimal (e.g., 3.3%=0.033)
Notes: A control efficiency formula is one method that can be used to estimate a reduction of emissions due to NSPS controls.

## Slide 76: Changes in Nonpoint Oil/Gas 2016 to 2028 beta
300,000
100,000
1.5M
0.5M
NOx
VOC
NOx
Notes: Changes in NOx emissions from base to future year can vary state-to-state or region-to-region.

## Slide 77: Changes in Point Oil/Gas 2016 to 2028 beta
150,000
50,000
80,000
20,000
NOx
VOC
NOx
Notes: States with largest point oil and gas NOx emissions are TX, OK, KS, CO, LA. Bar chart of VOC emissions shows that CENRAP and WRAP have the most emissions. Slight changes are projected by 2028 in CENRAP and significant increases in WRAP. 2014 is estimated quite differently in the WRAP region. Bar chart of VOC emissions shows that CENRAP and WRAP have the most emissions. Slight changes are projected by 2028 in CENRAP and significant increases in WRAP. 2014 is estimated quite differently in the WRAP region. Emissions are projected to decline in IA, MO, and KS, and increase in TX and CO.

## Slide 78: Possible Future Work for Oil and Gas Projections
Continue to examine methods to take basin-level information into account where possible
Include more state or county historical data when possible
Better incorporate state and any updated federal regulations on emissions
Improve NAICS and SCC cross-references
  Some states submit with different SCCs than others
Consider approaches for other non-production related point sources (e.g. pipelines and other supporting activities)

## Slide 79: Questions on Oil and Gas Projections?
Notes: Next: Caroline

## Slide 80: Non-EGU Point Projections: Aviation
Aircraft emissions are in ptnonipm sector
Projected itinerant ITN (i.e., take off and landing) operations information available from the Federal Aviation Administration’s (FAA) Terminal Area Forecast (TAF) System:
https://www.faa.gov/data_research/aviation/taf/
Two sets of projections factors used:
  State-level for low traffic airports
  Airport-specific factors for larger airports
  15,000 of 24,000 factors = 1.0 including most military aircraft; others could be less than or equal to 1.0
Notes: Review source data for background info

## Slide 81: Example Projection Factors for Aviation
Notes: Table of projection factors for aircraft at airports has columns FIPS, SCC, pROJFAC, POLL and comments. Factors differ by county and SCC, but state-aggregates are also available

## Slide 82: Non-EGU CoST Packets
Closures: 2016 beta platform
Control: 2016-2028 nonpt ptnonipm RICE NSPS beta platform
Control: 2016-2028 ptnonipm Natural Gas Turbines NSPS beta platform
Control: 2016-2028 ptnonipm Process Heaters NSPS beta platform
Control: 2016-202X ptnonipm AZ Regional Haze beta platform
Control: 2016-202X ptnonipm CISWI beta platform
Control: 2016-202X ptnonipm Consent Decrees and other comments
Control: 2016-202X ptnonipm NSPS Subpart Ja beta platform
Control: 2016-20XX MANEVU Sulfur beta platform
Control: 2016-20XX NC Boiler MACT beta platform
PROJECTION 2016-2028 industrial SCC beta platform
PROJECTION 2016-2028 industrial SCC-NAICS beta platform
PROJECTION 2016-2028 ptnonipm aircraft beta platform
PROJECTION 2016-2028 rail beta platform
Notes: Set of non-EGU CoST packets: closures, control, projections.

## Slide 83: Non-EGU Projections: Non-CoST
Some future-year sources do not exist in the NEI for the base year
  Biodiesel and cellulosic ethanol plants
  Other sources added based on comments
Take emissions for these sources as they are reported / provided
  These are put into separate inventory files
  Hard to project to additional future years

## Slide 84: Non-EGU Projections: Petroleum Refineries – NSPS Subpart JA
  Rule effective February 2016 – VOC reductions from controls at delayed coking units and storage vessels
  Across-the-board control factor for impacted units
    84% for delayed coking units; 49% for storage vessels

## Slide 85: Non-EGU Projections: CISWI Units – NSPS and Emission Guidelines
  Considers the MACT for incinerators, energy recovery units, waste-burning kilns, small, remote incinerators
  All impacted units are to have control devices in place by 2018
Existing control devices and baseline emissions based on a 2008-2009 Information Collection Request
Floor emissions represent all units’ emissions after employing least-cost controls to meet MACT standard

## Slide 86: Changes in Non-EGU Point 2016-2028
300,000
2016beta non-EGU Point SO2
2028-2016beta non-EGU Point SO2

## Slide 87: Projections High-level impacts: ptnonipm sector NOX
CoST can isolate the impact of each control/projection packet
Chart: 2028beta minus 2016beta
| Closures | Control: RICE NSPS | Control: NG Turbines NSPS | Control: Process Heaters NSPS | Control: AZ Regional Haze | Control: CISWI | Control: Consent Decrees | Control: NSPS Subpart Ja | Control: MANEVU Sulfur | Control: NC Boiler MACT | PROJECTION: Industrial SCC | PROJECTION: Industrial SCC-NAICS | PROJECTION: Aircraft | PROJECTION: Rail
Total | -1050.0146 | -4085.8346 | -3305.931 | -12568.9509 | -1377.525 | -1727.905 | -9118.6452 | -1.0283 | -51.7505 | -1807.7817 | 2037.5178 | 38170.0971 | 47499.0325 | 1980.6875

## Slide 88: Non-EGU Projections: Challenges/Limitations
Response to comments on prior platforms:
  Many different sources of data – need to correctly layer these so appropriate controls/projections apply
State/Regional-submitted data
  Some data provided for a complete range of years, but other data provided for 2023 but not for 2028
Promulgated vs proposed rules vs SIP inventories are confusing
Rapidly-changing world!
  2019 AEO released + 2017 NEI being developed

## Slide 89: Questions on Non-EGU Point?
Notes: Next: Alison

## Slide 90: Onroad Projections Overview
MOVES2014b is used to develop emission factors for light-duty and heavy-duty vehicles
Main components adjusted for projections:
  Regulatory impacts (e.g., Tier-3, LD & HD GHG/CAFE standards, Modifications to Renewable Fuel Standard (RFS2), Mobile Source Air Toxics Rule (MSAT), California LEVIII)
  Fuel composition changes
  Inspection and Maintenance (I/M) programs
  Vehicle age distributions (in some cases)
  Vehicle Miles Traveled (VMT) and other activity data
  Most of these changes are included in the approximately 300 representative county databases from which emission factors are computed
  SMOKE combines activity data and emission factors
Notes: CDB is where you update age distribution/fleet mix, I/M program. MOVES databases for LEV standards and regional fuel changes by year. Regulations are controlled by MOVES;

## Slide 91: Onroad Projections Data Flow
MOVS is run for each
representative county
County-specific
activity data
are used for
each county
Notes: Onroad mobile emissions are estimated using MOVES, activity data and the SMOKE modeling system.

## Slide 92: Onroad Emission Processes and Inputs
On-roadway emissions [Rate per Distance]
  Exhaust, evaporative, evaporative permeation, refueling, brake and tire wear
  Primary inputs: vehicle miles traveled (VMT), average speeds, speed profiles, and temperature (gridded, hourly)
Off-network emissions (i.e. parked vehicles)
  Exhaust from starts, evaporative, evaporative permeation, refueling, hot soak (after a trip) [rate-per-vehicle (RPV)]
  Evaporative fuel vapor venting and diurnal (when vehicles are parked for a long period) [rate-per-profile (RPP)]
  Primary inputs: vehicle population (VPOP) and Temperature
Hoteling:
  Extended idle and auxiliary power units (APU) for combination long-haul trucks
  Primary inputs: Hoteling hours and T (gridded, hourly) [rate-per-hour (RPH)]
Notes: VMT and HOTELLING are temporalized, VPOP is not

## Slide 93: Onroad Projections Details
Constant between base year and future year
  Meteorology
  Representative counties
    If change representative counties, will create artificial spatial inconsistencies between base and future years
  Spatial surrogates for gridding
  Speeds
  Temporal profiles
Speciation is not constant
  Dependent on model year, fuel, etc.
Approaches differ for short-term vs. longer-term
  MOVES CDBs updated and runs done for both
Notes: CDB is where you update age distribution/fleet mix, I/M program. MOVES databases for LEV standards and regional fuel changes by year. Regulations are controlled by MOVES

## Slide 94: Short-term Projection for 2016
FHWA provided urban / rural county-level VMT for 2016
  By road type: interstate, freeways, arterials, collectors, local
2016 VMT projected from 2014NEIv2 using state+urban and state+rural factors derived from FHWA VM-2 tables
  https://www.fhwa.dot.gov/policyinformation/statistics/2014/vm2.cfm
  https://www.fhwa.dot.gov/policyinformation/statistics/2016/vm2.cfm
  Use state overall factors when changes in urban/rural definitions between caused factors to be more different than they should be for two years of change
  State DOT web sites can sometimes have different trends than FHWA
Preserved 2014v2 ratio of VMT/hoteling hour for long-haul combination trucks in 2016
Preserved 2014v2 ratio of VMT/vehicle was in the 2016 vehicle Population (VPOP)
QA: Compare original and projected activity data

## Slide 95: Onroad NOx: 2016 vs 2014NEIv2
Notes: Changes due to fleet turnover – newer vehicles more efficient; note ND VMT is going down

## Slide 96: Longer-term VMT projections
Activity data for longer-term projections based on AEO
  Light-Duty gas, diesel and E-85
    Table 42: LD vehicle miles travelled by technology type
      Motorcycles, cars, light-duty trucks
  Heavy-Duty gas and diesel, Bus CNG
    Table 50: Freight Transportation Energy Use
      Heavy-Medium (Buses and Single Unit trucks)
      Heavy (Combo Unit Trucks)
  Light-duty Geographic variation using projected human population data
Notes: Two different tables (one for light-duty and one for heavy-duty vehicles) from the AEO are typically used to project VMT to a future year.

## Slide 97: AEO example: Light duty VMT
Notes: Light-duty VMT table from AEO (Table 42).

## Slide 98: AEO example: Growth Factors
AEO-specific categories are grouped to create growth factors
Notes: This chart shows examples of AEO growth factors by technology type and fuel from 2014 through 2023. MOVES supports emissions of light-duty vehicles for gas, diesel, E-85, and electric but not the items below the line: natural gas, propane, or fuel cells. Factors for LD gas are 1.1 from 2014 to 2023.

## Slide 99: VMT projections variation (1 of 2)
Use AEO to get magnitude of change nationally
Adjust light duty (LD) VMT projections geographically based on expected human population changes
Analysis indicated strong correlation between human population and LD VMT
Correlation between population and medium and heavy duty (MD/HD) VMT is not as strong
  Use national factors for medium and heavy duty

## Slide 100: VMT projections variation (2 of 2)
LD VMT projections for 2025 from 2011
National projection
With adjustment based on
human population changes
Notes: There is variation even in the national projection b/c of difference mix of vehicle/fuels by state/county

## Slide 101: Onroad Projection Details
Vehicle Population (VPOP) uses same projection factors as VMT
Hoteling
  Calculate the total hoteling hours from future year combination long-haul restricted VMT
  Split between auxiliary power units (APUs) and extended idling (EXT) changes in future years due to greater penetration of APUs
Speciation
  Changes in model year and fuels impacts not only the emissions but the speciation
  Speciation internal to MOVES2014 makes it possible to consider detailed model year, regulatory class, and fuel information

## Slide 102: Changes in Onroad NOx and VOC emissions 2016-2028
Notes: Top: NOx from 2016 and 2028 plotted on same scale – substantial reductions
Bottom: VOC for 2028 and percent reductions from 2016 – NOx reduction map shows even more reductions.

## Slide 103: Nonroad Projection Overview
Nonroad sector = Exhaust, evaporative, and refueling emissions from nonroad engines (not including CMV, aircraft and locomotives)
  Construction equipment, recreational marine, lawn & garden
Nonroad has been within MOVES since MOVES2014a
  Previously used National Mobile Inventory Model (NMIM)
Regulatory programs included:
  Nonroad spark-ignition engines
  Locomotive & marine engines less than 30L/cylinder
  Clean Air Nonroad Diesel Final Rule
Notes: Nonroad emissions projections are done within the MOVES modeling system.

## Slide 104: Nonroad Projection Details
Unlike onroad, can use the same input county databases as the base year
Run for future year with appropriate Meteorology (consistent with base year)
Fuels should be consistent with the future year and ideally with the onroad fuels
VOC speciation differs from base year to account for shift toward 10% ethanol fuels for nonroad
California-projected emissions used in CA
MOVES2014b included updated growth factors

## Slide 105: Nonroad updates in MOVES2014b
MOVES2014b (released Aug. 2018) improves estimates of emissions from nonroad equipment
  Updated Tier 4 engine technology categories to account for after-treatment configurations
  Updated Tier 4 engine population fractions, emission factors, and speciation profiles
  Updated nonroad marine diesel sulfur levels to be 15 ppm for 2014 and later (down from 55-56 ppm)
  Harmonized nonroad diesel sulfur with onroad diesel for most calendar years since 2007 (up from 11 ppm)
  Updated nonroad engine population growth rates with state-level, equipment sector-specific annual growth indices
    This is the primary driver of differences in emissions between MOVES2014b and previous versions of the model

## Slide 106: Nonroad sector-level national summary 2016 alpha vs beta
- Alpha produced with MOVES2014a include state inputs from 2014NEI
Beta produced with MOVES2014b; all emisisons in tons
See 2016 Wiki: http://views.cira.colostate.edu/wiki/wiki/9179
Note: emissions from Airport Support and Oil Field Equipment are excluded from nonroad inventories.
** Growth trends to future years also updated in MOVES2014b **
See MOVES2014b Nonroad Technical Reports (https://www.epa.gov/moves/nonroad-technical-reports)

## Slide 107: Recreational and Commercial Nonroad NOx: 2016ff and Changes from 2016fe
Notes: The spatial distribution of emissions varies by Nonroad sector, and the impacts from MOVES 2014b updates also vary.

## Slide 108: Pleasure craft and Total Nonroad NOx 2016ff vs 2018ff

## Slide 109: Questions on onroad or nonroad projections?

## Slide 110: International Projections
Canada
  Base year is 2015
  Projection factors to various years provided by Environment and Climate Change Canada
    Updated inventories computed by EPA based on factors
Mexico
  Mexico point, nonpoint, nonroad inventories projected to years 2018, 2025 and 2030 and interpolate as needed – better data needed
  Interpolate MOVES-Mexico outputs as needed between available years of 2014, 2017, 2020, 2023 and 2028
Notes: Future year emissions inventories for Mexico and Canada are available for point and non-point sources.

## Slide 111: 2028 Canada Afdust PM2.5 and Onroad NOx emissions with changes from 2016 at 36km

## Slide 112: Othar 2028 NOx and NH3 and changes from 2016

## Slide 113: Othpt SO2 and NH3
Notes: SO2 has some increases and decreases. Canada SO2 includes CMV-C3 in Canada in beta.
NH3: Note the waffle pattern in the base year that was corrected in the future year.

## Slide 114: Questions?
Any questions on international emissions projections?
Notes: Next: Jeff

## Slide 115: CMV and rail Projections
Rail includes on-rail line locomotives
  Yard Locomotives in point source inventory use different factors
The future year cmv and rail emissions account for increased fuel consumption based on Energy Information Administration (EIA) fuel consumption projections for freight
Regulatory programs:
  Final Locomotive-Marine rule for engines less than 30L/cylinder, Clean Air Nonroad Diesel Rule
  Category 3 marine diesel engines Clean Air Act and International Maritime Organization Standards
    CMV Exclusive Economic Zone (EEZ) reductions: SO2 reductions in EEZ 200 nautical miles from state waters by 2015, and implemented globally by 2020
Notes: Rules and standards in Regulatory programs must be understood and estimated in future-year emissions projections (e.g. Final Locomotive-Marine rule).

## Slide 116: National Projections for Rail NOx
 | 2016-to-2023 | 2016-to-2028
Passenger trains | +8.8% | +16.2%
Freight and Yard Locomotives | +0.8% | +4.7%
Notes: Note differences by pollutant and different factors for California

## Slide 117: Regional Projections for CMV C3 2016beta
Region | 2016-to-2023 NOX | 2016-to-2023 other pollutants | 2016-to-2028 NOX | 2016-to-2028 other pollutants
US East Coast | -6.1% | 27.7% | -7.5% | 49.7%
US South Pacific | -24.8% | 20. 9% | -34.0% | 45.9%
US North Pacific | -3.4% | 22.6% | -4.1% | 41.3%
US Gulf | -6.9% | 20.8% | -12.4% | 36.4%
US Great Lakes | 8.7% | 14.6% | 19.8% | 28.3%
Other | 23.1% | 23.1% | 42.6% | 42.6%8

## Slide 118: Regional CMV C3 emissions 2016, 2023 and 2028 beta
Region | Pollutant | SCC | SCC Description | 2016ff | 2023ff | 2028ff
US State Waters | CO | 2280003100 | Port Emissions | 2,624 | 3,295 | 3,829
US State Waters | CO | 2280003200 | Underway Emissions | 8,156 | 10,137 | 11,689
US Federal Waters | CO | 2280003200 | Underway Emissions | 45,047 | 55,954 | 65,536
US State Waters | NOX | 2280003100 | Port Emissions | 23,561 | 22,105 | 21,568
US State Waters | NOX | 2280003200 | Underway Emissions | 82,673 | 77,671 | 75,215
US Federal Waters | NOX | 2280003200 | Underway Emissions | 468,064 | 416,157 | 395,655

## Slide 119: Regional Projections for CMV C1/C2 2016beta
Pollutant | 2014-to-2016 | 2014-to-2023 | 2014-to-2028
CO | -1.4% | -2.7% | -1.1%
NOX | -7.4% | -34.6% | -48.7%
PM10 | -11.0% | -36.2% | -49.6%
PM2.5 | -11.0% | -36.2% | -49.6%
SO2 | -60.3% | -86.2% | -86. 5%
VOC | -8.0% | -37.0% | -51.4%

## Slide 120: Changes in CMV C3 NOx 2016-2028
Notes: Maps and charts of CMV and rail NOx emissions are shown. The states with the most NOx emissions are TX, LA, FL, CA, and NE. Emissions are projected to decrease substantially by 2028. The methods for estimating CMV NOx changed in 2014 and those emissions are quite a bit lower than 2011 or the 2011-based projections .

## Slide 121: Changes in CMV C1C2 NOx 2016-2028
Notes: Maps and charts of CMV and rail NOx emissions are shown. The states with the most NOx emissions are TX, LA, FL, CA, and NE. Emissions are projected to decrease substantially by 2028. The methods for estimating CMV NOx changed in 2014 and those emissions are quite a bit lower than 2011 or the 2011-based projections .

## Slide 122: Questions?
Any questions on CMV or rail projections?

## Slide 123: Ongoing work and New Directions
2016 modeling platform
  Workgroups wrapping up
  Preparing emissions for version 1 for the years 2016, 2023, 2028
  Beta platform for 2016 currently available
  V1.0 platform coming soon
Possible New Directions
    Projections of changes in land use/population
      Surrogates, New sources, Biogenics, Ag fertilizer
    Improve Mexico inventory
    Incorporate WRAP oil and gas and EGU inventories
    Fires: Impact on biogenics, future year modeling treatment

## Slide 124: Emissions Modeling Software and Data Downloads
The CMAS Center distributes many tools (https://www.cmascenter.org/)
  SMOKE, CMAQ, VERDI (visualization), the Surrogate Tool, Spatial Allocator, Speciation Tool, and the Control Strategy Tool which includes the Emissions Modeling Framework
SMOKE software and documentation is available from http://www.cmascenter.org/smoke
A WIKI for SMOKE that answers common questions about emissions modeling is here: https://www.airqualitymodeling.org/index.php

## Slide 125: Emissions Modeling Platform Data Availability
EPA’s modeling platform data, documentation, scripts available from
  https://www.epa.gov/air-emissions-modeling
  Version 6 platforms include:
    2011v6.3: January 2017 NODA (2011el/2023el), Final Cross-State Air Pollution Rule (CSAPR) Update (2011ek/2017ek), hemispheric case
  Version 7.0 platform for NATA based on 2014NEIv1
  2016 alpha platform with compatible 2014 and 2015
  Spatial surrogates available for 4km, 12km, 36km
  Speciation data for CB05, CB6, SAPRC07TB
  Temporal profiles for all sectors

## Slide 126: Emissions Modeling FTP site
Several versions of the 2011 platform plus versions of 2014,2015, and 2016 are available on the FTP site:
ftp://newftp.epa.gov/air/emismod
Notes: Tree of FTP site organization shows the various platforms organized according to the base year.

## Slide 127: 2016 beta Release Documentation
http://views.cira.colostate.edu/wiki/wiki/9169
Specification Sheets
27 documents in a standardized format
Describe the sector, the SCCs/sources included in the sector, data sources, processing methods
Graphical and tabular summaries of the data

## Slide 128: Downloading from IWDW
Once you log in with your account, select the components you need

## Slide 129: IWDW Interactive map / chart

## Slide 130: LADCO Example Stacked Bar Plot: National NOx Emissions by Sector
2011v6 20232011 20282011 2014 2016beta
https://www.ladco.org/technical/modeling-results/2016-inventory-collaborative/
Notes: Overall the 2016beta NOx inventory is lower in 2016beta than both 2011 (-20.4%) and 2014 (-10.6%). Declining emissions from most sectors moving from 2011 to 2016; largest changes in onroad mobile (-28.8%), nonroad mobile (-33%), and EGU point (-34.6%); increasing emissions in nonpoint (5%) and biogenic NO (5.9%)

## Slide 131: Also on LADCO: Gridded Plots e.g., 2016 Annual 12-km Gridded NOx (tons/year)
Notes: Roadways and urban areas present NOx emission hotspots, can also see some fires and large point sources

## Slide 132: Final Questions?
We hope that we have conveyed many of the consideration and complexities of emissions modeling
Any final questions for today?
Contacts: eyth.alison@epa.gov, vukovich.jeffrey@epa.gov, farkas.caroline@epa.gov