## Slide 1: Emissions Inventory Preparation for Air Quality Modeling (Base Year)
May 16, 2018
Alison Eyth, Jeff Vukovich, Caroline Farkas
EPA Office of Air Quality Planning and Standards
Emission Inventory and Analysis Group

## Slide 2: Goals of Class
To introduce you to the various tasks involved with preparing emissions inputs to air quality models for base (historic) years
  Focus is on the steps and data involved, not the details of running the scripts
To answer commonly asked questions about emissions modeling
Note: presentation is available for download: ftp://newftp.epa.gov/Air/nei/ei_training_may2018/emis_prep4aqm/
US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 3: Course Outline and Schedule
1:00 Background, Inventories, Tools, and QA
1:40 Emissions Modeling and Plume Rise
2:00 Spatial Allocation
2:25 Temporal Allocation
3:00 Break
3:15 Fugitive Dust, Biogenic, and Fire Emissions
3:45 Speciation
4:10 Onroad Mobile Sources
4:30 Final processing and QA steps
4:45 Any remaining questions
US EPA OAQPS, Emission Inventory and Analysis Group
Notes: Alison: intro on emissions modeling and why we do it, Jeff modeling/plume rise, Alison spatial, Caroline temporal, Jeff fugitive dust/bio/fires...; Caroline speciation, Alison Onroad and wrap up

## Slide 4: Background: Purpose and Contents of a Modeling Platform
Air quality modeling platforms are used to support air quality studies
  Use technically sound data and state-of-the-science tools
Major components of a modeling platform:
  Meteorological models (WRF) and met. data
  Boundary conditions (GEOS-Chem/Hemispheric CMAQ)
  Air quality models (CMAQ, CAMx)
  Emissions: base year (NEI)+NonUS, future year projections
  Other: ancillary data for emissions modeling, projections data, emissions modeling tools (SMOKE, etc) and scripts
US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 5: Air Quality Modeling Platform Components
Air Quality Model
Meteorological Model: wind,
temperature,
precipitation,
radiation, …
Boundary Conditions Concentrations of species at boundaries
Emissions
Ground level and elevated
Pollutant Concentrations
These are hourly
and in 3-D

## Slide 6: Why do Air Quality Modeling?
Regulatory Impact Assessments (RIAs)
  Model a base year focused on Criteria Air Pollutants (CAPs)
  Model a future year base case with on-the-books rules
  Model one or more cases that represent the rule
  Estimate costs and benefits of rule
National Air Toxics Assessment (NATA)
  Model a base year including as many Hazardous Air Pollutants (HAPs) as possible
  Compute risk based on CMAQ and AERMOD concentrations
Transport and Regional Haze Modeling
  Model a base year and a future year base case
  Perform source apportionment modeling to determine contribution of states and/or sectors to air quality issues
US EPA OAQPS, Emission Inventory and Analysis Group
Notes: These are common studies – there are others

## Slide 7: Performing Emissions Modeling
We use the Sparse Matrix Operator Kernel Emissions (SMOKE) modeling system and associated tools to process our emissions into air quality model-ready files (http://www.cmascenter.org/smoke)
The input emission inventories (e.g., NEI) can be annual, monthly, daily, or hourly
“Ancillary” data files help process inventories into gridded hourly emissions of the chemical species (e.g., NO, NO2, ISOP) used by the air quality model
Meteorological data such as temperature, precipitation, and radiation are needed to compute emissions and for some sectors temporalization (e.g., onroad mobile, biogenic, res. wood, agricultural)
Quality assurance steps and data summaries ensure data is properly transformed and mass is not lost
US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 8: Emissions Modeling Schematic
Meteorological Data: humidity,
temperature,
radiation, …
Ancillary Data Speciation and Temporal Profiles, Spatial Surrogates, cross-references, etc.
Emission
Inventories
Hourly, speciated
point and gridded
emissions
SMOKE
Quality Assurance Logs and Summaries

## Slide 9: Emissions Modeling Process
Steps and data needed to convert emissions inventories into the resolution and formats needed by air quality models
Emission Inventories (annual/ monthly/daily)
+ Meteorology
Hourly, speciated, gridded emissions for air quality modeling
Temporal Profiles
Speciation Profiles
Spatial Surrogates
US EPA OAQPS, Emission Inventory and Analysis Group
Temporal Allocation
Speciation
Spatial Allocation
Note: Plume rise is typically handled within the AQM

## Slide 10: Emissions Modeling Platforms
Contents:
  Starting point is a version of the National Emissions Inventory (e.g., 2014 NEI version 2)
  Related data sets needed for processing are also included
  Software and scripts that process inventories into AQM inputs
  Typically have a historic or “base” year and one or more future years
Historic platform development process:
  Base and future year inventories and met. data developed by EPA
  Data and software needed to process the inventories for AQM developed by EPA
  Platform released for public comment
  EPA incorporates comments into a new version of the platform
Now working on a more collaborative process
REPEAT

## Slide 11: Base Year Emissions from the National Emissions Inventory (NEI)
Data are submitted by states, locals, tribes (S/L/T) and EPA into the Emissions Inventory System (EIS)
Five NEI data categories - all annual totals except events
  Point/Facility Inventory (lat-lon locations): EGUs, airports, point oil and gas sources, commercial and industrial facilities
  Nonpoint (county-based) – fugitive dust, agricultural, residential, industrial/commercial fuel comb., gas stations, biogenic
  Onroad mobile sources (county): cars and trucks driving on roads
  Nonroad mobile sources (county): mobile sources not on roads including rec. marine, construction equip., lawn/garden, tractors
  Events (lat-lon, day): wildland and prescribed fires
US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 12: NEI Compilation and Schedule
EPA and S/L/T data are blended to create the NEI
Full NEI produced every third year (e.g., 2011, 2014, 2017)
  NEI Submissions due by end of the following year
    2014 NEI data due end of 2015; 2017 data due end of 2018
  EPA compiles the inventory within about a year of submission
    2014NEIv1 released September, 2016
    2017NEIv1 to be released by March 2020 (no v2 planned)
  “Type A” (large) point sources submitted every year
    2016 sources due 12/31/17 (plus 2 week grace period)
2014 NEI version 2 released early 2018
See https://www.epa.gov/air-emissions-inventories

## Slide 13: Recent and Upcoming Emissions Modeling Platforms
Multiple 2011 Platforms are available
Working on the 2014 NATA Platform
  Based on 2014NEIv2 (2014 only, no future years)
  Includes updated spatial surrogates, temporal profiles, and speciation profiles versus 2011 platforms
  Focus is hazardous air pollutants (HAPs)
Collaborative Effort for a new base year
  Not much ozone in the east in 2014
  The year 2016 was selected through a collaborative process between states, regional organizations and EPA
  States and MJOs wanted to be more involved in development of the next modeling platform
Notes: HAP platform from NATA affects some inputs and scripts compared to CAP-platforms
Some files different than CAP-focused platforms

## Slide 14: 2016 Platform Schedule
Several versions of emissions will be developed
  Alpha: preliminary version with 2016 emissions for some sectors and 2014 for the rest (March-April, 2018)
  Beta: improved version of 2016 emissions and preliminary projected emissions to 2023 and 2028 (Summer-Fall, 2018)
  V1.0: fully updated 2016 emissions and complete projected emissions for 2023 and 2028 (Winter, 2019)
Notes: Timing of projections is uncertain

## Slide 15: Recent Emission Modeling Platforms and Naming Convention
US EPA OAQPS, Emission Inventory and Analysis Group
2011v6.3 platform is based on updated 2011NEIv2
2011v6.3
  Emission modeling platforms have base years and can have future years that go with them (e.g., 2017, 2023)
2014v7.0 is the initial 2014 NATA modeling platform based on 2014NEIv1
2016 Platform is currently under development and uses a different nomenclature (i.e., alpha, beta, v1.0)
Base year being modeled
Specific NEI year (e.g., 6 means 2011 NEI was used)
Iteration of platform
(e.g., 3 is the third platform for 2011)

## Slide 16: Emissions Modeling Case Abbreviations
US EPA OAQPS, Emission Inventory and Analysis Group
A “case” is a specific set of AQM-ready emissions inputs and has an abbreviation or nickname
2011ek
Additional information can follow the main abbreviation and differs by case
  Speciation, control case, sensitivity adjustments, meteorological model configuration (e.g., 11g)
      Such as cb6, ctl, nox50 (e.g., 2011ek_cb6_11g)
Year being modeled
NEI base year (e.g., e=2011 NEI, f=2014 NEI)
Configuration of emissions inputs
(e.g., k is the 11th version for 2011)

## Slide 17
Case names appear on the web and FTP sites and in input file names
Notes: Note that ek comes before el which comes before en; not all versions are released – sometimes they are special studies, so the letters aren’t sequential

## Slide 18: EPA US 12km Modeling Platform Domains
US domains / grids use consistent map projections (Lambert)
Other domains also exist (e.g., 36km, 4km, hemispheric)
Many US domains include parts of Canada and/or Mexico
US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 19: Non-US emissions in the emissions modeling platform
Canada emissions & ancillary data (e.g., surrogates)
  Courtesy Environment Canada
  Used 2010 until 2013 and 2025 data provided in April, 2017
  Fire emissions provided for summer 2011 and other years
Mexico 2008 emissions and projections of these
  Based on Inventario Nacional de Emisiones de Mexico, 2008
  MOVES-Mexico data was developed for key years
  Base year fire emissions for Mexico derived from Fire INventory from NCAR (FINN):
    A daily fire emissions product for atmospheric chemistry models [also used for winter in Canada]
Hemispheric Transport of Air Pollution (HTAP) version 2 inventories used outside of North America in hemispheric runs
US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 20: 2014fa NOx Emissions Outside of the United States
US EPA OAQPS, Emission Inventory and Analysis Group
Top: Onroad sources in Canada and Mexico
Bottom: Non-US point sources and Commercial marine vessels outside of state waters

## Slide 21: Emissions Modeling Platform Sectors
Emission inventories are broken down into “sectors” used to prepare AQM-ready emissions for different parts of the inventory
Each sector has unique processing or inventory characteristics and a lowercase name (e.g., rwc)
Specific sectors vary by modeling platform but cover all sources in the inventory
Point source sectors keep their specific latitude-longitude locations throughout the processing
Nonpoint sectors are allocated to grid cells using spatial surrogates
EPA processes emissions separately for each sector then merges the ground-level emissions together to create final AQM-ready files for a case

## Slide 22: 2016 Platform Sectors: Point and Non-U.S.
Point and non-US Sectors | Sector Description
ptegu | Point sources that are Electric generating units (EGUs)
pt_oilgas | Point sources related to oil and gas production
ptnonipm | Point sources that are not EGUs nor related to oil and gas
ptagfire | Point source day-specific agricultural fires (was agfire)
ptfire | Point source day-specific wild and prescribed fires
ptfire_othna | Non-US point source day-specific fires in North America
cmv_c3 | Category 3 (large) Commercial Marine Vessels as points
othpt | Non-US point sources
othafdust_adj | Non-US area fugitive dust sources (Canada only)
othar | Non-US area (i.e., nonpoint) sources
onroad_can | Onroad mobile sources for Canada (was othon)
onroad_mex | Onroad mobile sources for Mexico (was othon)
US EPA OAQPS, Emission Inventory and Analysis Group

## Slide 23: 2016 Platform Sectors: Ground-level
Nonpoint Sectors | Sector Description
afdust_adj | Met.-adjusted area fugitive dust emissions
ag | Agricultural ammonia sources
beis | Biogenic emissions based on the BEIS model
cmv_c1c2 | C1&C2 Commercial marine vessels (nonpoint)
nonpt | Nonpoint sources not in other sectors
nonroad | Mobile sources that do not drive on roads or railroads, including recreational pleasurecraft
np_oilgas | Nonpoint oil and gas production-related sources
onroad | On-land mobile sources that drive on roads
onroad_ca_adj | Onroad mobile sources in California
rail | Locomotive sources on railroads
rwc | Residential wood combustion sources
US EPA OAQPS, Emission Inventory and Analysis Group
Notes: Our job as emissions modelers is to ensure there are quality inventories and ancillary data going into all of these sectors…

## Slide 24: Questions?
Any questions on basic concepts of emissions modeling?
Notes: Next: Jeff

## Slide 25: How do we Start Building a New Platform?
When a new NEI version becomes available, flat files (a .csv format) are output from EIS
  Point and nonpoint inventories are split into sectors
  Onroad, nonroad, and biogenic are inputs to the NEI release
Update ancillary files to account for new source classification codes (SCCs) and updated data
Perform quality assurance as needed (temporal, speciation, gridding)
Compare the inventories and results to a previous platform
  Create difference reports by state, county, and/or SCC
  Create charts and maps
  Example: 2016 platform development
Notes: Key inventory fields are FIPS code, pollutant, source classification code (SCC), and stack parameters

## Slide 26: 2014 vs 2016 Comparison
First, prepare excel workbook by sector, state, pollutant, case 1, case 2, absolute and percent changes; then apply filters to prioritize (e.g. > 1500)
sector | state | poll | ann_emis_ 2014fb | ann_emis_ 2016fc | diff_tons | percent diff
ptagfire | Arkansas | PM2_5 | 1,706 | 2,745 | 1,039 | 61%
ptagfire | California | PM2_5 | 3,596 | 5,689 | 2,093 | 58%
ptagfire | Florida | PM2_5 | 3,632 | 3,676 | 44 | 1%
ptagfire | Georgia | PM2_5 | 2,090 | 1,587 | -503 | -24%
ptagfire | Kansas | PM2_5 | 10,861 | 18,385 | 7,525 | 69%
ptagfire | Missouri | PM2_5 | 1,640 | 2,368 | 728 | 44%
ptagfire | North Dakota | PM2_5 | 1,969 | 3,241 | 1,272 | 65%
ptagfire | Oklahoma | PM2_5 | 6,124 | 9,545 | 3,421 | 56%
ptagfire | Texas | PM2_5 | 4,401 | 5,815 | 1,413 | 32%
ptagfire | Washington | PM2_5 | 1,694 | 1,334 | -359 | -21%
Notes: Note the substantial changes in the two years: some increases, some decreases…

## Slide 27: 2014-2016 EGU comparison
State | 2014 SO2 | 2016 SO2 | % diff SO2 | 2014 NOx | 2016 NOx | % diff NOx
Alabama | 119,919 | 25,337 | -79% | 50,489 | 28,674 | -43%
Arkansas | 76,046 | 46,706 | -39% | 38,626 | 26,968 | -30%
Florida | 99,628 | 40,453 | -59% | 73,740 | 62,611 | -15%
Illinois | 143,261 | 67,096 | -53% | 48,196 | 32,147 | -33%
Indiana | 294,339 | 89,911 | -69% | 110,290 | 83,170 | -25%
Kentucky | 201,871 | 76,290 | -62% | 86,816 | 57,586 | -34%
Louisiana | 76,774 | 45,851 | -40% | 46,285 | 47,462 | 3%
Michigan | 154,855 | 85,354 | -45% | 59,625 | 41,541 | -30%
Mississippi | 90,790 | 3,187 | -96% | 23,643 | 16,022 | -32%
Missouri | 134,326 | 100,798 | -25% | 74,883 | 57,335 | -23%
Ohio | 302,698 | 107,532 | -64% | 88,177 | 56,137 | -36%
Oklahoma | 76,791 | 49,439 | -36% | 39,450 | 25,130 | -36%
Pennsylvania | 278,498 | 98,839 | -65% | 129,423 | 83,300 | -36%
Texas | 346,244 | 247,044 | -29% | 124,892 | 108,655 | -13%
West Virginia | 101,586 | 42,515 | -58% | 72,631 | 52,307 | -28%
Notes: Note the large decreases of SO2 and NOx emissions for EGUs in just 2 years…

## Slide 28: 2014 vs 2016 County-level Comparisons
sector | state | county | poll | ann_emis_2014fb | ann_emis_2016fc | diff | pdiff
beis | Alabama | Autauga Co | CO | 2,458 | 2,756 | 298 | 12.1%
beis | Alabama | Autauga Co | NOX | 157 | 167 | 10 | 6.2%
beis | Alabama | Autauga Co | VOC_INV | 21,332 | 23,829 | 2,496 | 11.7%
beis | Alabama | Baldwin Co | CO | 7,276 | 8,206 | 930 | 12.8%
beis | Alabama | Baldwin Co | NOX | 399 | 433 | 34 | 8.6%
beis | Alabama | Baldwin Co | VOC_INV | 57,200 | 63,835 | 6,635 | 11.6%
beis | Alabama | Barbour Co | CO | 3,417 | 3,918 | 501 | 14.7%
beis | Alabama | Barbour Co | NOX | 151 | 164 | 14 | 9.0%
beis | Alabama | Barbour Co | VOC_INV | 30,439 | 35,010 | 4,572 | 15.0%
sector | state | county | poll | ann_emis_2014fb | ann_emis_2016fc | diff | pdiff
ptnonipm | Alabama | Autauga Co | CO | 2,475 | 2,482 | 7 | 0.3%
ptnonipm | Alabama | Autauga Co | NH3 | 71 | 72 | 0 | 0.3%
ptnonipm | Alabama | Autauga Co | NOX | 2,530 | 2,537 | 7 | 0.3%
ptnonipm | Alabama | Autauga Co | PM10 | 536 | 538 | 1 | 0.3%
ptnonipm | Alabama | Autauga Co | PM2_5 | 428 | 429 | 1 | 0.3%
ptnonipm | Alabama | Autauga Co | SO2 | 3,692 | 3,702 | 10 | 0.3%
ptnonipm | Alabama | Autauga Co | VOC_INV | 901 | 903 | 2 | 0.3%
Biogenic changes mainly due to meteorology; others due to # of days in year

## Slide 29: County-level Base and Difference Maps: Beef Cattle NH3
Maps help us see spatial variation and hot spots
Most of our county-level maps are created with Python
2011
2014

## Slide 30: Gridded Maps: Ptagfire Example
Gridded maps can be created with VERDI, PAVE, etc.
2014 PM2.5
2016 PM2.5
For some sectors (e.g., fires, biogenics) we create monthly maps

## Slide 31: Modeling Platform Data is not always the same as the NEI
Some modeling platform data are not the same as what is in the NEI
  Corrections to issues found after the NEI release
  New data becomes available after NEI release
  More detailed data is available than is stored in NEI
    Continuous Emissions Monitoring System (CEMS) data for EGUs are hourly by unit
    Nonroad data are computed monthly (summed in the NEI)
    Onroad and biogenics data computed as hourly emissions and then aggregated & summed for the NEI
  NEI uses average meteorological adjustments for afdust, but the modeling platform emissions are adjusted based on hourly, gridded met. data

## Slide 32: Questions?
Questions on new platform development or quality assurance?
Notes: Jeff continues

## Slide 33: Emissions Modeling with SMOKE
We use the Sparse Matrix Operator Kernel Emissions (SMOKE) modeling system and associated tools to process emissions into air quality model-ready files
  Smkinven: reads in the emission inventories
  Grdmat: computes gridding matrix using lat-lon locations and spatial surrogates
  Spcmat: computes speciation matrix using speciation profiles
  Temporal: temporally allocates emissions to hours using temporal profiles
  Elevpoint: Splits ground-level and elevated point sources
  Smkmerge: merges all matrices and temporalized emissions to create AQM-ready data for a sector
  Mrggrid: merges ground-level emissions from different sectors together into a complete ground-level file

## Slide 34: SMOKE Data Flow for a Generic Emissions Modeling Sector
Emission Inventory
Smkinven
Spcmat
Temporal
Grdmat
Speciation Matrix
Hourly Emissions
Gridding Matrix
Smkmerge
AQM-formatted emissions
These emissions are for one sector
SpeciationProfiles
Spatial Surrogates
Temporal profiles
SMOKE inventory

## Slide 35: Special Emissions Models
Biogenic Emission Inventory System (BEIS): part of SMOKE and CMAQ that creates air quality model-ready biogenic emissions
  SMOKE programs: Normbeis3, Tmpbeis3
Motor Vehicle Emission Simulator (MOVES):
  For onroad mobile sources: generates emission factors that can be combined with activity data (e.g., Vehicle miles traveled, speed) within SMOKE
    SMOKE programs: Met4moves, Movesmrg
  For nonroad mobile sources: generates county-level emission inventories for each month
    Previously done with National Mobile Inventory Model (NMIM) and NONROAD model

## Slide 36: Other Emissions Modeling Tools
Surrogate Tool: creates spatial surrogates from Shapefiles to put county emissions into grid cells
Speciation Tool: creates chemical speciation profiles from SPECIATE database profiles (e.g., NOx->NO+ NO2, PM2.5->EC+OC+..., VOC->…)
Gentpro: SMOKE program that creates meteorology-based temporal profiles
Python: helps with QA, creates reports and maps
Emissions Modeling Framework: graphical user interface that manages inventories and related data and modeling cases; creates summaries for QA and analysis; includes Control Strategy Tool

## Slide 37: Emissions Modeling Framework
Emission
inventories
are stored as
Datasets in the
Emissions Modeling
Framework
Notes: Mention the Dataset Manager

## Slide 38: EMF Showing Point Inventory (FF10)
Filter records using SQL

## Slide 39: Emissions Modeling Steps for Ground-level Sectors
Platform sector | Spatial | Speciation | Inventory resolution
afdust_adj | Surrogates | Yes | annual + met data
ag | Surrogates | Yes | annual or monthly
beis | Pre-gridded land use | in BEIS 3.6.1 | computed hourly
cmv_c1c2 | Surrogates | Yes | annual
nonpt | Surrogates | Yes | annual
nonroad | Surrogates | Yes | monthly
np_oilgas | Surrogates | Yes | annual
onroad, onroad_ca_adj | Surrogates | in MOVES 2014 | monthly activity, computed hourly
onroad_can | Surrogates | Yes | monthly
onroad_mex | Surrogates | in MOVES | monthly
rail | Surrogates | Yes | annual
rwc | Surrogates | Yes | annual
Notes: Highlight the differences in inventory resolution and speciation

## Slide 40: Emissions Modeling Steps for Non-U.S. and Point Sectors
Platform sector | Spatial | Speciation | Inventory resolution | Plume rise
othafdust | Surrogates | Yes | annual | 
othar | Surrogates | Yes | annual | 
othpt | Point | Yes | annual | in-line*
ptfire_mxca | Point | Yes | daily | in-line
pt_oilgas | Point | Yes | annual | in-line
ptegu | Point | Yes | annual & hourly CEMS | in-line
ptfire | Point | Yes | daily | in-line
ptagfire | Point | Yes | daily | in-line
ptnonipm | Point | Yes | annual | in-line
cmv_c3 | Point | Yes | Annual | in-line
* in-line means the plume rise can be done in CMAQ
Notes: Point out sectors with plume rise

## Slide 41: Plume Rise
Plume rise allows for sources to go vertically above the first layer of the air quality model (AQM has up to 35 layers)
The SMOKE Elevpoint program selects elevated or plume-in-grid point sources using the Briggs algorithm
  Most sources with plume height > 20m as elevated
  Sometimes we want all sources to have plume rise
Plume rise can be done with the SMOKE Laypoint program to compute layer fractions for each elevated point source
  For hemispheric applications, 3-D emissions are developed
Notes: Sectors that would all get plume rise include ptegu, cmv_c3, othpt

## Slide 42: Plume rise: Vertical allocation

## Slide 43: Plume Rise Formula
Stack parameters for point sources affect plume rise
  Height, diameter, velocity / flow, temperature
F = 0.25 x G x VS x DS2 x (TS - T)/TS
For F < 55, Plume rise = HS + 21.313 x F0.75/U otherwise: Plume rise = HS + 38.878 x F0.6/U where
  HS = Physical stack height (m)
  F = Buoyancy flux (m4/s3)
  G = Mean gravitational acceleration (9.80665 m/s2)
  VS = Stack gas exit velocity (m/s)
  DS = Inside stack diameter (m)
  TS = Stack gas temperature (K)
  T = Default ambient air temperature (293 K)
  U = Default wind speed (2 m/s)

## Slide 44: Plume Rise Requirements for AQMs Differ
3-D emissions files can be really big!
CMAQ can do “in-line” plume rise
  Provide CMAQ with hourly emissions with locations and stack parameters for any elevated sources
  Compute plume rise with hourly meteorological data
  A special plume rise treatment is used for fires that considers acres burned and heat flux
CAMx supports an in-line format for plume rise but does not have the same algorithm for fire plume rise
  We run SMOKE Laypoint to compute 3-D fires
  Point sources are then converted to CAMx format

## Slide 45: Allocation to Layers for AQ Modeling
Chart: Example Fire Plume Rise
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19












Layer number
Emissions

## Slide 46: Questions?
Any questions on SMOKE or plume rise?
Notes: Next: Alison

## Slide 47: Spatial Allocation
Spatial allocation is the process of mapping inventory emissions to modeling grid cells
We do this using spatial surrogates; there are many types and each has a unique code (ID)
  Population (100), Total agriculture (310), Railroad Density (261), Offshore shipping (806), Urban unrestricted daily VMT (222), Gas well count (698)
  A cross reference maps inventory SCCs to surrogate codes
Notes: Instead of assuming the emissions are uniformly distributed spatially, we use an attribute from another dataset to allocate the emissions to grid cells.

## Slide 48: Surrogate Tool
Java program that takes .csv files as input
  Runs the Spatial Allocator to prepare surrogates
Download from http://www.cmascenter.org
Performs gapfilling of surrogates
  When attributes used to compute a surrogates do not exist for a county, another surrogate is used
Outputs quality assurance products
  Sum of surrogate for each county (=1.0?), gapfilling
Some GIS datasets are too large to process with the Spatial Allocator (e.g., new roads, CMV))
  Working on a PostgreSQL tool with PostGIS to process these

## Slide 49: Data Used to Create a Spatial Surrogate with Surrogate Tool
Weight Shapefile: an attribute is selected from this spatial dataset to apportion values in a county into the model grid cells
  Population at the census tract block level (polygon)
  Lines representing railroads
  Point locations of oil and gas wells
Data Shapefile: spatial dataset that represents boundaries on which inventory is computed (e.g., U.S. counties, Canadian provinces)
Output grid: modeling grid cells

## Slide 50: Creating a Surrogate for Commercial Marine Vessels
Data = US counties
Weight = NOx emissions on shipping lanes
Output is US 12km grid
Notes: These spatial patterns are very different from what we would see if we assumed uniform distribution

## Slide 51: Spatial Surrogate values
Surg ID | County | Col | Row | Ratio | Comment*
806 | 01003 | 345 | 207 | 0.2 | 200/1000
806 | 01003 | 346 | 207 | 0.3 | 300/1000
806 | 01003 | 346 | 208 | 0.5 | 500/1000
806 | 01005 | 355 | 210 | 0.4 | 800/2000
806 | 01005 | 355 | 209 | 0.6 | 1200/2000
Value = sum of attribute in grid cell
sum of attribute in county
Values sum to 1 for each county / province
* Surrogates created using the Spatial Allocator include a comment that shows how the ratio was computed

## Slide 52: Updated CMV Surrogate
New spatial surrogate is based on 2013 data: https://www.marinecadastre.gov/data
US EPA OAQPS, Emission Inventory and Analysis Group
Notes: Keep in mind the NEI boxes – Pacific, Atlantic, Gulf, Off Washington

## Slide 53
Cross-references and profiles are used in emissions modeling to apportion wholes into parts:
X-REF table
Profiles table (sum to 1)
2505020121, 15 2505020122, 15
2294000000, 16
2296000000, 17
13 0.2, 0.3, 0.5
14 0.4, 0.4, 0.2
15 0.4, 0.3, 0.3
16 0.4, 0.5, 0.1
17 0.4, 0.4, 0.2
SCC, Surg. ID
ID, Grid cell 1, 2, 3
Using Cross-references and Profiles (Generically)

## Slide 54: Spatial Surrogate Cross reference
FIPS ST/CTY* | SCC** | Surrogate ID | Comments
000000 | 0040600241 | 801 | ! All counties
000000 | 0040600242 | 801 | ! All counties
000000 | 2505020121 | 801 | ! All counties
008000 | 2520100102 | 689 | 
048243 | 2520100102 | 693 | ! Replaced 698
048243 | 2520100102 | 693 | ! Replaced 698
*A surrogate can be applied to all counties using code 000000 or to specific states using state FIPS+”000”, or to specific counties ** Specific SCC assignments are always used (no hierarchy assumed)

## Slide 55: Some Spatial Surrogate Data Sources
2011 National Land Cover Database (NLCD)
U.S. Census American Community Survey
U.S. Census Topologically Integrated Geographic Encoding and Referencing (TIGER) data
U.S. DOT Highway Performance Monitoring System (HPMS) – Annual Average Daily Travel (AADT)
National Transportation Atlas Database (NTAD)
2014 NEI Oil and Gas Activity Data
2014 NEI Ports and Shipping Lanes

## Slide 56: Key Spatial Surrogates for CAPs
Sector | ID | Description | NH3 | NOX | PM2_5 | VOC
ag | 310 | NLCD Total Agriculture | 3,135,285 |  |  | 
onroad | 307 | NLCD All Development |  | 560,112 | 12,560 | 1,142,592
onroad | 222 | Urban Unrestricted AADT | 42,001 | 1,223,593 | 54,345 | 376,209
nonpt | 306 | NLCD Med + High | 22,268 | 239,863 | 290,187 | 864,662
onroad | 232 | Rural Unrestricted AADT | 25,027 | 987,683 | 33,882 | 201,764
nonpt | 100 | Population | 32,222 | 0 | 0 | 1,137,409
afdust | 310 | NLCD Total Agriculture |  |  | 1,169,400 | 
afdust | 304 | NLCD Open + Low |  |  | 1,116,883 | 
np_oilgas | 694 | Oil Production at Oil Wells | 0 | 4,375 | 0 | 1,104,120
np_oilgas | 698 | Well Count - Gas Wells | 15 | 388,677 | 6,726 | 623,925
onroad | 202 | Urban Restricted AADT | 24,687 | 790,075 | 30,439 | 149,645
rail | 271 | NTAD Class 1 2 3 Railroad Density | 362 | 767,307 | 22,868 | 39,121

## Slide 57: Quality Assurance of Spatial Allocation
Check SMOKE Grdmat logs to ensure all SCCs are mapped to spatial allocation profiles and only emissions outside the domain are not allocated to grid cells (do not want to drop emissions)
Review gridded emission plots by sector to ensure spatial patterns are reasonable (US sources are all in US, onshore emissions are all on land)
Compare post-SMOKE emissions to the inventory also helps to ensure that no emissions are dropped due to gridding
For point sources: check that inventory coordinates fall within county boundaries

## Slide 58: Maps Help us to QA Spatial Surrogates: cmv_c1c2 Example
2011el cmv_c1c2 NOx
2014fa cmv_c1c2 NOx
2014fa-2011el cmv_c1c2 NOx
101
58
0
-48.6
48.6

## Slide 59: Questions?
In this section we’ve covered some details on spatial allocation
Notes: Next: Caroline

## Slide 60: Temporal Allocation
Temporal allocation is the process of allocating inventory emissions to hourly emissions
Hierarchy of temporal allocation steps: annual -> month -> day -> hour
There are many types of temporal profiles for each resolution and each has a unique code
  Typically, SCCs are used to map temporal profiles to inventory sources
  Cross reference may also use FIPS, pollutant, etc.
More control with the format in SMOKE 3.6+
  e.g., Monday diurnal profile vs Friday diurnal profile
  Database-friendly for use in EMF

## Slide 61: Temporal Profile Examples
Chart: Fire Pits/Chimineas Day-of-Week Profile
| Monday | Tuesday | Wednesday | Thursday | Friday | Saturday | Sunday
Fire Pit/Chimenea | 67 | 67 | 67 | 67 | 67 | 331 | 331
Outdoor Hydronic Heater | 143 | 143 | 143 | 143 | 143 | 143 | 143
Chart: Monthly Temporal Activity for Outdoor Hydronic Heater & Recreational Residential Wood Combustion
| JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC
Fire Pit/Chimenea | 7936678.4452 | 5152428.9005 | 9708943.672 | 31990446.99 | 71197717.7494 | 80883570.6535 | 89576338.1223 | 79780274.3377 | 92111652.7274 | 64636125.6437 | 44774482.5626 | 18558839.307
Outdoor Hydronic Heater | 32147309.9923 | 30090132.1991 | 32185984.6883 | 26867334.2344 | 5173753.3937 | 2934499.5369 | 1785749.1026 | 2137746.7843 | 3903894.3352 | 26780359.7373 | 30633269.3935 | 31655667.5298
Chimenea
Fire Pit
Outdoor Hydronic Heater

## Slide 62: Diurnal Temporal Profile Examples
Chart: Outdoor Hydronic Heather Heat Load (BTU/hr)
| 12am | 1am | 2am | 3am | 4am | 5am | 6am | 7am | 8am | 9am | 10am | 11am | 12pm | 1pm | 2pm | 3pm | 4pm | 5pm | 6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12am
Heat Load (BTU/hr) | 34000 | 35000 | 36000 | 37500 | 39000 | 39000 | 37500 | 35000 | 33000 | 30000 | 27000 | 25000 | 23000 | 22500 | 23000 | 25000 | 26500 | 29000 | 31000 | 33000 | 34000 | 34000 | 33000 | 32500 | 34000
Notes: Note that profiles are between 0 and 1 but units of source data vary

## Slide 63: Excerpt from Temporal Cross Reference and Profile Files
SCC | FIPS | Facility | Unit | Releasept | process | Pollutant | Profile Type | Profile Num | Comment
2104009000 | 56045 |  |  |  |  | 0 | MONTHLY | 17001 | 
2104009000 | 56045 |  |  |  |  | 0 | DAILY | 56045 | 
2104009000 | 56045 |  |  |  |  | 0 | ALLDAY | 600 | 
2104008700 |  |  |  |  |  | 0 | MONTHLY | 17750 | “Fire pit"
2104008700 |  |  |  |  |  | 0 | WEEKLY | 61500 | “Fire pit"
2104008700 |  |  |  |  |  | 0 | ALLDAY | 600 | “Fire pit"
2104008610 |  |  |  |  |  | 0 | MONTHLY | 17751 | “Hydronic heater”
2104008610 |  |  |  |  |  | 0 | WEEKLY | 7 | “Hydronic heater"
2104008610 |  |  |  |  |  | 0 | ALLDAY | 1500 | “hydronic heater"
MonthID | Jan | Feb | Mar | Apr | May | June | July | Aug | Sept | Oct | Nov | Dec
17750 | 0.01 | 0.01 | 0.02 | 0.05 | 0.12 | 0.14 | 0.15 | 0.13 | 0.15 | 0.11 | 0.08 | 0.03
17751 | 0.14 | 0.13 | 0.14 | 0.12 | 0.02 | 0.01 | 0.01 | 0.01 | 0.02 | 0.12 | 0.13 | 0.15
WeekID | Sun | Mon | Tue | Wed | Thu | Fri | Sat |  |  |  |  | 
7 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | 0.14 | Equal days |  |  |  | 
61500 | 0.07 | 0.07 | 0.07 | 0.07 | 0.07 | 0.33 | 0.33 | Fire pit/chimenea |  |  |  | 
HourID | hr0 | hr1 | hr2 | hr3 | hr4 | hr5 | hr6 | hr7 | hr8 | hr9 | hr10 | hr11
600 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.01
1500 | 0.04 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.04 | 0.04 | 0.04 | 0.03
Profiles

## Slide 64: Temporal Settings by Sector
Platform sector short name | Inventory resolutions | Monthly profiles used? | Daily temporal approach | Merge processing approach | Process Holidays as separate days
afdust_adj | Annual | Yes | week | all | Yes
ag | Annual and Daily | Yes | all, hourly met | all | Yes
agfire | Annual | Yes | mwdss | mwdss | Yes
ptagfire | Daily | No | all | all | Yes
beis | Hourly | No | n/a | all | No
cmv | Annual | Yes | aveday | aveday | No
rail | Annual | Yes | aveday | aveday | No
nonpt | Annual | Yes | week | week | Yes
nonroad | Monthly | No | mwdss | mwdss | Yes
np_oilgas | Annual | Yes | Week | week | Yes
onroad | Annual & monthly1 | No | All | All | Yes
onroad_ca_adj | Annual & monthly1 | No | All | All | Yes
othafdust_adj | Annual | Yes | Week | All | No
othar | Annual & monthly | Yes | Week | week | No
onroad_can & mex | Monthly | No | Week | week | No
othpt | Annual | Yes | Mwdss | mwdss | No
pt_oilgas | Annual | Yes | mwdss | mwdss | Yes
ptegu | Daily & hourly | No | all | all | Yes
ptnonipm | Annual | Yes | mwdss | mwdss | Yes
ptfire and ptfire_othna | Daily | No | all | all | Yes
rwc | Annual | No | met-based | all | Yes
Notes: Note different inventory resolutions: annual, monthly daily, hourly; also different types of daily temporal profile approaches: all, week, average day, mwdss, met-based (merge approach is correlated to this), also whether holidays are treated differently

## Slide 65: Temporal Profile Data Sources
Some temporal profiles have been around a while
We look for data sources that can be used to update temporal profiles
Sometimes temporal profile updates happen as a result of reviewing model performance issues
  Recently EGU profiles for municipal waste combustors and nonroad profiles for construction and lawn and garden sources have been updated
To update profiles, we use studies or data when possible (e.g., rwc), otherwise we try to apply common sense knowledge of the source sector

## Slide 66: Airport Temporalization (1/2)
Airport diurnal temporal profiles updated for 2014v7.0 platform based on Aviation System Performance Metrics (ASPM) Airport Analysis
  https://aspm.faa.gov/apm/sys/AnalysisAP.asp
Chart: Diurnal Airport Profile
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 0.0049063 | 0.001684 | 0.00056241 | 0.00037596 | 0.0009042 | 0.0080459 | 0.033848 | 0.049378 | 0.061658 | 0.06211 | 0.063813 | 0.063037 | 0.061184 | 0.063396 | 0.062402 | 0.062101 | 0.06455 | 0.065184 | 0.064726 | 0.062192 | 0.053309 | 0.044071 | 0.02824 | 0.018322

## Slide 67: Airport Temporalization (2/2)
Weekly and monthly profiles based on FAA Operations Network Air Traffic Activity System
  http://aspm.faa.gov/opsnet/sys/Terminal.asp
Chart: Weekly Airport Profile
| Monday | Tuesday | Wednesday | Thursday | Friday | Saturday | Sunday
 | 0.14148 | 0.14867 | 0.15411 | 0.15353 | 0.15339 | 0.12702 | 0.1218
Chart: Monthly Airport Profile
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
 | 0.073346 | 0.070904 | 0.085182 | 0.085403 | 0.089158 | 0.088112 | 0.09213 | 0.090416 | 0.085495 | 0.089553 | 0.076555 | 0.073746

## Slide 68: Nonroad Temporal Profile Updates
Non-Road Category | Old Day of Week | New Day of Week | Old Hour of day | New Hour of Day
Construction | 18 | 19 | 26 | 26a
Commercial Lawn and Garden | 18 | 19 | 26 | 25a
Residential Lawn and Garden | 9 | 9 | 26 | 27
Agriculture | 18 | 18 | 26 | 25a
Construction and Comm. Lawn & Gdn lower on weekends in New
New diurnal profiles have lower overnight emissions
New Res. L & G
New ag +
comm L&G
Old

## Slide 69: Meteorology-based Temporalization
Some sectors have a significant temporal variation based on changes in the meteorology
GenTPRO
  SMOKE program that reads gridded meteorology and spatial surrogates
  Produces county-specific meteorology based profiles
  Used for platform sectors: ag (month->hour) and rwc (annual->day of year)
Other sectors influenced by meteorology
  Area fugitive dust (afdust)
  Biogenic emissions
  Onroad (discussed later)
  EGUs (indirectly)

## Slide 70: GenTpro: ag livestock
Meteorological fields used: temperature, wind speed, and aerodynamic resistance
Allocate monthly emissions to hour of month
Notes: These profiles are done by county

## Slide 71: Residential Wood Day-specific Temporal Allocation with GenTpro
Note in summer RWC near 0
Daily minimum temperature used to help allocate annual emissions to days of year
If min temp. above 50 degrees, no emissions
  Southern states use 60 degrees threshold
Notes: Colder days have more emissions. Uses daily minimum T
Threshold: if min T > threshold, 0 emissions that day
In this plot also get influence of non-met based RWC, eg. firepits that show up in the summer
Total annual emissions are preserved

## Slide 72: Special Steps for EGUs
Separate EGUs from nonEGUs in EIS flat file based on whether IPM_YN column is non-blank
Download latest CEMS data for base year of interest
Review the assignments to ORIS IDs in the flat file and how they match up to the CEMS data
Identify partial year CEMS reporters and sources that should not follow CEMS data at all (e.g., MWCs, cogens)
Run cemcorrect program to remove non-measured anomalies in CEMS data
Generate region/fuel-specific average temporal profiles for temporalization of sources without CEMS
Generate region/fuel-specific seasonal hourly profiles

## Slide 73: Outputs from UNC’s CEMS Data Correction Tool
Emissions spikes adjusted to average values when they are not flagged as measured in CEMS data flags
Removes spikes

## Slide 74: EGU Temporal Profiles and Matching
Removed non-measured data values from CEMS data to ignore emission spikes
Hierarchy of CEMS assignments:
  Use CEMS for all months (units with complete CEMS data) <-- Note: CEMS data replace the annual inventory
  Use CEMS for months where there are measurements; use regional averages for periods without measurements (e.g., partial-year reporters)
  Use regional averages (units without CEMS)
Regional average profiles
  IPM region- and fuel-specific average profiles used
  Different winter and summer versions of hourly profiles
Matching of CEMS database units and IPM units with EIS/platform point sources is key to success

## Slide 75: Map of EGU Profile Regions

## Slide 76: Average Month-day Profiles: Region- and fuel-specific
(yellow=gas, blue=coal, black=composite)
Region in W Texas
Region in E Oklahoma and W Arkansas
Profiles differ between regions
Notes: ERC West gas is being used for base load but also more as a peaking
SPP West gas and coal both seem to be used as base load but off-setting each other

## Slide 77: Mid-Atlantic CEMS Examples of Annual to Day-of-Year Allocation
Chart: Coal
Chart: Gas
Chart: Other
10x larger
Notes: 2017 is projected from 2011

## Slide 78: Dirunal Profiles: Winter vs. Summer
IPM region- and fuel-specific profile – mid-Atlantic

## Slide 79: QA of Temporal Allocation
Check SMOKE Temporal logs to ensure all sources are mapped to temporal profiles
Sum post-SMOKE daily emissions by sector to compare back to annual for inventory comparison
Perform various specialized analysis of EGUs (partial year reporters, spikes in CEMS data)
Check the PTSUP files to confirm that sources are using the correct temporal profiles
  i.e. that SMOKE is applying the xref correctly
Compare daily Smkmerge reports for rwc and ag for two different Tuesdays (for example) in the same month as they should be different (except NH3_FERT) due to the Gentpro temporalization

## Slide 80: Questions?
Does anyone have questions on temporal allocation?
BREAK
Notes: Next: Jeff

## Slide 81: Area Fugitive Dust Adjustments
AQ models tend to overestimate the impact of fugitive dust emissions
  Paved and unpaved roads, construction, mining, hooves
Prior to modeling, afdust emissions are reduced according to a gridded transport fraction
Transport fraction reduction factors depend on land use
  Forested areas will have a lower transport fraction (higher reduction)
  Wide open areas will have a higher transport fraction (lower reduction)
Additional meteorologically-based reductions for rain and snow-cover are applied to fugitive dust emissions later in the process

## Slide 82: Unadjusted Fugitive Dust
In NEI and Platform, dust emissions are adjusted

## Slide 83: Transport Fraction Plot
Red = high level of reduction; Gray = little reduction

## Slide 84: Impact of afdust Adjustments
Transport fraction
Precipitation adjustment
  Zero out hourly emissions when rain (> 0.01 inches) or there is snow)
Unadjusted emissions
Apply
Transport
Fraction
Precipitation
adjustment
Notes: Precipitation adjustment removes emissions so post-adjustment < annual inventory
Has a temporal and spatial aspect

## Slide 85: BEIS 3.6.1: Updated Biogenic Emissions
Updated leaf temperature algorithm in v3.6.1
  Leaf temperature calculated using canopy model rather than 2 meter temperature
BELD 4.1 land use based on:
  U.S. National Land Cover Database (NLCD) 2011
  Moderate Resolution Imaging Spectroradiometer (MODIS) for Canada and Mexico
  Forest areas constrained by canopy coverage
  2011 USDA Cropland Data Layer
Tree species from USFS Forest Inventory and Analysis (FIA) data
  Selected surveys from 2001 to 2014 to get a complete decadal US survey that bounds the years being modeled
SMOKE programs used:
  Normbeis3: normalized biogenic emissions
  Tmpbeis3: outputs gridded, speciated, hourly emissions

## Slide 86: Meteorological Variables Needed for BEIS 3.6.1
Variable | Description
LAI | leaf-area index
PRSFC | surface pressure
Q2 | mixing ratio at 2 m
RC | convective precipitation per met TSTEP
RGRND | solar radiation reaching surface
RN | nonconvective precipitation per met TSTEP
RSTOMI | inverse of bulk stomatal resistance
SLYTP | soil texture type by USDA category
SOIM1 | volumetric soil moisture in top cm
SOIT1 | soil temperature in top cm
TEMPG | skin temperature at ground
USTAR | cell averaged friction velocity
RADYNI | inverse of aerodynamic resistance
TEMP2 | temperature at 2 m

## Slide 87: Species Produced by BEIS
Carbon Monoxide (CO), Nitrogen Oxide (NO)
Acetaldehyde (ALD2)
Higher acetaldehyde (ALDX)
Formaldehyde (FORM)
Isoprene (ISOP)
Terpene (TERP)
Sesquiterpene (SESQ)
Ethene (ETH), Ethane (ETHA)
Internal (IOLE) and terminal olefins (OLE)
Ethanol (ETOH), Methanol (MEOH)
Paraffins (PAR)
No PM species…

## Slide 88: 2014 Annual Biogenic Emissions
Top: NO from soil (depends on temperature, precipitation, and fertilizer)
Bottom: Isoprene (produced during photosynthesis)

## Slide 89: Future Directions and Questions?
Examining MEGAN version 3 biogenic emissions estimates
Biogenic emissions modeling for Alaska
Possibly update land use used in transport fraction generation
Any questions on fugitive dust or biogenic emissions?
Notes: Next: Jeff continues

## Slide 90: NEI Fire Inventory Details
Includes daily “point” emissions from wildfires and prescribed fires
Emissions were estimated for PM2.5, PM10, CO, CO2, CH4, NOx, NH3, SO2, VOC, and 34 hazardous air pollutants (HAPs). PM2.5 emissions were further broken down into EC, OC, SO4, NO3, and PM fine
HAPs emission factors and fractions of PM2.5 components were provided by EPA
2014NEI made flaming and smoldering emissions available (to allow for differentiated treatment of plume rise and potentially speciation)
Fire Inventory from NCAR (FINN) is used for Hawaii and Puerto Rico

## Slide 91: Data Sources for NEI Fires
Data Sources included for NEI fire inventory development (non-NEI years typically use only data in red)
  State/local/tribal data
  National Association of State Foresters (NASF) WF data
  NOAA’s Hazard Mapping System (HMS) data
  Incident Status Summary (ICS-209) data (wild vs prescribed)
  Geospatial Multi-Agency Coordination (GeoMAC) fire perimeter Shapefiles
  USDA Forest Service Activity Tracking System (FACTS) Rx fire perimeter data
  U.S. Fish and Wildlife Service (USFWS) data
  U.S. Department of Interior (DOI) Rx data
Ancillary data sources
  Fuel moisture data from the USFS Weather Information Management System
  Fuel Characteristic Classification System (FCCS) fuel loading database

## Slide 92: NEI Fire Development Overview

## Slide 93: 2014 and 2016 Annual PM2.5 from Wild and Prescribed Fires
Top: 2014
Bottom: 2016
Some aspects of fires are similar
between years:
Prairie, gulf coast, South Florida
Locations of large fires vary –
particularly noticeable in West, MN

## Slide 94: Agricultural Fires
EPA estimates day-specific point-based agricultural fires based on satellite detects (Pouliot, 2017)
2014 PM2.5
2016 PM2.5
Any
questions
on
fires??
Notes: Next: Caroline

## Slide 95: Speciation
Mapping inventory pollutants to model species
  Model species are used in the air quality model (AQM)
  NOx, VOC (TOG), and PM are speciated
There are many types of speciation profiles and each has a unique code
  Typically use SCC and pollutant to X-ref speciation profile to inventory sources
  Cross reference may also use FIPS, facility, etc.
Different chemical mechanisms:
  Emissions should match chemical mechanism of AQM
  Different mechanisms have different list of model species
  Examples: CB05, CB6, SAPRC07
Notes: Model species are either individual chemical compounds are groups of compounds

## Slide 96: Obtaining Speciation Profiles
SPECIATE database
  Source of most speciation profiles in the platform
  SPECIATE 4.5 is the most recent version: https://www.epa.gov/air-emissions-modeling/speciate-version-45-through-40
  Includes basin-specific profiles for oil and gas sources
Speciation Tool
  Processes profiles from the SPECIATE database into the chemical mechanisms used by air quality models
  Written in PostgreSQL and Perl
  Available from cmascenter.org
  Separate training class for Speciation Tool

## Slide 97: Speciation Overview
Model species 1
Model species 2
Model species 3
Model species 4
Model species 1
Model species 2
Model species 3
Model species 4
Inventory Poll
Profile (%)
Speciated (mass)
MW1
Conversion to moles
MW2
MW3
MW4
Notes: Mass is conserved through speciation

## Slide 98: NOx Speciation
NOx is converted to following model species:
  NO
  NO2
  HONO
Example profiles:
profile | pollutant | species | massfrac
WHONO | NOX | NO2 | 0.092
WHONO | NOX | NO | 0.900
WHONO | NOX | HONO | 0.008
NHONO | NOX | NO2 | 0.100
NHONO | NOX | NO | 0.900

## Slide 99: PM2.5 Speciation
Older versions of CMAQ used “simplified” PM model species (AE5)
Recent versions of CMAQ use the aerosol module ISORROPIA v2 that requires additional PM model species (AE6)
species name | species description | AE5 | AE6
POC | organic carbon | Y | Y
PEC | elemental carbon | Y | Y
PSO4 | sulfate | Y | Y
PNO3 | nitrate | Y | Y
PMFINE | unspeciated PM2.5 | Y | N
PNH4 | ammonium | N | Y
PNCOM | non-carbon organic matter | N | Y
PFE | iron | N | Y
PAL | aluminum | N | Y
PSI | silica | N | Y
PTI | titanium | N | Y
PCA | calcium | N | Y
PMG | magnesium | N | Y
PK | potassium | N | Y
PMN | manganese | N | Y
PNA | sodium | N | Y
PCL | chloride | N | Y
PH2O | water | N | Y
PMOTHR | unspeciated PM2.5 | N | Y
pollutant | species | massfrac
PM2_5 | POC | 0.5019
PM2_5 | PEC | 0.1093
PM2_5 | PSO4 | 0.0033
PM2_5 | PNO3 | 0.0107
PM2_5 | PNH4 | 0.0034
PM2_5 | PAL | 0.0005
PM2_5 | PCA | 0.0007
PM2_5 | PCL | 0.0024
PM2_5 | PFE | 0.0004
PM2_5 | PK | 0.0014
PM2_5 | PMN | 0.0001
PM2_5 | PMOTHR | 0.0125
PM2_5 | PNA | 0.0014
PM2_5 | PNCOM | 0.3513
PM2_5 | PSI | 0.0001
PM2_5 | PTI | 0.0007
Prescribed Burning Composite Prof. (91109)
Notes: First four species (EC, OC, SO4, NO3) are in both; treatment of “the rest” differs; table on right is specific example for prescribed burns

## Slide 100: VOC Speciation
Inventory VOC is converted to Total Organic Gas (TOG)
  Example for Gas Exh E10: VOC * 1.199 = TOG (also includes methane)
TOG is then speciated according to the mechanism (species sum to 1.0):
  Different model species depending on the chemical mechanism (e.g., CB6)
pollutant | species | massfrac
TOG | ALD2 | 0.0145
TOG | ALDX | 0.0023
TOG | CH4 | 0.1416
TOG | ETH | 0.0596
TOG | ETHA | 0.0234
TOG | ETOH | 0.0157
TOG | FORM | 0.0145
TOG | IOLE | 0.0130
TOG | OLE | 0.0457
TOG | PAR | 0.3860
TOG | TOL | 0.1044
TOG | UNR | 0.0563
TOG | XYL | 0.1229
Gasoline Exhaust – E10 (8751a)
Model Species | Description
ALD2 | Acetaldehyde
ALDX | Propionaldehyde and higher aldehydes
BENZENE | Benzene*
CH4 | Methane*
ETH | Ethene
ETHA | Ethane
ETOH | Ethanol
FORM | Formaldehyde
IOLE | Internal olefin carbon bond
ISOP | Isoprene
MEOH | Methanol
OLE | Terminal olefin carbon bond
PAR | Paraffin carbon bond
TOL | Toluene and other monoalkyl aromatics
XYL | Xylene and other polyalkyl aromatics
Notes: Note model species molecular weights will vary with profile
  Some of the model species are lumped, e.g. for CB05 “PAR”

## Slide 101: VOC Integration Overview
Integration
  Process of taking select VOC HAPs from the inventory as “true” and then speciating the remaining VOC
  Want to avoid double counting of pollutants
  Want to speciate the remaining VOC, while taking into account HAPs that were removed
BAFM treated as explicit HAPs
  Benzene, Acetaldehyde, Formaldehyde, Methanol
NONHAPTOG
  Remaining TOG after removing explicit VOC HAPs
  NONHAPTOG = TOG – Total of BAFM species (moles)

## Slide 102: VOC Integration Example
pollutant | species | massfrac
TOG | ALD2 | 0.0145
TOG | ALDX | 0.0023
TOG | CH4 | 0.1416
TOG | ETH | 0.0596
TOG | ETHA | 0.0234
TOG | ETOH | 0.0157
TOG | FORM | 0.0145
TOG | IOLE | 0.0130
TOG | OLE | 0.0457
TOG | PAR | 0.3860
TOG | TOL | 0.1044
TOG | UNR | 0.0563
TOG | XYL | 0.1229
pollutant | species | massfrac
NONHAPTOG | ALD2 | 0.0019
NONHAPTOG | ALDX | 0.0025
NONHAPTOG | CH4 | 0.1519
NONHAPTOG | ETH | 0.0639
NONHAPTOG | ETHA | 0.0251
NONHAPTOG | ETOH | 0.0169
NONHAPTOG | FORM | 0.0010
NONHAPTOG | IOLE | 0.0139
NONHAPTOG | OLE | 0.0491
NONHAPTOG | PAR | 0.4067
NONHAPTOG | TOL | 0.1119
NONHAPTOG | UNR | 0.0234
NONHAPTOG | XYL | 0.1318
No integrate
Integrate
Gasoline Exhaust – E10 (8751a)
Notes: Total massfrac = 1 for both profiles
Still have FORM and ALD2 b/c of secondary formation, note much smaller
Note NONHAPTOG, i.e. need to go from NONHAPVOC -> NONHAPTOG
So have 2 sets of profiles: integrate and no integrate

## Slide 103: VOC Integration by Sector
Platform Sector | Approach for integrating
ptegu | No integration (i.e., integrated species in inventory ignored)
ptnonipm | No integration
ptfire, ptagfire | No integration
othfire | No integration
othar | No integration
othpt | No integration
onroad_can | No integration
onroad_mex | Full integration (MOVES-Mexico)
ag | N/A – sector contains no VOC
afdust, othafdust | N/A – sector contains no VOC
beis | N/A – contains specific VOC model species
nonpt, rail | Partial integration (BAFM; EBAFM for future year PFC)
np_oilgas | Partial integration (BAFM)
pt_oilgas | Partial integration (BAFM)
rwc | Partial integration (BAFM)
nonroad | Full integration (BAFM) (i.e., integrated species used)
cmv_c1c2 | Full integration (BAFM)
cmv_c3 | Full integration (BAFM)
onroad | Full integration (calculated in the MOVES2014 model)*
Notes: Partial integration: means some sources are integrated and others aren’t
Biog – beis creates model species explicitly
Onroad: MOVES2014 doing integration within model (next slide)

## Slide 104: Additional Speciation Concepts
NBAFM = integration of BAFM + naphthalene
  CMAQ CB6 has naphthalene as explicit species
  Used for 2014-16 platforms
COMBO files
  Method of combining 2 or more speciation profiles by pollutant/geography
  Example: combine E0 and E10 fuel profiles for portable fuel containers
Speciation can be used to group/track interrelated pollutants e.g., PAH’s for NATA

## Slide 105: Onroad speciaton
MOVES2014a does most of the needed speciation
  Has different profiles for different vehicle model years, regulatory classes, fuel types, and emission processes
  Previously used COMBO files or weighted profiles to approximate, but it was a coarse approach
  Can do an explicit mapping of profiles to sources if doing speciation within MOVES
PM2.5
  AE6 species coming directly from MOVES (as mass)
VOC
  16 pollutants are explicit, i.e. integrated
  Model species (moles) and inventory pollutants (mass) come directly from MOVES
  Need to specify chemical mechanism in the MOVES run
Notes: PM2.5: previous inventory polls from MOVES didn’t map cleanly to AE5 species

## Slide 106: QA of Speciation
Check Spcmat SMOKE logs to ensure that all sources have references to VOC and PM speciation profiles.
Sum model species to compare to VOC and PM2.5 inventory totals.
Compare integrated species to inventory for full and partial integration sectors.
Do a quick manual calculation of a species for a specific FIPS/SCC to ensure that the post-SMOKE value is using the correct profile (or profiles in the case of GSPRO_COMBO).
Check SMOKE logs for warnings or errors. For example:
  BAFM but no VOC for an integrate source
  No TOG conversion factor
  Skipping pollutant [X] for other than PM10 and *_NOI pollutants
Look at the output species to make sure all of the expected species are there for the specific mechanism (CB05 vs CB6 vs …).
Notes: Another Spcmat log message we look for is "Skipping pollutant [X]", which means that an inventory pollutant is being dropped. We expect to see this for PM10 (we speciate PM2.5 and pass through PMC instead) and _NOI pollutants (no-integrate BAFM, which we want to drop to avoid double counting speciated VOC), but if we see anything else getting skipped, that's a problem.

## Slide 107: Questions?
Any questions on speciation?
Notes: Next: Alison

## Slide 108: Onroad Emissions Modeling
Use representative EFs and county/ grid-specific activity data and meteorology to create emissions for all counties
Meteorological Preprocessor (Met4Moves)
MOVES
SMOKE
AQ model-ready files
Temperature ranges,
rel. humidity
EF tables
Gridded met
Run MOVES to get emission factors (EF) for representative counties for each temperature and speed needed
Met. Data from WRF
Activity Data

## Slide 109: Representative Counties
3000+ counties are mapped to approx. 300 representative counties according to: state, fuels, light duty age distribution, ramp fraction, I/M programs, emissions standards
Notes: Emphasize the county specific activity and the grid specific meteorology is used even if using rep counties.

## Slide 110: Onroad Emission Processes and Inputs
On-roadway emissions
  Exhaust, evaporative, evaporative permeation, refueling, brake and tire wear (Rate-per-distance)
  Primary inputs: vehicle miles traveled (VMT), average speeds, speed profiles, and temperature (gridded, hourly)
Off-network emissions (i.e. parked vehicles)
  Exhaust from starts, evaporative, evaporative permeation, refueling, hot soak (right after a trip) (Rate-per-vehicle)
  Evaporative fuel vapor venting and diurnal (when vehicles are parked for a long period) (Rate-per-profile)
  Primary inputs: vehicle population (VPOP) and Temperature (gridded, hourly, daily min/max)
Hoteling:
  Extended idle and auxiliary power units (APU) for combination long-haul trucks (Rate-per-hour)
  Primary inputs: Hoteling hours and T (gridded, hourly)
Notes: VMT and HOTELLING are temporalized, others aren’t

## Slide 111: Running MOVES
MOVES runs on Windows, but SMOKE runs on Linux so a translation step is required
For info on running MOVES to create emission factors for SMOKE-MOVES see: https://github.com/CEMPD/SMOKE-MOVES
runspecgenerator.pl creates MOVES configuration files
moves2smkEF.pl reads the MOVES output databases and converts them into a form that runs SMOKE

## Slide 112: On-roadway Processing (RPD)
Uses Standard SMOKE programs + Movesmrg
  Input “inventory” is VMT and SPEED data
Notes: Spcmat is still used, just to keep track of which EF are model species vs inventory.

## Slide 113: Onroad Hoteling
Hoteling = Overnight truck idling: extended idle and APU
States can submit hoteling hours by county
EPA uses combination long-haul truck VMT on urban + rural restricted roads to distribute hoteling hours to counties
Temporal profile is opposite of the driving profile
Spatial surrogate is based on truck parking spaces
Notes: Not idling at ports or bus stops, really about requirement to hotel for the long-haul trucks
Consider mentioning APU splits

## Slide 114: 2014NEIv1 Onroad NOx and Changes from 2011
Chart: Onroad NOx Trend
onroad NOx | 5707938.9756 | 4622760.3022 | 3859478.3819
2011
2014
2016
Although VMT typically
increases with time, emissions
decrease as newer cleaner vehicles penetrate the market

## Slide 115: Improved MOVES Inputs used in 2014NEIv2
Some states provided updated inputs
  9 agencies for onroad, 3 states for nonroad
EPA sponsored a project to decode year 2014 registration VINs into MOVES vehicle types by model year for both light-duty and heavy-duty vehicles
  Impacts age distributions and vehicle populations
  Includes data for populations of alternative fuel light-duty vehicles (i.e., diesel, CNG, E-85, electric)
  EPA derived VMT data based on the new VPOP data
Coordinating Research Council (CRC) A-100
  Used hourly telematics data to derive speed and VMT temporal distributions for lower 48 states for light-duty, medium-duty, and heavy-duty vehicles
EPA updated fuel properties data

## Slide 116: Input Data Updates from the CRC A-100 Study
Sponsored by the Coordinating Research Council (CRC)
Main data source: StreetLight Data, Inc.
  5 Billion observations over continental U.S.
  Passenger cars, commercial truck fleet management systems
  Sub-minute level data for 12 consecutive months
  Grouped by light-duty (LD), medium-duty (MD), and heavy-duty (HD); no car/truck split or age info available for LD vehicles
  5m spatial precision, 16 speed bins
Used data to derive
  VMT temporal distributions for MOVES and SMOKE temporal profiles
  Road type distributions supplemental to those from FHWA
  Speed distributions for MOVES plus speed inputs to SMOKE
    Populating all speed bins by road type, month, day, hour, vehicle type was a challenge outside of urban areas

## Slide 117: CRC A-100 Geographic Scale
18,644,352 road segments over the Continental U.S.
3,601 polygons of urban areas / clusters from the U.S. Census
* CRC A-100 plots courtesy ERG

## Slide 118: Spatial Groups Used
Example of Passenger Vehicles on Urban Unrestricted Roads
Counties for
which MOVES
inputs could be
populated shown in red;
others are based
on data for
the region and
urban/rural

## Slide 119: Speed Results by City
Compared Atlanta, Chicago, and Las Vegas
Patterns differed by city and from MOVES defaults
  Weekday patterns for passenger vehicles on urban restricted roads (highways) and unrestricted local roads shown below
  Note scales differ

## Slide 120: Speed by Vehicle Type
Found speed differences between LD, MD, and HD
  MD/HD speeds higher than LD in many cases
  Different areas have different patterns esp. on interstates
Chicago examples shown below – note scales differ

## Slide 121: Diurnal VMT Distributions by Vehicle Type – Chicago example
Note the differences in patterns weekdays vs weekends and LD/MD/HD
Data put into formats to support MOVES (weekday/weekend) and SMOKE (day-specific)

## Slide 122: Day of Week Temporal Profiles
A-100 data was prepared into MOVES dayVMTFraction and SMOKE day-of-week temporal profiles (SMOKE shown here)
Urban GA combination trucks
RURAL GA LD vehicles
Urban GA LD vehicles
Urban GA MD trucks

## Slide 123: Hoteling and On-roadway NOx by County
Hoteling follows interstates 187K tons (blue=900tpy) ->
Rate per Distance 4.1M tons exists in all counties (blue=9900tpy)

## Slide 124: Impacts of new Spatial Surrogates on 2011 Onroad NOx Emissions
Using 2011 surrogates
Using 2014 surrogates
Difference between 2011 and 2014 surrogates
On-network spatial surrogates now based on VMT
Many off-network surrogates are based on NLCD

## Slide 125: Off-network VOC by County
RPV VOC is 1.3M of 2.4M tons (blue=3600) -> NOx=746K of 4.8M tons)
Rate per Profile VOC 200K of 2.4M tons onroad VOC (blue=540)

## Slide 126: Questions?
Any questions on onroad emissions processing?

## Slide 127: Commercial Marine Vessels
CMV in the NEI is split into two categories:
  Category 3 (C3) (i.e., large) vessels with engine displacement above 30 liters that primarily use residual fuel blends
  C1 and C2 vessels that primarily use distillate fuels
  Recreational marine vessels are part of nonroad
Inventories computed for emissions in state waters (3-10 nautical miles) and federal waters out to 200 nautical miles from the U.S. coastline
  Port emissions are separated from underway
  Areas outside of 200 n.m. filled in from non-NEI data sources
“Modes” indicate what ships are doing and different emission factors are used for each
  M=maneuvering, H=hoteling, C=cruise, Z=reduced speed zone
EPA data used except for states that submitted for 2014NEIv1: NH, NJ, IL, TX, CA, WA
  More states submitted for 2014NEIv2 based on LADCO study

## Slide 128: Commercial Marine Data Sources and Modeling
Data sources for CMV in the 2014NEI
  Entrance and clearance data (2012)
    About 11,000 vessels linked to routes from origin port to destination port
    Hours of operation computed based on route and vessel type (e.g., bulk carrier, container, oil tanker) with reduced speed zones factored in
  Army corps of engineers waterborne commerce data for tugs and barges, bulk carriers, tankers, and other vessels
  2007 category 1 and 2 vessel study
  See 2014NEI TSD for more details
Modeling
  CMV modeling sectors were cmv (nonpoint) and othpt (point)
  Now: cmv_c1c2 and cmv_c3 including all U.S. waters
  Plume rise computed for cmv_c3 (pseudo-point sources which also help us represent shipping routes)
  New spatial surrogate available May, 2017

## Slide 129: U.S. State and Federal Waters

## Slide 130: New 12km CMV Spatial Surrogate based on marinecdaster data

## Slide 131: Modeling Ramp-up Period
For regional CAP-focused modeling, we typically have a ramp-up period of 10 days (i.e., starting on December 22 of the previous year)
  For most sectors, emissions from December of the modeled year are repeated during the ramp-up
  For biogenic emissions, data based on actual prior year meteorology are used
For hemispheric modeling, the ramp-up is longer – six to eight months
  Prior year fire emissions used for ramp-up

## Slide 132: Final Merging and QA
After all sectors have been processed through SMOKE programs, the ground-level emissions are merged using the SectorMerge script
  Runs the mrggrid program based on the Sector list file
  Only one input for ground-level but point sources can be given to CMAQ by sector without merging
    cmv_c3, ptegu, ptnonpim, pt_oilgas, ptagfire, ptfire, ptfire_othna, othpt
If CAMx is to be run instead of CMAQ, then CAMx conversion scripts must be run
  CAMx requires point files to be merged

## Slide 133: Final Low-level Merging
All ground-level files must be merged for both CMAQ and CAMx
  Biogenic emissions can be optionally computed within CMAQ
  Considers both day-specific and representative day emissions
afdust_adj
ag
cmv_ c1c2
nonpt
on-road
np_ oilgas
non-road
onroad_ca_adj
othar
oth afdust_adj
rail
rwc
onroad_can
onroad_mex
pt_oilgas
ptnonipm
Ptegu and fire sectors are all elevated
Merged 2D emissions for each day

## Slide 134: Example Sector List for 2016 Alpha Case
sector | sectorcase | Sectbaseyr | mrgapproach | prevyrspinup | endzip | mergesector
afdust_adj | 2016fd_cb6_16j | 2016 | all | SectBaseYr | Y | Y
ag | 2016fd_cb6_16j | 2016 | all | SectBaseYr | Y | Y
nonroad | 2016fd_cb6_16j | 2016 | mwdss_Y | SectBaseYr | N | Y
rail | 2014fd_cb6_16j | 2014 | aveday_N | SectBaseYr | N | Y
nonpt | 2014fd_cb6_16j | 2014 | week_Y | SectBaseYr | N | Y
np_oilgas | 2016fd_cb6_16j | 2016 | week_Y | SectBaseYr | N | Y
rwc | 2016fd_cb6_16j | 2016 | all | SectBaseYr | Y | Y
ptegu | 2016fd_cb6_16j | 2016 | all | SectBaseYr | Y | Y
ptnonipm | 2016fd_cb6_16j | 2016 | mwdss_Y | SectBaseYr | N | Y
pt_oilgas | 2016fd_cb6_16j | 2016 | mwdss_Y | SectBaseYr | N | Y
ptagfire | 2016fd_cb6_16j | 2016 | all | SectBaseYr | Y | N
ptfire | 2016fd_cb6_16j | 2016 | all | SectBaseYr | Y | N
cmv_c1c2 | 2014fd_cb6_16j | 2014 | aveday_N | SectBaseYr | N | Y
ptfire_othna | 2016fd_cb6_16j | 2016 | all | SectBaseYr | Y | N
onroad | 2016fd_cb6_16j | 2016 | all | SectBaseYr | Y | Y
onroad_ca_adj | 2016fd_cb6_16j | 2016 | all | SectBaseYr | Y | Y
othafdust_adj | 2016fd_cb6_16j | 2016 | all | SectBaseYr | N | Y
othar | 2016fd_cb6_16j | 2016 | week_N | SectBaseYr | N | Y
onroad_can | 2016fd_cb6_16j | 2016 | week_N | SectBaseYr | N | Y
onroad_mex | 2016fd_cb6_16j | 2016 | week_N | SectBaseYr | N | Y
othpt | 2016fd_cb6_16j | 2016 | mwdss_N | SectBaseYr | N | N
* Some sectors may come from another case
Notes: Mention that emissions from earlier cases can be merged into the same case
Also mention about how low-level emissions are merged but elevated are not

## Slide 135: QA of Merged Emissions
Look at the mrggrid logs to ensure that the correct case/sector files are merging and all sectors with ground-level emissions are included
Generate domain totals of the 2D and inline files and compare back to the sum of the sector-specific SMOKE annual reports
Check the size of the 2D merged emissions files to make sure that the file size is the same for each day (corrupted files will be smaller)
Sometimes compare day-specific or annual total gridded emissions to a previous run

## Slide 136: Base Year Anthropogenic Emissions in 2011, 2014, and 2016
Chart: 
| NH3 | NOx | PM2_5 | PM10 | SO2 | VOC
2011el | 3858634.0613 | 16816655.6494 | 2790705.6655 | 9125060.7644 | 6460582.6281 | 12532666.1648
2014fb | 3257233.322 | 15163903.031 | 2791502.6987 | 9294963.896 | 4990705.2141 | 12021553.5797
2016fc | 2997370.7956 | 13645967.335 | 2776829.3685 | 9572854.7107 | 3236235.7764 | 11653688.9299

## Slide 137: 2014 National Emissions by Sector
Chart: Annual Tons of NOx by Sector
| beis | cmv_c1c2 | cmv_c3 | nonpt | nonroad | np_oilgas | onroad | othar | othpt | pt_oilgas | ptagfire | ptegu | ptfire | ptnonipm | rail | rwc
2011 | 912730.6234 | 615357 | 839503 | 719546.2689 | 1620440.8011 | 667058.4809 | 5707938.9756 | 543673.2996 | 1411781.1526 | 509843.4261 | 46021.3948 | 2095118.6375 | 333403.5428 | 1213359.1764 | 792506 | 34508.0359
2014 | 903179.6535 | 546751 | 826462 | 793268.469 | 1383213.185 | 793465.6256 | 4622760.3022 | 828523.6362 | 1112941.6876 | 482646.4165 | 12900.2383 | 1758567.2082 | 246883.1421 | 1190348.7429 | 779800.6428 | 32253.8767
2016 | 979204.7758 | 546751 | 820027 | 796784.9796 | 1183097.7327 | 805609.4802 | 3859478.3819 | 867034.82 | 1115885.0501 | 446395.7215 | 18298.0484 | 1292012.4768 | 333226.1752 | 1189956.518 | 672247.1741 | 32388.9517
Chart: Annual Tons of SO2 by Sector
| cmv_c1c2 | cmv_c3 | nonpt | nonroad | np_oilgas | onroad | pt_oilgas | ptagfire | ptegu | ptfire | ptnonipm | rail | rwc
2011 | 10231 | 303908 | 275914.8783 | 4011.2062 | 17237.3922 | 28194.8461 | 66576.306 | 17751.8261 | 4670569.497 | 165789.0733 | 1049287.4022 | 7936 | 8964.274
2014 | 5621.4214 | 428019.6239 | 300203.8001 | 3153.6378 | 37795.5488 | 28323.7694 | 46770.7764 | 3870.7403 | 3241497.7714 | 130097.0753 | 880364.1183 | 6985.5841 | 8098.4222
2016 | 5636.3231 | 393864.3269 | 301345.1566 | 2549.4267 | 40610.5012 | 28723.2852 | 40897.9854 | 5636.0608 | 1533870.4417 | 180960.2937 | 874272.3258 | 695.9715 | 8133.9715
Chart: Annual Tons of NH3 by Sector
| ag | cmv_c1c2 | cmv_c3 | nonpt | nonroad | np_oilgas | onroad | pt_oilgas | ptagfire | ptegu | ptfire | ptnonipm | rail | rwc
2011 | 3520078.2804 | 382 | 65 | 94225.0768 | 2615.2057 | 0 | 120859.2904 | 5946.7711 | 3314.6905 | 25066.35 | 329396.1024 | 65989.5627 | 347 | 19744.8337
2014 | 2874005.3977 | 291.9745 | 28.4535 | 114007.6461 | 2235.3418 | 15.1881 | 103332.0647 | 332.8824 | 55657.1104 | 25932.8222 | 273952.9279 | 64751.4013 | 363.7049 | 16279.3344
2016 | 2593401.3085 | 293.82 | 28.519 | 114479.7901 | 2196.88 | 21.169 | 97160.7813 | 345.4065 | 80364.5642 | 27545.2816 | 388420.3252 | 64825.875 | 362.1991 | 16345.2013
Chart: Annual Tons of PM2.5 by Sector
| afdust_adj | cmv_c1c2 | cmv_c3 | nonpt | nonroad | np_oilgas | onroad | pt_oilgas | ptagfire | ptegu | ptfire | ptnonipm | rail | rwc
2011 | 923589.7931 | 19766 | 34097 | 403886.9238 | 154052.4745 | 16333.5107 | 188925.225 | 13934.5942 | 101345.7584 | 208133.9917 | 1844612.4791 | 320736.8916 | 23990 | 381913.5025
2014 | 953025.0347 | 14603.2278 | 50319.0536 | 569213.4055 | 132710.0394 | 20191.9569 | 157996.9186 | 11999.7485 | 49406.5063 | 183031.491 | 1482165.0495 | 292401.3277 | 23164.9701 | 333439.0186
2016 | 1004295.1087 | 14692.5488 | 48097.8901 | 570871.9448 | 108273.3238 | 20935.3852 | 133165.5407 | 11731.8562 | 68103.1685 | 150540.7714 | 2047170.6805 | 292121.1371 | 19150.6502 | 334850.043
Biogenic emissions comprise 71% of VOCs and fires 8%

## Slide 138: State-Sector Totals Report
State totals by sector before and after SMOKE

## Slide 139: CAMx Conversion
EPA always prepares the emissions files initially using CMAQ’s netCDF format
Scripts are provided to convert to CAMx:
  Map species from CMAQ model ready names to CAMx names
  Convert Merged gridded 2D emissions are from IOAPI format to CAMx model ready format “emis2d” files
  Merge gridded CAMx emissions with met-based surf zone sea-salt emissions files
  Convert inline CMAQ model ready emissions to CAMx point “ptsr” emissions for each sector
    This step requires that fires have been processed in 3D
  Merge the CAMx point “ptsr” emissions into a single point “mrgpt” file for the CAMx model

## Slide 140: Source apportionment
Source apportionment is used for transport and sector-based analyses
  Evaluate significant contribution by states
  Understand which sectors contribute to AQ issues
Source apportionment requires that all sectors have been tagged and written as CAMx ptsr emissions files
For most sectors, SMOKE can prepare both SA and non-SA outputs simultaneously
  Onroad for SA takes a lot of RAM and we run in shorter time chunks than our typical 7 days
Scripts are available for source apportionment runs
A standalone 2-D sea-salt file is read by CAMx (all others are in CAMx ptsr format)

## Slide 141: Emissions Modeling Software and Data
The CMAS Center (https://www.cmascenter.org/) distributes SMOKE, CMAQ, VERDI (visualization), the Surrogate Tool, Spatial Allocator, Speciation Tool, and the Control Strategy Tool which includes the Emissions Modeling Framework
SMOKE software and documentation is available from http://www.cmascenter.org/smoke
A WIKI for SMOKE that answers common questions about emissions modeling is here: https://www.airqualitymodeling.org/index.php

## Slide 142: Emissions Modeling Platform Data Availability
EPA’s modeling platform data, documentation, scripts available from
  https://www.epa.gov/air-emissions-modeling
  Version 6 platforms include:
    2011v6.3: October 2017 transport analysis (2011en/2023en), January 2017 NODA (2011el/2023el), Final Cross-State Air Pollution Rule (CSAPR) Update (2011ek/2017ek), hemispheric case
  Version 7.0 platform for NATA based on 2014NEIv1
  2016 alpha platform with compatible 2014 and 2015
  Spatial surrogates available for 4km, 12km, 36km
  Speciation data for CB05, CB6, SAPRC07TB
  Temporal profiles for all sectors

## Slide 143: Emissions Modeling FTP site
Several versions of the 2011 platform and preliminary versions of 2014,2015, and 2016 are available on the FTP site:
ftp://newftp.epa.gov/air/emismod

## Slide 144: Getting Started Running SMOKE
Scripts are available for the 2016 alpha platform on the FTP site, along with emissions, ancillary data, and summary reports

## Slide 145: 2016 Alpha Emissions and Summary Reports

## Slide 146: Final Questions?
Any final questions on the base year part of the training?
Contacts: eyth.alison@epa.gov, farkas.caroline@epa.gov, Vukovich.jeffrey@epa.gov