## Slide 1
Our Location on Wednesday, May 16th at 1 pm (1st floor EPA Building) is Room C111-C

## Slide 2: Help us Improve!
You will receive an email with a link to a survey to review the course(s) you attend at the Emissions Inventory Training Workshop.
Please take a few moments to let us know about your experience this week.
We welcome your feedback!

## Slide 3: Background on Ammonia and EPA methods for key Ammonia (NH3) sectors in the NEI
Tesh Rao, Jesse Bash
OAQPS/ORD
May 16, 2018

## Slide 4: General Information
Trainers
Tesh Rao, EPA, OAQPS
  Rao.Venkatesh@epa.gov
  919-541-1173
Jesse Bash, EPA, ORD
  Bash.Jesse@epa.gov
  919-541-0862
Logistics
This training runs from 1 pm to 5 pm
We will try to have a couple of small breaks
Questions always welcome, but if we are falling behind, we may ask for you to see us at a later time or during a break. Feel free to email us after this course is over as well.

## Slide 5: Course Outline
1:00-1:15 pm Introductions: Trainers and Attendees
1:15-1:50 pm General background on NH3 air quality and emissions
1:50-2:05 pm Short Break
2:05-2:55 pm CMU (Carnegie Mellon University) FEM (Farm Emissions Model) for estimating Livestock Emissions (EPA methods)
2:55-3:15 pm 2014 NEI (National Emissions Inventory) v2, 2017 NEI plans for Livestock
3:15-3:30 pm Short Break
3:30-4:25 pm EPA methods for estimating Fertilizer Emissions
4:25-4:40 pm 2014 NEI v2, 2017 NEI Plans for Fertilizer
4:40-5:00 pm Last set of questions/comments/suggestions, end of class

## Slide 6: Course Objectives
To introduce you to some background on NH3 and key sectors in the inventory
To introduce you to CMU’s FEM for estimating livestock NH3 emissions which was used as the basis for EPA estimates for the 2014 NEI
To introduce you to EPA/ORD’s methods for estimating fertilizer NH3 emissions, which was used as the basis for EPA estimates in the 2014 NEI
Outline 2014 results and plans for the 2017 NEI for both sectors
To provide you an opportunity to ask questions about all of the above
To offer collaboration on these important sectors, and listen to any suggestions/comments you may have moving forward

## Slide 7: Background on NH3

## Slide 8: NH3 is a significant air pollutant b/c of its impacts to land, water, and human health
Eutrophication, Deposition, and Fine PM formation are all important issues when you have excess NH3

## Slide 9: Some Background on NH3
Brief look at NH3 and atmospheric chemistry
Policy relevance of NH3
  Precursor insignificance demonstrations
  SIP development examples
  Standard-setting and regional haze
Model-measurement comparisons
  Suggest that NH3 emissions are too low
  Deposition issues
Emission inventories
  Sectors of importance as we move to the 2017 NEI focus
Resource-sensitive projects that need to be completed to address perceived shortcomings in inventories, measurements, and modeling of ammonia
  The emissions inventory is one of those key projects that need to be completed

## Slide 10: NH3 and atmospheric chemistry
NH3 is the primary basic gaseous compound in the atmosphere
NH3 is directly emitted (it’s not formed by photochemical reactions)
NH3 combines with gaseous acids (e.g., sulfuric acid and nitric acid) to form corresponding PM constituents (e.g., ammonium sulfate and ammonium nitrate)
Favorable meteorological conditions for ammonium nitrate formation are low temperature and high relative humidity, which often occur in winter or at night
PM formation can be limited by the availability of NH3 or the availability of acids (e.g, nitric acid formed from NOx emissions)
  Understanding which PM precursor limits PM formation is often critical for AQ management

## Slide 11: Policy Relevance: Precursor Demonstrations, SIP Development, Regional Haze, Standard Setting

## Slide 12: Precursor Insignificance Demonstrations
NH3 is a PM2.5 precursor under Clean Air Act subpart 4 nonattainment area provisions (January 2013 ruling)
Precursor insignificance demonstrations based on AQ modeling can be used to remove NH3 as a precursor for attainment plans and nonattainment New Source Review (NH3 is not a Prevention of Significant Deterioration precursor)
Precursor insignificance demonstrations are attractive because they can potentially avoid consideration of RACT(Reasonably Available Control Technology)/RACM (Reasonably Available Control Measures) controls
CARB will likely submit a demonstration for the San Joaquin Valley (SJV) where results will depend on the percent reductions in NH3 selected for modeling
The SJV demonstration (and demos for Cache Valley Utah and other areas) could depend on the accuracy of the modeling inventories

## Slide 13: SIP Development
South Coast Air Basin
  Projects funded by the Coordinating Research Council found that NOx emission reductions cause PM2.5 disbenefits, whereas NH3 reductions produce PM2.5 benefits
  Authors conclude that South Coast is pursuing the wrong control strategy by targeting NOx emission sources
  EPA modeling for 2010 indicates that NH3 reductions produce PM2.5 benefits under current conditions, but we have found issues with our NH3 modeling in South Coast (discussed below) and have not examined responsiveness for future years
Salt Lake, Cache, and Utah Valleys
  The limiting precursor (NH3 or NOx) for PM2.5 nitrate formation is uncertain
  Utah has been adding non-inventory NH3 emissions into model grid cells domain-wide to improve model performance
  Recently, the model-added NH3 has been found to have a large impact on sulfate formation in clouds and has raised questions about the reliability of the approach
  New data have recently become available from a 2017 field campaign, but these data have yet to be analyzed or compared with model predictions

## Slide 14: Standard Setting and Regional Haze
Standard Setting
  Secondary NOx/SOx/PM NAAQS: Ecosystem effects of PM ammonium deposition are included in the review, and CASAC (Clean Air Scientific Advisory Committee) has highlighted the importance of NH3:
    August 2017 letter: “Ammonia emissions are increasing in many regions of the U.S. and the CASAC recommends that EPA consider the need for developing National Ambient Air Quality Standards for reduced forms of nitrogen during the Risk and Exposure Assessment and Policy Analysis phases of this NAAQS review”
  PM NAAQS: Will likely be asked to consider NH3 emission controls in Risk/Exposure/Impact analyses
Regional Haze (RH) Planning
  Under-predictions of nitrate in the southwest in regional photochemical models, possibly related to under-predictions of NH3, present challenges to developing RH SIPs for the 2nd implementation period (2018-2028)
  Modeling to address BART (Best Available Retrofit Technology) provisions of the RH program can be sensitive to assumptions about background levels of NH3, which are uncertain

## Slide 15: Comparisons of AQ Model Predictions of NH3 with Measurements/Monitoring

## Slide 16
Source: Jesse Bash
Ammonia Monitoring Network (AMoN)
AMoN provides a national picture of two-week average NH3 concentration at mostly rural sites
2014 CMAQ NH3 predictions are compared with AMoN measurements (figure, left)
Seasonal profiles of the observations are generally captured by the model
However, the model underestimates observed concentrations

## Slide 17
Aircraft Measurements in South Coast Air Basin (CalNex-2010)
NH3 is under-predicted for aircraft transects near Riverside downwind of Chino dairy facilities (e.g., markers (1) and (4), above left)
NH3 is over-predicted for transects along San Gabriel Mountains near Pasadena, e.g., (3)
Nitrate predictions in Riverside are sensitive to NH3 emissions (above, right), and increased NH3 emissions lead to better model performance in Riverside
NH3, Modeled - Observed
Nitrate
Source: Kelly et al. (2014) Fine-scale simulation of ammonium and nitrate over the South Coast Air Basin and San Joaquin Valley of California during CalNex-2010. Journal of Geophysical Research-Atmospheres 119(6): 3600-3614.

## Slide 18
Bakersfield, 22 May – 28 June 2010
Pasadena and Bakersfield Ground Sites (CalNex-2010)
In Pasadena, NH3 tends to be over-predicted especially at night, consistent with aircraft transects in this region on previous slide
Some overpredictions occur overnight and could be related to underestimated vertical mixing in the model
In Bakersfield, NH3 is underestimated during the day when emissions are highest but is overestimated in the evening, possibly due to issues with nighttime mixing in the model
Source: Kelly et al. (2014) Fine-scale simulation of ammonium and nitrate over the South Coast Air Basin and San Joaquin Valley of California during CalNex-2010. Journal of Geophysical Research-Atmospheres 119(6): 3600-3614.

## Slide 19
Fresno
Hanford
Bakersfield
Turlock
Fresno
Hanford
Bakersfield
Turlock
Fresno
Hanford
Bakersfield
Turlock
2013 San Joaquin Valley DISCOVER-AQ
Source: Kelly et al. (2017) Modeling NH4NO3 during the 2013 San Joaquin Valley DISCOVER-AQ campaign [in prep]
Some consistency in observed and modeled spatial patterns of NH3 in SJV, but concentrations are underestimated significantly in source regions
However, in contrast to South Coast, model predictions of nitrate are not very sensitive to NH3 emissions in SJV (i.e., NH3 is not the limiting precursor) (not shown)

## Slide 20: NE Colorado: Boulder Atmospheric Observatory
~33 km
Denver
Greeley
RMNP
Colors indicate average NH3 emissions in model cells
BAO: Boulder Atmospheric Observatory
RMNP: Rocky Mountain National Park
Source: Kelly et al. (2016) Simulating the phase partitioning of NH3, HNO3, and HCl with size-resolved particles over northern Colorado in winter. Atmospheric Environment 131:67-77.
NH3 and NHx (NH3 + NH4+) are underestimated in the base simulation at the Boulder Atmospheric Observatory (BAO) southwest of the Greeley high-emission region
Closer agreement between model and measurements when NH3 emissions are increased by a factor of four
NHx

## Slide 21
Southeastern Aerosol Research and Characterization (SEARCH) Study
Source: Pye et al. (2015) Modeling the current and future roles of particulate organic nitrates in the southeastern United States, Environmental Science Technology
At the SEARCH site in Centreville, AL, model predictions are of similar magnitude as observations during summer of 2013
Some differences in diurnal profiles
Our modeling seems to show that the match between model-predicted NH3 and observations is better in the SE US

## Slide 22: Deposition of NHx relative to total N
NH4 + NH3 = NHx, which nationally makes up nearly half of all nitrogen deposition
Based on NADP TDEP (fused CMAQ and CASTNET) data
2011 Ratio of NHx to total N deposition
2011 total N deposition
Source: NADP TDEP

## Slide 23: Summary of NH3 Model Evaluations
National evaluations with AMoN data suggest the model is biased low but has a reasonable representation of seasonal patterns
Evaluations for regions with large livestock operations indicate that the model has significant under-predictions in these areas, although modeled emissions are elevated in these regions compared to surrounding areas
For some areas/periods (e.g., SEARCH and Pasadena), model predictions are in reasonable agreement with measurements or are biased high
Overall, model evaluations suggest that emissions are too low in many areas; however,
  NH3 is highly variable in space/time, so we need to use caution in interpreting short snapshots from field campaigns or sparse monitoring
  Issues with modeling the fate and transport of NH3 likely explain a portion of the model-measurement differences
  Issues with the spatial allocation of emissions could explain a portion of the differences

## Slide 24: General Emissions Inventory Issues related to NH3 emissions

## Slide 25: What is the issue?
Many papers have suggested that NH3 emissions may be too low in certain key sectors in the NEI based on modeling results and other analysis
EPA’s modeling is also showing an under-prediction between model output and monitored NH3 values
It remains unclear which sources may be underestimated—but Ag sources have been implicated, since they contribute most NH3 totals in the NEI

## Slide 26: NH3 in the 2014 NEI v2, ~ 3.6 millions tons total
Chart: 2014 NEI v1 Ammonia Emissiosn by Source
Chart: Ammonia Emissions by Source (from 2014 NEI v1)
Chart: Ammonia in the 2014 NEI
| Agriculture-Livestock Waste | Agriculture-Fertilizer Application | Fires | Residential/Commercial/Industrial/Fuel Combustion | Mobile sources | Other
 | 2075004.0625 | 786571.2931 | 402702.2901 | 161276.0923 | 111775.5015 | 56609.7855

## Slide 27: NH3 in the 2014 NEI v2, continued…
Top 15 EIS Sectors for NH3 in the 2014 NEI, Emissions shown in Short Tons (Total NH3 = 3.6 Million Tons)
Ag Livestock emissions have been fairly constant over time in the NEI. Fertilizer is actually seen going down from 2011 to 2014

## Slide 28: Emissions changes over time show NH3 to be stagnant
Chart: Emission Trends (thousand Tons)
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
NOx | 25167.3146 | 24932.0642 | 25026.2551 | 25123.2551 | 24967.3162 | 24697.8066 | 24382.383 | 24525.8479 | 24175.8095 | 22608.603 | 22335.2324 | 21377.5467 | 23845.1412 | 22536.957 | 21217.5205 | 20260.9555 | 19133.1911 | 18005.4268 | 16812.9891 | 15675.3352 | 14750.0835 | 14334.1111 | 13696.0435 | 13057.9759 | 12476.3784
PM10 | 27753 | 27345 | 27098 | 27364 | 28608 | 25820 | 22856.997 | 22908.629 | 22892.668 | 23383.385 | 23746.877 | 23707.594 | 20241.2044 | 20329.8106 | 20414.3709 | 20496.5153 | 20596.1266 | 20695.738 | 20401.9983 | 20021.3076 | 19645.0914 | 19396.5376 | 18648.2909 | 17900.0443 | 17151.7976
PM25 | 7560 | 7320 | 7198 | 7149 | 7542 | 6929 | 6724.344 | 6256.447 | 6260.626 | 7210.768 | 7288.015 | 6995.633 | 4674.115 | 4757.0754 | 4838.4581 | 4918.9677 | 5063.411 | 5207.8543 | 5015.5383 | 4989.3115 | 4965.455 | 4974.4348 | 4818.1868 | 4661.9387 | 4505.6907
SO2 | 23065.1492 | 22363 | 22072.7409 | 21764.273 | 21331.5089 | 18609.3474 | 18370.4745 | 18833.6797 | 18938.7073 | 17478.2663 | 16277.6763 | 15887.6245 | 14951.7296 | 14727.6086 | 14491.1076 | 14489.8323 | 13066.6399 | 11643.4474 | 10253.6648 | 9019.2446 | 7662.2153 | 6383.0026 | 4983.6401 | 4777.9492 | 4603.5596
VOC | 23125 | 22899 | 22659 | 22252 | 21932 | 21578 | 19001.341 | 18785.8922 | 18136.0313 | 17602.9026 | 16897.5084 | 16698.9347 | 17075.9741 | 16697.495 | 16300.364 | 15885.3361 | 16034.0685 | 16182.8009 | 14912.2221 | 14746.5632 | 14988.3796 | 15263.0154 | 14990.8585 | 14718.7016 | 14446.5447
NH3 | 4320 | 4384 | 4443 | 4518 | 4589 | 4659 | 4727 | 4817 | 4940 | 4857 | 4907 | 3689 | 3769.3781 | 3780.3903 | 3791.0987 | 3801.6267 | 3946.9649 | 4092.303 | 4161.2096 | 4117.0273 | 4072.845 | 4028.6627 | 3819.4029 | 3610.1431 | 3400.8833
CO | 143602.6433 | 136544.6433 | 134507.304 | 129363.9605 | 124470.1703 | 120072.4019 | 114356.0441 | 111117.1921 | 108725.9983 | 104033.128 | 102418.0061 | 98518.379 | 87981.3307 | 85541.1809 | 83095.6364 | 80645.8417 | 77937.0513 | 75228.2609 | 67454.9712 | 60552.4067 | 61570.9315 | 61060.1482 | 59093.1006 | 57126.0531 | 55159.0055

## Slide 29: Inventory-Related Issues
Ag Livestock
  Sector with most NH3 emissions in inventory
  For the 2014 NEI, used a revised CMU model that was run by a graduate student working for Peter Adams
  We have the source code, but more work needed to use for other emissions years
    EPA also working on analysis of NAEMS data and Emissions Estimation Models
    For NEI work, collaboration between OAQPS and ORD on-going. Considering additional university collaboration (only for NEI efforts)
Ag Fertilizer
  ORD provides emissions estimates based on their bidirectional (bidi) approach
  Research and model revisions continue (much more on this later)
Mobile Sources
  NH3 emissions have not been investigated by EPA for some time. Not currently an agency priority for mobile sources.
Fires
  OAQPS/ORD testing project is expected to give updated emission factors (EFs) for possible future use in EPA fire emissions approaches

## Slide 30: Short Break: Be back in 15 minutes please!

## Slide 31: CMU’s Farm Animal Ammonia emissions model (FEM)
Model developed by Carnegie Mellon University 2016

## Slide 32
Ammonia is a common by-product of animal waste due to the often inefficient conversion of feed nitrogen into animal manure (urine + feces). Livestock and poultry are often fed high-protein feed, which contains surplus nitrogen, to ensure that the animals' nutritional requirements are met. Nitrogen that is not metabolized into animal protein (i.e., milk, meat, or eggs) is excreted in the urine and feces of livestock and poultry where further microbial action (conversion of urinary urea to ammonia…the enzyme Urease, released in feces, reacts with urinary urea to form NH3) releases ammonia into the air during manure decomposition.

## Slide 33: 2014 NEI Efforts for Livestock Waste Ammonia Emissions
EPA was able to leverage work done via EPA’s Science to Achieve Results (STAR) grant to CMU, which enabled EPA to use an updated version of the CMU model to estimate livestock NH3 emissions in the 2014 NEI. Alyssa McQuilling (graduate student of Dr. Peter Adams at CMU) ran the model for v1 of the 2014 NEI.
We could not control deliverables nor understand the intricacies of the model as well as we wanted due to the structure of the grant and timing issues
We do have gaps in our current methods, and we are trying to improve these for the 2017 NEI
I am not an expert on the intricacies of the CMU model, and if there are questions that I (or others here) cannot answer, I will get you an answer as we begin to work on the 2017 NEI

## Slide 34: Sources of information
Alyssa McQuilling Thesis, February 2016
  "Ammonia Emissions from Livestock in the United States: From Farm-Level Models to a New National Inventory" (2016).
  http://repository.cmu.edu/cgi/viewcontent.cgi?article=1704&context=dissertations
Alyssa McQuilling and Peter Adams, publication, September 2015
  “Semi-empirical process-based models for ammonia emissions from beef, swine, and poultry operations in the United States,” Atmospheric Environment 120:127 - 136 · September 2015
Various presentations made by CMU professor Peter Adams on this subject
2014 v2 TSD, available currently on this FTP site: ftp://newftp.epa.gov/Air/nei/2014/doc

## Slide 35: General Overview of Semi-Empirical Process-Based Models for NH3 from Livestock
Farm-level emission factors in the literature vary by an order of magnitude due to the variations in manure management practices and meteorology
It is essential to capture this variability in emission inventories used, for example, for atmospheric modeling
Here (as the details will highlight), through a nitrogen mass balance with losses controlled by mass transfer resistance parameters, which vary with meteorological conditions, are tuned to match literature-reported and NAEMS-based (National Air Emissions Monitoring Study) EFs
Variations due to management practices are captured by having tuned factors that are specific to each set of practices
The resulting farm emissions models (FEMs) explain between 20 and 70% of the published EFs and typically estimate EFs within a factor of 2

## Slide 36: Ammonia Emissions Variability
Emissions depend on a variety of factors including
  Meteorology
  Management Practices
  Manure Characteristics
Lots of variability, how to build an inventory??
The approach here with the “updated” CMU FEM Model: emissions model instead of use of emission factors

## Slide 37
Scatter plot of fraction of input nitrogen volatilized as
ammonia, comparing application sub-model predictions
and experimental data showing range of measured data
(Pinder, et al., 2004) ---shows the variability that can be encountered

## Slide 38: Primary Meteorological Factors Affecting Ammonia Emissions, in general…
Temperature – temperature, emissions
  Higher temperature increases volatility of ammoniacal nitrogen
Wind speed – wind speed, emissions
  Higher wind speed decreases surface resistance
Precipitation – precipitation, emissions
  Precipitation allows for greater ground infiltration
pH also very important factor, will address later in presentation

## Slide 39: Process-based Models
Animal
Housing/grazing/
feedlot
Storage
Application
Volatilization
Volatilization
Volatilization
Excreta
Losses to soil, groundwater and biota
Track Nitrogen through manure management process
Includes mass balances and mass transfer laws
Goal is that such a model can capture the variability seen in measurements
Feed
Emissions ~ Nitrogen/Resistance (Wind, Temp)

## Slide 40: Overall objectives and goals
We want to build a national emissions inventory. We would like the data to also be applicable to air quality models
Therefore, the model’s focus should be on:
  Unbiased emission factors
  Seasonal cycle (daily variation would be even better)
  Regional scale variability in EFs
  Computational efficiency
  Scalability (do we have national inputs to drive model)
For Livestock, this leads to the following compromises
  Tune model to measurements rather than using “First Principles”
  Omit “details” when we don’t have national data (ventilation rates, for example) or no systematic regional variation
  Predicting results for an “average” farm, rather than a specific farm

## Slide 41: Approaches
Constant Emission Factors, Emissions = g/animal/day
x
# of Animals
Empirical Emission Factors, Emissions = F(temp, wind, etc.)
Semi-Empirical Process Model
First Principle Process Models
MORE EMPIRICAL
MORE PROCESS ORIENTED

## Slide 42: This approach versus earlier CMU work
Early 2000s, Rob Pinder did…
  process-based model for dairy only
  completed inventory using surrogate seasonal cycles for other livestock types
This work, Alyssa McQuilling…
  applied same process-based model framework to beef, swine, poultry
  first national inventory completely based on process-based modeling
  used NAEMS data
  various other updates

## Slide 43: Emissions Measurements (of NH3)
Historical Measurement Campaigns
Short-term monitoring deployments
Many researchers, many farms
Limited monitoring reporting of farm and measurement conditions
Spread of measurements poor (by season for example)
National Air Emissions Monitoring Study
At the time of this work, 1-3 years of data collection (long-term measurements of seasonal cycles)
Consistent measurement techniques
Extensive monitoring of meteorological and farm management conditions

## Slide 44: NAEMS Measurements
National Air Emissions Monitoring Study
~ 2 year measurement campaign
Dairy, swine, and chicken farms
Better contextual data
Long-term measurements, 2007-2010 … evaluate seasonal and daily variability
https://www.epa.gov/sites/production/files/2017-09/documents/_epaoig_20170919-17-p-0396.pdf

## Slide 45: Objectives
Build process-based FEMs for all livestock types
  Dairy cows (basically carried forward from previous work), Beef Cattle, Swine, Layer Chickens, Broiler Chickens
Evaluate the model(s), especially for seasonal and daily variability (using NAEMS data, for example)
Build National Inventory (the 2014 NEI in our case)
See if results help improve air quality modeling evaluations

## Slide 46: Methods: Details
Animal
Housing/grazing/
feedlot
Storage
Application
Volatilization
Volatilization
Volatilization
Excreta
Losses to soil, groundwater and biota
Each farm has a manure management train with mass balances on: 1) ammoniacal nitrogen, 2) urea, and 3) manure volume
Each component (e.g., housing, storage, …) has NH3 volatilizations and thus ammonia emissions
Feed
Emissions ~ N/Resistance (Wind, Temp)

## Slide 47: Methods: Details
Animal
Housing/grazing/
feedlot
Storage
Application
Volatilization
Volatilization
Volatilization
Excreta
Losses to soil, groundwater and biota
Emissions Computed:
EF = {A * [TAN] * H*}/r
EF: Emissions Factor ------------------ Key Output
A: Surface Area Fouled by Manure ---------- Model Parameter
H*: Henry’s Law Equilibrium Constant --------- Model Parameter
[TAN]: Total Ammoniacal Nitrogen Concentration -------- Mass Balance
r: Mass Transfer Resistance Parameter-- TUNED TO OBSERVATIONS

## Slide 48: FEM Submodel Flow
Data flows through each submodel:
Nitrogen and water
From literature or previous submodel
Submodel
(e.g. swine storage)
Daily Average Emission Factor
Inputs
Outputs
Nitrogen and water balance
(goes to next submodel)
Adjusted parameters
Meteorological data
From National Climate Data Center (NCDC)
Mass balances on each sub-model
What isn’t emitted remains in the same sub-model
Transfers between sub-models only occur when “Scheduled” based on farming practices.
  For example, housing manure may be cleaned out daily and take to storage for dairy cows but less often for poultry
  Similarly, manure is taken out of storage and applied at various points in the year

## Slide 49: Methods: Details
Emissions Computed:
EF = {A * [TAN] * H*}/r
r = ra +rb+ rs
Aerodynamic and quasi-laminar resistances: standard atmospheric theory
SURFACE RESISTANCE:
Tuned to match measured EFs!!
rs = function (Meteorology and Practices)
e.g. for Beef Feedlots
rs=H1T + H2u + C
Where H1 and H2 are constants and tuned to capture variability due to temperature and windspeed

## Slide 50: The “r” resistance term is very important!!
Each box has its own equation for r. E.g. storage has its own equation and housing has a different one. Moreover, each practice type has its own r equation, e.g. tie stall dairy housing has a different equation than free-stall dairy housing. In general, the r equations are also functions of meteorology. This approach to specifying the r is how the model makes the emissions depend on practices and meteorology.
Animal
Housing/grazing/
feedlot
Storage
Application
Volatilization
Volatilization
Volatilization
Excreta
Losses to soil, groundwater and biota

## Slide 51: Methods: Summary
How does the model get seasonal (daily) variability?
  Resistance depends on meteorological variables
How does the model get variability due to practices?
  Separate resistance sub-model for each
    Livestock type
    Manure management stage: housing, storage and application
    Major practice: e.g. deep-pit and shallow-pit swine housing
  Other differences (e.g. frequency of house clean-out)
Regional variation is a combination of meteorology and practices
  The met data pulled from NCDC is actually according to their “climate zones”. There are ~200 of them. So EFs for different counties in the same climate zone will be the same for the same farming practices. Note, however, that this is not really an inherent limitation of the CMU model – just the structure of the input data used.

## Slide 52: Model evaluation
Since the tuning is done to have no bias versus observations, the fact that the model predicts the right magnitude is not evidence that the model is working as it would be if it were a purely untuned first-principles model
  Evaluation of the model is done against the same data used for tuning. This is a documented weakness since everything is not totally independent.
  Ideally we would want to tune based on some data and test based on other, but there simply isn’t that much data
However, the evaluation does provide an useful quantification of how well a relatively simple mass balance model (there are much more complex farm models out there) can explain “variability” in emissions factors in a complex system.
Model performance evaluated primarily in terms of R value and mean fractional error between observed and modeled EFs

## Slide 53: FEM: Tuning and Evaluation
Beef Feedlots
Swine Housing
Broiler Housing
Layer Housing
Unbiased (because the models have been tuned, and the error between model predictions and measured EFs are minimized)
R2 values ranges from 0.2 for Beef to 0.7 for layers
Modeled EFs are generally within a factor of 2 of measured…at farm scale

## Slide 54: Role of “Contextual Information”
Not all studies report all required input parameters (e.g. feed or manure nitrogen)
Measurements need to report feed N, other practices, and meteorological conditions to put results in context and be useful to process-based models and inventories
Versus all studies
Vs studies reporting N
Notes: A-B:
Figure 2a shows the model evaluation for the beef feedlot submodel of the beef cattle farm emission model. The figure shows that the model has some skill in reproducing the literature reported emissions for feedlot beef production. Figure 2b shows the model evaluation for beef feedlots where information about the nitrogen content of feed and/or excreta is presented with the emission factor. This figure highlights the importance of reporting dietary nitrogen and nitrogen excretion rates in the literature, because with this extra information we were better able to simulate ammonia emission factors for beef feedlots than when we did not have this information, increasing the r2 value of the data from 0.21 to 0.36.

## Slide 55: Open vs Enclosed Sources
Swine Housing: Enclosed
Swine Storage: Open
Open (outdoor) sources are more difficult to measure … need to infer emissions rate from downwind concentrations….must make dispersion assumptions
Notes: Here is a side-by-side comparison of all four animal types for which a farm emission model has been developed. I’ve displayed the evaluation of each animal’s housing submodel.
You can see from the figure the variation in both the amount of literature data available for each animal type as well as the ranges of emission factors that each animal type spans, just for the housing portion of manure management.
You’ve seen the beef and swine results in previous slides, so focusing on the lower row:
Broiler chickens have a short life cycle and, as a result, we have chosen to report emission factors in terms of grams of ammonia volatilized per animal unit per day, where 1 animal unit (AU) is 500 kg. This avoids dealing with the complicated task of separating the effects of differences in temperature and other meteorological conditions and difference in bird weight, which changes rapidly. Unfortunately this is not a perfect solution as there is some evidence that emission factor per bird weight changes over the course of the production cycle, though there is no consensus on how the emission factor changes. Model results in Figure 2e show an R2 value of 0.29 with the data reported from the literature from farms in the United States. It is important to know the outdoor temperature even at enclosed facilities because the outdoor temperatures often drive ventilation rates and affect how much ammonia is volatilized within the barn. Model results in Figure 2f show an R2 value of 0.65 with the data reported from the literature from farms in the United States.

## Slide 56: Further (seasonal) evaluation examples using NAEMS Farms
Free Stall Dairy Barn, NY
Shallow Pit Swine Housing, NC
Litter-based Broiler Housing, CA
These graphs show seasonal cycle of emission factors compared to that predicted by the corresponding FEM
Typically, Dairy and Swine Farms have peaks in the summer while layers and broilers typically have winter peaks
FEMs seem to capture the NAEMS data well (R2 values range from 0.6 to 0.9)

## Slide 57: Evaluation: Daily Variability
Daily variability in housing emissions tends to be better characterized by the model than storage emissions
Free-Stall Dairy House in Indiana
Dairy Lagoon in Indiana

## Slide 58: Development of a National Emissions Inventory
Meteorology
National Climate Data Center (NCDC)
Temperature, Precipitation, and Wind Speed
Daily Time Resolution, Climate Division Spatial Resolution
Management Practices
National Animal Health Monitoring Survey
Housing type, Storage type, Application methods
Multi-state regional spatial resolution
Animal Population
USDA Agricultural Census
County level animal numbers from 2012

## Slide 59: Regional Farming Practices: An Example
Regional variation in housing, storage and application practices
Swine shown as an example here
The MW includes ID, IA, MN, MT, ND, NE, SD, WI, and WY
The Eastern states include CT, DE, IL, IN, ME, MD, MA, MI, NH, NJ, NY, OH, PA, RI, and VT
All other states in Southern Region

## Slide 60: Inventory Calculations
Run FEM for county-specific meteorology to produce daily emission factors
  Repeat for all farm practices
Compute a county composite EF as a weighted average across all manure management practices in that county
  Repeat for all animal types
County-based Emissions = (Emissions Factor) x (Animal Population)
  Resulting data has structure of emissions = f(county, day, livestock type, “practice”) where “practice” is shorthand for the different housing/storage/application configurations that prevail in a county
Result is ammonia emissions with:
  Daily temporal resolution
  County spatial resolution
  …by livestock type, management stage, practice

## Slide 61: 2011 Results: National Totals
Seasonal and daily variability apparent
Summer emissions dominated by swine
Beef and broilers more important during wintertime (relative to swine)
Layers have reverse seasonal emission pattern

## Slide 62: Spatial Distribution
San Joaquin Valley, Poultry and Cattle Production
Iowa, Beef and Swine Production
NC Coastal Plain, Broiler and Swine Production

## Slide 63: Regional Emission Factors
NC Swine EF about double that of IA (annual)
Higher EFs in warmer places
Differences in practices less significant than Temperature differences
Note also different EFs within a given state

## Slide 64: Animal Contributions vs 2011 NEI
Similar magnitude of emissions in 2011 FEM inventory and 2011 NEI
Much greater swine emissions in FEM inventory (swine storage emissions higher in NAEMS compared to prior literature)
Much smaller contribution from dairy

## Slide 65: Conclusions, observations, caveats
Framework: process-based model tuned to observed emissions factors
  Captures regional and seasonal variability
  Unbiased overall compared to EFs used in tuning
FEM captures seasonal cycle and practice differences; limited on daily variability
The general approach: Measurements -> process model -> prediction EFs everywhere
  …whereas a more traditional approach skips the middle step and just tries to take the measured EF that most closely matches the situation at hand. In the process-model approach, hopefully, the model learns something important, e.g. about T-dependence, and uses that to interpolate (and extrapolate) to other conditions that don’t exactly match those measured.
First national inventory based on process based modeling was 2011
  similar total emissions as NEI 2011
  swine ↑ but dairy ↓
  stronger seasonal cycle

## Slide 66: Conclusions, observations, caveats
EF measurements more useful if they also report “context”
  meteorology, pH, manure N, etc.
Manure management / farm practice data is as much of a limiting factor as EF measurements
pH is a very important parameter for governing NH3 emissions
  With the current FEM, the Henry’s law constant takes pH into account
  Many sensitivity studies show pH to be very important
  Challenge for inventory building because there is no national database of manure pH
  So, when building the inventory, the model uses a “typical value” for pH.
  When we tune or otherwise evaluate the models against specific measurements, we use the actual manure pH value – if it was measured and reported. Frequently, it’s not. When it’s not reported, we’re forced to use a “typical value” again.
This same methodology was used to develop the 2014 NEI v2, the next section will outline how that was done

## Slide 67: Extra Slides for Livestock Portion of Course

## Slide 68: Submodel Calculations
Each submodel relies on 3 mass balance equations to track changes in:
  Manure volume
    Increases due to deposits and precipitation
    Decreases due to emission and infiltration
  Urea concentration
    Decreases due to hydrolysis and infiltration
  Total ammoniacal nitrogen (TAN) concentration
    Increases due to urea breakdown
    Decreases due to volatilization and infiltration

## Slide 69: Submodel Mass Balance Equations

## Slide 70: National Inventory Contruction (cont.) - Composite EF Diagram
Daily EF a,b,c,d1
Daily EF a,b,c,d2
Fraction c,d1
Composite EFa,b,c
Fraction c,d2
x
x
Where: a = animal type
b = day
c = county
d = management practice
Daily EF a,b,c,dx
Fraction c,dx
x

## Slide 71: Regional Manure Management Practices
Used data from most recent USDA National Animal Health Monitoring Surveys (NAHMS)
Informs on type of animal housing, manure storage and manure application methods
Data available by U.S. region

## Slide 72: Animal Populations
2012 USDA Animal census
  County-level, grown to 2014 levels using available survey data at the time of v1 inventory development
  Includes dairy cows, beef cows, feedlot beef cows, swine, layer chicken, and broiler chickens
  Data was reviewed for missing parameter data and filled in with reasonable values
Notes:   Data was reviewed for missing parameter data and filled in with reasonable values
    Counties without data assumed to have average “missing county” population
      (State animal population – animal population attributed to counties)/ number of counties with missing animal population
    Counties in states with unknown total population were assumed to have a population of zero
      This occurred in 1 state for swine and 4 states for beef feedlots

## Slide 73: FEM Results
Found ammonia emissions depend strongly on temperature and nitrogen and less on wind speed and precipitation
Emission factors recommendations from earlier EPA guidelines fall within the range of emissions factors produced by the FEM
Model performance evaluated primarily in terms of R value and mean fractional error between observed and modeled EFs

## Slide 74: 2014 NEI v2 Livestock Emissions

## Slide 75: U.S. Ammonia Emissions Sources, 2014 NEI v2
Chart: 
| Agriculture-Livestock Waste | Agriculture-Fertilizer Application | Fires | Residential/Commercial/Industrial/Fuel Combustion | Mobile sources | Other
 | 2075004.0625 | 786571.2931 | 402702.2901 | 161276.0923 | 111775.5015 | 56609.7855
Figure A – U.S. ammonia emissions sources (3.6 million tons)
Figure B – U.S. livestock ammonia sources (2.1 million tons)
Chart: 
| Beef Cattle | Dairy Cattle | Swine | Broilers | Layers | Everything Else
 | 668218.6227 | 250577.5899 | 710005.5602 | 224585.9547 | 72599.8711 | 149016.4639
A)
B)

## Slide 76: Livestock waste emissions in the NEI
These are the only five SCCs that EPA reports their data into for the 2014 NEI (there are others that SLTs can choose to report into):
EPA estimates NH3 and VOC emissions for these SCCs
Livestock is inventoried in NonPoint (annual/county totals)
SCC | SCC Level 1 | SCC Level 2 | SCC Level 3 | SCC Level 4
2805002000 | Miscellaneous Area Sources | Agriculture Production - Livestock | Beef cattle production composite | Not Elsewhere Classified
2805018000 | Miscellaneous Area Sources | Agriculture Production - Livestock | Dairy cattle composite | Not Elsewhere Classified
2805025000 | Miscellaneous Area Sources | Agriculture Production - Livestock | Swine production composite | Not Elsewhere Classified
2805007100 | Miscellaneous Area Sources | Agriculture Production - Livestock | Poultry production - layers with dry manure management systems | Confinement
2805030004 | Miscellaneous Area Sources | Agriculture Production - Livestock | Poultry Waste Emissions | Broilers

## Slide 77: General methods for going to 2014 NEI v2
After reviewing the v1 estimates based on the methods outlined previously, we:
  Found errors in allocations of emissions to counties
  Had several states ask us to use more up-to-date animal population data
In going to the v2 inventory:
  We corrected the county allocation errors
  We estimated revised 2014 county-level animal populations using USDA 2014 Survey and 2012 Census data. Then constructed the v2 inventory using EFs from CMU’s v1 model.
  We did not alter the FEM model in going from v1 to v2, so used the same 2011 meteorology
  We added VOC emissions to this sector

## Slide 78: 2014 NEI v2 – Animal Population Revisions
Animal population data were obtained primarily from the 2014 USDA National Agricultural Statistics Service (NASS) Quick Stats program
  As many counties as possible across the United States
  Single farm counties/types not reported (NR) for confidentiality
  Not as complete as the USDA Census
USDA 2012 Census used to augment the 2014 Survey for NR
  Unclear if NR is 0 or grouped
  If 2014 county/type = NR and 2012 reported, 2014 pop = 2012 pop x state 2014pop / 2012 pop
County/types with NR in 2012 and 2014
  Diff = 2014 state –  2014 counties
  NR counties = Diff / (Number of NR counties)

## Slide 79: Details – Animal Populations
Animal Type | Source
Chicken Broilers | The inventory reflects the 2012 state level totals, because no 2014 data is available in the Survey at either the county or state level. The NR county gap fill described in previous slide used as needed.
Chicken Layers | The inventory is based primarily on the 2012 Census. There were 30 states with 2014 state level population data, and the 2012 county level populations for those states were adjusted to reflect the change in population between 2012 and 2014 state level totals.

## Slide 80: Details – Animal Populations
Animal Type | Source
Swine | The NEI 2014 v1 inventory had four states with 2014 county level data (MT, NC, ND, OK). These states were not changed for v2. The other 46 states were updated to reflect the 2014 state-level total. The county populations were adjusted to reflect the change in population between 2012 and 2014 state level totals.

## Slide 81: Details – Animal Populations
Animal Type | Source
Dairy Cattle | Counts are based on 2014 Survey data where available, and counties with missing data are “gap filled” using the algorithm described earlier.
Beef Cattle | Counts are based on 2014 Survey data where available, and counties with missing data are “gap filled” using the algorithm described earlier.

## Slide 82: Details – Population Gap Filling
 | Beef Cattle | Dairy Cattle | Swine | Chicken Layers | Chicken Broilers
Number of counties with gap filling (3,071 counties in database) | 776 (25%) | 973 (32%) | 643 (21%) | 433 (14%) | 621 (20%)
Number of states with no gap filling | 5 | 4 | 9 | 6 | 3

## Slide 83: VOC Emissions
Prior to 2014 NEI, VOC emissions had not been estimated by EPA for the livestock waste
Calculated VOC emissions using the ratio of VOC to NH3 emissions from livestock waste.
Calculated an average VOC/NH3 ratio of 0.08 using data at the county level where both VOC and NH3 were reported in 2014 NEI v1 by SLTs (from 3 states, total of about 110 counties)
Applied this ratio to the 2014 NEI v2 NH3 livestock inventory to develop the county and animal type specific VOC inventory
  About 150,000 tons of VOC nationally estimated using this approach

## Slide 84: Comparisons between EPA’s estimates and SLT submissions
Animal Type | States Submitting NH3 Emissions | 2014 State NH3 (tons/year) | 2014 v2 EPA NH3 in these States (tons/year)
Beef Cattle | CA, GA, ID, IL | 110,107 | 102,717
Dairy Cattle | GA, ID, IL | 38,400 | 14,116
Swine | CA, GA, ID, IL | 35,154 | 50,227
Chicken Layers | CA, GA, ID | 12,424 | 8,804
Chicken Broilers | CA, GA, ID | 56,240 | 45,559
We used the states’ submissions in the NEI when they were submitted over EPAs
The NEI is thus a combination of EPA data and SLT-submitted data
When a SLT submits emissions, they are not required to submit the accompanying activity data
Reasonably good agreement when aggregated across SLTs (EPA estimates low for dairy cattle and chicken categories)

## Slide 85: Beef Cattle: Population and NH3 Emissions– 2014 NEI V2

## Slide 86: Dairy Cattle: Population and NH3 Emissions– 2014 NEI V2

## Slide 87: Swine: Population and NH3 Emissions– 2014 NEI V2

## Slide 88: Chicken Layers: Population and NH3 Emissions– 2014 NEI V2

## Slide 89: Chicken Broilers: Population and NH3 Emissions– 2014 NEI V2

## Slide 90: NH3 Emissions from all Livestock – 2014 NEI V2

## Slide 91: Looking forward to the 2017 Process
Apply CMU model code, after testing and revising/updating as needed, as possible, for the final inventory (resource dependent)
Consider options for developing a draft inventory sooner using 2017 census data (collected and compiled by OAP) for animal populations and EFs from the 2014 CMU model
Increase collaboration and science for this sector
Rethink and revise methods for VOC estimates (resources permitting)
Include silage VOC emissions on dairy farms as a source (dependent on resources, data availability and methods development)
Develop methods for AK, HI, PR and VI
Ask SLTs to submit animal count data for their states, after review of draft estimates…

## Slide 92: Short Break: Be back in 15 minutes please!!

## Slide 93: Fertilizer NH3 Emissions in the 2014 NEI

## Slide 94: NH3 Bidirectional Exchange
Measurements show that NH3 can deposit or emit
  Depending on meteorology and soil, plant nitrogen status, and ambient NH3 concentration
Traditionally emissions and deposition have been modeled separately
NH3 bidirectional exchange has been incorporated into the Community Multiscale Air Quality (CMAQ) Modeling system
  Consistent representation of NH3 emissions and deposition
Walker et al 2013

## Slide 95: NH3 Fertilizer Emissions
SCC Code 2801700099
EPA was able to leverage work done in an EPA/ORD and USDA Agriculture Research Service (ARS) collaboration
  Develop the methodology to run the USDA’s Environmental Policy Integrated Climate (EPIC) field scale model on a continental domain
EPIC output is used by US EPA’s CMAQ model to estimate NH3 emissions from fertilizer considering bidirectional exchange

## Slide 96: Modeling of NH3 Emissions in CMAQ
Meteorology (WRF)
Agricultural Modeling (EPIC)
Air Quality Modeling (CMAQ)
Diagnostic Emission Estiamtes

## Slide 97: Primary Meteorological Factors Affecting Fertilizer Ammonia Emissions
Temperature – temperature, emissions
  Higher temperature reduces the soil equilibrium ammonium concentration
Wind speed – wind speed, emissions
  Higher wind speed decreases surface resistance
Precipitation – precipitation, emissions
  Precipitation dilutes the ammonium available for evasion in the soil
Soil pH – pH, emissions
  Higher soil pH favors reduces the soil equilibrium ammonium concentration

## Slide 98: USDA’s Environmental Policy Integrated Climate (EPIC) Simulations for CMAQ

## Slide 99: USDA EPIC Model
Environmental Policy Integrated Climate (EPIC) Model
  Assess the effect of soil erosion on productivity.
  Predict the effects of management decisions on:
    Soil, water, nutrient, and pesticide movements
    Impact on soil loss, water quality, and crop yields for areas with homogeneous soils and management
We have developed an interface to run EPIC for CMAQ applications
  Fertilizer Emission Scenario Tool for CMAQ (FEST-C)
    Available at https://www.cmascenter.org/fest-c/
  Includes EPIC and data needed to run for the contiguous US

## Slide 100: EPIC Inputs
Soil hydrological properties, type and pH
  USDA National Resources Inventory agricultural soil survey data
Crop area
  BELD 4 land use data
Crop Type
  2012 census of agriculture survey data
Crop management
  USDA Farm Production Regions based on census of agriculture data
Meteorological data
  Weather Research and Forecast (WRF) precipitation, wind speed, min and max daily temperature

## Slide 101: EPIC Crops Modeled for CMAQ Applications
Fertilizer Emission Scenario Tool for CMAQ (FEST-C)
  Interface to run EPIC on the contiguous US domain and formats EPIC output for CMAQ
  Includes USDA survey data for farm practices and crops grown
    Mapped to CMAQ domain
Set up to models 21 crops
  Hay, Alfalfa, Grass, Barley, Beans Edible, Corn Grain, Corn Silage, Cotton, Oats, Peanuts, Potatoes, Rice, Rye, Sorghum Grain, Sorghum Silage, Soybean, Spring Wheat, Winter Wheat, Canola, Beans, Other Crops
  Other crops modeled as corn
  Crop rotation is modeled
  Biogenic nitrogen fixation and mineralization of organic material are modeled

## Slide 102: NH3 in the Nitrogen Cycle
Processes considered in CMAQ coupled to the USDA Environmental Policy Integrated Climate (EPIC) model
Cooter et al 2012

## Slide 103: Scale of input data
Cooter et al 2012
Model Grid Resolution
  Meteorology
  Land use
Hydrologic Unit Code 8
  Subbasin level soil properties
County (census of agriculture data)
  Crop and associated fertilizer types
  Cropping system practices (e.g. injected versus broadcast)
  Irrigation
USDA Production Regions
  Similar cropping methods

## Slide 104: Running EPIC with FEST-C for CMAQ
What input data do I need?
  Simulation cell size, domain extent and projection
  MCIP formatted meteorological data on same domain as you will run CMAQ
  MODIS and NLCD data layers
What data are provided/generated
  Land use coverage (location of agricultural land)
  Soils (pH, texture, nutrient status)
  Agricultural management
What do I get out?
  Land use file required for bidirectional CMAQ
  Daily agricultural depth of fertilizer application and fertilizer amount
  Initial soil chemistry status
  Fertilizers application rates and estimated crop yields
Available at https://www.cmascenter.org/fest-c/

## Slide 105
The FEST-C User Interface – facilitates user-generated CMAQ-ready fertilizer input for any gridded domain, grid cell resolution and weather year by creating and submitting executable scripts.

## Slide 106
EPIC Application
Fertilizer Sales
Gronberg and Spahr (2012)
Running EPIC for CMAQ
The system does a reasonable job reproducing regional patterns of reported agricultural fertilizer purchases and use

## Slide 107: CMAQ Bidirectional NH3 Simulations

## Slide 108: Modeling NH3 exchange
CMAQ with bidirectional exchange connects the emission and deposition of NH3 from cropping systems to ambient concentrations
  Important for emissions and deposition weeks to months following fertilization
  Captures the impact that vegetation coverage has on emissions

## Slide 109: CMAQ with Bidirectional NH3 Exchange
Modeled
EPIC
Data
Fertilizer Applied?
Modeled
WRF
Data
Yes
CMAQ Modeled Soil NH4
Soil Moisture
& Temperature
Ammonium, pH, and
application method
Nitrification
NH4→NO3
CMAQ Modeled
Atmospheric NH3
Atm NH3 > soil NH3?
Deposition
Emissions
Yes
No

## Slide 110: CMAQ with Bidirectional NH3 Exchange
Requires setting a few environmental variables
  Setting the soil N file, EPIC outputs, and flags to run the model
Currently works only with WRF in a retrospective simulation mode, the Pleim-Xu land surface scheme
  CMAQ v5.3 will have options to work with WRF land surface schemes capable of forecasting
Emissions, NH3_Emis in kg ha hour, are output in the CMAQ Dry Deposition file
  Currently estimates agricultural and natural emissions
Emissions are removed from the soil pool in the model
  Ensures emissions cannot exceed nitrogen input

## Slide 111: NEI V2 Fertilizer NH3 Emissions

## Slide 112: 2014 NEI V2 estimates
Ran EPIC with updates to fertilizer application to pasture and hay
  Reduced application in the Southeast US
Emission estimates from a 2014 CMAQ v5.1 simulation
Tabulated monthly and annual emission estimates
Emissions reduced in Southeast and TX, increases in parts of CA and Upper Midwest
Cooler spring temperatures in 2014 accounted for some emission reductions

## Slide 113: 2014 NEI V1 estimates
(Ton per County)

## Slide 114: 2014 NEI V2 estimates
(Ton per County)

## Slide 115: 2011 versus 2014 Meteorology
Differences in emissions are due to meteorological dependence on emission factor and improvements to EPIC pasture and hay management

## Slide 116: Looking forward to 2017 NEI
Similar as 2014 NEIv2
NH3 emission model is being made more consistent with representation of fluxes in the Comprehensive Air Quality Model with Extensions (CAMx) and for other pollutant species in CMAQ
  Higher emissions in some agricultural regions due to more explicit modeling of agriculture and updated algorithms
Additional evaluation of technique against observations to give more credibility to 2017 NEI, if successful
  Agricultural and non-agricultural field observations
Biogenic and agricultural NH3 emissions output explicitly
Updating FEST-C to use 2016 Census of agriculture activity data to better represent current farm management practices

## Slide 117: Data that could help 2017 NEI development
EPIC activity data
  Fertilization rates, types and application depths, planting and harvesting dates, crop types
Cross Infrared Sounder (CrIS) NH3 retrieval
  Daily satellite NH3 data, ~1 ppb detection limit, 15-8 km grid resolution
  Retrieval algorithm delivered to NASA
This data will help in identifying source areas and seasonality of NH3 emissions
  Spatial and temporal allocation of animal sectors
  Identify areas where more detail may be necessary to improve fertilizer emissions
What you can do to help
  Crop activity data, farm nutrient management
Shailesh Kharol et al. In prep. 2018

## Slide 118: Appendix

## Slide 119: References
Walker, J.T., Jones, M.R., Bash, J.O., Myles, L., Luke, W., Meyers, T.P., Schwede, D., Herrick, J., Nemitz, E., Robarge, W., 2013, Processes of ammonia air-surface exchange in a fertilized Zea Mays canopy, Biogeosciences, 10, 981-998
Cooter, E.J., Bash, J.O., Benson V., Ran, L.-M., 2012, Linking agricultural management and air-quality models for regional to national-scale nitrogen deposition assessments, Biogeosciences, 9, 4023-4035
Bash, J.O., Cooter, E.J., Dennis. R.W., Walker, J.T., Pleim. J.E., 2013, Evaluation of a regional air-quality model with bi-directional NH3 exchange coupled to an agro-ecosystem model, Biogeosciences, 10, 1635-1645
Pleim, J.E., Bash, J.O., Walker, J.T., Cooter, E.J., 2013, Development and testing of an ammonia bi-directional flux model for air-quality models, J. Geophys. Res. 118, doi:10.1002/jgrd.50262

## Slide 120
Modeled NH3 exchange example
=++
Emiss
9 s m-1
7 s m-1
197 s m-1
182 s m-1
1200 s m-1
48 s m-1
6 µg m-3
2 µg m-3
422 µg m-3
24 µg m-3
400 s m-1
From Pleim et al. 2013 with observed data from Walker et al. 2013
=
From Bash et al. 2013 to estimate just the emission component

## Slide 121: NEI V1 Fertilizer NH3 Emissions

## Slide 122: 2014 NEI V1 estimates
Data available at the time
Recent 2011 simulation with bidirectional exchange
2014 and 2011 EPIC simulations
Estimated monthly emission factors from the latest 2011 CMAQ simulation and applied to 2014 EPIC output
  Annual fertilizer estimates were similar
  Emission factors estimated are a function of meteorology
  County level emissions include biogenic and fertilizer NH3

## Slide 123: 2014 NEI V1 estimates