## Slide 1: Barge Davy Crockett Response
Columbia River Toxics Reduction Work Group Discussion
Jim Sachet March 8, 2011

## Slide 2: Location & Background

## Slide 3: Status

## Slide 5: Incident Summary
Mystery Sheen on CR – Jan 14
Sheen on CR – Jan 20, 21; D Crockett source
Sheen on CR – Jan 27, 28; D Crockett source
Jan 27 – sheen 11 mi long, down to I-5 Bridge
Estimate of volume of discharge = 70 gal based on dimensions, time, thickness

## Slide 6: Sampling Results
Source samples from tanks, spaces, containers on the vessel
  Analysis for HCID, PCB, VOC, SVOC, Metals
  HCID indicates presence of diesel, lube oil and gasoline range hydrocarbons
Environmental samples
  Sheen; analysis for HCID
  Sediment; analysis for HCID, PCB

## Slide 7: Preliminary Report on PCB, Metals
Source samples
  Tanks in the machine space appear to be where PCBs are present, various samples show levels at < 0.001 mg/kg to a high of 33 mg/kg
  Metals found in some samples include copper, chrome, cadmium, zinc, nickel and lead
  Also found solvents in samples of oil in two small tanks; MEK and PCE
  Bunker fuel in deep tanks; No PCBs, No heavy metals, very low VOC, specific gravity 0.96

## Slide 8
Environmental samples
  Sheen samples; HCID show diesel and lube oil discharged, also suspect some release of bunker based on behavior of sheen near vessel
  Sheen samples not sufficient to run for PCB
  Sediment samples near vessel; 6 samples with 1 sample showing detect for PCB (0.0636 mg/kg)

## Slide 9: What Else?
Response Coordination and Organization
Geographic Response Plans
Spill Response Plan, Resources, Targets for recovery & storage
Outreach to Stakeholders & Public
Budget & Funding
Investigation
Next Steps

## Slide 10: Questions
Jim Sachet, Ecology Spill Response, SOSC
360/407-6328
jsac461@ecy.wa.gov
Rebecca Post, Ecology Spill Response, Sampling Specialist
360/407-7114
repo461@ecy.wa.gov