## Slide 1: RAZOR-AQ Data Review
Draft – Do not quote or cite

## Slide 2: Visual GAM Residual Analysis
Site selected for large difference between smoke and non-smoke-day residuals.
Plot shows good predictive capability in 2022 and 2023.
Large residual June 29, 30 and July 1 coincides with smoke identification.
ETYPE==1
Grey boxes and *

## Slide 3: Visual GAM Residual Analysis
Site selected for small difference between smoke and non-smoke-day residuals.
GAM does not predict nearly as many non-smoke exceedance days as observed.
Residuals are larger on non-smoke days with higher observed ozone.
Given large non-smoke-day residuals, the smoke day residual is not likely just "smoke".
ETYPE==1
Grey boxes and *

## Slide 4: Key Technical Concerns
GAM does not predict non-smoke ozone episodes in the Eastern and Central US
  West has 4647 days over 70 ppb with no HMS and GAM predicts 2877 days (62%).
  Central has 812 days over 70 ppb with no HMS, but GAM predicts just 91 (11%)
  East has 528 days greater than 70 ppb with no HMS, but GAM predicts just 44 (8%)
GAM residual is positively correlated with total observed ozone
  Smoke days and non-smoke days with observed O3 > 70 ppb have large residual.
  Non-smoke days > 70 ppb average residual: All: 9.5 ppb; West: 8 ppb; Central: 14.3 ppb; East: 14.6 ppb
Interpretation of residual as SMOKE impact depends on higher smoke-day residuals comparable mixing ratios.
  Is there a potential for bias-adjusted smoke-day (SD) residuals?
  At >70 ppb in the West, SD residuals are ~8 ppb larger than NSD
  At >70 ppb in Central, SD residuals are only ~2 ppb larger than NSD
  At >70 ppb in the East, SD residuals are only ~4 ppb larger than NSD
Can the PM2.5 threshold be modified to increase the difference in residual?
  The difference between SD and NSD residuals doesn’t change a lot
  Are there other methods to better separate smoke days? Or are the ozone differences small?

## Slide 5: RAZOR-AQ Methods
Technical approach
  Uses MDA8 ozone data from May-Sep 2018-2023
  Develop a separate statistical model for each of 600 ozone monitoring sites
  Provides a quantitative estimate of ozone contributions from fires in ppb
Steps
  Identify a set of days that are not influenced by smoke (ETYPE = 0) for use as a training dataset to develop model using the following 2 criteria:
    HMS map shows no overhead smoke (HMS = 0)
    PM2.5 is not elevated (PM2.5 < PM2.5_crit)
  For each monitoring site, develop a generalized additive model (GAM) which predicts ozone based on various meteorological parameters
  Calculate daily ozone contributions from fires as the difference between the observed ozone and the GAM predictions

## Slide 6: Key Assumptions
Residual is reasonably attributed to the smoke because the GAM trained on non-smoke-days
  Lee and Jaffe test this by comparing the residual on non-smoke days to smoke day
  Does the residual correlate with total observed ozone concentration?
  Does the difference between smoke days (SD) and non-smoke days (NSD) change geographically?
Smoke days have been appropriately selected
  The combination of surface PM2.5 critical value and HMS polygon overhead appropriately separates SD and NSD
    If it is too high, there will be no smoke days.
    If it is too low, there will be too many false positives.
  Technical issues that complicate determination of PM2.5 critical value
    PM2.5 is not a normal distribution
    PM2.5 has a seasonal signal
    PM2.5 levels may be changing over time
      Emissions reductions leading to decreasing trends in anthropogenic PM2.5 over time
      Increase fire activity leading to increasing PM in certain locations over time
For cases where SD concentrations are higher than the highest NSD concentration in the training set: extrapolation of GAM results is appropriate

## Slide 7: Overall model performance of GAM for NSD
Across entire dataset (all sites and NSD days) model performance is quite good
  Correlation = 0.88
  MB = 0.2 ppb
  NMB = 0.5%
  SD = 6.1 ppb

## Slide 8: model performance of GAM for NSD days > 70 ppb
Model performance degrades on ozone exceedance days
  Correlation = 0.56
  MB = -9.5 ppb
  NMB = -12.5%
  SD = 7.7 ppb
Bulk of NSD data is at lower concentrations
  MDA8 <= 70 ppb: n = 293,173 site-days (98%)
  MDA8 > 70 ppb: n = 5988 site-days (2%)
  Since there is a separate GAM model for each site, fewer number of data points in GAM for any particular site
    Divide by ~600 site but the distribution of high days is variable across sites
Common issue with statistical models
  they often do a good job at capturing the mean response
  performance deteriorates near the tails of the distribution
  exceedance days are near the tail of the ozone distribution

## Slide 9: Does the residual correlate with total observed ozone concentration?
Plot includes all datapoints where ETYPE = 0 (i.e. NSDs)
Residual plotted against observed MDA8 ozone
  Bins with MDA8 > 70 highlighted in shaded blue area
  Number of data points in each bin listed at bottom of plot
Clear systematic positive residuals on NSDs when observations > 60 ppb
Clear systematic negative residuals on NSDs when observations < 40 ppb
Residuals are centered near zeros for observations between 40 and 60 ppb where the bulk of the data points reside

## Slide 10: GAM struggles to predict high values in the Eastern and Central US
Eastern US
Only a single site-day across 5 years predicted to have MDA8 ozone > 80 ppb (NSDs and SDs)
GAM predictions across NSDs:
  Max: 79.6 ppb
  99.9th percentile: 67.8 ppb
  99th percentile: 61.2 ppb
  98th percentile: 58.8 ppb
Observed values across NSDs:
  Max: 99 ppb
  99.9th percentile: 79 ppb
  99th percentile: 67 ppb
  98th percentile: 64 ppb
Central US
Only 5 site-days across 5 years predicted to have MDA8 ozone > 80 ppb (NSDs and SDs)
GAM predictions across NSDs:
  Max: 87.0 ppb
  99.9th percentile: 71.4 ppb
  99th percentile: 64.6 ppb
  98th percentile: 62.2 ppb
Observed values across NSDs:
  Max: 112 ppb
  99.9th percentile: 86 ppb
  99th percentile: 73 ppb
  98th percentile: 69 ppb

## Slide 11: GAM predicts more high values in the Western US but still underpredicts upper percentiles
In the Western US, almost 1000 site-days across 5 years predicted to have MDA8 ozone > 80 ppb (NSDs and SDs)
GAM predictions across NSDs in the Western US:
  Max: 114.8 ppb
  99.9th percentile: 90.0 ppb
  99th percentile: 76.7 ppb
  98th percentile: 71.6 ppb
Observed values across NSDs in the Western US:
  Max: 138 ppb
  99.9th percentile: 102 ppb
  99th percentile: 83 ppb
  98th percentile: 78 ppb

## Slide 12: Does the residual correlate with total observed ozone concentration?
Note that correlation is not discernable when comparing against GAM predicted MDA8 (green) rather than observed MDA8 (black)

## Slide 13: Correlation between residuals and observed MDA8 persists across regions

## Slide 14: Comparison of residuals from Training (HMS = 0) and Smoke days (ETYPE == 1)
For bins starting at 50 ppb and above: residuals on SDs are larger than residuals on NSD
  For some bins, confidence intervals overlap
  Smoke impact would more appropriately be quantified as difference between expected residual in the absence of smoke (black boxes) and actual residual on a smoke day (blue boxes) rather than the residual itself
  Challenge: when looking at a single site (n = 770 days), is it possible to determine expected residual in the absence of smoke as a function of MDA8?
    For some sites n for days > 70 is very small or zero

## Slide 15: Comparison of NSD vs SD residuals by region
SD and NSD residuals are more similar in the East and Central regions than the West
For East and central regions there are fewer than 20 NSDs with observed values > 90 ppb across all sites
  Should we expect GAM to reliably predict those high days if they were absent from training set?
  Across all sites and dates, GAM rarely predicts and O3 values > 80 ppb
Even days > 70 are infrequent in all regions

## Slide 16: Map of residuals at 70+ ppb observations by site for SD, NSD, and difference
Non-smoke-day residuals (left), smoke-day-residuals (middle) and difference (left) for 70+ ppb days. Circles are individual monitors and background is an average of sites on a 2.5 degree grid.

## Slide 17: Thoughts on alternative methods for determining critical values for identifying smoke days
PM2.5 is not a normal distribution
  Could explore using quantile function
PM25. has a seasonal signal
  Explore how critical value might change by month
Impact on residual values plotted for 10 different methods of identifying PM2.5 critical value (next slide)
  Based on annual: mean+1std, 84.134475-percentile, 90-percentile, 95-percentile, mean+2std
  Based on monthly: mean+1std, 84.134475-percentile, 90-percentile, 95-percentile, mean+2std
Anthropogenic emissions controls should be bringing PM2.5 down
  Could trends be removed? (not tested)
How do critical values compare to EPA PM2.5 tiering tool?
  available at: https://www.epa.gov/air-quality-analysis/pm25-tiering-tool-exceptional-events-analysis

## Slide 18: sensitivity of residual difference of training and smoke days to alternative critical values
Sensitivity of difference in smoke-day and non-smoke-day (HMS == 0) residuals to alternative criteria. The left panel is in absolute magnitude and the right is as a percent of non-smoke-day residual. The difference is weighted toward the west, which has more non-smoke-days greater than 70 ppb. This leads to a smaller average non-smoke-day for the country.

## Slide 19: Thoughts for further investigation
Exploration of statistical methods geared towards predicting tails of the distribution
Exploration of residual “bias-correction” as a function of observed ozone based on residual bias on NSDs
Exploration of fitting GAM models using only days > 60 ppb or days > 70 ppb
Sample size may limit feasibility of some options