## Slide 1: Statistical Regression Modeling of Ozone in St. Louis
Michael Needham
EPA R7 ARD

## Slide 2: Motivation
Statistical Regression Modeling is listed in the EPA exceptional event demonstration guidance as a way to provide additional evidence that ozone measurements may have been influenced by wildfire smoke.
General Principle:
Use a statistical model to predict ozone concentrations based only on meteorological variables
Calculate the residual between predicted and observed ozone concentrations
This residual provides an estimate (in ppb) of the impact of unincluded variables (i.e., smoke) on ozone
Temperature
Ozone
Humidity
Cloudiness

## Slide 3: Simple Example
The observed ozone concentration at a monitor was 76 ppb…
A statistical model based on meteorological variables predicted the ozone concentration to be 64 ppb…
The residual (76-64=12 ppb) suggests that smoke may have increased ozone concentrations at the monitor by 12 ppb
Lots of caveats with this statement… but this is the general idea

## Slide 4: Methods & Data

## Slide 5
Preprocess Data
Remove historic days with potential smoke impact so that models are only trained on “smoke-free” days
Split data into training and testing sets to reduce the chance of overfitting
Train and Evaluate Regression Models
Iteratively train models against several metrics (accuracy, true positive rate, true negative rate, etc.)
Evaluate trained models against the testing data
Investigate High O3 Concentrations in St. Louis
Take the “best” model and apply to smoke-influenced days in St. Louis during summer 2023
Determine whether statistical modeling supports or fails to support wildfire impacts on ozone concentrations
Methods & Data - General Procedure

## Slide 6: Methods & Data
Air monitor data from St. Louis Blair Street Station
Meteorological observations (in-situ) from St. Louis Lambert Airport
Period of study: 2017-2023
  Ozone Season: include May, June, July, August, and September
Daily data (daily mean, daily average, etc. as appropriate for variable)
Met Data from Lambert Airport
AQS/AirNow Data from Blair Street Station

## Slide 7: Methods & Data – Smoke Influenced Days
Remove smoke-influenced days from the training/testing data using the method of Brey and Fischer (2016) and others
2 criteria to ID a smoke-influenced day:
  There is a HMS smoke polygon over the monitor; and
  The PM2.5 concentration at the monitor is greater than 1 above the ozone-season (May-Sept) mean PM2.5 concentration

## Slide 8
Variable Name | Description | Source | Justification
TMAX | Maximum daily temperature | NCEI Climate Data Online (data link, documentation) | “Variations in weather conditions play an important role in determining ozone concentrations. Ozone is more readily formed on warm, sunny days when the air is stagnant. Conversely, ozone production is more limited when it is cloudy, cool, rainy, or windy” – EPA Trends in Ozone Adjusted for Weather Conditions
RHUM | Average daily relative humidity | NCEI CDO | 
WINDSPD | Average daily sustained windspeed | NCEI CDO | 
WINDDIR | Average wind direction (8-point compass) | NCEI CDO | Wind direction may provide information on transport of ozone precursors from stationary sources
SWALL | Daily average downward surface shortwave flux | CERES SYN1deg (data link) | See justification for TMAX, above
CLDFRC | Daily average cloud fraction | CERES SYN1deg | See justification for TMAX, above
DAYOFWEEK | Monday, Tuesday, etc. | N/A | Accounts for weekly cycle in the emission of ozone precursors
DAYOFYEAR | Julian day of the year | N/A | Accounts for seasonal cycle in the emission of ozone precursors
YEAR | N/A | N/A | Accounts for possible trends in ozone concentrations over several years
Methods & Data - Regression Model Variables
Additional variables were considered, but were not found to be important…

## Slide 9: Three Regression Models
Multiple Linear Regression (MLR)
Pros:
Generalized Additive Model (GAM)
𝑌= 𝛼_0+ 𝑓_0 (𝑥_0)+ 𝑓_1 (𝑥_1)+ … + 𝑓_𝑛 (𝑥_𝑛)
Pros:
Random Forest Regression (RFR)
𝑌=𝐹(𝑋)=𝐹(𝑥_0,𝑥_1,…,𝑥_𝑛 )
Pros:
Easy to implement and interpret
Resistant to Overfitting
Cons:
Limited by linear functions
Includes nonlinear interactions
Cons:
Can be difficult to interpret
Easy to overfit
Model Y as a sum of linear terms
𝑌= 𝛼_0+ 𝛽_0 𝑥_0+ 𝛽_1 𝑥_1+ … + 𝛽_𝑛 𝑥_𝑛
Model Y as a sum of (possibly, but not necessarily) nonlinear terms
Includes nonlinear interactions
Cons:
Can require significant model tuning based on subject matter experience
Easy to interpret because of sums
Machine learning model based on many decision trees (i.e., “Forest” )
Multiple Linear Regression (MLR)
Generalized Additive Model (GAM)
Random Forest Regression (RFR)
It turns out that the GAM works the best in this study of the three models explored…

## Slide 10: Model Results (Testing Data)
Multiple Linear Regression shows lowest correlation between predicted and observed values
Random Forest Regression shows highest correlation but also the largest bias for high ozone days
Generalized Additive Model Regression shows smallest bias and spread for high ozone days.

## Slide 11: GAM Interpretation
The GAM’s prediction is based on the sum of the “partial dependance function” for each input variable, plus an intercept.
  Y = s0(TMAX) + s1(RHUM) + … + intcpt
These functions indicate that GAM is making predictions consistent with the understanding of ozone processes:
  High TMAX → High Ozone
  High RHUM → Low Ozone
  Low WINDSPD → High Ozone

## Slide 12: From the guidance…
Procedure
Use the regression model to predict MDA8 O3 based on meteorology
Find the 95%-ile of all positive residuals
  Add the 95%-ile to the prediction and subtract this sum from the observation to estimate smoke impacts on ozone
  Equivalently: if the residual is greater than the 95%-ile, then smoke may have positively influenced ozone
Must also investigate the top 5%-ile for non-smoke days

## Slide 13: GAM Prediction 2023 Ozone Season
GAM predicts high ozone concentrations in late-May and June…
…also predicts lower concentrations later in the season
Large Positive Residuals:
June 6 – June 20th
Above the 95th percentile…
Smoke impacts?
this 95th percentile threshold is specifically mentioned in the guidance

## Slide 14: GAM Prediction 2023 Ozone Season
High Ozone Period:
Gam predicts “wiggles” from weather patterns

## Slide 15: Analysis of top 5%-ile of residuals
Most >95% days in the absence of smoke are not high ozone days
Regression model supports the conclusion that ozone exceedance events on 6/6/2023 and 6/10/2023 may have been influenced by smoke
Does not support the conclusion of smoke impacts on other ozone exceedance days for this monitor:
  5/24/2023
  5/29/2023
  5/30/2023
  6/3/2023
  * 6/9/2023
  6/14/2023
  6/15/2023
  6/17/2023
  6/20/2023
  6/23/2023
*6/9/2023 may be considered part of the same event as 6/10/2023

## Slide 16: Matching Day Analysis

## Slide 17
 | O3 | TMAX | RHUM | WINDSPD | SWALL
Target Day (e.g., 6/6/2023) | 94 ppb | 89F | 46.7% | 3.2 mph | 318.9 Wm-2
Comparison Set STDV | - | 8.5 F | 11.2% | 2.7 mph | 71.4 Wm-2
Matching Day Range | - | 80.5-97.5 | 35.5-57.9% | 0.5-5.9 mph | 247-390 Wm-2

## Slide 19: Next Steps
Include 12 hour HYSPLIT trajectories as a potential additional predictor variable
  12HR Distance of back-trajectory
  Quadrant of vector between initialization point and 12HR back-trajectory endpoint (e.g., did the airmass come from the NE, SW)

## Slide 20: References and Links
References
  Brey and Fischer, (2015)
  Studies using GAMs for Ozone
    Gong et al., (2017)
    McClure and Jaffe, (2018)
    Lee and Jaffe, (2023)
EPA Ozone Wildfire Guidance

## Slide 21: GAM with Additional Variables

## Slide 23
I only trained one GAM for each station (trained on 2017-2022 then predicted 2023) so I didn’t look at how the intercept may change with time.
The intercepts were fairly large, near 40 ppb (see below). Although pretty consistent among these four stations. I attached a figure with some plots of the GAM for blair street to get a sense of model performance for 2017-2023 (and a similar figure for the basic multiple linear regression with the same data, which still performs reasonably but does not generalize as well to the validation set).
| AQSID | GCV | Intercept |
|-------------------------------|
| 171570001 | 4.920 | 39.563 |
| 290470005 | 3.421 | 40.023 |
| 290990019 | 6.909 | 39.354 |
| 295100085 | 6.175 | 40.243 |
(Note that I have been working with the python pyGAM package instead of the mgcv R package that most studies I have read have used. Eventually I would like to compare to make sure that both give similar results for the same data, since the python package is in a much earlier stage of development)

## Slide 24
Could there be 5 different GAMs per site, one per year and make 5 different estimates of 2023?
Could 2022 and/or 2024 be predicted as well?
Could 2023 be part of the training case and predict other years?