## Slide 1: Overview
Provide a multi-year representation of air quality impacts from different types of fires in North America
  Develop new fire emissions to reflect new emission (SERA) factors and provide more specificity for types of prescribed and agricultural fires
  Annual 36 km CMAQ modeling covering North America (36US3 domain) run with source apportionment tracking fire emissions for 2016 through 2023
  Intend to do finer scale modeling for one of the years (most likely 2022)
Leverage existing time-series projects for CMAQ inputs
  EQUATES + CDC Phase

## Slide 2: 22 total categories tracked for contribution
Anthropogenic emissions
  1) mobile and 2) stationary
Natural sources including biogenics, lightning, and ocean
Lateral boundary inflow (natural and anthropogenic from outside the model domain) and all other sources not tracked for contribution
Wildfire
  U.S., Canada, Mexico+Caribbean
Prescribed fire
  Broadcast burns, pile burns, and grassland (Flint Hills only)
  Rangeland (pasture), midwest ditch burns, soybeans, corn, cotton, fallow, rice, sugar cane, wheat, soybeans+winter wheat
Open burning

## Slide 3
All sources
Wildfire U.S.
Non-U.S. wildfire*
Prescribed fire*
Ag fire*
Open burning
Anthropogenic*
Natural
2023 Monthly Average PM2.5 Carbon

## Slide 4
All sources
Wildfire U.S.
Non-U.S. wildfire*
Prescribed fire*
Ag fire*
Open burning
Anthropogenic*
Natural
2023 Monthly Average MDA8 OZONE

## Slide 7: CMAQ input overview
Will have new fire emissions files for all years that will be consistently developed
How best to develop some level of consistency in the other model inputs over time given that EQUATES stops in 2019 and more recent years are needed
  Need 2021 and 2023 WRF/MCIP (OAQPS)
  Need 2022 and 2023 emissions
  108 HEMI runs and BCON files for all years
  BCON not that important for North American fire impacts but it would be nice to have some kind of consistency there rather than falling back to average monthly values for some of the newer years