## Slide 1: CAMD EJ Analytics for EGUs
March 2021

## Slide 2: Two Complementary Efforts
CAMD(EJ) Tool
  Web-based mapping tool that introduces EJ concepts to CAMD data users on a plant-by-plant basis
  Primarily public-facing
  Contextualizes each EGU individually in the fleet, showing plant attributes, emissions, and nearby demographics
  Highlights vulnerability of nearby population
Both efforts will ultimately be methodologically consistent, accessible, and fully transparent
  Methodology that allows EPA to evaluate relative EJ implications of all plants comprehensively
  Primarily for EPA analysis
  Identifies and ranks EGUs based on potential to affect disproportionately-impacted communities
  Considers pollution burden and vulnerability, nearby and downwind
Screening Analysis Methodology

## Slide 3: Screening Analysis: How to evaluate EGUs based on their potential to affect disproportionately-impacted communities?

## Slide 4: Screening Analysis: How to evaluate EGUs based on their potential to affect disproportionately-impacted communities?
Two key questions
  How to determine the extent to which a community might be considered disproportionately impacted?
  How to determine which EGUs might negatively impact a community?
We have been learning from what states, cities, and NGOs have been doing to answer similar questions
Currently working on a draft approach as a starting point with two near-term objectives:
  Facilitate outreach
  Inform preliminary internal policy discussions

## Slide 5: Question 1: How to determine the extent to which a community might be considered disproportionately impacted?
Cumulative Impacts
Identifies communities most impacted by pollution by considering both pollution burden and vulnerability together.
Combines all EJSCREEN indicators (pollution burden and population characteristics)
Socioeconomic Factors Only
Identifies communities vulnerable to pollution based on two demographic indicators (percent of low-income and people of color), regardless of potential pollution burden
Single EJSCREEN indicator (demographic index)

## Slide 6: Cumulative Impact Scores (DRAFT)
Note: Blocks groups that fall within the "76-100" category are in the top 25% of scoring areas (as opposed to having the top 25% of cumulative impact scores).
Higher cumulative impact scores identify communities that are disproportionately impacted by pollution
Considers pollution burden and increased vulnerability to pollutants

## Slide 7: EJSCREEN Demographic Index
Socioeconomic factors are community characteristics that result in increased vulnerability to pollutants
Does not consider existing environmental health threats

## Slide 8: Question 2: How to determine whether an EGU might negatively impact a community?
Proximity Analysis
Identifies all communities within a given radius of each EGU
Captures potential air, water, waste, and other impacts
Transport modeling
Identifies all communities to which each EGU might impact air quality
Captures downwind air pollution impacts

## Slide 9: Proximity Analysis
All EGUs linked to the census block groups that are within a 5km radius
Able to quickly filter EGUs based on nearby census block group ranking

## Slide 10: Proximity Analysis: Ranking EGUs
Account for EGUs located near many disproportionately-impacted communities
Considers:
  Number of nearby disproportionally-impacted communities
  Relative difference in disproportionate impacts that communities face
  Total population
Next step: consider emissions

## Slide 11: Air Transport Modeling
Using HYSPLIT to estimate particle trajectories from fossil-fired EGUs
Combining these trajectories estimates a plume that can be layered on top of communities
Like proximity analysis, can link EGUs to downwind communities

## Slide 12: Potential Applications
Screening Analyses
  How to prioritize EGU emissions reductions from an EJ perspective?
  Which EGUs might negatively affect disproportionately-impacted communities?
  Which EGUs have more potential than others to affect disproportionately-impacted communities? How many communities? Population? Potential to emit?
  Which of those EGUs are at higher risk of closure?
Facilitate outreach and discussion, by asking stakeholders:
  How can these approaches be improved?
  How can we make this work more useful to the public?
Policy Analyses
  Which policy options are projected to have a greater impact on EGUs that affect disproportionately-impacted communities?
  What share of health benefits might accrue to disproportionately-impacted communities?

## Slide 13: CAMD(EJ) Tool: Presenting publicly available power plant data together with EJSCREEN data in order to highlight the demographics of areas surrounding power plants

## Slide 14: CAMD(EJ) Tool Goals
Promote the awareness and use of CAMD Power Sector data, eGRID, and EJSCREEN.
Introduce EJ concepts and data to users already familiar with CAMD data.
Encourage users to take advantage of available EPA data in their EJ analyses and investigations.
Provide a data set that allows users to perform EJ analytics.
Start a conversation with the public, NGOs, other agencies, and within EPA.

## Slide 15
Map the U.S. fossil fuel-fired power plants (~3,400)
Step 1

## Slide 16: Step 2
Layer EJSCREEN Data
An EPA developed environmental justice screening tool that provides maps and data reports
Data is available at the census block group
A 95th percentile means that an area has an equal or higher % population (e.g., low-income) than where 95% of the US population lives.

## Slide 17: Step 3
Proximity Analysis
Summarize the demographics of residents within a 3-mile buffer of each plant
Designed to represent the average resident within the buffer,
Provides an estimate of the total population residing in the buffer
Initial approach overlays CAMD/eGRID data and EJSCREEN socioeconomic data but may evolve based on lessons from the screening analysis.
Less than 50%ile to 87%ile
Less than 50%ile to 84%ile

## Slide 18: Starting with EJSCREEN Data
Environmental Indicators (11)
  Such as ozone level in air, amount of vehicular traffic nearby, and proximity to waste and hazardous chemical facilities or sites
Demographic Indicators and Demographic Index
  Percent low-income, percent people of color, less than high school education, linguistic isolation, individuals under age 5, and individuals over age 64
  Demographic Index is based on the average of two demographic indicators (percent low-income and percent people of color).
EJ Indexes (11)
  An EJ index summarizes how an environmental indicator and demographics come together in the same location.
Socioeconomic
CAMD(EJ)

## Slide 19: CAMD(EJ) Map
The community demographics for each plant location will be presented
Highlighted plants are in communities that meet or exceed 80th percentile for one or more demographic indicators
Percent low-income, percent people of color, less than high school education, linguistic isolation, individuals under age 5, individuals over age 64

## Slide 20
CAMD(EJ) Map
Selecting a marker will display plant-level data
Facility information and attributes, operating data, generation, emissions, and demographics for the adjacent communities
Also available via a spreadsheet

## Slide 21: CAMD(EJ)Map Layers
≥80%ile
Low Income
People of Color
Less than high school education
Linguistically Isolated
Population less than 5
Population over 64
Tribal
EJSCREEN Indicators

## Slide 22: Percentile Graphs: Demographic Indicators Drilldown

## Slide 23: Population Percentage Graphs: Low-Income & People of Color Scatter
Quadrant | Findings
A | 895 plants (26%) are greater than the low-income national median and less than the people of color national median
B | 934 plants (27%) are greater than the low-income national median and greater than the people of color national median
C | 410 plants (12%) are less than the low-income national median greater than the people of color national median
D | 1,201 plants (35%) are less than the low-income national median and less than the people of color national median