## Slide 1: “NEXUS” Multi-Pollutant Analysis Tool Development: Status and Progress
Carey Jang, AQAD/Air Quality Modeling Group
AQ Model Apps Team meeting, Jan. 13, 2021
Data Viewer Module
Data Input Module
Data Query Module
“NEXUS 1.5” available on OAQPS’s Shared Drive at: “G:\SHARE\NEXUS\NEXUS 1.5\”
or at EPA’s new FTP site: ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/

## Slide 2: NEXUS Tool Development
Motivation: Develop a new multi-pollutant analysis tool to identify and assess areas with high ambient levels and/or health risks associated with PM2.5, O3, and air toxics
Phase-1: Develop a GIS-based NEXUS prototype with a user-friendly graphical interface to provide analysis and visualization functions of potential multi-pollutant AQ issues at national level (continental US)
Phase-2: Expand the NEXUS tool to allow users to dial into an EPA region, State, or metropolitan area and provide data query and V/A functions for “AQ and emissions” information over the selected region of interest
2

## Slide 3: Expected Use of NEXUS Tool
The NEXUS tool will allow users to do the following:
  National screening for areas with MP issues: Phase 1 development will provide ability to quickly screen areas across nation that have combination of high air quality and/or risk levels for O3, PM2.5 and air toxics.
  Area screening to understand nature of MP problem: Phase 2 development will provide ability to ‘dial-into’ specific areas to determine extent to which common emissions sources are causing the MP issues.
OAQPS expects to use this tool to engage with Regions and identify areas that would potentially benefit most from MP approaches to reduce emissions (including current NAs and Advance areas).
The NEXUS tool will essentially provide a ‘conceptual model’ of MP issues to facilitate engagement with state/local/tribal agencies and community stakeholder groups.
3

## Slide 4: NEXUS Tool : Schedule & Installation
Work Plan | Date
Developed a NEXUS prototype to provide MP analysis at national level (Phase 1) | April 2020
Developed a working NEXUS version with a new three-module design and regional level analysis (Phase-2) | August 2020
Developed a fully functional NEXUS tool and on-line User’s Manual | Dec. 2020
Upgrading NEXUS tool for Beta test & preparing for public release | Jan. ~ July 2021
Download “NEXUS” tool: The “NEXUS 1.5” package (“NEXUS v1.5 setup.exe” & “NEXUS 1.5 Data.exe”: run both to install) is available at OAQPS’s Shared Drive at G:\SHARE\NEXUS\NEXUS 1.5\ or at EPA’s new FTP site ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
(Note: Require software installation privilege to install “NEXUS tool” at EPA’s PCs)
4

## Slide 5: NEXUS Tool : Briefing Schedule
Audience | Date
AQAD & HEID – DD & Management Team | Sept. 25, 2020
Air Toxics Team | Nov. 3, 2020
AQPD – DD & Management Team | Dec. 10, 2020
OID – DD & Management Team | Jan. 25, 2021
SPPD – DD & Management Team | Jan 27, 2021
OAQPS – Office Director | Feb 1, 2021

## Slide 6: NEXUS Tool: Three Key Modules
Data Viewer module
Data Input module
Data Query module
View and create interactive Map/Data/Chart/Table
Provide flexible selections & mapping of “Ambient” and/or “Risk” levels of PM2.5, O3 and air toxics
Provide regional analysis for “EPA region”, “States”. CBSA”, and “County”
Link and display major emission sources locations & emitted pollutants info.
Allow to update & change input data files
Provide data preview and filter functions
Extend to use 10 input data files now (publicly available, ~4 GB)
Quick turnaround to run & save to a new “project” using new input data files
Expand data field selections and flexibility for exploratory/advanced users
Provide overlaying map and summary table for data query results
Current data query based on selected data fields: “Ambient/Risk, Advance area, Socio-demographic (EJ) area, NA Area, Class I area”

## Slide 7: NEXUS Tool: Data Input Module
Currently, there are 10 input data files used (publicly available)
Allow users to update/preview/filter Input data files
Run and Save to a new project after loading new input data files
7
Total files size ~4 GB

## Slide 8
Data Input Module: Input Files & Attributes
Data Input File Names | Data Format | Data Description | Data Source | Data Period
“2014 O3 & PM2.5 fused Ambient & Risk” | Geodataset | O3/PM2.5 ambient & risk data at county/census tract level | from OAQPS MP team | 2014
“2014 NATA Risk” | Geodataset | Air toxics ambient & risk data at county/census tract level | from OAQPS MP team | 2014
“O3_DV_2009_2018” | Excel | O3 design values at county level | From EPA public website: https://www.epa.gov/air-trends/air-quality-design-values | 2009 to 2018
“PM_DV_2009_2018” | Excel | PM2.5 design values at county level | From EPA public website: https://www.epa.gov/air-trends/air-quality-design-values | 2009 to 2018
“Advance areas O3_PM” | Geodataset | O3 & PM2.5 Advance Areas | from OAQPS MP team | 2018
“Index of Poverty_ Disadvantage” | Excel | Index of poverty/disadvantage at county level | from Univ. of Michigan website: https://poverty.umich.edu/projects/understanding-communities-of-deep-disadvantage/ | 2017
“NEI_County_CAPs” “NEI_Facility_HAPs_ CAPs” | Geodataset | Major emission sources and facility info. of CAPs & HAPs at county level | From OAQPS public website: ftp://newftp.epa.gov/EPADataCommons/OAR/OAQPS/NEI/NEI_Facility_HAPs_CAPs.zip ftp://newftp.epa.gov/EPADataCommons/OAR/OAQPS/NEI/NEI_County_CAP.zip | 2008, 2011, 2014
“2014 NEI_NATA Emissions” | Access Database (*. accdb) | NATA emissions data from 2014 NEI database, including various source groups | From EPA public website: https://www.epa.gov/national-air-toxics-assessment/2014-nata-assessment-results#emissions | 2014
“Class1_FederalAreas” | Geodataset | Mandatory Class 1 Federal Areas | From Mandatory Class 1 Federal Areas Web Service: https://edg.epa.gov/data/public/OAR/OAQPS/Class1/Class1Areas.zip | —
8

## Slide 9: NEXUS Tool Demo: 2014 NEXUS Case
9
Launching Page
Roadmap for Demo:
(Use example cases)
National View: Use “NEXUS” across pollutants to provide an initial “SCREEN” at the national level by providing an indicator where there may be a common set of sources contributing to Multi-pollutant issues.
Regional View: Dial into a region or area of interest to understand the pollutant/source connections, and potential for more effective and efficient multi-pollutant solution.
2008

## Slide 10: Discussion and Next Steps (1)
10
    Short-term:
    GOAL: Upgrade/improve NEXUS tool to reflect latest data & information and MP team’s feedbacks
    Currently expect FY21 funding to support NEXUS -- perhaps $50k from AQAD
      Update NEXUS data to 2017
        2017 data for O3, PM2.5 & Air Toxics risk/ambient/emissions
        Tribal boundaries & socioeconomic/demographic data for EJ
      Add O3, PM2.5, and Air Toxics monitoring data
      Update metrics/indicators (e.g., risk metrics, EJ indicators)
    Engage across Office to determine how this tool may best inform or be used for OAQPS’s Air Toxic Strategy programs
      Consider addition of screening-level analysis & assessment capabilities (e.g., proximity analysis w/ EJ)

## Slide 11: Discussion and Next Steps (2)
11
    Long-term:
    Upgrade and prepare NEXUS for Beta test with EPA Regions followed by public release & training
    Based on Office wide engagements, exercise updated NEXUS tool with 2017 data to inform Multi-pollutant, Air Toxics, and EJ efforts as appropriate
    Develop plan for routine updates and maintenance of the NEXUS tool to best support OAR/OAQPS programs and determine appropriate extensions as need and resources provide.

## Slide 12: “NEXUS 1.5”: Quick Tutorial
Carey Jang
Download “NEXUS” tool: The “NEXUS 1.5” package (“NEXUS v1.5 setup.exe” & “NEXUS 1.5 Data.exe”: run both to install) is available at OAQPS’s Shared Drive at: G:\SHARE\NEXUS\NEXUS 1.5\
or at EPA’s new FTP site:
ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
(Note: Require software installation privilege to install “NEXUS tool” at EPA’s PC)
12

## Slide 13: NEXUS Tool: On-line User’s Manual
13
Hot link to User’s manual’s “Data Viewer” chapter (same for “Data Input” & “Data Query”
Click “book” icon to launch “User’s manual”

## Slide 14: NEXUS Tool: Data Viewer Module
Select & adjust “Ambient” & “Risk” levels
“Advanced Option”: provide HAPs & species selections
14
Click “File” to open or save a project
Switch between 3 key modules
Loaded NEXUS project file name

## Slide 15: Data Viewer Module: Selections & Map Display
Select & adjust “Ambient” & “Risk” threshold levels for color map display
“Apply” new selections to “Radio button” panel
15

## Slide 16: Data Viewer: “Apply” New Selections
New selections will appear on-the-fly in “radio button” panel and map display
“Apply” new selections
16
“Check” new selections

## Slide 17: Data Viewer Module: Base Map & Color
17
Click to change color & transparency
“Base Map”: Change boundary lines and background map
“Right-click” map to save image

## Slide 18: Data Viewer: “Region Selection”
Allow to select “EPA regions”, “States”, or “CBSA”
18

## Slide 19: Data Viewer: Select EPA Region/State/CBSA
19
Examples:
EPA Region 4
NC
Louisville CBSA

## Slide 20: Data Viewer: Major Emission Sources
20
Click “Emission Sources” tab to display emission sources (green dots) and launch new window
Click any “facility” to link & display source location and emission information

## Slide 21: Data Viewer: Major Emission Sources
21
Allow to scroll down to county-level (e.g., Wake County, NC)
Wake county, NC

## Slide 22: Data Viewer: Top “x” Emission Sources
22
Durham county, NC
Provide selection of CAPs precursors & HAPs species

## Slide 23: Data Viewer: EPA Region Table Generator
23
“EPA Region Table Generator” is still under development, but a preview of example “EPA Region 4” tables can be provided

## Slide 24: Data Viewer: Data Search & Filter
Click “+” to add filters; Click “x” to remove current filter;
Click “Output data…” to output current page records or all records
Show specified records per page.

## Slide 25: Data Query Module: Main Page
25
Region Selection
Data Query qualifier selection
Map Overlaying selection
Detachable “Attribute Table”
11111111
Data Query Configuration

## Slide 26: Data Query Module: Configure Data Query
26
“Data Query Filter” allows to select “qualifiers” for query
“Data Query Preview” displays the selected “qualifiers” at the same time

## Slide 27: Data Query Module: Overlaying Map
27
Overlaying Map selection

## Slide 28: Data Query Module: Attribute Table
28
Detachable “Attribute Table”
Filter/link/export functions (to be completed)

## Slide 29: Data Query Module: Attribute Table
29
Click a “record” to link and display its location & info.

## Slide 30: Data Input Module: Data Preview
Click to change input data file
Click to view data
Click to run & save project
Click to view data
Select a table to view if there are multiple tables in the selected data source file
Check to use filter to query data

## Slide 31
End
31

## Slide 32: RoadMap for NEXUS Tool Demo (1)
National Screening (2014 Data)
Replicate 2008 NEXUS map with O3/PM2.5 concentrations above NAAQS and NATA risk estimates above selected percentile of top 10%
  What happens to areas at lower O3/PM2.5 NAAQS levels?
  What happens to areas current over O3/PM2.5 NAAQS if change HAP risk percentile?
Provide NEXUS map on risk basis: O3/PM2.5 BenMAP mortality risk based on fused surfaces and NATA risk estimates above selected percentile of top 10% for all pollutants
  What happens to MP areas as one changes percentile to top 20% or others?
  What is relationship between Heavy Metal HAPs risk (top 10%) and PM2.5 risk to identify potential co-pollutant issues?
  What is relationship between Gas/VOC HAPs risk (top 10%) and O3 risk to identify potential co-pollutant issues?
32

## Slide 33: RoadMap for NEXUS Tool Demo (2)
Regional/State/CBSA/County Screening
EPA Region 4 Example
  Areas with MP risk in top 10% across O3, PM2.5 and HAPs
  Louisville CBSA: General view and then dial into “Jefferson County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
33

## Slide 34: RoadMap for NEXUS Tool Demo (3)
Data Query: State/CBSA/County Views
Advance Areas
  Initial view of national level information using the Advance Area definition to show overlay with MP areas
  Region 5 => Minneapolis Example: General view and then dial into “Dakota County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
34

## Slide 35: RoadMap for NEXUS Tool Demo (4)
Data Query: State/CBSA/County Views
Socio-Economic/Demographic (EJ) Areas
  Initial view of national level information using the Poverty/Disadvantaged indicator to show overlay with MP areas
  Region 5 => Detroit Example: General view and then dial into “Wayne County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
35

## Slide 36
NEXUS Demo: Example Cases
    Data Input module:
    Expand 1->10 inputs data files; Plan to update to 2017 (CDC & NATA)
    Data Query Module:
    Expand fields/flexibility: Exploratory users
    Configure DQ” window: Select Advance Area, EJ, 2017 DVs => Apply map
    Overlay Map & Detachable table summary
    Select “EPA Region 5” => “Advance + EJ”
    Change color transparency & Google Map
    CBSA: Minneapolis-> Major emis. sources
    Facility (Xcel Energy - Black Dog)
    Dakota Co. ->
      “PM2.5 + H.M.HAPs” (Xcel Energy)
      “VOC + NOx + G&V HAPs” (Flint Hills)
    Back to “EPA Region 5” -> EJ: Select “Disadvantage & under”
    CBSA: Detroit -> Wayne Co. ->
      “NOx + SOx” (DTE Elec.)
      “PM2.5 + H.M.HAPs” (AK Steel, US Steel)
    CBSA: Cincinnati -> Butler Co. (AK Steel) (Cincinnati News article)
36
    Main GUI:
    Mimic 2008 MP report; County-based map
    Color/legend setup; Exceed “Ambient or risk” threshold defined in “Center panel”
    Click “county” to show “Data Content”
    Center panel & Left panel
    On-line User’s Manual & PPT Tutorial
    Nation View :
    “Ambient”: PM2.5: 12 -> 10 ug/m3; O3: 70 -> 65 ppb; “Risk”: Air Toxic 10% ->0%-> 20%
    All Risk only: O3:10%, PM:10%, AT: 10%
    Advanced: Heavy-metal HAPs, G&V:10%
      Co-PM risk: PM: 10%, H.M. HAPs: 10%
      Co- PM/NA: 12 ug/m3, H.M HAPs:10%
      Co-O3 risk: O3: 10%, G&V HAPs: 10%
      Co- O3/NA: 70 ppb, G&V HAPs:10%
    Advanced: H-M: Chromium & G-V: HCHO
    EPA Region/State/CBSA View:
    “dial-in” for regional (all risk: 10%)
    EPA Regions: R4/R5/R9 -> States: NC/CA -> CBSA: RDU
    “right-click” -> Major Emis. Sources
    Change color transparency/Google Map
    Major Emission Sources:
    CBSA: Louisville -> Jefferson Co. -> Facility (Louisville G&E)
    SO2/NOx/HAPs, Facility, Data Content;
    Top X Emission Sources: CAPs & HAPs
Notes: 1. Thank Cen/Gao/Luo/Chen; 2. HZ more visits; 3. AP on HZ