## Slide 1: Pilot Application of Deep Learning Response Surface Model (DeepRSM) and Preliminary Comparisons with Other Source Contribution Methods
Carey Jang, Jim Kelly and Joey Huang,
Model App Team Briefing, 5/10/2023
DeepRSM/HDDM/ISAM in “FAST-CE 3.5”
DeepRSM in “RSM-VAT 2.9”
CMAQ BF vs. DeepRSM, HDDM & ISAM
“FAST-CE 3.5” package (“FAST-CE 3.5 Setup.exe” & “* Data.exe”: run both to install) is available at EPA’s NewFTP site: https://gaftp.epa.gov/aqmg/cjang/FAST-CE/FAST-CE 3.5/* (or /RSM-VAT/RSM-VAT 2.9/*)
NOx and/or VOC reduction
O3 MDA8 (ppb), 2018 July Avg
CMAQ BF: NOx or VOC
pf-RSM BF: NOx or VOC DeepRSM BF: NOx or VOC
pf-RSM
DeepRSM
HDDM
ISAM
CMAQ BF: Total
ISAM/O_PSAT
RSM/DeepRSM
DDM/HDDM
USA domain or
10 Climate regions
VOC 75% reduction
NOx 75% reduction
NOx 25% reduction
NOx 50% reduction
(NOx & VOC)
Notes: spatial field: A Spatial Field refers to air pollution estimates made at the center of each grid cell in a specified modeling domain. For example, MATS might calculate ozone design values for each grid cell in the modeling domain. Several types of Spatial Fields can be calculated for ozone and PM.
利用环境监测数据、模型数据（主要是CMAQ模拟的结果）作为模型输入，并利用优化的数理统计技术对大气复合污染状况进行模拟，实现对环境空气质量标准的达标评估。其中包括point estimate和spatial field estimate。

## Slide 2: Outline
  Overview of Source Contribution & Control/Response Modeling
  Development & Evolution of Response Surface Modeling (RSM)
  Original RSM  Extended RSM (E-RSM)  Polynomial Function RSM (pf-RSM) ->  “Deep Machine Learning” RSM (DeepRSM)
  Ongoing and Recent RSM Applications/Comparisons & Publications
    DeepRSM: 2018 CMAQ PM-NAAQS pilot study for USA domain & 10 climate regions
    Appendix A:
    pf-RSM/CMAQ E-US case: O3 & PM2.5 nonlinear responses (Kelly et al., 2021, Atmosphere)
    pf-RSM/BFM/OSAT/HDDM comparisons: O3 case study (Fang et al., 2021, Environ. Pollution)
    BFM/PSAT/RSM comparisons: PM2.5 case study (Li et al., 2021, Frontier ES&E)
  DeepRSM Prototype in “FAST-CE 3.5” & “RSM-VAT 2.9“
    FAST-CE 3.5: DeepRSM V/A & compare vs. “ISAM/O_PSAT/HDDM”
    RSM-VAT 2.9: “Prepare CMAQ”, “Running RSM”, and “QA & validation” modules
Summary & Next Steps: “DeepRSM”
2

## Slide 3: Source Contribution & Control/Response Modeling (Emission-based, “Reduced Form Modeling”)
“Source Apportionment & Sensitivity” Modeling (Chem. regime: Baseline case)
  “Source Apportionment Modeling” (Chem. approximation)
    CAMx’s OSAT/PSAT/APCA, CMAQ’s ISAM &TSSA, etc.
  “Source/Receptor Sensitivity Modeling” (Math. approximation)
    Decoupled Direct method (DDM/HDDM), Adjoint method, etc.
“Control/Response” Modeling (Chem. regime: Control case)
  “Brute Force” Modeling (e.g., “zero-out” region/sector/pollutant)
  “Response Surface Modeling” (RSM): Rapid AQ responses of emissions control
    Previous USA applications: REMSAD (PM2.5):2008, CAMx (O3):2009, CMAQ (EGU-RSM): 2011 (Math./Stat. approximation)
    Original RSM  Extended RSM (E-RSM): 2015  Polynomial Functions RSM (pf-RSM): 2019  Deep Machine Learning RSM (DeepRSM): 2022 (Math. & Chem. approximation)
3

## Slide 4
Source Contribution & Control/Response Modeling for Supporting Policy Assessment
4
Ozone (ppb)
Natural
Local Contribution
Upwind States
International
U.S. EPA Source apportionment modeling for assessing source contributions to PM2.5 & O3 from emissions
Ozone Source Contribution
(example, not to scale)
(Courtesy of Dr. Kirk Baker)
Inform control strategy development:
  O3, PM2.5, Reg haze SIPs & RIAs
Transport rules or Transport SIPS:
  Assess “significant contribution” of sources in upwind states to downwind states
Sector impact assessments:
  EGU, Transportation, Industrial Boiler, etc.
NAAQS Area designations:
  Provide analysis for States to assess impacts from boundaries
Single source Impact assessments:
  PSD/NSR permitting
Exceptional events demonstrations:
  Assess impacts of special events such as fire
Characterizing international contribution:
  179b demonstrations
4

## Slide 5: RSM: Instant AQ Responses to Emissions Control
Response Surface Model (RSM):
A reduced form model built upon multiple “brute-force” AQ model simulations to provide rapid response of AQ (O3 & PM2.5 species) to emission changes
Major advantage: provide “instant” & “infinite” emissions control (region/sector/pollutant) scenarios with effective representation of non-linear chemistry of O3 and PM2.5 species
5
Ambient Concentration
Emission ratio
0
1
“real atmosphere”
Sensitivity (e.g., DDM, HDDM)
Source Apportionment (e.g., OSAT/PSAT, ISAM)
RSM
Base

## Slide 6
Policy Factors
(Emission Factors)
Air quality
RSM
1.Selection
Source A- Local NOx
Source B- Regional VOC
Source C- Area NOx
…
2.Sampling
Source A
Source B
Source C
3.Simulation
4.Statistic
Empirical Best Linear Unbiased Predictors (EBLUPs)
Latin Hypercube Sample (LHS)
Hammersley quasi-random Sequence Sample (HSS)
Multi-case CMAQ simulations
“4S” Steps in RSM (Traditional RSM)
Instant AQ
Response Surface
6
Base
Control
Resource-intensive
“Region/Pollutant
/Sector” Factors
Control Matrix
Create RSM
Experimental Design

## Slide 7: How to reduce number of model runs while improving/maintaining RSM accuracy?
Motivation for Advanced “RSM” Development:
7

## Slide 8: Evolution and Development of RSM
How to further reduce number of model runs required in RSM?
Xing et al., ACP, 2011
Wang et al., ES&T, 2011
Zhao et al., GMD, 2015
Xing et al., ES&T, 2017
Zhao et al., ACP, 2017
Xing et al., ACP, 2018
Deep-RSM
8
E-RSM
Air
Region C
Region B
Region A
Region A
Region B
Real-time pollutant responses
to multi-region sources
•
Chemistry
•
Transport
•
Indirect
RSM
Air
pollutant
Emissions
Change
Real-time pollutant responses
to emissions change
pf-RSM
Pollutant A (PM)
Pollutant B (O3)
RSM w/
Temporal
Polynomial
Functions
Pollutant A (PM)
Pollutant B (O3)
Pollutant A (PM)
Pollutant B (O3)
Multi-pollutant responses
based on polynomial functions
AQM
Air
pollutant
Emissions
Single scenario
NOx
NH3
SO2
POA
VOC
Xing et al., ES&T, 2020
Xing et al., Atm. Res., 2022
Model runs required: > 1000s >100s >20
2 (Base & Control)

## Slide 9: “pf-RSM” Methodology
“pf-RSM”: Response Surface Model based on Polynomial Functions
Chemistry:
Degree of
Non-linearity
Chemistry:
Term of
Interactions
Only 3rd step involved in training samples (i.e., model runs), and thus significantly reduces
# of model runs required for accuracy (20~30 runs per selected control region)
Xing et. al., 2018, Atmos. Chem. & Phys., https://doi.org/10.5194/acp-18-7799-2018
Polynomial Functions
9
Modeling:
Coefficients of Polynomial term

## Slide 10: Deep Machine Learning “DeepRSM”
DeepRSM: “Deep Learning” “Indicator-based” pf-RSM
Xing et. al., ES&T, 2020 (Further details please see Appendix B)
Traditional RSM | “pf-RSM” | “DeepRSM”
>100s | 20~30* | 1*
# of model runs needed for maintaining RSM accuracy in predicting control responses （* for each selected control region or sector）
Combine
pf-RSM
and
Deep Learning CNN
to predict
Nonlinear PM2.5 & O3 responses to emissions control
10

## Slide 11
“PM_NO3” serves as a good indicator for QA & Validation (nonlinearity)
(“PM_NO3“ Jan. monthly avg., “Out-of-Sample Validation”)
11
PM_NO3
Response
PM_NO3
Conc.
How good is RSM in replicating CMAQ?
QA & Validation:
“ O3,
PM2.5, PM_SO4
PM_NO3 “
for Jan. & July 2016
are given in Appendix C
PM 2.5
Response
PM 2.5
Conc.

## Slide 12
12
  Appendix A:
  Recent RSM Applications/Comparisons & Publications
    pf-RSM/CMAQ E-US pilot study: O3 & PM2.5 nonlinear responses (Kelly et al., 2021, Atmosphere)
    CMAQ-BF//pf-RSM/OSAT/HDDM comparisons: O3 case study (Fang et al., 2021, Environ. Pollution)
    CMAQ-BF/pf-RSM/PSATcomparisons: PM2.5 case study (Li et al., 2021, Frontier ES&E)
Appendix A: Recent pf-RSM Applications/Publications
Appendix B: DeepRSM Supplemental Information
Appendix C: Running DeepRSM in “FAST-CE” & “RSM-VAT”

## Slide 13
13
1. RSM/CMAQ E-US Case: “RSM” vs. “CMAQ” Responses
Comparisons of AQ changes (monthly avg.): pf-RSM vs. CMAQ for a 60% reduction in anthropogenic NH3, NOx, SO2, and VOC emissions
Jan. 2016
CMAQ
DO3_MDA8
RSM
DO3_MDA8
CMAQ
DPM_SO4
RSM
DPM_SO4
vs.
vs.
CMAQ
DPM_NO3
RSM
DPM_NO3
vs.
CMAQ
DPM_OM
RSM
DPM_OM
vs.

## Slide 14
14
1. RSM/CMAQ E-US Case: PM2.5 nonlinear chemistry
Comparisons of AQ conc. predicted by pf-RSM vs. CMAQ over all CBSAs for man-made emission reductions from 0 to 100%.
July 2016
(Jan. 2016 given in Appendix A)
Summary - NOx emission reductions were more effective for reducing PM2.5 and O3 concentrations than SO2, NH3, or VOC emission reductions. NH3 emission reductions effectively reduced nitrate concentrations in January but increased secondary organic aerosol (SOA) concentrations in July.
14

## Slide 15
Comparisons of O3 source impacts & contributions by 25%/50%/75/100% multi-region emission cuts
Accumulative source impacts and contributions
Source impact analysis:
BFM, HDDM & RSM-BFM: Predict consistently the impacts of accumulative source emissions; HDDM deviates from BFM under larger perturbations;
Source contribution analysis:
RSM-DM: Represent well for accumulative source contribution and non-linear O3 chemistry
OSAT: fails to represent the nonlinear response of O3 to incremental emission changes.
Receptor region: Guangzhou (September, 2017)
2. CMAQ-BF/OSAT/HDDM/pf-RSM comparisons: O3 case study
15

## Slide 16: 3. CMAQ-BF/PSAT/RSM comparisons: PM2.5 case study
16
“Source contribution analysis based on advanced modeling approaches for PM2.5 over the PRD region, China“ (Li et al., 2021, submitted to J. of Environ. Modeling)

## Slide 17: 3. BFM/PSAT/RSM comparisons: PM2.5 Sectoral Responses
17
Sectoral contributions of PM2.5 predicted by BFM and RSM are very similar
BFM and RSM predicted lower contributions of “Mobile“ sector than PSAT and modestly higher contribution of “Agriculture“ sector
Industrial
processes
Mobile
Stationary
sources
Agricultrue
Dust
BFM
RSM
PSAT
36
36
9
4.5
36
PM2.5 Jan. Avg.

## Slide 18
18
  Running RSM Using “FAST-CE” and
  “RSM-VAT” Tool
  Experimental Design: “Prepare CMAQ” module
  Running “pf-RSM”
  Performance evaluation: QA & “Out-of-Sample Validation”
  (Further details of “Quick Tutorial” and QA provided in “Appendix C”)
Five-Region RSM/CMAQ
One-Region RSM/CMAQ
    CMAQ “Eastern US” 12-km pilot cases based on “pf-RSM”
Easier than you think !
Appendix C

## Slide 19: 2018 CMAQ PM-NAAQS pilot case for O3 and PM2.5 over USA domain & 10 climate regions
DeepRSM Pilot Application in USA
19

## Slide 20: 2.1 Model configuration and control matrix design of Entire US domain
2.1.2 Control Matrix Design for Entire US domain 2018
Training cases: 21 US 2018 daily cases from January to December of 2018
（#1 - #21：21 cases * 12 months = 252 monthly runs）
OOS cases: 5 US 2018 daily cases from January to December of 2018
（#22 - #26：5 cases *12 months = 60 monthly runs）
2.1.3 Data set of DeepRSM
1-21： training cases
22-26： Out of sample validation
Model domain: Entire US domain
1 Region: USA
4 Pollutants: NOx, SO2, NH3, VOCs
1 Sector: All manmade(ALL_MM)
4 factors = 4 pollutants * 1 region * 1 sector
26 CMAQ simulation cases: 1 base case, 19 cases created by HSS method (0-1.2) for non-linear factors, 1 clean boundary conditions, 5 cases for out of sample (OOS)
2.1.1 CMAQ Configuration
CMAQ Version: CMAQ5.3.2
Model domain grids: 396 * 246
Grid resolution：12km * 12km
Chemical mechanism: cb6r3_ae7_aq
Simulation Period: The whole year of 2018
Control Matrix

## Slide 21: 3.1 Model configuration and Data set of Climate-Region
3.1.2 Climate-Region division
DeepRSM Model: obtained from US 2018 daily cases training (January to December, not divided into regions, treating the entire United States as a single region)
Building multi-region RSM cases: 11 daily cases in July(1 base case, 1 clean boundary conditions per region)
OOS cases: 5 daily cases in July
3.1.3 Data set of building climate-region RSM
1,222-231: used to build climate-region RSM
287-291: Out of sample validation
Model domain: 10 regions
The continental United States was divided into 10 regions based on climate zones:
10 Regions: CEN_CR, NE_CR, NPR_CR, NW_CR, S_CR, SE_CR, SW_CR, UPMW_CR, W_CR, OTHER
3.1.1 CMAQ Configuration
CMAQ Version: CMAQ5.3.2
Model domain grids: 396 * 246
Grid resolution：12km * 12km
Chemical mechanism: cb6r3_ae7_aq
Simulation Period: July 2018
Control Matrix
CEN_CR
NPR_CR
NW_CR
S_CR
SE_CR
SW_CR
UPMW_CR
NE_CR
W_CR
OTHER

## Slide 22: 3.2 Validation of US Climate-Region July 2018 DeepRSM
Case (July) for monthly average MDA8 O3 in Scatter plot with color density
RSM VS CMAQ:
RSM VS CMAQ (Base Response):

## Slide 23: 3.2 Validation of US Climate-Region July 2018 DeepRSM
Case (July) for monthly average MDA8 O3 in concentration map
ACONC.291
ACONC.290
ACONC.289
ACONC.288
ACONC.287
Notes: Ambient： Spatial distribution of pollutant concentration in control scenario

## Slide 24: 3.2 Validation of US Climate-Region July 2018 DeepRSM
Case (July) for monthly average MDA8 O3 in concentration response map
ACONC.291
ACONC.290
ACONC.289
ACONC.288
ACONC.287
Notes: Response： The difference between the baseline scenario and the control scenario

## Slide 25: 3.2 Validation of US Climate-Region July 2018 DeepRSM
Case (July) for monthly average PM2.5 in Scatter plot with color density
RSM VS CMAQ:
RSM VS CMAQ(Base Response):

## Slide 26: 3.2 Validation of US Climate-Region July 2018 DeepRSM
Case (July) for monthly average PM2.5 in concentration map
ACONC.291
ACONC.290
ACONC.289
ACONC.288
ACONC.287
Notes: Ambient： Spatial distribution of pollutant concentration in control scenario

## Slide 27: 3.2 Validation of US Climate-Region July 2018 DeepRSM
Case (July) for monthly average PM2.5 in concentration response map
ACONC.291
ACONC.290
ACONC.289
ACONC.288
ACONC.287
Notes: Response： The difference between the baseline scenario and the control scenario

## Slide 28: 4.2 Comparison of source attribution evaluation method results
4.2.1 The result of NOx or VOC reduction with different method in July
The total amount of DeepRSM and Opf-RSM source contribution is generally consistent with “Total”, demonstrating the accuracy of their simulations, but both their VOCs exhibit a slight negative contribution, indicating that there are still problems with the algorithms.
CMAQ BF: NOx or VOC
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
HDDM
ISAM
CMAQ BF: Total
NOx or VOC each reduction in Jul 2018
CMAQ BF: NOx or VOC
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
HDDM
CMAQ BF: Total
O3 MDA8 Jul Avg (ppbv)
Note: All source attribution results in section 4 are for the entire US domain.
Note: “Total” means the difference between the base case and the control case (100%, 75%, 50% and 25% reduction of NOx, VOC, NH3 and SO2).
CMAQ BF: NOx or VOC
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
HDDM
CMAQ BF: Total
CMAQ BF: NOx or VOC
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
HDDM
CMAQ BF: Total

## Slide 29: 4.1 Comparison of source attribution evaluation method results
4.1.1 The result of NOx & VOC reduction with different method in July
NOx & VOC reduction in July 2018
O3 MDA8 (ppb), 2018 July Avg
CMAQ BF: NOx & VOC
Opf-RSM BF: NOx & VOC
DeepRSM BF: NOx & VOC
Opf-RSM
DeepRSM
HDDM
ISAM
CMAQ BF: Total

## Slide 30: DeepRSM Training Report and Source Apportionment
Contents
4. O3 Source Attribution Evaluation in US Cases
3. DeepRSM Training Report of US Climate-Region July 2018
5. PM2.5 Source Attribution Evaluation in US Cases
2. DeepRSM Training Report of Entire US domain 2018 Case
1. What is DeepRSM?

## Slide 31: 4.1 Configuration of source attribution evaluation method
4.1.2 Configuration of ISAM
The 12 built-in sources were merged into three. For NOx (VOCs), set all species to zero except those belonging to NOx (VOCs):
1 Sector: All manmade(ALL_MM)
2 Pollutants: NOx, VOCs
Species:
NOx : NO, NO2
VOCs : TOL, XYLMN, BENZENE, NAPH, PAR, PRPA, MEOH, ETH, ETOH, OLE, ACET, FORM, GLY, KET, ETHY, ALD2, ETHA, IOLE, ALDX, ISOP, TERP, APIN
4.1.1 Configuration of DDM and HDDM
CMAQ Version: CMAQ5.3.2
Model domain grids: 396 * 246
Grid resolution：12km * 12km
Chemical mechanism: cb6r3_ae7_aq
Simulation Period: July in 2018
Model domain: the entire of US
 | EGGNOx | EPTNOx | ECMVNOx
NOx | GR_EMIS_N, GR_FIRE_N | PT_EGU_N, PT_NEGU_N, PT_OILG_N, PT_RXF_N, PT_F_N, PT_OTHF_N, PT_AGF_N, PT_OTH_N | PT_C1C2_N, PT_C3_N
 | EGGVOC | EPTVOC | ECMVVOC
VOCs | GR_EMIS_V, GR_FIRE_V | PT_EGU_V, PT_NEGU_V, PT_OILG_V, PT_RXF_V, PT_F_V, PT_OTHF_V, PT_AGF_V, PT_OTH_V | PT_C1C2_V, PT_C3_V
CMAQ Version: CMAQ5.3.2
Model domain grids: 396 * 246
Grid resolution：12km * 12km
Chemical mechanism: cb6r3_ae7_aq
Simulation Period: July in 2018
Model domain: the entire of US
1 Sector: All manmade(ALL_MM)
The results of HDDM and DDM will be compared with the results of Opf-RSM and DeepRSM, and the specific comparison chart will be shown on the next slides.

## Slide 32: 4.2 Comparison of source attribution evaluation method results
4.2.1 The result of NOx or VOC reduction with different method in July
The total amount of DeepRSM and Opf-RSM source contribution is generally consistent with “Total”, demonstrating the accuracy of their simulations, but both their VOCs exhibit a slight negative contribution, indicating that there are still problems with the algorithms.
ISAM
CMAQ BF: NOx or VOC
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
HDDM
DDM
CMAQ BF: Total
NOx or VOC each reduction in Jul 2018
CMAQ BF: NOx or VOC
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
HDDM
DDM
CMAQ BF: Total
O3 MDA8 Jul Avg (ppbv)
CMAQ BF: NOx or VOC
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
HDDM
DDM
CMAQ BF: Total
CMAQ BF: NOx or VOC
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
HDDM
DDM
CMAQ BF: Total
Note: All source attribution results in section 4 are for the entire US domain.
Note: “Total” means the difference between the base case and the control case (100%, 75%, 50% and 25% reduction of NOx, VOC, NH3 and SO2).

## Slide 33: 4.2 Comparison of source attribution evaluation method results
4.2.2 The result of NOx or VOC reduction with different method in August
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
NOx or VOC each reduction in Aug 2018
O3 MDA8 Aug Avg (ppbv)
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM

## Slide 34: 4.2 Comparison of source attribution evaluation method results
4.2.3 The result of NOx or VOC reduction with different method in September
NOx or VOC each reduction in Sep 2018
O3 MDA8 Sep Avg (ppbv)
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM

## Slide 35: 4.2 Comparison of source attribution evaluation method results
4.2.4 The result of NOx or VOC reduction with different method in October
NOx or VOC each reduction in Oct 2018
O3 MDA8 Oct Avg (ppbv)
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM
Opf-RSM BF: NOx or VOC
DeepRSM BF: NOx or VOC
Opf-RSM
DeepRSM

## Slide 36: DeepRSM Training Report and Source Apportionment
Contents
4. O3 Source Attribution Evaluation in US Cases
3. DeepRSM Training Report of US Climate-Region July 2018
5. PM2.5 Source Attribution Evaluation in US Cases
2. DeepRSM Training Report of Entire US domain 2018 Case
1. What is DeepRSM?

## Slide 37: 5.1 PM2.5 Source Attribution Evaluation in US Cases
As shown in the figure below, the results of DeepRSM and Opf-RSM source contribution analysis are almost similar.
Opf-RSM BF
DeepRSM BF
Opf-RSM
DeepRSM
Opf-RSM BF
DeepRSM BF
Opf-RSM
DeepRSM
Opf-RSM BF
DeepRSM BF
Opf-RSM
DeepRSM
Opf-RSM BF
DeepRSM BF
Opf-RSM
DeepRSM
Note: “BF” means controlling NOx, VOC, NH3 , SO2 or PM2.5 in turn.

## Slide 38: Summary of Source Contribution & Control Impact Modeling Techniques
Modeling Techniques | Strengths | Limitations
Brute Force (BF) Method | Conceptually simple and easy to implement Traditionally served as baseline for AQ control response & impact assessment | Computationally expensive Not suitable for source apportionment
OSAT/PSAT/APCA (CAMx) & ISAM (CMAQ) | Computationally efficient Well documented and broadly applied Effective for multi-source (region/sector) apportionment assessment | Treatment of nonlinear chemistry Predict only positive contributions so it may not provide disbenefit analysis (e.g., NOx disbenefit to O3 & PM2.5) Each precursor contributing only to a single PM2.5 species (e.g., NOx/SO2/NH3 only to PM-NO3-/ PM-SO42-/PM-NH4+, respectively), and no SOA treatment
DDM/HDDM | Computationally efficient Well documented and broadly applied Can be used other than region/sector analysis (e.g., VOCs reactivities: “IR” ) | Limitations in predicting large emission reductions (e.g., > 30% cut) PM2.5 applications not fully supported yet
RSM & pf-RSM | Instant AQ response to emissions control Can replicate BFM effectively Well documented and applied | Computationally intensive Limited applications in USA May not be suitable for source apportionment
DeepRSM | Effective for control/response and multi-source contribution assessment Deep Learning “DeepRSM” is very promising in computational efficiency and accuracy | Need further performance evaluation & applications in USA
38

## Slide 39: Take Home Messages & Next Steps
  “No one best tool to fit for all”:
    Each modeling technique has its own strengths & limitations
    Selecting a “best-fit” technique is depending upon policy analysis objectives
  “Source contribution” vs. “Control/Response” modeling:
    They seem similar but two different modeling assessment techniques
      Source Contribution: Chemistry regime based on “Baseline” case
      Control Response: Chemistry regime based on “Control” case
  Suggested Work Plan & Next steps:
  Complete “2018 CMAQ” pilot case study for O3 & PM2.5 (species) and DeepRSM implementation on “FAST-CE” & “RSM-VAT”
    QA/evaluate & compare “DeepRSM” vs. CMAQ-BF, ISAM (O3 & PM2.5) & HDDM (O3)
    Develop pilot applications of “DeepRSM” to support regulatory modeling analysis
39

## Slide 40
Carey Jang, U.S. EPA, Jang.carey@epa.gov
Appendix A:
    CMAQ/RSM E-US O3 & PM2.5 nonlinear responses (Kelly et al., 2021, Atmosphere)
    BFM/OSAT/DDM/RSM comparisons: O3 case study (Fang et al., 2021, Environ. Pollution)
    BFM/PSAT/RSM comparisons: PM2.5 case study (Li et al., 2021, Submitted to JEM)
Appendix B:
“DeepRSM” Supplemental information
Appendix C:
1. Running DeepRSM in “FAST-CE 3.5”
2. Running DeepRSM in “RSM-VAT 2.9”:
Note: Based on 2018 CMAQ 12-km pilot case with one USA domain or 10 climate regions
40

## Slide 41
41
  Recent RSM Applications/Comparisons
  & Publications
    RSM/CMAQ E-US pilot study: O3 & PM2.5 nonlinear responses (Kelly et al., 2021, Atmosphere)
    BFM/OSAT/HDDM/RSM comparisons: O3 case study (Fang et al., 2021, Environ. Pollution)
    BFM/PSAT/RSM comparisons: PM2.5 case study (Li et al., 2021, Frontier ES&E)
Appendix A

## Slide 42
42
1. RSM/CMAQ E-US Case: O3 & PM2.5 nonlinear responses
20 (runs for non-linear NOx, SO2, NH3, VOC factors)
+ 2 (runs for linear primary PM2.5)
2016 Eastern U.S. CMAQ case using “pf-RSM” (Jan. & July)
5 control factors = 5 Pollutants (NOx, SO2, NH3, VOC & primary PM2.5)
22 total CMAQ runs (12-km, January & July) used for “RSM Training Samples”
30 “out-of-sample” runs for QA & validation (20 “NOx, SO2, NH3, & VOCs emission cuts: 20/40/60/80/100%” + 10 “random”)
Atmosphere 2021, 12(8), 1044; https://doi.org/10.3390/atmos12081044
42

## Slide 43
43
1. RSM/CMAQ E-US Case: “RSM” vs. “CMAQ” Responses
July
2016
Comparison of AQ changes (monthly avg.) predicted by pf-RSM vs. 30 “Out-of-sample” (OOS) CMAQ simulations
Jan.
2016
43

## Slide 44
44
1. RSM/CMAQ E-US Case: “RSM” vs. “CMAQ” Responses
Comparisons of AQ changes (monthly avg.): pf-RSM vs. CMAQ for a 60% reduction in anthropogenic NH3, NOx, SO2, and VOC emissions
Jan. 2016
CMAQ
DO3_MDA8
RSM
DO3_MDA8
CMAQ
DPM_SO4
RSM
DPM_SO4
vs.
vs.
CMAQ
DPM_NO3
RSM
DPM_NO3
vs.
CMAQ
DPM_OM
RSM
DPM_OM
vs.

## Slide 45
45
1. RSM/CMAQ E-US Case: PM2.5 nonlinear chemistry
Comparisons of AQ conc. predicted by pf-RSM vs. CMAQ over all CBSAs for man-made emission reductions from 0 to 100%.
July 2016
(Jan. 2016 given in Appendix A)
Summary - NOx emission reductions were more effective for reducing PM2.5 and O3 concentrations than SO2, NH3, or VOC emission reductions. NH3 emission reductions effectively reduced nitrate concentrations in January but increased secondary organic aerosol (SOA) concentrations in July.
45

## Slide 46
46
1. RSM/CMAQ E-US Case: PM2.5 nonlinear responses
Change in (a) pH and (b) fine-particle water conc. for 60% NH3 emissions reduction
July
2016
pH
H2O
Summary - NOx emission reductions were more effective for reducing PM2.5 and ozone concentrations than SO2, NH3, or traditional VOC emission reductions. NH3 emission reductions effectively reduced nitrate concentrations in January but increased secondary organic aerosol (SOA) concentrations in July.

## Slide 47: 2. OSAT/DDM/BFM/RSM comparisons: O3 case study
BFM: brute-force method; RSM-BFM: response surface modeling with BFM; HDDM: high-order decoupled direct method;
RSM-DM: response surface modeling with differential method; OSAT: ozone source apportionment technology
Source impact modeling
2017 PRD emission inventories
Source contribution modeling
Response surface modeling
NOx and VOC emission contributions from multiple regions to O3
NOx and VOC emission impacts from multiple regions on O3
2017 PRD meteorological data
Emission sources (i.e., precursors, regions, sectors)
NOx and VOC emission contributions from multiple sectors in multiple regions to O3
WRF-CMAQ
WRF-CAMx
BFM
HDDM
RSM-BFM
RSM-DM
OSAT
Flow scheme for O3 source impact and contribution analysis using multiple modeling approaches

## Slide 48: 2. OSAT/DDM/BFM/RSM comparisons: O3 case study
Correlation between the CMAQ and CAMx
The magnitude and variation of CMAQ and CAMx simulations are in good agreement.
CMAQ simulations .vs CAMx simulations for baseline O3 concentration in all grids of the D3
CMAQ simulations .vs CAMx simulations for O3 time series in four representative sites of the PRD
(September, 2017)

## Slide 49: 2. OSAT/DDM/BFM/RSM comparisons: O3 case study
Out-of-sample validation of the RSM performance
CMAQ simulations .vs RSM predictions for O3 concentration (left) and response (right) in all grids of the D3
(a) Case 1
Slight control
(b) Case 1
Moderate control
(September, 2017)

## Slide 50: 2. BFM/OSAT/HDDM/RSM comparisons: O3 case study in PRD, China
WRF-CMAQ: BFM/HDDM/RSM
WRF-CAMx: OSAT
Domain: Nesting (27km, 9km, and 3km)
14 vertical layers
Period: July & Oct. 2015, and Sept. 2017
  Sector & pollutant emissions source factors:
  NOx from on-road, non-road, stationary sources, and others (industries, and biomass burning);
  VOC from on-road, industries, solvent utilization, and others (storage & transportation, waste treatment, biomass burning, and non-road)
Fang, et al., 2021, “Source impact & contribution analysis of ambient ozone using multi-modeling approaches
over the PRD region, China”, Environmental Pollution; https://doi.org/10.1016/j.envpol.2021.117860
7 Source regions (urban clusters):
  7 source cities (Guangzhou, Foshan, Zhongshan & Zhuhai, Jiangmen, Dongguan & Shenzhen, Huizhou, Zhaoqing & Others)
50

## Slide 51: Source Contribution: “RSM-BFM” (Brute Force) vs. “RSM-DM” (Differential)
RSM-BFM：regards the difference in O3 concentrations under the base and single source control scenarios as the source impact;
RSM-DM：differentiates the emission changes into small incremental intervals and sums up the O3 response in each interval as the source contribution.
……
Accumulated source impacts are different (typically higher than) from actual O3 response because of the non-linear interactions between NOx and VOC on O3)
VOCs only
control impact
Accumulated source contributions now agree with actual O3 response derived from the CMAQ under the simultaneous control of NOx and VOC emissions
51
NOx only
control impact
NOx & VOCs simultaneous control impact
Fang et al., EP, 2021

## Slide 52
Comparisons of O3 source impacts & contributions by 25%/50%/75/100% multi-region emission cuts
Accumulative source impacts and contributions
Source impact analysis:
BFM, HDDM & RSM-BFM: Predict consistently the impacts of accumulative source emissions; HDDM deviates from BFM under larger perturbations;
Source contribution analysis:
RSM-DM: Represent well for accumulative source contribution and non-linear O3 chemistry
OSAT: fails to represent the nonlinear response of O3 to incremental emission changes.
Receptor region: Guangzhou (September, 2017)
2. BFM/OSAT/HDDM/RSM comparisons: O3 case study in PRD, China
52

## Slide 53: 2. OSAT vs. RSM-DM : O3 Sectoral Contribution Analysis
Multi-sectoral O3 source contributions predicted by RSM-DM vs. OSAT
Major contributing sectors to O3 in Guangzhou:
OSAT vs. RSM-DM : Local NOx Mobile contribution makes the key difference; regional NOx transport all show positive contributions to urban receptors
OSAT: local on-road mobile NOx and solvent utilization VOC emissions.
RSM-DM: local industrial process and solvent utilization VOC emissions;
Receptor region: Guangzhou (September, 2017)
Sectoral contribution from each source region
Percentage of sectoral contribution from the entire D3 domain
RSM-DM
OSAT
Urban
Receptor
53

## Slide 54: 2. RSM-DM: O3 Seasonal Source Contribution Analysis
Multiregional dynamic O3 source contributions predicted by RSM-DM
July, 2015 (Summer)
October, 2015 (Fall)
Major contributors (July):
NOx emissions from upwind areas are major contributors; local NOx emissions also show positive contributions
Major contributors (Oct.):
VOC emissions from local and upwind areas are major contributors; Local NOx emissions can be negative contributors unless stringent control (100%)
54
Receptors

## Slide 55: 3. BFM/PSAT/RSM comparisons: PM2.5 case study
55
“Source contribution analysis based on advanced modeling approaches for PM2.5 over the PRD region, China“ (Li et al., 2021, submitted to J. of Environ. Modeling)

## Slide 56: 3. BFM/PSAT/RSM comparisons: PM2.5 Sectoral Responses
56
Sectoral contributions of PM2.5 predicted by BFM and RSM are very similar
BFM and RSM predicted lower contributions of “Mobile“ sector than PSAT and modestly higher contribution of “Agriculture“ sector
Industrial
processes
Mobile
Stationary
sources
Agricultrue
Dust
BFM
RSM
PSAT
36
36
9
4.5
36
PM2.5 Jan. Avg.

## Slide 57: 3. BFM/PSAT/RSM-DM comparisons: PM2.5 case study
57
“RSM-DM“ generally predicted lower “NOx“ & “Mobile“ sector contributions and higher other sectors contributions than “PSAT“ in major cities mainly due to lower (or negative) predictions of local NOx contributions
(Urban receptor: GZ-Guangzhou, PM2.5 January avg.)
(receptor)
(receptor)
(receptor)

## Slide 58: 3. PSAT/BFM/RSM comparisons: PM2.5 case study
58

## Slide 59: 3. PSAT/BFM/RSM comparisons: PM2.5 case study
59
Comparison of the contributions to monthly mean PM2.5 concentrations from different source regions and pollutants in GZ and SZ in January. GZ: Guangzhou, SZ: Shenzhen, FS: Foshan, DG: Dongguan, ZS: Zhongshan, OTH: all the other areas in the d03 domain.

## Slide 60: 3. PSAT/BFM/RSM comparisons: PM2.5 case study
60
Comparison of the contributions to monthly mean PM2.5 concentrations from different source regions and sectors in GZ and SZ in January. GZ: Guangzhou, SZ: Shenzhen, FS: Foshan, DG: Dongguan, ZS: Zhongshan, OTH: all the other areas in the d03 domain.

## Slide 61: 3. PSAT/BFM/RSM comparisons: PM2.5 case study
61
Comparison of the percentage contributions to monthly mean PM2.5 concentrations from different source sectors in GZ and SZ in January. GZ: Guangzhou, SZ: Shenzhen.

## Slide 62: 3. PSAT/BFM/RSM comparisons: PM2.5 case study
62
Comparison of PM2.5 source contributions calculated by BFM, RSM, and PSAT respectively for emissions from (a) industrial process, (b) mobile, (c) stationary combustion, (d) agriculture, (e) dust, and (f) other sources at national-controlled air-monitoring sites of the PRD in January (each point represents the monthly averaged source contribution value at each monitor site).

## Slide 63: “DeepRSM” Supplemental information
Appendix B:
63

## Slide 64: “DeepRSM, Deep-learning-based RSM”
CTM
RSM
ERSM
pf-RSM
DeepRSM
Air pollutant
Air pollutant 1
Air pollutant 2
High dimensional Kriging interpolation
High dimensional Kriging interpolation
Polynomial equation
Source emission in region A
Source emission in region B
Source emission in region C
Specific 3D mode control scenario
Air pollutant
Source emission
Source emission
2009-2011
2015-2016
2018-2019
2019-2020
Xing et al., ACP, 2011
Wang et al., ESorT, 2011
Zhao et al., GMD, 2015
Xing et al., ESorT, 2017
Zhao et al., ACP, 2017
Xing et al., ACP, 2018
Xing et al., ES&T, 2020
Xing et al., Atm. Res., 2022
NOx
NH3
SO2
POA
VOC
Air pollutant 1
Air pollutant 2
Further reduce the number of air quality simulation cases required to build the RSM model.

## Slide 65: RSM with Polynomial Functions: pf-RSM
PM2.5
O3
NOx
2nd
3rd
4th
5th
1st
NH3
1st
2nd
3rd
SO2
1st
POA
1st
VOC
1st
2nd
3rd
High order (non-linear) for NOx, NH3 and VOC
14/15 coefficients of polynomial terms can be derived from 20~30 samples
(per control region)
Low order (linear) for
SO2 and POA
Xing et al., 2018, Atmos. Chem. & Phys. (18) : https://doi.org/10.5194/acp-18-7799-2018
65

## Slide 66: Deep Machine Learning “DeepRSM”
DeepRSM: “Deep Learning” “Indicator-based” pf-RSM
Xing et. al., ES&T, 2020 (Further details please see Appendix B)
Traditional RSM | “pf-RSM” | “DeepRSM”
>100s | 20~30* | 1*
# of model runs needed for maintaining RSM accuracy in predicting control responses （* for each selected control region or sector）
Combine
pf-RSM
and
Deep Learning CNN
to predict
Nonlinear PM2.5 & O3 responses to emissions control
66

## Slide 67: “DeepRSM” Publication (2020)
67
Xing et. al., ES&T, 2020
https://pubs.acs.org/doi/10.1021/acs.est.0c02923
“DeepRSM”
Still needs to be tested for U.S. pilot cases and implemented in RSM-VAT

## Slide 68: DeepRSM: Deep Machine Learning with pf-RSM
68
The CNN architecture of the DeepRSM with optimized polynomial structure for predicting the air quality response functions. (“Conv3x3BN”: 3x3 convolution followed by batch normalization; “LeakyReLU”: leaky rectified linear unit activation function; “FC”: fully connected layer)

## Slide 69: “Indicator-based” DeepRSM
69
14 coefficients of terms in in responding to 18 chemical indicators for O3 and PM2.5 (example)
O3
PM2.5

## Slide 70: DeepRSM: Deep Machine Learning with pf-RSM
70
pf-RSM and DeepRSM performance in predicing PM2.5 responses to emissions in different numerical experiments. -TT: training based on same spatial domain but different days than testing; -DT: training based on different spatial domains than testing; -DTF5, -DTF20, and -PolyDTF20: -DT experiments based on fine-tuning procedure. Results are based on Jan. 30 for control scenario #35 in Table S1 (emission change ratios of NOx, SO2, NH3 and VOC are 92.0%, -84.2%, -98.0%, and -33.6%, respectively).

## Slide 71: DeepRSM: Deep Machine Learning with pf-RSM
71
The isopleths of PM2.5 response to NOx/VOC (a) and SO2/NH3 (b) emission change (baseline = 1) predicted by pf-RSM and DeepRSM for the CN27 domain (the values are averages of all grid cells and days; the color dots represent the simulated value in CMAQ)

## Slide 72
Carey Jang, U.S. EPA, Jang.carey@epa.gov
Appendix A:
    CMAQ/RSM E-US O3 & PM2.5 nonlinear responses (Kelly et al., 2021, Atmosphere)
    OSAT/DDM/BFM/RSM comparisons: O3 case study (Fang et al., 2021, Environ. Pollu.)
    PSAT/BFM/RSM comparisons: PM2.5 case study (Li et al., 2021, Submitted to JEM)
Appendix B:
“DeepRSM” Supplemental information
Appendix C:
1. Running DeepRSM in “FAST-CE 3.5”
2. Running DeepRSM in “RSM-VAT 2.9”:
Note: Based on 2018 CMAQ 12-km pilot case with one USA domain or 10 climate regions
72

## Slide 73
73
  Running DeepRSM in “FAST-CE” and
  “RSM-VAT” Tool
  Experimental Design: “Prepare CMAQ” module
  Running “pf-RSM”
  Performance evaluation: QA & “Out-of-Sample Validation”
  (Further details of “Quick Tutorial” and QA provided in “Appendix C”)
Five-Region RSM/CMAQ
One-Region RSM/CMAQ
    CMAQ “Eastern US” 12-km pilot cases based on “pf-RSM”
Easier than you think !
Appendix C

## Slide 74
“RSM” in “FAST-CE” : O3 & PM2.5 Nonlinear Responses
Five Climate Regions:
NE
SE
Cen
Up_MW
Other
74
“FAST-CE
2.5”
With
RSM
DeepRSM/HDDM/ISAM in “FAST-CE 3.5”
DeepRSM in “RSM-VAT 2.9”
ISAM/O_PSAT
RSM/DeepRSM
DDM/HDDM
USA domain or
10 Climate regions
Notes: 1. Thank Cen/Gao/Luo/Chen; 2. HZ more visits; 3. AP on HZ

## Slide 75
“DeepRSM” in “FAST-CE 3.5”
One USA domain
Or
10 Climate Regions:
75
Running
DeepRSM in
“FAST-CE”
ISAM/OSAT&PSAT
RSM/DeepRSM
DDM/HDDM
Notes: 1. Thank Cen/Gao/Luo/Chen; 2. HZ more visits; 3. AP on HZ

## Slide 76: RSM EUS example: “O3” Non-linear Chemistry under NOx incremental control
Jan. O3 responses to NOx Emissions cut %
benefit
disbenefit
25%
50%
75%
100%
NOx Emissions cut only
Select 25%, 50%, 75%, 100% NOx Emissions cut only (corresponding CMAQ results provided in Appendix)
76
NOx emissions cut could lead to disbenefit (increase) of “O3”
in January
“O3”
could turn from disbenefit to benefit under incremental
NOx emissions control (25%/50%/75%/100%)

## Slide 77
O3 responses to NOx cut (Jan.)
O3 responses to NOx cut (July)
PM_SO4 responses to NOx cut (Jan.)
PM_SO4 responses to NOx cut (Jan.)
benefit
disbenefit
benefit
disbenefit
benefit
77
“O3” & “PM_SO4”
non-linear
interactions under incremental NOx emissions control (25%/50%/75%/100%)
NOx emissions cut
led to disbenefits (increases) of
“O3” & “PM_SO4”
in January,
but led to benefits (decreases) in July
Notes: 1. Thank Cen/Gao/Luo/Chen; 2. HZ more visits; 3. AP on HZ

## Slide 78: Workflow to Create & Run “RSM” in “RSM-VAT”
Experimental Design
(RSM-VAT)
Run CMAQ
Emission control matrix
Region control NetCDF file
Emissions control (DESID) run script
CMAQ results
Run RSM Project
(RSM-VAT)
RSM results
(Control Matrix module)
(CMAQ Preparation module)
(CMAQ Preparation module)
Main Workflow for
Running “RSM-VAT”
Visualization & Analysis
(RSM-VAT)
78
Prepare CMAQ
  “RSM-VAT Quick Tutorial” provided in “Appendix C”

## Slide 79
1. Create/Input RSM Option
2. Model Data Input Option
3. Validation & Q/A Option
79
Running RSM-VAT to create RSM
4. Vis./Analysis
Option
“RSM-VAT” Quick Tutorial is available

## Slide 80: “ CMAQ Preparation ” Module in RSM-VAT: Set up model domain and create CMAQ run scripts
1. Select the step ①.
3. Click to start generating NetCDF file for selected regions.
Step 2: Create region control NetCDF file based on regional GIS shapefile (.shp)
2. Click to select regions used to merge（CEN_CR,NE_CR,SE_CR,UPMW_CR,OTHER）
80
Pre-set (default) regions/areas for
1. NOAA Climate
regions
2. States
3. CBSAs

## Slide 81: ”The Detailed Emissions Scaling, Isolation, and Diagnostic (DESID) module in the Community Multiscale Air Quality (CMAQ) Modeling System version 5.3”, Murphy, et al., 2020, GMD
Step #4: Generate CMAQ run scripts using “DESID” module’s “region/sector/pollutant” emissions control functions
1. Select the step ③.
2. Click to create CMAQ run scripts
based on DESID module.
Use the NetCDF file generated from step ② as the input.
81
“CMAQ Preparation” Module in RSM-VAT: Create CMAQ run scripts based on “DESID” emissions control module

## Slide 82: RSM-VAT: Main Page & Key Modules
82
“Experimental Design” module to prepare CMAQ data for creating RSM）
“Visualization & Analysis” module to display map/data/chart & QA rsults
Main panel to set up RSM input files and run/create RSM results
For first test run, Click “Next” all the way thru until all “green lights” flash

## Slide 83: QA & Evaluation: “Compare” and “Out-of-Sample” Validation
83
“Out-of-Sample Validation” Tab provides “RSM” vs. “CMAQ” comparisons (Con. & Response)
QA & Validation:
“ O3,
PM2.5, PM_SO4
PM_NO3 “
for Jan. & July 2016
are given in Appendix C

## Slide 84: RSM-VAT: Launching Page & User’s Manual
Click module name to invoke online User’s manual
For first test run, Click “Next” all the way thru until all “green lights” flash
84

## Slide 85
Carey Jang, U.S. EPA, Jang.carey@epa.gov
85
End