## Slide 1: Incorporating the WESTAR EGU Analysis into ERTAC Inputs
Updated 10/24/2019
Wendy Jacobs (CT) and Doris McLeod (VA)

## Slide 2: WESTAR Report: Unit Specific Data Added
Retirements impacting 2028 (capacity calcs from ERTAC)
  AZNM: Coal=9,000 MW (AZ, NM)
  NWPP: Coal=4,950 MW (MT, NV, WA, OR, UT, WY)
  RMPA: Coal=1,680 MW (CO, WY)
  CAMX: Coal=2,000 MW (UT)
  Boiler Gas=500 MW
Retirements after 2028:
  AZNM=1,800 MW coal
  NWPP=5,600 MW coal
  RMPA=1,000 MW coal
AZ: Five new CTs added at Ocotillo Power Plant in 2020
Three coal to gas switches, about 1,000 MW

## Slide 3: WESTAR Report: Emissions/Controls Data Added
NOx and SO2 rates for Ocotillo’s five new CTs
NOx and SO2 rates for new boiler gas units
New NOx control listings, 14 coal fired units
New SO2 control listings, 5 coal fired units
In situations where the WESTAR report noted retirement or control by SCR, control by SCR was assumed.

## Slide 4: AZNM (AZ and NM) Growth Rates
AZNM 2016 coal capacity ~ 14,600 MW.
AZNM 2028 coal capacity ~ 5,475 MW after inclusion of WESTAR retirements
The AZNM annual growth rate for coal (20162028)
  0.805 AEO2018 High Oil and Gas case
  0.787 AEO2019 High Oil and Gas case (draft)
Initial ERTAC run using AEO2018 High Oil and Gas indicated significant coal fired capacity was needed in 2028.
In later ERTAC runs, transferred about 5,360,000 MW-hrs in 2028 from coal to simple cycle to reduce need for coal capacity

## Slide 5: Coal Activity Comparison
 | WESTAR Scenario 1* | WESTAR Scenario 2* | ERTAC 16.0 | ERTAC 16.0 + WESTAR Data (WESTAR6 run)
 | 2028 MW-hr | 2028 MW-hr | 2028 MW-hr | 2028 MW-hr
AZ | 17,975,815 | 15,998,536 | 27,592,528 | 24,501,146
CO | 23,892,415 | 22,001,630 | 21,285,823 | 19,723,355
MT | 11,730,562 | 10,837,604 | 11,255,496 | 10,189,928
ND | 30,643,429 | 28,047,531 | 29,161,211 | 28,408,665
NM | 10,038,417 | 8,836,742 | 16,332,195 | 14,021,925
NV | 1,162,858 | 1,079,600 | 1,520,250 | 919,239
SD | 2,455,317 | 2,275,369 | 2,246,706 | 2,280,765
UT | 19,744,160 | 18,432,040 | 13,479,207 | 17,080,532
WY | 38,674,834 | 35,530,523 | 32,472,109 | 31,805,915
Total | 156,317,807 | 143,039,575 | 155,345,524 | 148,931,469
AZ and NM ERTAC activity a bit higher than WESTAR estimates.
ERTAC use of conservative AEO growth rate for AZNM region most likely explanation (AEO2018 HOG).
* Scenario 1 uses the maximum annual data for years 2016-2018 while Scenario 2 uses the average annual data for years 2016-2018.

## Slide 6: Coal NOx Emissions Comparison
 | WESTAR Scenario 1 | WESTAR Scenario 2 | ERTAC 16.0 | ERTAC 16.0 + WESTAR Data (WESTAR6 Run)
 | 2028 tpy | 2028 tpy | 2028 tpy | 2028 tpy
AZ | 9,283 | 8,247 | 24,746 | 12,704
CO | 11,778 | 10,706 | 14,082 | 9,862
MT | 8,671 | 8,046 | 10,587 | 7,776
ND | 33,804 | 30,771 | 38,197 | 30,494
NM | 5,719 | 5,156 | 28,137 | 8,233
NV | 281 | 261 | 1,364 | 215
SD | 1,102 | 1,022 | 988 | 1,002
UT | 21,797 | 20,311 | 15,032 | 19,037
WY | 25,270 | 23,055 | 26,287 | 20,935
Total | 117,705 | 107,575 | 159,420 | 110,260
Coal retirements helped bring state level NOx emissions in line with WESTAR 2028 analysis.
ERTAC AZ and NM estimates continue to be somewhat higher than WESTAR predictions, probably due to conservative AEO growth rate (AEO2018 HOG) for AZNM region resulting in higher activity.
Total NOx from the nine states are within the WESTAR range when using the WESTAR adjustments with the ERTAC inputs.

## Slide 7: Coal SO2 Emissions Comparison
 | WESTAR Scenario 1 | WESTAR Scenario 2 | ERTAC 16.0 | ERTAC 16.0 + WESTAR Data
 | 2028 tpy | 2028 tpy | 2028 tpy | 2028 tpy
AZ | 8,135 | 7,318 | 10,361 | 10,194
CO | 9,969 | 9,146 | 9,106 | 8,493
MT | 5,177 | 4,766 | 6,518 | 4,701
ND | 39,997 | 36,261 | 38,390 | 36,097
NM | 2,923 | 2,607 | 6,671 | 4,129
NV | 171 | 159 | 1,732 | 107
SD | 961 | 890 | 849 | 862
UT | 7,226 | 6,752 | 4,992 | 6,327
WY | 23,507 | 21,518 | 23,434 | 19,329
Total | 98,066 | 89,417 | 102,074 | 90,239
Retirements, controls helped bring state level SO2 emissions in line with WESTAR 2028 analysis.
ERTAC AZ and NM estimates continue to be somewhat higher than WESTAR predictions, probably due to conservative AEO 2019 HOG growth rate for AZNM region, resulting in higher activity.
Total SO2 from the nine states are within the WESTAR range when using the WESTAR adjustments with the ERTAC inputs.

## Slide 8: Other Observations and Future Updates
May need to review growth rates, especially for AZNM
  Growth Subcommittee is resource-constrained
Is there an update to the WESTAR report’s unit level information available?
  Additional controls?
  Additional retirements or fuel switches?