## Slide 1: Emissions Inventory Development and Preparation for Modeling

## Slide 2: Instructors
Anne Pope
US EPA/OAQPS
pope.anne@epa.gov
Tom Driscoll
US EPA/OAQPS
driscoll.tom@epa.gov

## Slide 3: Our Goals
Explain basic elements of air pollution that are relevant to emissions inventories, the history behind air regulatory and inventory programs, and why it is important to develop an air pollutant emissions inventory periodically
Provide information on how to develop an air pollutant emissions inventory using detailed examples
Explain how air pollutant emissions inventories are used for modeling

## Slide 4: Overview
Introduction
  Basic elements of air pollution that are relevant to emissions inventories
  History of Air Program
  Uses/ Reasons to Prepare Air Pollutant Emissions Inventories
Pollutant Definitions, Pollutant grouping for modeling
Source Category Definitions
Emission Inventory Modeling Parameters
Emission Inventory Compilation
Point Sources
Nonpoint Sources
Fires
Mobile Sources
Wrap Up!

## Slide 5: Introduction
Notes: History of air Toxics Programs
Air Toxics is a Complex Program
Air Toxics are a Public Health Concern
Major Risk Reductions Have Been Achieved to Date but More Are Needed
Inventories are a crucial part in tracking emission and risk reductions

## Slide 6: Air Pollution - Definition
Presence of substances in the air in concentrations that create health and environmental problems
Sources
  Naturally occurring
  Man-Made
Mixture
  Gases
  Water Droplets
  Particles

## Slide 7
Air Pollution Effect on Humans
Notes: The shows whole cycle for air pollution for humans.
Sources: Stationary (factories, residences, etc.) and Mobile (Onroad and Nonroad)
Dispersion: Pollutants carried short or long distances by wind. Air quality is highly dependent on weather conditions. The movement of air affects general air quality. Winds help to dissipate air pollutants, whereas stagnant air can promote the buildup of pollutants to unhealthy conditions
Transformation: Natural substances and air pollutants react with each other to form different compounds. Examples: SO2 reacts with water vapor to form sulfuric acids, , resulting in in acid rain. NOx, VOC and other components react in sunlight to form ozone. Formaldehyde is secondarily formed in the atmosphere.
Deposition: Pollutants are deposited either by dry deposition (without precipitation) or wet deposition (precipitation). Most of the water droplets carried by air eventually fall to the earth as precipitation. Air pollutants are washed from the atmosphere in precipitation to the earth. Deposition of air pollutants then becomes land and water pollution.
Evaporation and Reentrainment: pollutants from land and water are also taken up back into the air.
Exposure to humans: occurs after deposition.
Inhalation (breathing)
Dermal (skin)
Ingestion (diet) – discuss bioaccumulation/ bio-magnification. As pollutant moves up food chain, some air pollutants become more concentrated as they are transferred along the food chain. Ex. Mercury.
Health effects on humans; target organs
Cancer endpoint
Noncancer endpoints – respiratory effects (asthma, coughing, reduced lung capacity, etc.), birth defects, reproductive (reduced sperm counts), neurological (methyl mercury affects muscle control), etc.

## Slide 8: Emission Types
Anthropogenic (man-made)
  Stationary sources
    Indoors
    Outdoors
  Mobile sources
    Onroad
    Nonroad
    ALM
Natural
  Plants and soils
  Lightning and volcanoes
  Wildfires
<number>
Notes: <number>
<footer>
<header>
<date/time>
In describing a given air mass and the chemical reactions occurring therein, both anthropogenic and natural sources of primary emissions must be considered and their relative importance evaluated. The importance of emission source types can vary by geographic area, by pollutant, and by season.
Natural air pollutants have always been part of earth’s history. Particulate matter and variety of gases from volcanoes, forest fires and decaying organic matter in oceans and swamps enter the atmosphere at irregular intervals. Naturally produced greenhouse gases have contributed to periods of global warming.
Plants and soils – In the open seas and in marshes and swamps, decay processes produce levels of methane gas. Plants also release pollutants directly to the air that contribute to ozone formation.
Volcanoes – contribute particulate matter, ash and gases into the atmosphere. Their emission can affect visibility and the temperature of the earth.
Forest fires – contribute variety of pollutants, ash and smoke.

## Slide 9: Adverse Impacts of Air Pollutants
Health and environmental effects can be acute or chronic
Impact of substance is related to:
  Atmospheric lifetime of pollutant
  Concentration of pollutant
  Exposure of organism to pollutant
  Dose response of pollutant
Emission inventories are an important component of risk assessment studies

## Slide 10: Atmospheric Lifetime of Pollutants
Often discussed as half-life or the natural lifetime of a pollutant with respect to reactive species such as OH (hydroxyl radical)
Depends on balance between sources and sinks (removal mechanisms)
Half-life range for compounds in the troposphere is from seconds hours to weeks to years
Affects transport properties of pollutant
Effects of deposition, suspension, and re-entrainment

## Slide 11: Concentration Units
Concentration of Air Pollutants may be reported in following units:
Parts per million (ppm) or parts per billion (ppb)
  For gaseous pollutants
  Assumes a dimensionless volume fraction (Vpollutant:Vair)
Microgram per cubic meter (µg/m3)
  For gaseous pollutants and particles
Conversion of µg/m3 to ppm
  µg/m3 = ppm x 40.9 x molecular weight of pollutant (MW)
Example:
  Convert 0.120 ppm of O3 to µg/m3 when MW of O3 = 48
  0.120 ppm x 40.9 x 48 = 236 µg/m3

## Slide 12: Human Health Effects
Air pollutants can cause acute or chronic health effects.
The impact on health depends on:
  Age and overall health condition of the individual
  Exposure time and dose
Common health effects
  Cancer and Noncancer Effects
  In severe conditions, death
Birth Defects, Miscarriages
Cancer
Asthma, Chronic Bronchitis
Skin
Rashes
Birth Defects
Miscarriages
Cardiovascular,
Kidney, Liver
Damage
Nervous System
Damage
Respiratory System Damage
Developmental Problems
in Children
Notes: <number>
<footer>
<header>
<date/time>
• The World Health Organization (WHO) has estimated that each year millions of people worldwide die or suffer serious health effects from air pollution. Air pollution causes respiratory diseases, asthma, chronic obstructive pulmonary disease, cardiovascular disease, and cancer. WHO estimates place deaths from air pollution worldwide at approximately 1.4 to 6 million per year. Health effects range from coughing and bronchitis to heart disease and lung cancer. The most vulnerable groups are infants and young children, the elderly, and people already suffering from conditions like asthma and emphysema. (*WHO, Fact Sheet No. 187, September 2000)
• Numerous studies show direct links between mortality rates and daily ambient concentrations of fine particulate matter (i.e., PM10 or smaller). One major study in Indonesia, estimated that 1,400 deaths, 49,000 emergency room visits, and 600,000 asthma attacks could be avoided if PM levels in that area were brought down to WHO standards.
• In studies of some populations, 30-40% of asthma cases and 20-30% of all respiratory disease cases can be linked to air pollution and high ambient concentrations of pollutants. Studies in Brazil demonstrated that a 75 μg/m3 increase in NO2 concentrations was related to a 30% increase in deaths from respiratory illness in children under 5 years of age.
• According to WHO documents, particulate matter causes more detrimental health effects to people than any other pollutant. PM components include coarse particles such as soil and mineral ash and fine particles found in wood smoke and engine exhausts. The large reliance on coal for energy results in significant PM emissions and the potential for resultant health effects.
• Indoor air pollution health effects in Asia from sources such as coal cooking stoves and heaters are particularly pronounced. Such activities can produce PM concentrations as high as 10,000 μg/m3, which is higher than even ambient pollution in some of the world’s more polluted cities.

## Slide 13
Long Range Transport of Persistent Pollutants
Notes: <number>
<footer>
<header>
<date/time>
When these pesticides are applied or they are generated from some process, they don’t just stay in one place. They evaporate and travel on the wind, then they condense and fall back to earth. And because they persist, when it warms up again, they evaporate again and travel farther before condensing and falling back to earth.
Some are more mobile than others and make their way to the Arctic where they accumulate in the food chain and affect large mammals (polar bears) and humans.

## Slide 14: Air Quality Management Model
<number>
Establish and Consider
Health and
Environmental Goals
What reductions are needed?
- Are reductions needed?
- From which sources?
How to Achieve
Reductions/Solve
Problems
Implement
and
Enforce
Evaluate
Results
Notes: <number>
<footer>
<header>
<date/time>
We have discussed air pollution – what it is , sources of air pollution, effects of air pollution, and types of pollutants.
The goal of an air quality management program is to improve air quality in a geographic area in order to improve the quality of life for a population.
The air quality management model depicts how air quality is typically managed by agencies. It is a loop that is continuously applied over time to address new problems as they arise and revise older strategies if needed.
The basic steps include:
Establish health and environmental goals your air quality program wants to achieve
Determine what reductions in emissions and risks are needed to achieve established goals
Determine how to achieve the reductions (voluntary, regulatory, economic incentives, partnerships, etc.)
Implement reductions and enforce regulations if established
Evaluate results after implementation of reductions
Revise program if results do not meet established goals or if new problems not addressed by goals arise
In the model, emissions inventories are used to determine what reductions are needed and to evaluate results (pink boxes).

## Slide 15: Summary: Principles of Air Pollution
Air pollutants can be directly emitted by anthropogenic
and natural sources to the atmosphere or formed
in the atmosphere by chemical reactions
Air pollutants can have impacts on a local,
regional, or global scale
Air pollutants have human health and environmental
effects
Humans may be exposed to air pollutants indoors or
outdoors
Focus of training is on:
  CAPs for which air quality standards have been established by various agencies
    PM, CO, NO2, SO2, Pb, NH3, O3
  Air toxics - HAPs
The air quality management model is an approach for describing how air pollution control programs may be established and implemented
<number>
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Air Pollution Control in the 21st Century
1920 1950 1970 1980 1990 2000
City
/Town
County
State/
Multi-Counties
Nation/
Multi-State
International
Think
Globally
Act
Locally
Notes: Present background is 20-40 ppb

## Slide 17: Scale of Air Pollution Problems
Local Scale
  Impacts from a single source or group of sources
  May examine health impacts on specific receptors
Regional Scale
  500 to several thousand km2
County to Continental Scale
  Scale
  Tens of thousands of km2
  May address international
  transboundary pollution
Global Scale
  Transport of pollutants across globe

## Slide 18: US Air Pollution Program History
PHS Air Pollution Control Act
Research Tech. Assistance for Air Pollution Control
1st
CAA
65
CAAA
67
CAAA
Prevention & Abatement of Air Pollution
Mobile Sources
SIPS
1955
1963
1965
1967
70 CAAA
EPA
1970
Air Quality for CAPS & HAPS
77
CAAA
1977
PSD
Mobile Sources
6 NESHAPS
(1977 thru 1989)
1989
Benzene NESHAP
10-6 as Ample Margin of Safety
1990
90
CAAA
HAPS:
202–Mobile Air Toxics
129–Combustion – Sources
112b–List 189 HAPS
112d–MACT
112f– Residual Risk
112c6–7 PBTS
112c3/112k–Urban Area Source
112m–Great Waters
112n–Special Studies, Hg
FUTURE
Notes:   1970 CAAA Air Toxics (also called Hazardous Air Pollutants or HAPs)
    “Chemicals which may reasonably be anticipated to cause adverse effects” Focus on Cancer
Required EPA to: Decide what chemicals are HAPs and put them on a list
Regulate emissions of HAPs with an “Ample Margin of Safety”
Identify, take public comment, list and regulate in 1 year
Determine what is “safe”
“Safe” is not necessarily risk free
Base decision on what is “safe” only on human health
Will always be marked with uncertainty
Determine “ample margin of safety”
    Once you determine what a ‘safe’ emission level is, set the regulation to allow less emissions
    This will provide an “ample margin,” beyond what is “safe”
The 1970 Amendments regulated individual chemicals based on human health effects
The 1990 Amendments:
First, regulate source categories based on existing technology -MACT
After MACT, evaluate and reduce remaining risk (i.e., residual risk) still posed by major source categories - Allows EPA time to improve risk assessment methods
Congress added provisions to study and reduce risk in urban areas - Community-level risk assessments & Area source program
Motor vehicle and fuel standards

## Slide 19: 1990 Clean Air Act CAP Requirements
CERR – Consolidated Emissions Reporting Rule, Mandatory reporting of CAP Emissions Inventories by state and local agencies and tribes
AERR – Air Emission Reporting Rule, replaces CERR, proposed
Handouts 1 and 2
Notes: The amendments to the Clean Air Act in 1990 had a particular focus on air toxics.
The risk-based NESHAP program was tedious and needed to be changed.
HAP were listed for control, EPA was directed to develop a source category list and schedule for MACT standards (not risk based, but control-technology based), etc.

## Slide 20: 1990 Clean Air Act Toxics Requirements
http://www.epa.gov/ttn/atw/eparules.html
Section 112(d) MACT source category
  Handouts 3 and 7
Section 112(b)HAP listing/delisting
Section 112(k), Urban Area Source Program
  Handouts 4, 5, and 7
Section 112(c)(6)
Section 112(f), Residual Risk Program
  Handouts 6 and 7
Section 112(m), Great Waters Program
Section 112(n), Special Studies, e.g., Hg
Notes: The amendments to the Clean Air Act in 1990 had a particular focus on air toxics.
The risk-based NESHAP program was tedious and needed to be changed.
HAP were listed for control, EPA was directed to develop a source category list and schedule for MACT standards (not risk based, but control-technology based), etc.

## Slide 21: What Is an Air Pollutant Emission Inventory?
Inventory - current comprehensive listing by sources of air pollutant emissions in a geographic area during a specific time period
Point Sources
Mobile OnRoad Sources
Mobile NonRoad Sources
NonPoint Sources
ALM
Notes: Sources:
Stationary Point and Nonpoint
Mobile Onroad, Nonroad, ALM
Geographic area
Global
National
Regional
Local (city or neighborhood)
Facility
Specific Time Period
Hour
Day
Month
Season
Year

## Slide 22: Why Do We Need Air Emission Inventories?
Public interest in clean air
Fundamental Component of Air Quality Management Plan
  To identify sources and problem areas
  To establish a baseline for future planning
  To develop air quality control plans and mitigation strategies
  To establish regulations and permit conditions for industrial facilities and basis for emissions trading programs
Notes: <number>
<footer>
<header>
<date/time>
One primary reason for EIs is public interest in clean air. Are citizens getting sick from air pollution (increased visits to hospitals; complaints about coughs, runny eyes, etc.; increase in cancer incidences)? Are environmental effects occurring (decreased crop yields, odors, destruction of property)? Causes (pollutants and sources of health and environmental effects)
What purpose do inventories serve in environmental protection and air quality management programs? Inventories are the fundamental building block of an air program. It is difficult to plan and implement a meaningful and successful air quality program without benefit of a good inventory.
They indicate what is the baseline or starting point for assessing the status of a source's or an area's air quality problems. Inventories also give perspective on the nature of air quality problems, i.e., are the problems the result of emissions from point, nonpoint, or mobile sources, and what specific sources may need to be targeted. What are the pollutants and their emissions? What sources emit pollutants? Where and when are pollutants emitted from the sources?
After identifying the problem, air quality control plans can be established using data from the baseline inventory. A high quality emission inventory provides the information needed to determine the type and extent of controls that may be required. The inventory assists in the formulation of control and maintenance strategies.
These strategies may include regulations, permit program or an emissions trading program. Emission Inventories are important part of these strategies.
  - Industrial facilities need to know their emissions to determine specifications for control equipment
  - Regulators use inventories to calculate permit fees for normal operations and penalties for excess emissions
  - Regulators may create emission trading program to reduce emissions by setting up a banking and/or trading program. Industries may be able to bank emissions by removing polluting equipment and then using credits when applying for permits to build or modify new facilities that generate new emissions. Goal is keep net emissions below previous emission level. Emission inventories are used to calculate emission credits generated from pollution reduction activities.
A high quality emission inventory provides the information needed to determine the type and extent of controls that may be required. The inventory assists in the formulation of control and maintenance strategies.

## Slide 23: Why Do We Need Air Emission Inventories?
Fundamental Component of Air Quality Management Plan
  To measure progress/changes over time to achieve cleaner air (track trends or progress toward air quality goals)
  To determine compliance with environmental regulations
Notes: <number>
<footer>
<header>
<date/time>
Inventories are also indirect indicators of overall air quality changes. Emission trends help to determine if air quality control programs are successful. Uncertainty analyses can be used to identify areas for improvement in emission inventories.
Regulations are often established for facilities. Emission Inventories are needed to determine:
If regulations apply to a facility. The facility can use the emission inventory to evaluate the expected impact of future actions (what if emission controls are added, what if operating hours were reduced, what a different fuel source is substituted, etc.)
    Actual – best estimate of emissions over a time period; based on actual rates of production; assumes control equipment properly operating
    Potential – maximum rate of release over a time period; based on maximum throughput equipment capacity
If affected facilities comply with the regulations.
Environmental treaties such as the United Nations Framework Convention on Climate Change (UNFCC) have emission inventory reporting requirements.

## Slide 24: Why Do We Need Air Emission Inventories?
To use in Modeling
  Air quality modeling predict ambient concentration
  Exposure modeling and risk assessments predict human health and ecological risks
To help site ambient monitors
Notes: <number>
<footer>
<header>
<date/time>
One primary use of air emission inventories is modeling: Ambient air quality modeling and risk assessments. The use of inventory data as inputs of air quality modeling is crucial. If the quality and completeness of the inventory data used in the modeling is poor, the modeling results will be ineffective in determining the impact of pollution.
Modeling requires different data elements in an inventory than in inventories used to track trends. Costs increase substantially when modeling is involved due to the level of detail in the inventory that is needed for modeling.
Inventory results can be used to help in deciding where to site ambient monitors. The cost to operate ambient monitors to assess air pollution problems is much greater than preparing emission inventories. One approach used in air quality management is to first compile an emission inventory to determine sources and locations with air pollution problems. Then using the emission inventory information, you can decide where to site ambient monitors to further investigate air pollution problems.

## Slide 25: Why Do We Need Air Emission Inventories?
Global Assessments
  To understand the impact of air pollution from your country on other nations
  To determine compliance with international treaties, for example, United Nations Framework Convention on Climate Change (UNFCCC)
Notes: <number>
<footer>
<header>
<date/time>
Inventories are also indirect indicators of overall air quality changes. Emission trends help to determine if air quality control programs are successful. Uncertainty analyses can be used to identify areas for improvement in emission inventories.
Environmental treaties such as the United Nations Framework Convention on Climate Change (UNFCC) have emission inventory reporting requirements.
Growing evidence of intercontinental transport of O3, PM, Hg & POPs based on observational and modeling studies (Jacob/GRL/1999, Fiore/JGR/2002, Jaffe/AE/2002, Jacob/RPO/2003).
Intercontinental Transport of Air Pollutants (POPS, PM, O3, and Hg) can significantly impact air quality over the USA and other regions
Importance of impacts will increase in the future due to rapid growth in Asian emissions (Streets/AE/2001&2003
Impact of trans-Pacific transport is persistent thru the year; maximum impact of Asian emissions to the USA occurred in the Spring (~1.3 ug/m3 of PM2.5 and ~2.3 ppb of O3 in the West; ~0.9 ug/m3 and ~1 ppb in the East, monthly average)
Future year simulations (2030) showed that sustainable development scenarios will significantly improve air quality in both Asia and North America

## Slide 26: What Do You Use Air Emission Inventories for in Your Agency?
Describe your country’s air quality management program
  Goals
  Problems: Pollutants and sources
  Reduction strategies (regulations, voluntary reductions, trading, etc.)
  Implementation and Enforcement activities
  Evaluation of results
Describe how emission inventories are used in your air quality management program.
Describe potential uses for emission inventories in your air quality management program.
Notes: <number>
<footer>
<header>
<date/time>
Each country should spend a few minutes describing their program and the uses of EIs in their air quality management programs.
First write down description working as a group per country. Then discuss results with class.

## Slide 27: Questions or Comments?
<number>