## Slide 1
Source Category Definitions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Point, Nonpoint, and Mobile Sources are Needed for a Complete Air Toxics Inventory

## Slide 3: What Is an Air Pollutant Emission Inventory?
Inventory - current comprehensive listing by sources of air pollutant emissions in a geographic area during a specific time period
Point Sources
Mobile OnRoad Sources
Mobile NonRoad Sources
NonPoint Sources
ALM
Notes: Note similarities with criteria pollutant inventory, differences

## Slide 4: Point Sources
Major Sources: Stationary sources that have the potential to release 10 tons per year (TPY) of any one HAP or 25 TPY of a combination of HAPs
Area Sources: Stationary sources that have the potential to release less than 10/25 TPY
Emissions may be released from equipment leaks, when materials are transferred from one location to another, or during discharge through emissions stacks or vents
Notes: The definition of Major vs Area Sources is different in HAP inventories than criteria pollutant inventories. This is where the “10/25 tpy” phrase comes from that we might use (the 1990 CAA).
Point source locations are identified using either latitude/longitude or Universal Transverse Mercator (UTM) coordinates. These sources can be located by overall facility coordinates or stack-specific coordinates.
Point sources include stack emissions and fugitives (non-stacks within the facility). Fugitive emissions may be greater for some facilities than stack emissions.

## Slide 5: Point Source Considerations
Point source cutoffs/local thresholds
Major vs Area definition
MACT vs Non-MACT source categories of HAPs
Other federal regulations, state and local regs
Detail needed:
  Plant, unit, process, stack (emission release point)
  Location, stack parameters, control device info,
  Pollutants
  Operation schedule (for example, 7 days a week, 24 hr/day)
  Process description (for example, SCC)
  Facility description (for example, NAICS code)
Notes: Generally, discernible industrial facilities are easy to identify as point sources. They have easy to recognize emission points and will be required to obtain permits to be constructed and operate. Confusion can sometimes occur in defining what facilities are treated as point sources in terms of smaller sources that do not have easy to recognize smoke stacks and visible pollution (e.g., smaller VOC sources like printers). Point sources will usually be defined by an actual or potential emissions threshold and this can vary by region.
For example, in the U.S., a VOC point source in one state may be one emitting a minimum of 10 tons/yr, while in another country the same source may have a point source threshold of 50 tons/yr. This can bring up issues of emissions double counting, which will be discussed later in this section.
Don’t have to use the 10/25 tpy cutoff, but it fits in well with a Title V program.
Detail needed for a HAP point source inventory is similar to a criteria inventory, with MACT codes added.

## Slide 6: Nonpoint Sources
Called “area” sources in a criteria pollutant inventory and in some emission processing tools (SMOKE)
Include smaller point source facilities grouped by source category
  Gasoline stations
  Dry cleaners
  Car painting shops
  Small electroplaters
Notes: In many areas, nonpoint sources are defined as having emissions below some minimum threshold. They are inventoried as a source category group and not individually. It is possible for a source type to exist as both a point and nonpoint source. For example, the rotogravure graphic arts print shop on the corner could be a nonpoint source, but the rotogravure facility printing the largest magazine in the country may be significant enough to be treated as a point source. Both may be rotogravure printers, but they do not have the same emissions characteristics and are not inventoried the same way, even though both are printers.
A good point source air toxics inventory may include many smaller facilities such as gas stations, degreasers, Stage I, and dry cleaners. Point source thresholds will determine if a category is inventoried as a point or nonpoint source.

## Slide 7: Other Nonpoint Sources
Sources such as wildfires and prescribed burnings that may be more appropriately addressed by other programs rather than through regulations developed under certain air toxics provisions (section 112 or 129) in the Clean Air Act. For example, wildfires and prescribed burning are being addressed through the burning policy agreed to by the Interim Federal Wildland Policy.
Other examples
  Residential wood combustion
  Residential combustion of household waste (backyard barrel burning)
Notes: These are same as criteria inventory. Note wildfires are big source of HAPs—benzene, 1,3 butadiene.

## Slide 8: Other Nonpoint Sources
  Wildfires and Prescribed Burns
    2002 NEI – inventoried as hourly events with latitudes/longitudes
    Allows better modeling of specific events
Notes: These are same as criteria inventory. Note wildfires are big source of HAPs—benzene, 1,3 butadiene.

## Slide 9: Nonpoint Source Considerations
Includes source categories that overlap with point source inventory
HAP point source inventories often include small sources such as dry cleaners and gas stations (treated as area sources in a criteria inventory)
MACT vs non-MACT source categories of HAPs
Other federal regulations, state and local regs
Detail needed:
  County level
  SCCs, NAICS
  Shape files
Notes: Can have some MACT categories (or portions) in nonpoint inventory. Example: Graphic arts.
Will discuss how to remove overlap in Nonpoint sources

## Slide 10: Mobile Sources
Onroad - Vehicles found on roads and highways (e.g., cars, trucks, buses)
  20 HAPs
  Diesel particulate matter and diesel exhaust organic gases
Nonroad - Mobile sources not found on roads and highways
  2/4 stroke engines in lawn mowers, construction vehicles, farm machinery
ALM
  Aircraft
  Locomotives
  Commercial marine vessels

## Slide 11: Mobile Source Considerations
Contribution by source category varies geographically
Federal, state, and local regulations
Diesel PM
NMIM

## Slide 12: Onroad Mobile Sources
MOBILE 6.2 model
Vehicle types
Vehicle Miles Traveled (VMT)
Fuels used
Notes: Exhaust emissions: emissions released from the tailpipe of the vehicle
Evaporative emissions: emissions released through evaporative processes from vehicle points such as the fuel tank, fuel lines, carburetor, and crank case.

## Slide 13: Nonroad Mobile Sources
Nonroad Equipment
  NONROAD model yields criteria pollutant estimates
  Fuels used
  Activity data
  Emission factors
  Speciation profiles
Notes: Construction equipment can include tractors, bulldozers, backhoes, etc. Industrial equipment can include forklifts and other in-plant vehicles. Agricultural equipment involves tractors, harvesters, combines, etc.
Lawn and garden relates to portable equipment for private residential, commercial, and industrial activities.

## Slide 14: Aircraft
Commercial air carriers, air taxis, general aviation, helicopters, and military aircraft
FAA’s Emissions and Dispersion Modeling System (EDMS) for commercial carriers
Activity data
Emission factors
Speciation profiles
Airports in 2002 NEI as point sources
Notes: Aircraft emissions correlate with airports and can include airport support vehicles (baggage carts, aircraft pushback vehicles, auxiliary power units and aircraft refueling) as well.

## Slide 15: Locomotives
Long haul, passenger, yard, and Commuter Class II/III trains
GIS data available for long haul and passenger trains
Need local data for yard and commuter trains
Emission factors
Speciation profiles

## Slide 16: Commercial Marine Vessels
Cruise ships
Container ships
Tankers
Barges
GIS data available for underway operations
Need local data for ports
Emission factors
Speciation profiles
Notes: Vessels include both inland commercial and recreational vessels and oceanic vessels such as fishing boats, cruise ships, military ships, tug boats, private vessels, commercial marine freight/cargo vessels.

## Slide 17: Natural Sources
Natural biological and geological
phenomenon which generate
air emissions (nonanthropogenic)
Biogenic emissions:
  VOC emissions from vegetation
Geogenic emissions:
  NOx emissions from soil (denitrification)
  SOx emissions from volcanoes
  and geothermal activity
May include wind erosion, wildfires
Notes: <number>
<footer>
<header>
<date/time>
Wind erosion and wildfires may be included in either/or the nonpoint or natural source type.

## Slide 18: Indoor Sources
Outdoor Air Pollution
  Indoor air can become contaminated from numerous sources
  Indoor air can have significantly higher concentrations of air pollutants than outdoor air
  EPA currently does not regulate indoor sources of air pollutants
Notes: Not going to be addressed here.
For many years, study of air pollution focused almost entirely on outdoor air. Outbreak of Legionnaire’s disease during summer of 1976 helped refocus attention on indoor air problems. People spend 80 – 90 % of their time indoors – in homes, schools, places of work, entertainment, etc. The % of time spent indoors tends to be greatest for people who are most susceptible to risks of air pollution – elderly, very young and those who are ill.
Indoor environments are less self-cleansing. Indoor environments are often tightly sealed with constant temperatures that promote air stagnation. Airborne pollutants can reach high concentrations more quickly than outdoor pollutants and can persist for longer periods of time if the air is not properly ventilated.
Sources:
Combustion – gas appliances, heating systems, vehicle exhaust from attached garages, cooking
Building materials and furnishings – asbestos form insulation and ceiling tiles, dioxins from bleached fabrics, formaldehyde from pressed wood products
Household cleaning/maintenance products – pesticides, personal care and hobby products, cleaning products
Biological contaminants – mold, mildew, bacteria, pollen, viruses, dust mites, and animal dander
Radon – radioactive decay of radium found in many types of rocks and soils
Prevention: Ventilation, Reduce water seepage into homes, Maintenance of all appliances where combustion occurs

## Slide 19: Other Types of Sources
  There are a number of other important sources of air toxics that aren’t so easy to categorize or count
    Accidents
    Long-range transport of air pollutants
    Historical background (CCl4)
Notes: Accidents not addressed. Tracked through other EPA programs.
CCl4= carbon tetrachloride