## Slide 1: QA/QC Example: 2002 Point Sources

## Slide 2
QA/QC: Example 2002 NEI for HAPs
Initial Format & Data Integrity QC Checks
Format QC:
Is file readable?
Mandatory elements
Non-Mandatory elements
Referential integrity
Invalid codes
Range checks
Blend/Merge data records
Complete database coverage
for facilities, source categories,
pollutants, geographic area
Other Data Sources:
MACT and sec. 129 data
TRI
Industry
EGU CEM
Augment data elements
Complete data needed for emissions modeling
Stack parameters
Other data fields
Default flags
Draft NEI to public review
S/L/Ts, Industry,
EPA, public
EPA evaluates & incorporates revisions and new data
Final QC
EPA Receives S/L/T data in NIF via CDX
Final NEI
Content QC:
Emission Outliers
Duplicates
MACT Code assignment
External reviewers submit data/revisions to EPA
Content QC
QC & Augmentation of Locational Data

## Slide 3: Goals of the 2002 NEI
Stick to schedule
Use standardized format for data inputs and outputs
Consistently use best data
Improve QA/QC
    Reduce number of missing sources
    Reduce errors in geographic coordinates
    Reduce number of missing stack parameters
    Improve consistency in nonpoint sources across nation
    Improve quality of emission estimates
Reduce number of nonpoint source categories by increasing number of categories inventoried as point sources
Integrate criteria and HAP emissions where feasible

## Slide 4: QA/QC: Example 2002 NEI
Goals of QC/QA Program
  Identify and correct duplicate facility, site, and emissions data
  Identify and correct erroneous emissions data
  Verify coordinate data
  Review stack parameters
  Identify and correct format errors
Types of QC conducted by EPA
  Format QC - identify potential errors with format
  QC of Locational Data - verify facility locations
  QC of stack parameters
  Content QC - identify emission errors

## Slide 5: QA/QC: Example 2002 Format QC
QC Activities include:
  Checks data integrity (relational data base with required key fields)
  Evaluate properties of data fields
    Name
    Data type (text, numeric types)
    Length – maximum length of each field
    Mandatory fields reported
  Evaluate code values with acceptable values in code tables
  Conduct range checks
    Maximum and Minimum
Corrective Actions resulting from QC include:
  Referential integrity violations
    Remove duplicate records and records with null and zero values
    Work with agencies and tribes to correct records by creating needed records or removing records
  Code Values
    Correct invalid codes
    Assign new codes not included in code table, e.g., additional HAPs that are not included in Pollutant Code Table
  Range Checks
    Contact agencies and tribes to verify that reported value is correct,
    Correct values

## Slide 6: How Do I Augment Location Coordinates
Convert coordinates to correct units if necessary
Verify all emission release points are within 3 km of one another
Make sure coordinates are in correct county
Replace bad/missing coordinates

## Slide 7: How Do I Augment Locational Coordinates?
Replace coordinates within a facility.
  For stacks where distance between points should not be > 3km, then:
  Use average Site Latitude and Longitude calculated from valid points to replace outliers

## Slide 8: How Do I Augment Locational Coordinates?
Replace bad/missing coordinates outside of county boundary using the hierarchy below.
Use Facility Specific Data
  Average Site Latitude and Longitude calculated from valid points
Use Geocoding software
  First QA and correct address and zip codes
  Then use Geocoder
    Exact Matches
    Near - match to single street block
    Zip code +2 Zip code 5 (47% of GEOCODER matches)
    Zip code 3 - match to 3 digit zip code
    Ambig - match to one of possible multiple street segments
Use data from previous inventory
Use company website
Use maps from the web
Assign Site Release Point at County Centroid if coordinates cannot be found

## Slide 9: How Do I Augment Locational Coordinates?
3. Assign location coordinate default flags. Example from 2002 NEI.
Default Code | Description
Exact | Match is to within a unique intersection or within a single side of a single street block.
Near | Match is to a single street block but the correct placement within block is unknown.
Zip code+2 | Match to a 5-digit zip code, plus the first two digits of the 4-digit extension.
Zipcode5 | Match to a 5-digit zip code
Zipcode3 | Match to multiple 3-digit zip codes based on postal service Sectional Center Facility (SCF).
Ambig | Match is to multiple street segments
Cntycent | County centroid.
NEI Fac Table | Coordinate found in the NEI Historical Facility Table
Site-Avg. | Average of accurate coordinates of other emission release points at the same site

## Slide 10: How Do I Augment Stack Parameters?
Stack Parameters: height, diameter, temperature, velocity, and flow rate
Procedure:
  Replace missing and invalid emission release point type
  Replace missing and invalid parameters associated with fugitive emissions release points
  Replace missing, invalid, or inconsistent parameters associated with non-fugitive release points
  Assign stack parameter default flags
Notes: Volume VI of the EIIP document series address completeness checks.

## Slide 11: How Do I Augment Stack Parameters?
  Replace missing and invalid emission release point type
    Emission Release Point Types:
      Fugitive
      Non-Fugitive (stack):
        Vertical, Horizontal, Goose Neck,
        Vertical with Rain Cap, Downward Facing vent
    Replace invalid emission release point types based on source category
      Fugitive
      Non-fugitive
    Proceed to Step 2 if Emission Release Point Type is fugitive and to Step 3 if Emission Release Point Type is non-fugitive

## Slide 12: How Do I Augment Stack Parameters?
Replace missing and invalid parameters associated with fugitive emissions release points
  If Stack Height is between 0.1 and 100 ft, replace remaining parameters with defaults. Proceed to Step 4.
  If Height is invalid, replace all parameters with defaults. Proceed to Step 4
  Non-Fugitive Stack Parameter Defaults:
      Height: 10 ft
      Temperature: 72 ˚F
      Diameter: 0.003 ft
      Velocity: 0.0003 ft/sec
      Flow: 0 ft3/sec

## Slide 13: How Do I Augment Stack Parameters?
3. Replace missing, invalid, or inconsistent parameters associated with non-fugitive release points
Compare parameters to the following min/max values:
Height: 0.1 – 1200 ft
Temperature*: 50 – 1800 ˚F, Verify T is greater than 250 ˚F for incinerators
Diameter: 0.1 – 50 ft
Velocity: 0.1 – 100 ft/sec
B. Determine if out of range value is acceptable for source category.
C. If all parameters are acceptable, proceed to Step D. If any parameter is missing or out of range, proceed to Step E.

## Slide 14: How Do I Augment Stack Parameters?
3. Replace missing, invalid, or inconsistent parameters associated with non-fugitive release points
D. Evaluate internal consistency between parameters
  Stack Height < Stack Diameter.
    If Stack Height > Stack Diameter, replace all 5 parameters. Proceed to Step E.
    If Stack Diameter< Stack Height, evaluate Flow Rate Consistency.
  Reported Flow Rate and Calculated Flow Rate are within 10% of each other
    Flow rate =((Pi)*(Diameter/2))2 *Velocity
  If internal consistency is met, process is complete. If internal consistency is not met, proceed to Step E.

## Slide 15: How Do I Augment Stack Parameters?
3. Replace missing, invalid, or inconsistent parameters associated with non-fugitive release points
E. Replace missing, invalid or inconsistent parameters using following hierarchy. Proceed to Step 4.
  Calculated flow rate or velocity.
  SCC default unless SCC is 39999999
  MACT Code default
  SIC Code default
  National default
Height: 10 ft
Temperature: 72 ˚F
Diameter: 1 ft
Velocity: 15 ft/sec
Flow: 12 ft3/sec

## Slide 16: How Do I Augment Stack Parameters?
Assign stack parameter default flags to indicate how stack parameters have been defaulted in the inventory. For example:
  0 = Original value (not a default)
  1 = SCC default
  2 = SIC Code default
  3 = National default
  4 = Calculated value
  5 = MACT Code default

## Slide 17: How Do I Identify and Fill Emission Data Gaps?
Perform additional searches of databases to identify appropriate surrogate data
Use the existing inventories to spatially allocate emissions
Extrapolate emissions from other geographic areas
Project emissions data from past inventories within the same geographic area. Includes both future growth and control.
    Growth: Expected growth in an geographic region by industry sector
    Control strategy: Expected impact of modified or additional control regulations
Notes: Data gaps may be the result of:
-Pollutants unaccounted for due to lack of credible EF
-Facilities that are missing or unaccounted for due to incomplete source lists
-Source categories that have not been considered due to lack of credible EF or activity data
You can check existing inventories and permit files by source category

## Slide 18: How Do I Augment Emissions for Pollutants?
How do I augment for individual compounds when a compound group is reported?
Pollutants are often not speciated in original data submitted to agency. Examples include: PM2.5, PM coarse and fine, metals such as mercury and chromium
Speciation methodology exists for some pollutant groups.
  Mercury speciation factors
  Chromium speciation factors for hexavalent and trivalent chromium
  EPA NEI Data Augmentation Point Source Report
  SPECIATE for PM coarse and fine

## Slide 19: QA/QC: Example Content QC
QC Activities:
Identify duplicate emissions
  Identify facilities having different IDs, but identical latitude and longitude
    Similar names – missing coordinate data, addresses, etc.
    Different names – change in ownership/name, use of subsidiary names, use of abbreviated names, etc.
  List top emitters of each pollutant
    Identify facilities with same reported emissions of each pollutant
County State | NTI Unique Facility ID | Facility Name | MACT Code | SIC Code | HAP | Emissions | Data Source
Person NC | NTI37037 | Progress Energy | 1808-1 – Utility Coal | 4911 | Mercury | 0.6 | MACT
Person NC | NTINC0592 | Roxboro CP&L | 1808-1 – Utility Coal | 4911 | Mercury | 0.6 | State
Notes: Example: Same facility in inventory under different names

## Slide 20: QA/QC: Example Content QC
Corrective Actions
Correct Duplicate Facilities and Emissions
  Evaluate pollutant emissions at potential duplicate facilities
  If all pollutants are duplicated, delete one facility
  If only some pollutants are duplicated, delete only emission records for duplicated pollutants
County State | NTI Unique Facility ID | Facility Name | MACT Code | SIC Code | HAP | Data Source | Resolution
Person NC | NTI37037 | Progress Energy | 1808-1 Utility Coal | 4911 | Lead, Mercury, Nickel | MACT | Delete Lead. Merge under one Unique Facility ID
Person NC | NTINC0592 | Roxboro CP&L |  | 4911 | Lead, Mercury, POM | State | Delete Mercury, Merge under one Unique Facility ID

## Slide 21: QA/QC: Example Content QC
Identify Outliers and Missing Emissions
  Significant changes between 96 and 99 emissions by facility, category, county, and state
  Significant variation (high std deviation) within 99 draft data for facilities within source categories
  Individual facility checks
    Identify top emitters for each pollutant nationwide
    Rank each facility based on emissions nationwide
    List top emitters for each pollutant/source category combination
Correct Outliers
  Investigate outliers by contacting organizations who provided the data
  Make corrections to emissions
  Add missing facilities and source categories

## Slide 22: QA/QC: Example Content QC
Example Outlier QC:
Pollutant Name: Mercury
# Facilities: 24660
99 Point Source Emissions (tpy): 5.35E+06
96 Point Source Emissions (tpy): 124
Max Site %: 99.9
Maximum Emissions (tpy): 5.35E+06
Minimum Emissions (tpy): 1.18E-012
Standard Deviation: 3.4E+04
Range: 5.35E+06
Maximum Emitter: Transamerican Waste Central Landfill, Inc.
NTI Facility ID: NTIMS1091185 (State data)