## Slide 1
Fires Emission Inventory
Development
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Types of Fires
  Wildfires
  Prescribed burns
  Ag field burning
  Slash burning
Notes: These are same as criteria inventory. Note wildfires are big source of HAPs—benzene, 1,3 butadiene.

## Slide 3: Pollutants
Primarily particulate matter (PM10, PM2.5) emissions that relate to health & visibility concerns
Other pollutants are also emitted:
  CO
  Carbon dioxide (CO2)
  NOx
  SOx
  VOCs
  HAPs
  Methane (CH4)
  NH3
Notes: <number>
<footer>
<header>
<date/time>
South Africa’s woodland resources cover close to one third of the total land area and include a great number of woodland types, attributable to the diversity and geographical range of this biome.
Forest types include dry bushveld areas dominated by hearty acacia species to commercial eucalyptus forests and community wattle groves located at higher elevations.
Fire is a natural and cyclical phenomenon in the woodlands of South Africa. It is also a major source of a number of criteria, greenhouse gases, and hazardous air pollutants.

## Slide 4: 2002 NEI Methodology
  Wildfires and Prescribed Burns
    2002 NEI – inventoried as hourly events with latitudes/longitudes
    Allows better modeling of specific events
Notes: These are same as criteria inventory. Note wildfires are big source of HAPs—benzene, 1,3 butadiene.

## Slide 5: Fires Source Data Elements
Fire Identification
  Name and ID – e.g., NC-CC- 221-1; Jordan Lake Forest Controlled Burn
  Land Manager
  Location Description
  Event classification – wildfire, prescribed burn,
  ag burning, etc.
  Reoccurrence – Has a fire previously occurred
  at this location? – e.g. ag burning
  Ignition Source – How was the fire ignited?
  Acreage Burned
  Date Range – Start and End dates
Notes: Source Category Description:
Source Classification Code (SCC) define air pollution emissions processes in terms of process equipment and material throughput (e.g., dry bottom, bituminous coal boiler) SCCs are similar to European SNAP (Selected Nomenclature for Air Pollution) codes. More information on SNAP codes and their use in the emission inventory process can be found in the document EMEP/CORINAIR Emission Inventory Guidebook – 3rd Edition (http://reports.eea.eu.int/EMEPCORINAIR3/en)
MACT Code
North America Industry Classification System (NAICS Code)
Standard Industrial Classification (SIC) Code – optional, replace with NAICS

## Slide 6: Fires Source Data Elements
Daily Operating Parameters
  Date
  Event Type – wildfire, prescribed burn, ag burning, etc.
  SCC
  Source Location
    Country, State, County, Tribe, Province, City, District, Grid Cell,
    Latitude and Longitude
  Acreage Burned – 240 acres
  Burn Rate – rate at which fire burned for date (10 acres/hr)
  Perimeter Shape File – perimeter of fire if reporting geospatial shape file
  % Perimeter Affected – percent of perimeter affected by the fire, e.g., 90%
Notes: Source Category Description:
Source Classification Code (SCC) define air pollution emissions processes in terms of process equipment and material throughput (e.g., dry bottom, bituminous coal boiler) SCCs are similar to European SNAP (Selected Nomenclature for Air Pollution) codes. More information on SNAP codes and their use in the emission inventory process can be found in the document EMEP/CORINAIR Emission Inventory Guidebook – 3rd Edition (http://reports.eea.eu.int/EMEPCORINAIR3/en)
MACT Code
North America Industry Classification System (NAICS Code)
Standard Industrial Classification (SIC) Code – optional, replace with NAICS

## Slide 7: Fires Source Data Elements
Daily Operating Parameters
  Fire Type
    Flaming
    Smoldering
  Fuel Type – type of vegetation burned, e.g., field crop, pine forest, etc.
  Burn Type – predominate configuration of fuel burned, e.g., pile, windrow, broadcast, etc.
  Fuel Loading – fuel per acre available for consumption
  % Fuel Consumed - % fuel consumed in a geographic area
  10 Hour Fuel Moisture – e.g., 5 %
  Heat Release – amount of heat in BTUs per day for the fire
Notes: Source Category Description:
Source Classification Code (SCC) define air pollution emissions processes in terms of process equipment and material throughput (e.g., dry bottom, bituminous coal boiler) SCCs are similar to European SNAP (Selected Nomenclature for Air Pollution) codes. More information on SNAP codes and their use in the emission inventory process can be found in the document EMEP/CORINAIR Emission Inventory Guidebook – 3rd Edition (http://reports.eea.eu.int/EMEPCORINAIR3/en)
MACT Code
North America Industry Classification System (NAICS Code)
Standard Industrial Classification (SIC) Code – optional, replace with NAICS

## Slide 8: Fires Source Data Elements
Emissions By Pollutant Species (CAS number)
  Pollutant
  Amount (tons/year, kg/day, g/second)
  Estimation calculation methods
    Include emission factor if this method is used
    Source of emissions factor, if this method is used
  Emissions uncertainty
Notes: Source Category Description:
Source Classification Code (SCC) define air pollution emissions processes in terms of process equipment and material throughput (e.g., dry bottom, bituminous coal boiler) SCCs are similar to European SNAP (Selected Nomenclature for Air Pollution) codes. More information on SNAP codes and their use in the emission inventory process can be found in the document EMEP/CORINAIR Emission Inventory Guidebook – 3rd Edition (http://reports.eea.eu.int/EMEPCORINAIR3/en)
MACT Code
North America Industry Classification System (NAICS Code)
Standard Industrial Classification (SIC) Code – optional, replace with NAICS

## Slide 9: Example Wildfire Emissions Calculation
Inputs needed for emission estimates
  Fuel type
  Fuel loading (available fuel burned, not total fuel)
  Hectares or tons burned
  Emission rate (kg/Mg, fuel specific)
Typically only annual summaries will be available
Emissions = Tons Burned x Emission Rate
Notes: <number>
<footer>
<header>
<date/time>
South Africa’s woodland resources cover close to one third of the total land area and include a great number of woodland types, attributable to the diversity and geographical range of this biome.
Forest types include dry bushveld areas dominated by hearty acacia species to commercial eucalyptus forests and community wattle groves located at higher elevations.
Fire is a natural and cyclical phenomenon in the woodlands of South Africa. It is also a major source of a number of criteria, greenhouse gases, and hazardous air pollutants.

## Slide 10: Wildfire PM10 Emissions Estimation Example
Notes: <number>
<footer>
<header>
<date/time>
This is a simple example to compute emissions for two different wildfires. One fire is in a chaparral forest ( which is roughly similar to South Africa’s bushveld), another in a conifer forest ( similar to forests of the Drakensburgs). To get emissions, just multiply the fuel loading by the acres burned and the emission factor.
Unfortunately, it is often difficult to obtain detailed burn data for individual fires. Typically, the most accessible wildfire data is summarized on an annual regional basis. In this case, more generic fuel loadings and emission factors will need to be used for computing the wildfire emissions. The references on the following slide provide some options for how to do this.

## Slide 11: Questions or Comments?
<number>