## Slide 1: TRI Data Quality Activities -- An Overview
Velu Senthil
Toxics Release Inventory Program

## Slide 2: Best Readily Available Information
Use readily available data (including monitoring data) collected pursuant to other provisions of law
Where such data are not readily available, use reasonable estimates
If available data known to be non-representative, facilities must make reasonable estimates using the best readily available information
Base reasonable estimates using published emission factors, material balance calculations, or engineering calculations
Do not use emission factors or calculations if more accurate data available
TRI does not require additional monitoring or measurement beyond what other laws/regulations require or are part of routine plant operations
What is readily available can change over time (e.g., new information)
Recommendation: Carefully document decision making used (e.g., assumptions & calculations)
Notes: Use readily available data (including monitoring data) collected pursuant to other provisions of law, or, where such data are not readily available, "reasonable estimates" of the amounts involved.
If available data (including monitoring data) are known to be non-representative, facilities must make reasonable estimates using the best readily available information.
Reasonable estimates of the amounts released should be made using published emission factors, material balance calculations, or engineering calculations.
You may not use emission factors or calculations to estimate releases if more accurate data are available.
No additional monitoring or measurement beyond that required under other provisions of law or regulation or as part of routine plant operations is required for purpose of completing Form R

## Slide 3: How Does EPA Help to Ensure the Quality of TRI Data?
  TRI data quality efforts – year-around
  Guidance, outreach, training, assistance
  TRI-MEweb, Data Processing Center
  Electronic Facility data profiles
  Data quality calls
  Enforcement

## Slide 4
Data Flow
Data Quality
CDX - Central Data Exchange DQ - Data Quality DPC - Data Processing Center NA - National Analysis TRI - Toxics Release Inventory TRI-MEweb – Toxics Release Inventory Made Easy Web
National Analysis Release
Ad Hoc DQ calls, enforcement
NA DQ calls
TRI-MEweb & DPC verify reports
Guidance, outreach, training, & assistance
Interim Data Release
EPA Receives Reports
Facility makes threshold determination and files TRI reports
TRI Reporting Data Flow and Data Quality Activities

## Slide 5: TRI Guidance
  Guidance
    General
      Reporting Forms and Instructions
    Chemical Specific
    Industry Specific
    Questions & answers
    Guide Me

## Slide 6: Training, Assistance and Outreach
  Online training
    Basic
    Advanced
  Classroom training
    Some regions
    Private parties
  TRI Assistance
    Call center
    Regional and HQ staff

## Slide 7: TRI ME web, TRI DPC, eFDP
  TRI ME web
  TRI DPC
  eFDP

## Slide 8: Why Data Quality Calls?
Conduct Data Quality Calls bi-annually – Summer & Winter
  National Analysis Data Quality Calls in Summer: focused on National Analysis
  Ad Hoc Data Quality Calls in Winter: focused on specific issues
Benefits of Data Quality Calls
  Assures higher-quality National Analysis dataset
  Delve directly into specific data quality issues
  Identify enhancements for TRI-MEweb
  Compare TRI data to other EPA datasets

## Slide 9: Analyses for Data Quality Calls
Engineering Analysis
  Industry-Specific
  Chemical-Specific
Increasers / Decreasers Analysis
Other Data Quality Issues
  Persistent Bioaccumulative Toxic (PBT) Chemicals
  HAPs, Carcinogens, RSEI
  TRI-MEweb Certification Issues, P2 issues
Comparison of TRI Data with Other EPA & Non-EPA Data
  National Emissions Inventory (NEI)
  Discharge Monitoring Reports (DMR)
  Chemical Data Reports (CDR)
  Biennial Reporting System (BRS)
  Risk Management Program (RMP)
  Tier II Reports

## Slide 10: NEI Data
Office of Air and Radiation (OAR) releases National Emissions Inventory (NEI) data once every 3 years
  Hazardous air pollutants (HAPs) from industrial facilities
  Use data from states, TRI and facilities’ test data
  Most of the HAPs are also listed on TRI chemical list
Hypothesis: Certain facilities that report to NEI are also expected to report to TRI
  Many TRI sectors are also covered in NEI
  TRI listed HAPs

## Slide 11: Comparison of NEI-TRI Air Releases
Downloaded NEI data from Emissions Inventory System (EIA) Portal
Adjusted NEI and TRI CAS numbers
Combined EIS-TRI crosswalk table with updated information
Identified facilities with significant variations of air release values between TRI and NEI

## Slide 12: CDR Data
Office of Chemical Safety and Pollution Prevention (OCSPP) collects chemical data reports (CDR) from manufacturing facilities
  Manufacturing volumes, number of employees and other information
  5015 individually listed chemicals on TSCA Inventory
  Approximately 770 chemicals reported to CDR
  Overlaps with 271 TRI chemicals and chemical categories
Hypothesis: Certain facilities that report to CDR are expected to report to TRI
  Chemical manufacturing industry sectors
  TRI listed chemicals
  Exceeds employee threshold

## Slide 13: DMR Data
Office of Waste Management (OWM) issues NPDES permits
Facilities submit Discharge Monitoring Reports (DMRs) to states and EPA works with states to populate that data in ICIS-NPDES
  Reporting frequency varies as specified in permits
DMR tool pulls information from NPDES database
Hypothesis: Certain facilities with NPDES permits are expected to report to TRI
  Covered industry sector
  TRI listed chemicals
  Exceeds activity threshold amounts

## Slide 14: TRI-Tier 2 Comparison-1
States maintain Tier 2 Reports
Several TRI Chemicals are reported under Tier 2 Reporting
What is Included in this Analysis?
  Approximately 25 states
Background on Tier 2 and TRI
R1: CT, MA, NH, VT, ME, & RI
R2: NJ, & NY
R3: VA
R4: AL, FL, GA, MS, NC, SC, & TN
R5: MI, MN, & WI
R6: AR, & TX
R7: IA, & NE
R8: ND, MT, & UT
R9: AZ, & NV
R10: ID & WA

## Slide 15: TRI-Tier2 Comparison-2
Most States do not give access to their Tier 2 Reports
Hypothesis: Certain facilities that report Tier 2 Reports are expected to report directly to TRI (under section 313 of EPCRA)
  Manufacturing industry sectors
  TRI listed chemicals
  Exceeds employee threshold

## Slide 16: TRI-Tier 2 Comparison-3
Downloaded Tier 2 data from E-Plan, individual states and regional Tier 2 coordinators
Confirmed chemical identity between Tier 2 and TRI chemicals using Chemical Abstracts Service (CAS) numbers
Obtained NAICS and number of Employees for Tier 2 facilities
Matched Tier 2 facilities with FRS and TRI database
Identified possible TRI non-reporters and never-reporters
Double-checked facilities’ operational status
Analytical Approach

## Slide 17: TRI-RMP Comparison
Hypothesis: Certain facilities that report RMP Reports are expected to report directly to TRI (under section 313 of EPCRA)
  RMP industry sectors also be covered under TRI
  TRI listed chemicals and RMP chemicals
  Exceeds employee threshold
Quantities in-Process
Identified non-reporters and never-reporters

## Slide 18: Results and Follow Up
Results
Under-Reporters / Over-Reporters
Non-Reporters
  Chemical
  Facility
Never-Reporters
Follow Up
Data Quality Calls
Enforcement

## Slide 19: TRI Facilities Revisions – RY07-14
RY | Total Facilities | Total Facilities* | #Facilities that Revised* | Percent Revised
2007 | 23359 | 23126 | 2015 | 8.7%
2008 | 22769 | 22555 | 1864 | 8.3%
2009 | 21894 | 21698 | 2026 | 9.3%
2010 | 21737 | 21542 | 1423 | 6.6%
2011 | 21742 | 21562 | 2094 | 9.7%
2012 | 21847 | 21708 | 1178 | 5.4%
2013 | 21897 | 21772 | 1005 | 4.6%
2014 | 21783 | 21657 | 546 | 2.5%
* - These counts omitted multi-establishment facilities |  |  |  | 
Chart: TRI Facilities Revision Rate - RY07-14
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Total Facilities* | 23126 | 22555 | 21698 | 21542 | 21562 | 21708 | 21772 | 21657
#Facilities that Revised* | 2015 | 1864 | 2026 | 1423 | 2094 | 1178 | 1005 | 546
Percent Revised | 0.087131 | 0.082642 | 0.093373 | 0.066057 | 0.097115 | 0.054266 | 0.04616 | 0.025211

## Slide 20: Revisions of Facilities with New and Existing Tech Contacts – RY07 - 14
RY | Total Facilities* | #Facilities that Revised* | Percent Facilities with No New Tech Contacts that Revised | Facilities with no new Tech. Contacts* | Facilities with atleast one new Tech. Contact* | # Facilities that revised and had a new Tech. Contact* | Percent Facilities with New Tech Contacts that Revised
2007 | 23126 | 2015 | 7.5% | 16805 | 6321 | 749 | 11.8%
2008 | 22555 | 1864 | 7.6% | 16796 | 5759 | 580 | 10.1%
2009 | 21698 | 2026 | 8.8% | 17200 | 4498 | 507 | 11.3%
2010 | 21542 | 1423 | 5.9% | 17120 | 4422 | 418 | 9.5%
2011 | 21562 | 2094 | 9.2% | 16425 | 5137 | 575 | 11.2%
2012 | 21708 | 1178 | 4.9% | 16661 | 5047 | 361 | 7.2%
2013 | 21772 | 1005 | 4.0% | 16562 | 5210 | 335 | 6.4%
2014 | 21657 | 546 | 2.4% | 16589 | 5068 | 142 | 2.8%
* - These counts omitted multi-establishment facilities |  |  |  |  |  |  | 
Chart: TRI Facilities with New and Exixsting Tech Contacts Revisions - RY07-14
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Percent Facilities with No New Tech Contacts that Revised | 0.075335 | 0.076447 | 0.088314 | 0.058703 | 0.092481 | 0.049037 | 0.040454 | 0.024353
Percent Facilities with New Tech Contacts that Revised | 0.11849 | 0.10071 | 0.11272 | 0.094527 | 0.11193 | 0.071528 | 0.064299 | 0.028019

## Slide 21: Scope of TRI Program Data Quality Activities
EPA undertakes a range of data quality efforts so that EPA can assure TRI data users that published TRI information is of known quality and of sufficient quality to meet the needs of intended end uses.
1) Detection of anomalies / reporting issues
2) Investigation of potential reporting errors
3) Identification and implementation of changes that would remediate known errors and reduce the prevalence of reporting errors in the future
4) Review of the efficacy of the remediation actions
TRI Data Quality Assurance and Control Model

## Slide 22: Enforcement
Data Quality
  Over-reporting
  Under-reporting
Non-Reporters
  Facility
  Chemical(s)
Never Reporters

## Slide 23: Summary
TRI Program is committed to helping facilities submit high quality TRI data:
  Data Quality Calls
  Guidance
  TRI-MEweb
  Training
  TRI Information Center
  Outreach

## Slide 24: Contact Information
Velu Senthil: (202)-566-0749; senthil.velu@epa.gov

## Slide 25: Help us Improve!
You will receive an email with a link to a survey to review the course(s) you attend at the Emissions Inventory Training Workshop.
Please take a few moments to let us know about your experience this week.
We welcome your feedback!