## Slide 1: Updates to model algorithms and inputs for the Biogenic Emissions Inventory System (BEIS) model
Jesse Bash, Kirk Baker, George Pouliot, Donna Schwede, Tom Pierce

## Slide 2: Overview of presentation
BEIS overview
  BVOC emissions model with 193 plant species groups and support for NLCD and MODIS plant functional types
  Can be run coupled to CMAQ or offline using modeled meteorology
BEIS updates
  Updated land use
  Two major updates to canopy model
    Implemented a leaf temperature algorithm
    Dynamic two layer canopy algorithm
  Better integration with CMAQ-WRF system
    Uses WRF land surface physics and CMAQ air-surface exchange algorithms
Model simulations coupled to CMAQ with WRF meteorology
  2009 4km California domain compared to BEARPEX observations
  2011 12km continental US domain compared to monitoring network observations

## Slide 3: Biogenic Emissions Landuse Data (BELD) Processing
Input Data
FIA V5.1 data
NLCD Canopy Coverage
NLCD Land Use (US)
MODIS Land Use (Global)
Allometric Scaling
Spatial Kriging
Leaf Biomass
Above Ground Biomass
Calculate Grid Scale Emission Factor
Evaluation
BEIS 3.4 Emission Factors
Model Ready Emission Factors
r = 0.925
NMB = -20.5%
NME = 31.1%
Blackard et al. 2008
Blackard et al. (2008) Mapping U.S. forest biomass using nationwide forest inventory data and moderate resolution information, Remote Sensing of the Environment, 112:1658-1677

## Slide 4: FIA Interpolated data
County Species Allocation
Kriged Allocation

## Slide 5: Isoprene BFRS
 | NMB | NME | RMSE | Spearman ρ
MEGAN | 238% | 251% | 4.70 ppb | 0.57
BEIS | 44% | 72% | 1.44 ppb | 0.60
Updated BEIS | -16% | 59% | 1.12 ppb | 0.58
Isoprene estimates are improved with the interpolated FIA BELD data and updated BEIS canopy model

## Slide 6: MVK + MACR BFRS
Simulations with MEGAN emissions overestimate MVK + MACR
  May be capturing high SOA for the wrong reason
Simulations with updated BEIS better captures these products
 | NMB | NME | RMSE | r
MEGAN | 102% | 126% | 2.21 ppb | 0.49
BEIS | -25% | 44% | 0.66 ppb | 0.45
Updated BEIS | -21% | 53% | 0.77 ppb | 0.62

## Slide 7: CONUS evaluation results and conclusions
Species | Network | Base BEIS |  |  | Updated BEIS |  | 
 |  | NMB | NME | r | NMB | NME | r
O3 | AQS | 3% | 37% | 0.567 | 8% | 30% | 0.721
Isoprene | AQS | 19% | 103% | 0.468 | 20% | 87% | 0.549
NOX | AQS | 40% | 96% | 0.437 | 46% | 94% | 0.475
TNO3 | CASTNet | -30% | 36% | 0.788 | -23% | 32% | 0.799
TNO3 | NADP | -30% | 51% | 0.642 | -28% | 51% | 0.638
BEIS and BELD have been updated
Evaluate well against BEARPEX BVOC and network observations
Better captures Isoprene and terpene gradients from Sacramento to BFRS
Evaluate against other field campaigns
  SOAS/SENEX, DISCOVER AQ 2011, CALNEX/CARES, CABERNET
Evaluate and update BEIS emission factors
  Urban forestry surveys (particularly important in Southwest)

## Slide 8: Thanks and Questions