## Slide 1: Updates to model algorithms and inputs for the Biogenic Emissions Inventory System (BEIS) model
Jesse Bash, Kirk Baker, George Pouliot, Donna Schwede, Tom Pierce

## Slide 2: Outline
Non-methane biogenic VOC (BVOC) emissions overview
Updates to the BEIS canopy model
Updates to the Biogenics Emissions Landuse Database (BELD) input data
Evaluation against California observations and comparison to MEGAN
Conclusions
Future work for the next CMAQ release

## Slide 3: BVOC emissions
Global BVOC emissions are approximately an order of magnitude higher than anthropogenic VOC emissions
Atmospheric BVOCs are precursors of ozone and organic aerosols
Enhances the impact of anthropogenic pollutants on air quality
  Impacts the oxidative state of the atmosphere
Impacts climate through short-lived radiative forcers
BVOC emissions are sensitive to solar radiation, temperature, drought, phenology, etc.
  Sensitive to climate change
Parameterization of emissions remain uncertain

## Slide 4: Updates to BEIS Canopy Model
Two major updates to canopy model completed
  Implemented a leaf temperature algorithm
    Previously used the 2 m ambient air temperature
    Measured emissions factors based on leaf temperature
  Two layer canopy algorithm
    Previously used canopy solar radiation based on non-linear PAR and isoprene relationship through a forest canopy
    Emissions are non-linear with respect to solar radiation and temperature
Updates better integrated with CMAQ-WRF system
  Uses WRF land surface physics and CMAQ air-surface exchange algorithms
  Still working on dynamic LAI (phenology) and plant stress induced emissions

## Slide 5: Updates to BEIS Canopy Model
Leaf temperature model energy balance approximated
  Using WRF surface fluxes and CMAQ resistances
  Parameterizes radiative and convective heat exchange
  Estimated for a sun and shade layers of the canopy
Compares well against Duke Forest observations
Similar performance as MEGAN’s iterative multilayer canopy model

## Slide 6: Updates to BEIS Canopy Model
Leaf temperature model energy balance approximated
  Using WRF surface fluxes and CMAQ resistances
  Parameterizes radiative and convective heat exchange
  Estimated for a sun and shade layers of the canopy
Compares well against Duke Forest observations
Similar performance as MEGAN’s iterative multilayer canopy model
 | Mean (K) | Mean Bias (K) | Mean Error (K) | RMSE | R
Obs | 302.6 | - | - | - | 1
MEGAN | 304.1 | 1.5 | 1.7 | 2.0 | 0.99
BEIS | 300.9 | -1.7 | 2.9 | 3.6 | 0.94
Updated BEIS | 304.2 | 1.6 | 1.8 | 2.2 | 0.98
*One degree increase in temperature at 300 K results in a 12.9% increase in
isoprene emissions

## Slide 7: Updates to BEIS Canopy Model
Two layer canopy model
  A sunlit and shaded layers of the canopy are modeled
  The layers change with solar zenith angle and light intensity
  Both direct and diffuse solar radiation is modeled
  Leaf temperatures and incoming solar radiation for each layer are estimated
  Emissions are estimated for each layer and summed for total canopy emissions
Sunlit leaves behave similarly to the upper layers of the MEGAN model
Temperature in the shade layer is less variable than in the lower layers in MEGAN
  MEGAN algorithms appear to be unstable in the lower canopy but have little impact on emissions

## Slide 8: BEIS Canopy Model Summary
A sun/shade layer canopy model closely integrated with WRF and CMAQ surface flux processes has been developed
  Negligible impact on run time due to analytical approximations of leaf temperatures
Conceptually similar to the MEGAN canopy model
  Sensitive to incoming solar radiation and leaf area index
  Similar leaf temperature results
Better matches the assumptions used to derive BVOC emission factors
  Published emissions factors are based on leaf temperatures
Results in approximately an 18% increase in isoprene emissions

## Slide 9: Revised BELD input data
Initial goal was to harmonize CMAQ/WRF land use data
  CMAQ/WRF now using 2001-2006 National Land Cover Dataset (NLCD) and MODIS data
Required combining multiple datasets
  2001 & 2006 NLCD and MODIS data for land use categories and canopy coverage
  2002-2013 Forest inventory and analysis (FIA) tree species data
  2002 & 2007 USDA census of agriculture data for cropping data
Compared county level versus interpolated vegetation species fractions
  Both allocated to land use by NLCD canopy coverage fraction

## Slide 10: FIA Interpolated data
Estimated species specific foliar biomass from FIA measurements
Biomass estimates kriged to NLCD forest land use categories
  Latitude, longitude, elevation, and NLCD land use type was used
  All FIA sample plots were within 75 km of one another ~250,000 plots in the CONUS
NLCD land use data criteria was applied to FIA survey data
  Tree = tree greater than 5 m tall
  Forest = greater than 20% canopy coverage
  Deciduous forest = more than 75% foliage shed in winter
  Evergreen forest = more than 75% of foliage retained in winter

## Slide 11: FIA Interpolated data
Error due degradation of the location tested
  x and y location adjusted by random (mean = 0, s.d. = 1 km)
  Less than approximately 1 % difference or 4 or 12 km grid resolution
Qualitative comparison against published biomass data looks promising – quantitative analysis in progress

## Slide 12: County level vegetation species
FIA location data is degraded to protect privacy of land owners
  Location data is approximately ± 1 km accurate
  County code tag is correct
Aggregated FIA county level vegetation species fraction
  Based on above ground biomass

## Slide 13: Model Simulations
2009 Simulations of the BEARPEX field campaign
34 layer 4 km gird resolution WRF simulations
CMAQ 5.0.1 with original BEIS, updated BEIS and BELD, and MEGAN
  Incremental simulations were done but will not be presented here
Quantitatively evaluated against BEARPEX observations at Blodgett Forest Research Station (BFRS)
Qualitatively evaluated (not pared in time) against CARES observations at Sacramento, CA and Cool, Ca
Evaluated against AQS and IMPROVE observations

## Slide 14: Why Central CA?
Large gradient in isoprene from Sacramento to BFRS
Large gradient in vegetation type and biomass
Cool and BRFS are in the same county
  Evaluate the county level FIA aggregation

## Slide 15: Isoprene

## Slide 16: Isoprene BFRS
 | NMB | NME | RMSE | Spearman ρ
MEGAN | 238% | 251% | 4.70 ppb | 0.57
BEIS | 44% | 72% | 1.44 ppb | 0.60
Updated BEIS | -7% | 54% | 1.00 ppb | 0.55
Isoprene estimates are improved with the interpolated FIA BELD data and updated BEIS canopy model

## Slide 17: Isoprene CARES
BEIS does not capture isoprene gradient
MEGAN overestimates but captures gradient
Updated BEIS captures the gradient and better captures the magnitude

## Slide 18: Terpenes

## Slide 19: Terpene BFRS
 | NMB | NME | RMSE | Spearman ρ
MEGAN | -50% | 57% | 0.58 ppb | 0.50
BEIS | 3% | 71% | 0.69 ppb | 0.35
Updated BEIS | -10% | 67% | 0.65 ppb | 0.35
Error in terpene estimates are reduced in the updated BEIS simulation however the bias also increased

## Slide 20: Terpene CARES
BEIS and MEGAN do not capture terpene gradient
Updated BIES simulations captures the gradient and better captures the magnitude

## Slide 21: Methanol

## Slide 22: Methanol BFRS
 | NMB | NME | RMSE | Spearman ρ
MEGAN | -78% | 78% | 10.85 ppb | 0.40
BEIS | -83% | 83% | 11.25 ppb | 0.54
Updated BEIS | -80% | 80% | 10.98 ppb | 0.49
All three model simulations underestimated methanol emissions at BFRS

## Slide 23: Methanol CARES
Cool-BFRS methanol gradient not captured
  Sacramento did not have valid observations
All models underestimate observed methanol

## Slide 24: Sesquiterpenes

## Slide 25: Sesquiterpenes BFRS
 | NMB | NME | RMSE | Spearman ρ
MEGAN | 287% | 293% | 0.22 ppb | 0.33
BEIS | -17% | 65% | 0.05 ppb | 0.38
Updated BEIS | -31% | 66% | 0.05 ppb | 0.37
MEGAN results in overestimates
Updated BEIS increases the model bias but does not increase the model error much

## Slide 26: CA evaluation results
Updated BEIS simulations better capture the isoprene and terpene gradients observed from Sacramento to BFRS and concentrations at BFRS
None of the emission models evaluated well against methanol observations
MEGAN simulations overestimated observed isoprene and sesquiterpenes by more than 200%
Updated BEIS simulations generally had lower model error but also had increases in bias in terpene and sesquiterpene estimates
  Will return to this at the end of the presentation

## Slide 27: CA Ozone
Updates to BEIS Canopy model and land use data improve modeled O3 performance at AQS sites in the domain
 | NMB | NME | RMSE | r
MEGAN | 19.6% | 30.8% | 14.4 ppb | 0.78
BEIS | 17.6% | 29.2% | 13.6 ppb | 0.79
Updated BEIS | 17.3% | 28.9% | 13.4 ppb | 0.79

## Slide 28: CA Aerosols
Updated BEIS simulations improved total aerosol estimates
MEGAN simulations have lowest bias and error
  Due to organic PM
  Despite poor BVOC performance
 | NMB | NME | RMSE | r
MEGAN | -15.1% | 45.5% | 4.3 ug m-3 | 0.76
BEIS | -40.1% | 57.0% | 5.1 ug m-3 | 0.78
Updated BEIS | -37.6% | 51.9% | 4.5 ug m-3 | 0.79

## Slide 29: Organic Aerosols

## Slide 30: Organic Aerosols
Differences between MEGAN and BEIS
  Driven by oligomers and sesquiterpenes
Sesquiterpenes are higher than BEARPEX/CARES observations in MEGAN
Oligomers composed of oxidized isoprene products

## Slide 31: MVK + MACR BFRS
Simulations with MEGAN emissions overestimate MVK + MACR
  May be capturing high SOA for the wrong reason
Simulations with updated BEIS better captures these products
 | NMB | NME | RMSE | r
MEGAN | 102% | 126% | 2.21 ppb | 0.49
BEIS | -25% | 44% | 0.66 ppb | 0.45
Updated BEIS | -14% | 49% | 0.77 ppb | 0.54

## Slide 32: MVK + MACR CARES
Modeled gradients are flat from COOL to BFRS
Updated BIES simulations captures the observed magnitude best at Cool

## Slide 33: Impact on atmospheric chemistry
Changes in BVOC emissions result in changes in OH and HO2
This cascades through the model as changes in NOx, SOx and aerosols

## Slide 34: Impacts oxidized species
Updated BEIS resulted in increase in NO3 aerosol at IMPROVE sites
  Reduces bias and error over BEIS and MEGAN results
  Increase in ambient HNO3 concentrations
Improves model O3 evaluation
 | NMB | NME | RMSE | Spearman ρ
MEGAN | -76% | 85% | 0.42 ug m-3 | 0.78
BEIS | -74% | 87% | 0.43 ug m-3 | 0.79
Updated BEIS | -71% | 82% | 0.39 ug m-3 | 0.79

## Slide 35: Conclusions
The BELD data set has been updated
  2001/2006 NLCD
  FIA 5.1 survey data
  Census of agriculture data
BEIS canopy algorithms have been updated
  More consistent with CMAQ/WRF parameterization
  More consistent with measurement data and contemporary BVOC emission models
Evaluate well against BEARPEX BVOC and AQS/IMPROVE network observations
Better captures Isoprene, terpene and methanol gradients from Sacramento to BFRS

## Slide 36: Future work
Eliminate bioseasons file
  Use dynamic LAI following WRF/Meteorological model LAI
Add the impact of temperature/PAR history
Impact of BVOC emissions due to vegetative stress
Evaluate kriged biomass data against independent (satellite + in situ) estimates generated for national carbon stock estimates
Evaluate against other field campaigns
  SOAS/SENEX, DISCOVER AQ 2011, CALNEX/CARES, CABERNET
Evaluate and update BEIS emission factors

## Slide 37: Future work
BELD reports emissions factors (EF) in mass per area
  Assumes a biomass for each modeled species to scale measured EFs
Develop BEIS with leaf biomass based emission factors
  Use FIA / NLCD derived biomass for emission factors
  Will improve results at BFRS where current BEIS estimates are low
    FIA based biomass estimates are higher at BFRS

## Slide 38: Thanks and Questions

## Slide 39: Formaldehyde

## Slide 40: Formaldehyde BFRS
 | NMB | NME | RMSE | Spearman ρ
MEGAN | -50% | 54% | 3.7 ppb | 0.52
BEIS | -49% | 52% | 3.5 ppb | 0.54
Updated BEIS | -46% | 49% | 3.4 ppb | 0.54
All models underestimate observed concentrations
Updated BEIS simulation improves results

## Slide 41: Acetaldehyde

## Slide 42: Acetaldehyde BFRS
 | NMB | NME | RMSE | Spearman ρ
MEGAN | -62% | 63% | 1.26 ppb | 0.49
BEIS | -14% | 35% | 0.82 ppb | 0.60
Updated BEIS | 4% | 39% | 0.92 ppb | 0.61
MEGAN simulations underestimate observations
Updated BEIS is less biased but does have higher error

## Slide 43: OH BFRS
 | NMB | NME | RMSE | Spearman ρ
MEGAN | -79% | 81% | 74 ppq | 0.15
BEIS | -59% | 70% | 67 ppq | 0.07
Updated BEIS | -57% | 66% | 64 ppq | 0.12
Model underestimates likely a combination of model chemistry and BVOC emissions
OH observations are uncertain