## Slide 1: EPA/ORD Great Lakes Related Modeling and Measurement Research
June 2024

## Slide 2: Background
Michigan specifically requested ORD investigate inconsistencies between model predictions of O3 and ambient data over time at monitors currently exceeding the O3 NAAQS on the eastern shore of Lake Michigan
  Michigan’s concerns are not unique; many areas are having similar issues where models (CMAQ and CAMx) predict O3 levels below the NAAQS while monitored levels remain above the NAAQS
Need exists to leverage ongoing research and where needed initiate new efforts related to modeling and measurements to better understand sources and processes important for O3 formation in the Great Lakes Region

## Slide 3: Why are Models Overly Optimistic About Future O3?
Since many areas across the U.S. have a similar inconsistency between model projected O3 and measurements and this is common to both CMAQ and CAMx the main problem is most likely overly optimistic reductions in precursors emissions (NOX) from a ubiquitous source (mobile)
  EPA’s emission models for onroad and nonroad predict large year-to-year decreases in emissions; even small decreases in each county would result in substantive decreases in regional O3 that may be unrealistic
  Modest onroad emission reductions related to technology implementation and fleet turnover may be offset by increased vehicle miles traveled or increased emissions related to intermodal activity driven by changing consumer habits
  Are nonroad emissions really decreasing? As NOX emissions decrease in point source sectors the nonroad contribution to an area’s inventory is relatively substantial
We should continue to evaluate other aspects of the modeling system important for predicting O3 in the Great Lakes region: meteorology, deposition, biogenic/geogenic emissions, chemistry, etc.

## Slide 4: Emissions Changes over Time and Space
New effort using measurements (routine in-situ, satellite products, field study data) to illustrate where and how much key O3 precursors are changing over time and whether or not this is generally consistent with emission model predictions (Baker/Valin/OAQPS)
Average June NO2 Column Density (TROPOMI)
Anomaly from the 2018-2023 average for 2019, 2021, 2022, and 2023
Warm colors indicate an increase in NO2 and cool colors a decrease in NO2

## Slide 5: Ongoing ORD Efforts
Characterize local and regional sources of O3 and precursors
Looking more closely at trends in emissions, ambient (in-situ), and remotely sensed pollutants (O3, NOX, VOC) in the region (Baker/Valin/OAQPS?)
New hemispheric and finer continental scale CMAQ simulations with aerosol nitrate photolysis for 2017 to look at potential for increased regional O3 (Baker/Hogrefe/Sarwar)
Model evaluation using EPA oxidized nitrogen gas measurements at upwind CASTNET sites in that region in 2023 and 2024 (Valin/Baker)
Characterize local and regional physical processes (meteorology, deposition, chemistry) important for O3
New multi-scale application of WRF for the 2017 LMOS period (Pleim/Gilliam/Baker)
Evaluate CMAQ predicted O3 flux using field study measurements at Bondville, Illinois (Valin/Baker/Bash/Hogrefe)
Use detailed chemistry measurements from AGES+ measurement campaigns to assess local and regional ozone production with CRACMM (Pye)
Average June 2018-2023 NO2 column density (TROPOMI)
Key Local and Regional Source Areas

## Slide 6: Collaborative Projects with Groups Outside ORD
Ongoing discussions/collaborations with LADCO and Wisconsin DNR regarding PAMS enhanced monitoring; potential to expand to Michigan EGLE and NOAA Great Lakes research center (Valin)
Initiating a new collaborative effort with academic groups (Dan Horton; Northwestern and Dan Goldberg; GWU) and LADCO on fine scale (~1 km) modeling for Chicago to examine the impacts of heavy-duty trucks and intermodal facilities (Baker/Pleim)
  Leverage ORD efforts to model 2023 field studies
Collaboration with Region 7 staff looking at sources of O3 in St. Louis and springtime O3 in the central plains (Baker)
Collaboration with Environment and Climate Change Canada (ECCC) modeling sources of O3 in southern Ontario and southeast Michigan (MOOSE field study 2021) (Baker)

## Slide 7: Additional Opportunities
EPA could leverage ongoing field measurement efforts and make additional deployments of assets into the Great Lakes region to provide more data for model evaluation
  Augment efforts at CASTNET sites in the region upwind of Chicago
    ACE.406.1.4 "Characterizing regional surface ozone in north-Central US with emphasis on assisting downwind regions in nonattainment of ozone NAAQS" Valin, Lukas
  Renew previous efforts to develop a site or sites along the eastern shore of Lake Michigan
    ACE.406.1.3 “Air Quality in U.S. Megacities” Valin, Lukas
Invest more into the fine scale emissions and modeling efforts for Chicago as part of the collaboration with Northwestern/LADCO
  Application of the coupled WRF-CMAQ model and/or MPAS-CMAQ