## Slide 1: Research Needs for the Great Lakes Region & Support the CMAQ Transition from WRF to MPAS
July 2024

## Slide 2: Policy Concerns in the Great Lakes Region
Michigan specifically requested ORD investigate inconsistencies between model predictions of O3 and ambient data over time at monitors currently exceeding the O3 NAAQS on the eastern shore of Lake Michigan
  Michigan’s concerns are not unique; many areas are having similar issues where models (CMAQ and CAMx) predict O3 levels below the NAAQS while monitored levels remain above the NAAQS
  This suggests the problem is with a ubiquitous emissions sector, most likely mobile (onroad and nonroad)
  EPA’s emission models for onroad and nonroad predict large year-to-year decreases in emissions while measurements suggest NOX and VOC have not decreased in recent years
  Modest onroad emission reductions related to technology implementation and fleet turnover may be offset by increased vehicle miles traveled or increased emissions related to intermodal activity driven by changing consumer habits
Need exists to leverage ongoing research and where needed initiate new efforts related to modeling and measurements to better understand sources and processes important for O3 formation in the Great Lakes Region

## Slide 3: What are the local and regional sources of O3 and precursors?
Regional
New hemispheric and finer continental scale CMAQ simulations with aerosol nitrate photolysis for 2017 to look at potential for increased regional O3 (end of 2024)
Model evaluation using EPA oxidized nitrogen gas measurements at upwind CASTNET sites in that region in 2023 and 2024 (end of 2025)
  ACE.406.1.4 "Characterizing regional surface ozone in north-Central US with emphasis on assisting downwind regions in nonattainment of ozone NAAQS" Valin, Lukas
Collaboration with Region 7 staff looking at sources of O3 in St. Louis and springtime O3 in the central plains (ongoing)
Local
New collaborative effort with academic groups (Dan Horton; Northwestern and Dan Goldberg; GWU) and LADCO on fine scale (~1 km) modeling for Chicago to examine the impacts of heavy-duty trucks and intermodal facilities (end of 2025)
  Leverage ORD efforts to model 2023 field studies
Ongoing discussions/collaborations with LADCO and Wisconsin DNR regarding PAMS enhanced monitoring (ongoing)
Regional and Local
Looking more closely at trends in emissions, ambient (in-situ), and remotely sensed pollutants (O3, NOX, VOC) in the region (end of 2024)

## Slide 4: What local and regional physical processes (meteorology, deposition, chemistry) are important for O3?
New multi-scale application of WRF for the 2017 LMOS period (end of 2024)
Evaluate CMAQ predicted O3 flux using field study measurements at Bondville, Illinois in 2023 and 2024 (end of 2025)
Use detailed chemistry measurements from 2023 AGES+ measurement campaigns to assess local and regional ozone production with CRACMM (end of 2025/early 2026)
Collaboration with Environment and Climate Change Canada (ECCC) modeling O3 in southern Ontario and southeast Michigan (MOOSE field study 2021) (end of 2025)
Potential to do new measurements at a site along the eastern shore of Lake Michigan in collaboration with Michigan EGLE and NOAA Great Lakes research center (TBD; unfunded)
  ACE.406.1.3 “Air Quality in U.S. Megacities” Valin, Lukas

## Slide 5: CMAQ transition from WRF to MPAS
Ongoing and planned modeling and measurement efforts by ORD for the Great Lakes region provide an opportunity to evaluate the MPAS/CMAQ system and illustrate how that system might offer new opportunities to more efficiently address multiscale and multipollutant air quality problems
  Persistent high O3 in the Great Lakes region is related to multi-scale emissions sources (local to continental) and complicated by the complex meteorological interactions at land-lake interfaces
  Anticipate additional multiscale modeling needs in this region for new PM2.5 nonattainment areas
MPAS/CMAQ will be compared to multi-scale predictions from the WRF/CMAQ system, routine measurements, and special field measurements available for the region
Additional efforts specific for MPAS/CMAQ to consider how that system may afford some efficiency in modeling the many spatial scales and source/receptor areas important for capturing air pollution in the Great Lakes region