## Slide 2
Small scale nuclear reactors
  Onshore
  Offshore
Fusion

## Slide 3
The rapid expansion of data centers and AI is driving a re-evaluation of nuclear energy as a viable solution to meet soaring electricity demands. Small Modular Reactors (SMRs) have emerged as the ideal candidate due to their scalability, safety features, and ability to provide a reliable, carbon-neutral power source.
In October 2024, tech giants Amazon and Google announced significant investments in the advanced nuclear sector. Amazon partnered with Dominion Energy and X-energy to deploy up to 5 GW of small modular reactors (SMRs) by 2039, with Amazon investing $500 million in X-energy. Google signed a Master Plant Development Agreement with Kairos Power to deploy a fleet of 500 MW of advanced reactors by 2035 to power its data centers.
In 2024, 14 major global banks, including Bank of America and Morgan Stanley, pledged their support for nuclear energy during the New York Climate Week, aligning with COP28’s objective to triple nuclear capacity by 2050.
https://www.technologyreview.com/2024/10/01/1104387/2024-climate-tech-companies-kairos-power-molten-salt-nuclear-reactors/

## Slide 4: Nuclear Reactor Technology
Nuclear reactor technology is evolving rapidly, with key innovations that could significantly impact the future of energy production.
Notable developments include Molten Salt Reactors (MSRs) from companies such as Kairos Power and Terrestrial Energy, which are focused on increasing safety and efficiency, with commercial applications expected by the mid-2030s.
High-Temperature Gas Reactors (HTGRs), with China’s HTR-PM already operational, offer impressive efficiency, while US-based X-energy is advancing similar technologies.
These advanced reactors are not only well-suited to generate electricity but also provide industrial heat, aiding in decarbonization efforts and integrating seamlessly with renewable energy sources for stable power generation.

## Slide 5: Nuclear Fuel Technology
Accident Tolerant Fuels (ATFs), which offer enhanced safety features, are set to enter commercial trials, marking a major step forward in reactor safety.
High-Assay Low-Enriched Uranium (HALEU) is expected to become more readily available, providing a crucial component for the next generation of reactors.
TRISO fuel, recognized for its safety and performance, will be commercially produced, with X-energy taking the lead in its deployment.
Additionally, thorium fuels are under exploration, particularly in India, for their potential advantages in terms of waste reduction and proliferation resistance.
Efforts are also underway to advance nuclear fuel recycling technologies, with new facilities potentially coming online in the coming years.

## Slide 6: HALEU
Enrichment Level: HALEU contains 5-20% U-235, a distinction from standard low-enriched uranium (LEU), which is below 5%.
Power Density: The higher concentration of fissile material in HALEU allows for more compact reactor cores and more efficient energy generation compared to traditional LEU fuels.
Applications: HALEU is crucial for advanced and small modular reactors, enabling them to achieve high power densities, operate for longer periods, and produce less waste.

## Slide 7: HALEU
Advanced Reactor Designs: Many next-generation reactor designs, such as small modular reactors (SMRs), are optimized to use HALEU fuel for higher performance and compact designs.
Extended Fuel Cycle: The higher fuel efficiency provided by HALEU can lead to longer operational cycles, reducing the need for frequent refueling.
Waste Reduction: By increasing fuel efficiency, HALEU can contribute to a reduction in nuclear waste over time.

## Slide 8: HALEU Challenges
Supply Chain: The United States and other nations have historically relied on LEU, so a robust domestic HALEU supply chain needs to be developed.
Regulatory Frameworks: Existing nuclear fuel cycle frameworks were designed for LEU, and new regulations are needed to address the specific requirements of HALEU.
Production Costs: The enrichment process to produce HALEU is resource-intensive, and companies are developing advanced technologies like laser-based isotope separation to produce it more efficiently.

## Slide 9: TRISO
TRISO fuel is considered the world's most robust nuclear fuel because each of its TRi-structural ISOtropic particles acts as its own containment system, consisting of a uranium-based kernel enclosed by multiple layers of carbon and silicon carbide (SiC).
This design prevents the escape of radioactive fission products and allows TRISO fuel to withstand extremely high temperatures and radiation, making it virtually "meltdown proof".
TRISO fuel is used in advanced reactor types like high-temperature gas reactors, molten salt-cooled reactors, and small modular reactors.

## Slide 10: TRISO
It is not that TRISO fuel is inherently difficult to make, but rather that it is a complex and highly specialized process that is currently very expensive and difficult to execute at a large scale. The main challenges involve achieving the required extremely high quality control for billions of individual fuel particles and establishing a reliable supply chain for the necessary materials.
The supply chain for TRISO fuel is currently limited and uncertain, which increases costs and complicates scaling up production.
High-assay low-enriched uranium (HALEU): TRISO fuel often uses HALEU, which is more highly enriched than standard reactor fuel. The infrastructure for producing HALEU is still developing and faces a "chicken-and-egg" situation, where producers are hesitant to invest without a clear demand signal
Specialized equipment: The unique fluidized beds and other equipment needed for TRISO production have not yet been produced at an industrial scale, contributing to the high costs

## Slide 11: Fusion
Sept 18, 2025 Congressional hearing on fusion technology indicated that fusion electricity might provide baseload to the grid in the 2030s at the earliest; significant investment is needed maintain this timeline or to move it closer in time
While ambitious claims suggest commercial fusion power in the late 2020s or early 2030s, the scientific consensus points to widespread grid integration occurring much later, likely after 2050 or 2060.
Key milestones include the ITER project targeting net-energy operation in the mid-2030s, followed by the DEMO prototype in the 2050s.
  ITER: The international research project in France plans for net-energy-profitable operation around 2035, leading to a full-scale commercial prototype (DEMO).
  A "DEMO fusion test" refers to the tests conducted by DEMO (DEMOnstration Power Plant)-class nuclear fusion reactors, which are designed to be the next step after the ITER experiment. These tests aim to demonstrate the net production of electricity from a sustained nuclear fusion reaction, moving beyond proving the scientific feasibility of fusion to proving its commercial viability. While ITER will show net energy from fusion, DEMO will focus on creating a full power plant concept that can produce electricity for the grid.
Private companies like Commonwealth Fusion Systems (CFS) aim for pilot plants by the early 2030s
Many experts emphasize the extensive engineering and fundamental research still required for large-scale, grid-level deployment.

## Slide 12
Inventory of current onshore and offshore active small scale nuclear reactors
Where are Planned reactors?
What emissions of radionuclides are expected? Other pollutants?
Are these intended to provide energy to a specific facility or be part of the grid? How might these entering the grid impact fossil fuel emissions in the future?
  Can model changes to EGUs with CMAQ to estimate cobenefits in air pollution
  Can project changes in future emissions with GCAM
What are coal fired power plan radionuclide emissions? How do they compare to traditional nuclear power plants and new small scale facilities?
What kinds of new technology are being anticipated? Pros and cons
What about fusion?

## Slide 13
The Outer Continental Shelf Lands Act (OCSLA) is a 1953 U.S. federal law that grants the government jurisdiction over the Outer Continental Shelf (OCS) and its energy and mineral resources. The Bureau of Ocean Energy Management (BOEM) is a U.S. Department of the Interior agency that, under the authority of OCSLA, manages the OCS's energy and mineral resources, including offshore oil, gas, and wind
BOEM may have jurisdiction over offshore nuclear reactors installed on the OCS. I think BOEM and NRC may be talking about how to share jurisdiction about authorizing these activities.
If BOEM did authorize the activity, OCSLA's mandate to regulate AQ would more than likely also apply, and BOEM would probably need regs to do so.

## Slide 14
Compile energy capacity of built and planned reactors and compare with EGUs and offshore wind farms
Compile inventory of existing facilities
Where does the waste go?
Where would they likely be located? Near oil & gas facilities displacing the need for those facilities to have their own cogens? How far offshore would they realistically be placed?
How might this additional energy capacity impact fossil fuel or onshore nuclear?
Can they be modeled in GCAM?
More realistic for Hawaii and territories in oceanic areas like PR and Guam?
Show the Russian plant schematic
What kind of fuel and core?
BOEM has not heard about any for an environmental impact assessment so far
What about onshore small scalable reactors?

## Slide 15
An Offshore Floating Nuclear Power Plant (OFNP) is a nuclear power plant built in a shipyard, moored offshore, combining a nuclear reactor and floating rig
Floating nuclear power is different from traditional nuclear power plants in two ways.
First, a floating nuclear reactor generally has a smaller capacity. Instead of thousands of megawatts seen in conventional plants on shore, the small modular reactors (SMRs) of floating nuke plants are typically around 300 MW or less.
Second, the reactor is floating at sea, and thus mobile, but delivering power to shore.
the U.S. Navy has nuclear reactors on many of their vessels, but the distinction is that these vessels don’t contribute to the power grid on shore.

## Slide 16: Electrical Generation Comparison
How does the electrical generation capacity of offshore wind energy projects compare to onshore facilities?
Distribution of energy capacity for EGUs (facilities with NOX emissions > 100 tpy) compared against planned energy capacity for offshore wind projects shown at left

## Slide 17
Offshore floating nuclear power is not a new concept. The United State’s first foray into floating nukes was actually led by the U.S. Army.
Constructed in 1967, the USS Sturgis MH-1A was a 10 megawatt floating nuke plant.
It was a converted Liberty Ship that was originally intended to supply power in combat zones or remote areas. Although the vessel was never in a combat zone, it did supply power to the pumps in the locks of the Panama Canal Zone from 1968 to 1975.
The Sturgis was defueled in 1977 and is currently being decommissioned in Galveston, TX.

## Slide 18
The concept of a floating nuclear power plant was first developed in the U.S. in the 1970s. Plans for a plant to be located off the coast of New Jersey were canceled due to rising costs and environmental opposition
There are no operational offshore nuclear power plants in the U.S. at this time.
the U.S. Department of Energy funded a study into small modular reactor-based floating plants in 2022
Russia has become a leader in the 21st century with its Akademik Lomonosov. China is also actively building floating reactors
A joint project between NuScale Power and Canadian company Prodigy was announced in 2022 to develop North American floating plants. Core Power also plans mass production of floating nuclear power plants through its "Liberty programme," aiming for the mid-2030s.

## Slide 19
The first operational offshore nuclear power plant is Russia's Akademik Lomonosov, located in the Chukotka region and powering the town of Pevek.
The Akademik Lomonosov is in Pevek, Chukotka, a permanent site in the Russian Arctic. Other locations in Russia are planned for offshore oil and gas field development, including the Kola and Yamal peninsulas, Dudinka on the Taymyr Peninsula, and Vilyuchinsk on the Kamchatka Peninsula
https://lynceans.org/wp-content/uploads/2021/05/Russia-Akademik-Lomonosov-FNPP-converted.pdf