## Slide 1: “NEXUS” Multi-Pollutant Advanced Screening Tool OAP/CCD Briefing
Beth Landis, HEID/Climate, International, & Multi-Media Group
Carey Jang, AQAD/Air Quality Modeling Group
05/26/22
Data Viewer: National/Regional Level
Proximity Analysis: Community Level
1

## Slide 2: Multi-Pollutant Team Members
HEID
  Beth Landis / Kimber Scavo
  Matt Woody / Kelly Rimer
  Robin Langdon / Darryl Weatherhead
  Sara Terry
  Carrie Wheeler
  Rob Pinder
  Chris Davis
OID
  Amanda Kaufman
  James Payne
  Loren Fox
AQAD
  Carey Jang / Tyler Fox
  Jim Kelly
  Shannon Koplitz
  Joe Mangino
  Jeanette Reyes
AQPD
  Rich Damberg / Megan Brachtl
  Mia South
SPPD
  Lisa Conner
2

## Slide 3
Overview
3
Multi-Pollutant (MP) Background
NEXUS 3.0
  Overview
  Climate
  Data Inputs and Major Functions
  Briefings/Demos
  Recent Updates
  Current and Potential Uses
  EPA Regional Beta Testing Team
  Next Steps
Climate Discussion
Live Demo

## Slide 4
Support a comprehensive, MP treatment of air quality problems to effectively improve air quality and make the most efficient use of available resources
  Primary Goal - identify & evaluate local control strategies targeting emissions of O3 & PM2.5 and their precursors while at the same time reducing Air Toxics of concern for communities to maximize both health benefits and air quality improvements
MP planning has the potential to reduce the costs and increase benefits associated with air quality management (AQM)
Supports S/L/T air agencies in developing MP, risk-based AQM plans and implementing strategies that reduce air pollution emissions & improve public health
Success has been demonstrated in Detroit and SC; another project is currently underway in Louisville, KY
Tools needed to analyze MP data are either available currently or being developed in OAQPS (e.g., NEXUS)
Multi-Pollutant Background
4

## Slide 5: NEXUS: Overview
“NEXUS” is an advanced screening tool for multi-pollutant (MP) risks and EJ/Demographic analysis developed by OAQPS’s MP team
“NEXUS” integrates a suite of MP data, including emissions, monitoring, modeling, fused AQ data and health risk data for PM2.5, O3 & air toxics as well as EJ/demographic data, into one single platform to allow national and areal overlay mapping & analysis of MP ambient & risk data
“NEXUS” provides MP analysis across from national level “Phase 1” to regional (EPA region/State/CBSA) level “Phase 2”, and now down to community level “Phase 3” (Proximity analysis” in census tract-level)
We expect to use this tool in conjunction with Regions and identify areas that would potentially benefit most from MP approaches to reduce emissions (including current NA areas)
We also expect that it can have additional value-added uses across the Office for Air Toxics, Environmental Justice and other programs
The NEXUS tool will essentially provide a ‘conceptual model’ of an area’s MP issues to facilitate engagement with state/local/tribal agencies & community stakeholder groups
5

## Slide 6: NEXUS: Climate
NEXUS originally developed as an air quality planning tool; however, we recognize the importance of climate considerations in that context
Would like to incorporate EPA indices for climate that are developed and available in other tools (if resources available):
  EJSCREEN
  Justice40 Climate and Economic Justice Screening Tool
  Heat indices & stressors (OAQPS & ORD)
  Climate Related Social Vulnerability Indicators (OAP)
6
Currently includes CO2e emissions information
Also considering what types of climate indices we could develop or bring in from external sources

## Slide 7: NEXUS: Data Inputs and Major Functions
O3, PM2.5 & Air Toxics Monitoring Data
(2002-2020 & -2018)
O3, PM2.5 & Air Toxics Risk Data &
Conc. (fused AQ) Data
(2017 & 2014)
(Census tract-level)
NEI County &
Facility Emissions
(2017 & 2014)
O3 & PM2.5
Ambient/Design Value
(2012-2020)
(County-level)
Environmental Justice & Demographic Data
(from EJSCREEN)
Advance Area
Class-I Area
Tribal Area
Multi-Pollutant
Ambient and/or Risk National & Areal Mapping
Map Overlay with NAA, Advance Area, Class-I Area, or Tribal Area
Display Major Point Emissions Sites/Data
Display Monitoring Sites & Trend Data
Data Query, Search, Filter & Export
Provide Source Category Emissions
Provide Sector Emissions Summary
Proximity Screening Analysis
Include EJ/Demographic Indicators
NEXUS
7

## Slide 8
9/25/2020– AQAD & HEID
11/3/2020 – MP Team
11/4/2020 – Air Toxics Group
12/10/2020 – AQPD
1/25/2021 – OID
1/28/2021 – SPPD
2/1/2021 – Peter/SMT
4/12/2021 – HEID & AQAD
5/17/2021 – Peter/SMT
5/24/2021 – MP Team
6/29/2021 – ORD
7/12/2021– HEID & AQAD
7/19/2021 – OID
8/10/2021– OAP
8/26/2021 – OAR
8/27/2021 - OP
8/30/2021 – OEJ
8/30/2021 - Region 4/Louisville
9/7/2021 – RO Air Division Directors
9/20/2021 – OAR Demo
10/14/2021 – OP/NCEE
11/2/2021 – RO APMs
11/8/2021- RO APMs Demo
11/16/2021 – R1 (RARE) Project
11/28/2021 – AQAD All-Hands
11/23/2021 – R3 NEXUS Beta Testers
2/15/22 – AQPD (NSRG, OPG & SLPG)
2/17/22 – AT Strategy Mgmt & Mitigation Team
3/15/22 – OID (CTPG)
4/26/22 – EPA NEXUS Beta Testing Team
4/28/22 – AQAD (AAMG)
5/3/22 – HEID & AQAD
5/4/22 – Air Toxics Data Analysis Team
5/10/22 – ADVANCE Workgroup
5/26/22 - OAP/CCD
TBD – SPPD, MJOs
NEXUS/MP: Briefings and Demos
“Fascinating… phenomenal… I’m blown away!”
- Caroline Freeman (R4 ADD)
“Breathtaking… incredibly powerful… I feel like we discovered nuclear fusion!”
- Joe Goffman (OAR Acting AA)
8

## Slide 9
NEXUS: Recent Updates
9
NEXUS “2.2” (Dec. 2021)
  Updated 2017 BenMAP risk and fused concentration data for PM & O3
  Upgraded “Monitoring sites/data” module
  Developed “Proximity analysis module” prototype for MP risks and EJ screening
NEXUS “2.3” (Jan. 2022)
  Updated 2017 air toxics risk data (received in Dec. 2021)
  Upgraded “Proximity analysis module” for MP risks and EJ screening
NEXUS “2.4” (March 2022)
  Included BenMAP “Morbidity risk” data in “proximity analysis” module
  Added “Map layers” tab in “Data Viewer” module to provide map overlaying for MP risks & EJ indicators, PM2.5 & O3 NA areas, Advance areas, Tribal areas, Class I areas, etc.
NEXUS “2.5” (April 2022)
  Developed “Select Sites” functions for user-defined locations (census tracts), monitoring sites, and emissions sector group under “Proximity Analysis” module
  Consolidated “Data Query” module into “Data Viewer” module and added “Attribute Table” to view census tracts information of MP risk & EJ attributes
NEXUS “3.0” (May 2022)
  Finalized beta release package (NEXUS version 3.0) ready for downloading at: https://gaftp.epa.gov/aqmg/cjang/NEXUS/NEXUS-3.0/
  Completed NEXUS 3.0 “Quick Tutorial PPT” and “Online User’s Manual”

## Slide 10
NEXUS: Current and Potential Uses
10
OAQPS Monitoring Group exploring use of NEXUS to inform assessment of the nation’s PM2.5 monitoring network and determine if sites located in/near communities with potential EJ concerns (driven by current PM NAAQS review)
  AAMG noted that NEXUS could be useful in Regional review of their states’ Annual Monitoring Network Plans
MP Risk Priority Areas: develop a list of high MP risk areas to share with Regions and engage in potential MP area projects/efforts
  “Regional packets”— tabular and graphical data for each high MP risk area to discuss with Regions and determine which may be most ‘ripe’ for MP solutions
Advance area/Regional SIP planning efforts: develop conceptual model information consistent with EPA’s SIP modeling guidance that addresses nature of air quality within the area
  “Conceptual model” area packet—tabular and graphical data for each planning area to discuss with AQPD and/or Regions to be value added in AQ planning efforts and identify potential for MP considerations as part of these efforts.
EJ Screening for outreach purposes and to inform programs with an emphasis on Federal permitting
  Possible EPA Regional Beta tester project
Engage with EPA Beta Testing Team to define additional uses of need/value to Regions

## Slide 11
NEXUS: Beta Testing Team
11
Vision
  We envision the EPA Beta Testing Team as a group of OAR and regional office members that see the benefit of NEXUS and plan to use it on a routine basis to assist in their job duties.
  We would like feedback to help shape the direction of future tool development and ensure we are making updates and additions that are most beneficial to those Regions who are encouraging a multi-pollutant approach to air quality management.
  We would like to identify specific applications to collaborate on with Regions, e.g.:
    Select area with MP and potential EJ concerns and explore a MP approach using NEXUS.
    Support EJ screening and related analysis for Federal permit or related action.
Participants from all EPA Regions & OAQPS

## Slide 12
NEXUS: EPA Beta Testing Team Timeline
12
5/9/22 – release NEXUS 3.0 and Quick Tutorial
5/18/22 - demo NEXUS 3.0 to EPA Beta Testing Team
6/17/22 - review and provide written comments on NEXUS 3.0
6/29/22 - meet to discuss NEXUS 3.0 comments
Fall – release updated version of NEXUS incorporating comments from EPA Beta Testing Team (assuming funding available)
Fall/Winter 2022 - update NEXUS with 2018 data, when available

## Slide 13
NEXUS: EPA Beta Team Next Steps
13
EPA Beta Testing Team download, install, review, and provide comments on NEXUS 3.0 by 6/17/22
Questions to consider during review:
  What are some priority areas in your region that could benefit from the use of NEXUS to inform MP discussions regarding air quality planning and emission reduction efforts?
    Non-attainment areas, Advance areas, at-risk or overburdened communities, others?
  How do you anticipate using NEXUS, with its current capabilities, to assist with your program needs and daily work expectations?
  How do you anticipate NEXUS could be used, with its current capabilities, by others in your Region?
  What capabilities could be added to NEXUS to facilitate its use and value to your Region?
  Are you interested in NEXUS becoming a publicly available tool for our SLTs?

## Slide 14
NEXUS: OAQPS Next Steps
14
Briefings for OAQPS and OAR Management (Summer 2022)
Partner withing EPA on use of NEXUS for programmatic purposes
Pursue funding for requested updates:
  Address comments and feedback from EPA Beta Testing Team
  Include “Climate risk” indicators (as 5th metric)
  Update EJ/demographics data to be consistent with new “EJScreen 2.0” dataset
  Include top air toxic cancer risk drivers in the “proximity analysis” module
  Update to 2018 MP platform (O3, PM2.5, and Air Toxics data)
  Explore the feasibility of developing a web-based NEXUS version (similar to EJScreen)

## Slide 15
NEXUS: Climate Discussion
15
What climate indicators would be most appropriate/insightful to include in NEXUS?
  What current climate indicators are you working with and find most informative?
  What climate indicators or elements would be most beneficial to consider:
    In air quality planning efforts?
    By EPA?
    By SLTs?

## Slide 16: “NEXUS 3.0” Live Demo
16

## Slide 17: “NEXUS 3.0”Beta Release Version: Quick Tutorial
Download “NEXUS” tool: The “NEXUS 3.0” package (“NEXUS 3.1 Setup.exe” & “NEXUS 3.0 Data.exe”: run both “*.exe” files to install) can be downloaded at EPA’s new FTP site:
https://gaftp.epa.gov/aqmg/cjang/NEXUS/NEXUS-3.0/*
Note: Require software installation privilege or “Power Broker” (limited installation privilege) to install “NEXUS tool” at EPA’s PCs; Please check “This PC\Documents\My NEXUS files\data\* (\tool\*, \result\*)” to see if NEXUS tool & input dataset have been installed successfully. If feasible, please un-install previous version first to ensure a successful installation.
17
OAQPS Multi-Pollutant team, 5/25/2022

## Slide 18: NEXUS Tool: On-line User’s Manual
Click “book” icon to launch “User’s manual”
Hot link to User’s manual’s “Data Viewer” chapter (same for “Data Input” module)
18

## Slide 19: NEXUS Tool: Data Viewer Module
Select & adjust “Ambient” or “Risk” levels
“Advanced Option”: provide HAPs & species selections
Click “File” to open or save a project
Switch between 2 key modules
NEXUS project file name
Select desired ambient data (DV) year (2013-2020)
19

## Slide 20: Data Viewer: “Apply” New Selections
New selections will appear in “Slider bars” panel and map display
“Apply” new selections
“Check” boxes to add or remove “Ambient” and/or “Risk” selections
“Slider bars” allow to select & adjust “Ambient” and/or “Risk” threshold levels to display corresponding color map
20

## Slide 21: NEXUS Update: EJ/Demographics Metric and Data
EJ/Demographic metric is displayed with “green dash” for counties exceeding selected threshold
21

## Slide 22: Data Viewer: “Reset” New Selections
“Reset” new selections
default configuration
risk-based value
risk-based in %tile
risk-based in desired %tile
22

## Slide 23: Data Viewer Module: Map Layers menu
“Map Layers” menu: Provide (show/hide) map overlaps of various areas, AQ metrics and boundary lines
Click “X” to close “Map Layers” menu
23

## Slide 24: Data Viewer Module: Configure Base Map & Color
“Base Map” menu: Change boundary lines and background map (e.g., “Google Map”)
Click “color map” to change color & transparency
“Right-click” map to save map image
24

## Slide 25: Data Viewer Module: MP Risk Ranking
Click “CBSA Risk Ranking” to provide MP risk ranking by CBSA or County
Check box to include EJ/demographic index as part of CBSA ranking
25

## Slide 26: Data Viewer: “Region Selection”
Allow to select “EPA regions”, “States”, or “CBSA”
26

## Slide 27: Data Viewer: Select EPA Region/State/CBSA
Examples:
EPA Region 4
State: NC
Louisville CBSA (KY/IN)
27

## Slide 28: Data Viewer: Major Emission Sources
Click “Display Emission Sources” tab (or “right-click”) to display emission sources and launch new window
Click any “facility” to link & display source location and emitted pollutants information. Same facility emitting various pollutants can be identified with the same highlighted color.
28

## Slide 29: Data Viewer: Major Emission Sources
Allow to scroll down to CBSA-level (e.g., Durham CH CBSA ) or County-level
Durham CH CBSA
Emissions ranking by “color” of circles from red (higher) to blue (lower)
Color Legend for facilities emissions
29

## Slide 30: Data Viewer: Top “x” Emission Sources
Durham county, NC
Provide selection of Facility or Source Category
Provide selection of Facility & Source Category
30

## Slide 31: Data Viewer: “Source Category Emissions”
“Source Category Emissions” module provide five source categories, including “Point”, “Non-Point”, “On-Road”, “Non-Road”, and “Event” emissions for the selected region, CBSA, or county.
For “Non-Point”, including Resident Wood Combustion (RWC) emissions.
31

## Slide 32: Data Viewer: “Sector Emissions Summary”
“Sector Emission Summary” function allow to select major CBSAs and provides source and sector emissions summary to support “Sector Prioritization” effort
32

## Slide 33: Data Viewer: “Sector Emissions Summary”
Summary table
Emissions
Frequency & Rank
Summary plot
33

## Slide 34: NEXUS Update: “Monitoring Data/Sites”
Monitor Site/Data
Click to select monitor site & pollutant
Click to display
AQ trend at monitor site
Click menu (or right-click) to display “Monitor Sites/Data”
Use different symbol to display each pollutant’s “monitoring sites” e.g., PM2.5 (triangle), O3 (star), etc.
AQ trend
Include only those monitor sites with data since selected year
Color Legend for monitor sites
List the monitor sites by ranking the data based on selected year
34

## Slide 35: NEXUS Update: “Attribute Table” (1)
“Right-click” map to select “Display Attribute Table ” to launch “Attribute Table”
“Attribute Table” provides information of “counties” displayed. This table will display “census tract” information under “Proximity analysis” module.
35

## Slide 36: NEXUS Update: “Attribute Table” (2)
Provide “filter/search/export functions
Click to show/hide Filter settings
Click to show selected record on map
Click to output data as Excel file
Click “Reset” to clear all filter criteria
Click a “record” to link and display its location & info.
Click “+” to add filters; Click “x” to remove current filter;
Show specified records per page.
36

## Slide 37: Data Viewer: EPA Region Table Generator
“EPA Region Table Generator” provides attainment status of O3 and PM2.5 and their DVs; also allows to select any EPA region based on data updated to 2020.
37

## Slide 38: Data Viewer: Data Search & Filter
Click “+” to add filters; Click “x” to remove current filter;
Click “Output data…” to output current page records or all records
Show specified records per page.
Click the “Select by map” to get the information of counties which are displayed on “Map” module
38

## Slide 39: Data Input Module: Data Preview
Click to view data
Click to run & save project
Select a table to view if there are multiple tables in the selected data source file
Check to use filter to query data
“Transparency” & “Open-Source”:
All NEXUS input/output data files are available under:
“This PC\Documents\My NEXUS files\Data (\Result)”
Click to change input data file
39

## Slide 40
NEXUS update:
Proximity Analysis
Module
(Census tract-level)
40

## Slide 41: Two ways navigate to Proximity Analysis Module
Or double click any monitor site or facility to launch “Proximity Analysis” module.
Click any monitor site, facility or county, and then “right-click” to select “Display Proximity Analysis”.
41

## Slide 42: Proximity Analysis Module: Overlaying Map
“Set up Threshold” panel (similar to Data Viewer module) allows to identity those geographic areas exceeding the selected thresholds.
Allow to select AQ mortality or morbidity risks, AQ concentration and EJ/demographic indicators and display overlaying map.
Check/un-check to display/hide overlaying map of selected metrics
42

## Slide 43: Proximity Analysis Module: Overlaying Map
Click “Reset” button to reset all values to default (or to a specified %tile if all indicators are selected in %tile)
Provide a “toggle” choice to select “Risk %tile” or “Risk value”
43

## Slide 44: Proximity Analysis Module: Configure Color & Transparency
Click any “color tile” to configure color legend & transparency
Move “Slider bar” to select desired “Radius of analysis”
44

## Slide 45
Create “Summary Plot” and “Summary Table” for a selected census tract, monitor site or emitting facility
Summary Plot
Proximity Analysis Module: Summary Plot & Summary Table (1)
Summary Table
45

## Slide 46: Proximity Analysis Module: Summary Plot & Summary Table (2)
Summary table
Summary plot
Select one or more indicators to plot summary results for selected site(s) within radius, county/CBSA/State/EPA Region and Nation avg.
Click “Output” button to export summary table to an Excel file (*.xlsx)
Set “Radius of analysis” and threshold of air toxics to show summary results for selected site(s) within radius
List top 3 risk drivers within radius of sites
Click to select the desired scale of highlighted numbers
46

## Slide 47: Proximity Analysis Module: “Select Sites” Functions (1)
Click “Select Sites” to select one or a group of monitor sites, facilities, census tracts, or user-defined locations under “Select Sites” pop-up window
47

## Slide 48: Proximity Analysis Module: “Select Sites” Functions (2)
Click the “Create individual Sites” or “Create National Sites Table” to provide proximity analysis for individual sites
Click the “Output” button to export to an Excel file.
National & State avg. table
National table for all selected individual sites
Include only census tracts falling within the area of specified radius, with an area ratio larger than x% (10% by default)
Select all
48

## Slide 49: Proximity Analysis Module: “Select Sites” Functions (3)
1. Click to select the desired scale of highlighted numbers
2. Set max. & min. values and then click the “Rebuild” button to rebuild the color legend
4. Click “Apply” or “OK” button to apply new setting
Configure
color legend:
Check/uncheck to display/ hide highlighted colors
3. Customize the numerical range for each color legend
49

## Slide 50: Proximity Analysis Module: “Group” Summary Plot & Table
Summary plot & table for a group of census tracts, monitor sites, facilities or locations (latitude/longitude)
Summary table
Summary Plot
Select sites
①Click “Select Sites”
② Select a group of sites
③Click “Apply”
④Click “Summary Table” or “Summary Plot”
50

## Slide 51: Proximity Analysis Module: Display Site information
Click a facility or monitoring site or a census tract to show the detail information
51

## Slide 52
NEXUS 3.0
Quick Tutorial Slides
End
52