## Slide 1: “NEXUS” Multi-Pollutant Advanced Screening Tool SPPD All-Hands
Beth Landis, HEID/Climate, International, & Multi-Media Group
Carey Jang, AQAD/Air Quality Modeling Group
06/23/22
Data Viewer: National/Regional Level
Proximity Analysis: Community Level
1

## Slide 2: Multi-Pollutant Team Members
HEID
  Beth Landis / Kimber Scavo
  Matt Woody / Kelly Rimer
  Robin Langdon / Darryl Weatherhead
  Sara Terry
  Carrie Wheeler
  Rob Pinder
  Chris Davis
OID
  Amanda Kaufman
  James Payne
  Loren Fox
AQAD
  Carey Jang / Tyler Fox
  Jim Kelly
  Shannon Koplitz
  Joe Mangino
  Jeanette Reyes
AQPD
  Rich Damberg / Megan Brachtl
  Mia South
SPPD
  Lisa Conner
2

## Slide 3: NEXUS: Overview
“NEXUS” is an advanced screening tool for multi-pollutant (MP) risks and EJ/Demographic analysis developed by OAQPS’s MP team
“NEXUS” integrates a suite of MP data, including emissions, monitoring, modeling, fused AQ data and health risk data for PM2.5, O3 & air toxics as well as EJ/demographic data, into one single platform to allow national and areal overlay mapping & analysis of MP ambient & risk data
“NEXUS” provides MP analysis across from national level “Phase 1” to regional (EPA region/State/CBSA) level “Phase 2”, and now down to community level “Phase 3” (Proximity analysis” in census tract-level)
We expect to use this tool in conjunction with Regions and identify areas that would potentially benefit most from MP approaches to reduce emissions (including current NA areas)
We also expect that it can have additional value-added uses across the Office for Air Toxics, Environmental Justice and other programs
The NEXUS tool will essentially provide a ‘conceptual model’ of an area’s MP issues to facilitate engagement with state/local/tribal agencies & community stakeholder groups
3

## Slide 4: NEXUS Example: Display Major Point Sources

## Slide 5: NEXUS Example: Proximity Analysis for Facility

## Slide 6: NEXUS Example: Proximity Analysis for Electric Utilities

## Slide 7: “NEXUS 3.2” Live Demo
7

## Slide 8: “NEXUS 3.2”Beta Release Version: Quick Tutorial
Download “NEXUS” tool: The “NEXUS 3.2” package (“NEXUS 3.2 Setup.exe” & “NEXUS 3.0 Data.exe”: run both “*.exe” files to install) can be downloaded at EPA’s new FTP site:
https://gaftp.epa.gov/aqmg/cjang/NEXUS/NEXUS-3.0/*
Note: Require software installation privilege or “Power Broker” (limited installation privilege) to install “NEXUS tool” at EPA’s PCs; Please check “This PC\Documents\My NEXUS files\data\* (\tool\*, \result\*)” to see if NEXUS tool & input dataset have been installed successfully. If feasible, please un-install previous version first to ensure a successful installation.
8
OAQPS Multi-Pollutant team, 5/25/2022

## Slide 9: NEXUS Tool: On-line User’s Manual
Click “book” icon to launch “User’s manual”
Hot link to User’s manual’s “Data Viewer” chapter (same for “Data Input” module)
9

## Slide 10: NEXUS Tool: Data Viewer Module
Select & adjust “Ambient” or “Risk” levels
“Advanced Option”: provide HAPs & species selections
Click “File” to open or save a project
Switch between 2 key modules
NEXUS project file name
Select desired ambient data (DV) year (2013-2020)
10

## Slide 11: Data Viewer: “Apply” New Selections
New selections will appear in “Slider bars” panel and map display
“Apply” new selections
“Check” boxes to add or remove “Ambient” and/or “Risk” selections
“Slider bars” allow to select & adjust “Ambient” and/or “Risk” threshold levels to display corresponding color map
11

## Slide 12: NEXUS Update: EJ/Demographics Metric and Data
EJ/Demographic metric is displayed with “green dash” for counties exceeding selected threshold
12

## Slide 13: Data Viewer: “Reset” New Selections
“Reset” new selections
default configuration
risk-based value
risk-based in %tile
risk-based in desired %tile
13

## Slide 14: Data Viewer Module: Map Layers menu
“Map Layers” menu: Provide (show/hide) map overlaps of various areas, AQ metrics and boundary lines
Click “X” to close “Map Layers” menu
14

## Slide 15: Data Viewer Module: Configure Base Map & Color
“Base Map” menu: Change boundary lines and background map (e.g., “Google Map”)
Click “color map” to change color & transparency
“Right-click” map to save map image
15

## Slide 16: Data Viewer Module: MP Risk Ranking
Click “CBSA Risk Ranking” to provide MP risk ranking by CBSA or County
Check box to include EJ/demographic index as part of CBSA ranking
16

## Slide 17: Data Viewer: “Region Selection”
Allow to select “EPA regions”, “States”, or “CBSA”
17

## Slide 18: Data Viewer: Select EPA Region/State/CBSA
Examples:
EPA Region 4
State: NC
Louisville CBSA (KY/IN)
18

## Slide 19: Data Viewer: Major Emission Sources
Click “Display Emission Sources” tab (or “right-click”) to display emission sources and launch new window
Click any “facility” to link & display source location and emitted pollutants information. Same facility emitting various pollutants can be identified with the same highlighted color.
19

## Slide 20: Data Viewer: Major Emission Sources
Allow to scroll down to CBSA-level (e.g., Durham CH CBSA ) or County-level
Durham CH CBSA
Emissions ranking by “color” of circles from red (higher) to blue (lower)
Color Legend for facilities emissions
20

## Slide 21: Data Viewer: Top “x” Emission Sources
Durham county, NC
Provide selection of Facility or Source Category
Provide selection of Facility & Source Category
21

## Slide 22: Data Viewer: “Source Category Emissions”
“Source Category Emissions” module provide five source categories, including “Point”, “Non-Point”, “On-Road”, “Non-Road”, and “Event” emissions for the selected region, CBSA, or county.
For “Non-Point”, including Resident Wood Combustion (RWC) emissions.
22

## Slide 23: Data Viewer: “Sector Emissions Summary”
“Sector Emission Summary” function allow to select major CBSAs and provides source and sector emissions summary to support “Sector Prioritization” effort
23

## Slide 24: Data Viewer: “Sector Emissions Summary”
Summary table
Emissions
Frequency & Rank
Summary plot
24

## Slide 25: NEXUS Update: “Monitoring Data/Sites”
Monitor Site/Data
Click to select monitor site & pollutant
Click to display
AQ trend at monitor site
Click menu (or right-click) to display “Monitor Sites/Data”
Use different symbol to display each pollutant’s “monitoring sites” e.g., PM2.5 (triangle), O3 (star), etc.
AQ trend
Include only those monitor sites with data since selected year
Color Legend for monitor sites
List the monitor sites by ranking the data based on selected year
25

## Slide 26: NEXUS Update: “Attribute Table” (1)
“Right-click” map to select “Display Attribute Table ” to launch “Attribute Table”
“Attribute Table” provides information of “counties” displayed. This table will display “census tract” information under “Proximity analysis” module.
26

## Slide 27: NEXUS Update: “Attribute Table” (2)
Provide “filter/search/export functions
Click to show/hide Filter settings
Click to show selected record on map
Click to output data as Excel file
Click “Reset” to clear all filter criteria
Click a “record” to link and display its location & info.
Click “+” to add filters; Click “x” to remove current filter;
Show specified records per page.
27

## Slide 28: Data Viewer: EPA Region Table Generator
“EPA Region Table Generator” provides attainment status of O3 and PM2.5 and their DVs; also allows to select any EPA region based on data updated to 2020.
28

## Slide 29: Data Viewer: Data Search & Filter
Click “+” to add filters; Click “x” to remove current filter;
Click “Output data…” to output current page records or all records
Show specified records per page.
Click the “Select by map” to get the information of counties which are displayed on “Map” module
29

## Slide 30: Data Input Module: Data Preview
Click to view data
Click to run & save project
Select a table to view if there are multiple tables in the selected data source file
Check to use filter to query data
“Transparency” & “Open-Source”:
All NEXUS input/output data files are available under:
“This PC\Documents\My NEXUS files\Data (\Result)”
Click to change input data file
30

## Slide 31
NEXUS update:
Proximity Analysis
Module
(Census tract-level)
31

## Slide 32: Two ways navigate to Proximity Analysis Module
Or double click any monitor site or facility to launch “Proximity Analysis” module.
Click any monitor site, facility or county, and then “right-click” to select “Display Proximity Analysis”.
32

## Slide 33: Proximity Analysis Module: Overlaying Map
“Set up Threshold” panel (similar to Data Viewer module) allows to identity those geographic areas exceeding the selected thresholds.
Allow to select AQ mortality or morbidity risks, AQ concentration and EJ/demographic indicators and display overlaying map.
Check/un-check to display/hide overlaying map of selected metrics
33

## Slide 34: Proximity Analysis Module: Overlaying Map
Click “Reset” button to reset all values to default (or to a specified %tile if all indicators are selected in %tile)
Provide a “toggle” choice to select “Risk %tile” or “Risk value”
34

## Slide 35: Proximity Analysis Module: Configure Color & Transparency
Click any “color tile” to configure color legend & transparency
Move “Slider bar” to select desired “Radius of analysis”
35

## Slide 36
Create “Summary Plot” and “Summary Table” for a selected census tract, monitor site or emitting facility
Summary Plot
Proximity Analysis Module: Summary Plot & Summary Table (1)
Summary Table
36

## Slide 37: Proximity Analysis Module: Summary Plot & Summary Table (2)
Summary table
Summary plot
Select one or more indicators to plot summary results for selected site(s) within radius, county/CBSA/State/EPA Region and Nation avg.
Click “Output” button to export summary table to an Excel file (*.xlsx)
Set “Radius of analysis” and threshold of air toxics to show summary results for selected site(s) within radius
List top 3 risk drivers within radius of sites
Click to select the desired scale of highlighted numbers
37

## Slide 38: Proximity Analysis Module: “Select Sites” Functions (1)
Click “Select Sites” to select one or a group of monitor sites, facilities, census tracts, or user-defined locations under “Select Sites” pop-up window
38

## Slide 39: Proximity Analysis Module: “Select Sites” Functions (2)
Click the “Create individual Sites” or “Create National Sites Table” to provide proximity analysis for individual sites
Click the “Output” button to export to an Excel file.
National & State avg. table
National table for all selected individual sites
Include only census tracts falling within the area of specified radius, with an area ratio larger than x% (10% by default)
Select all
39

## Slide 40: Proximity Analysis Module: “Select Sites” Functions (3)
1. Click to select the desired scale of highlighted numbers
2. Set max. & min. values and then click the “Rebuild” button to rebuild the color legend
4. Click “Apply” or “OK” button to apply new setting
Configure
color legend:
Check/uncheck to display/ hide highlighted colors
3. Customize the numerical range for each color legend
40

## Slide 41: Proximity Analysis Module: “Group” Summary Plot & Table
Summary plot & table for a group of census tracts, monitor sites, facilities or locations (latitude/longitude)
Summary table
Summary Plot
Select sites
①Click “Select Sites”
② Select a group of sites
③Click “Apply”
④Click “Summary Table” or “Summary Plot”
41

## Slide 42: Proximity Analysis Module: Display Site information
Click a facility or monitoring site or a census tract to show the detail information
42

## Slide 43
NEXUS 3.0
Quick Tutorial Slides
End
43