## Slide 1: “NEXUS” Multi-Pollutant Analysis Tool Development: Status and Progress
OAQPS/AQPD Briefing
December 10, 2020
Carey Jang & Beth Landis
Data Viewer Module
Data Input Module
Data Query Module
“NEXUS 1.5” available on OAQPS’s Shared Drive at: “G:\SHARE\NEXUS\NEXUS 1.5\”
or at EPA’s new FTP site: ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
1

## Slide 2: Overview
NEXUS Tool Development
  Expected Use
  Schedule
Key Modules
Questions NEXUS can Answer & Examples: AQPD focused
Live Demo
Discussion & Next Steps

## Slide 3: NEXUS Tool Development
Motivation: Develop a new multi-pollutant analysis tool to identify and assess areas with high ambient levels and/or health risks associated with PM2.5, O3 and air toxics
Phase-1: Develop a GIS-based NEXUS prototype with a user-friendly graphical interface to provide analysis and visualization functions of potential multi-pollutant AQ issues at national level (continental US)
Phase-2: Expand the NEXUS tool to allow users to dial into an EPA region, State, or metropolitan area and provide data query and V/A functions for “AQ and emissions” information over the selected region of interest
3

## Slide 4: Expected Use of NEXUS Tool
The NEXUS tool will allow users to do the following:
  National screening for areas with MP issues: Phase 1 development will provide ability to quickly screen areas across nation that have combination of high air quality and/or risk levels for O3, PM2.5 and air toxics.
  Area screening to understand nature of MP problem: Phase 2 development will provide ability to ‘dial-into’ specific areas to determine extent to which common emissions sources are causing the MP issues.
OAQPS expects to use this tool to engage with Regions and identify areas that would potentially benefit most from MP approaches to reduce emissions (including current NA and Advance areas).
The NEXUS tool will essentially provide a ‘conceptual model’ of MP issues within an area to facilitate engagement with state/local/tribal agencies and community stakeholder groups.
4

## Slide 5: NEXUS Tool : Schedule & Installation
Work Plan | Date
Developed NEXUS tool prototype and Phase-1 functions | Dec. 2019 ~ April 2020
Developed Phase-2 functions and deliver first working (interim) NEXUS tool | May ~ July 2020
Developing a fully functional NEXUS tool for beta-testing and on-line User’s Manual | Aug. ~ Dec 2020
Download “NEXUS” tool: The “NEXUS 1.5” package (“NEXUS v1.5 setup.exe” & “NEXUS 1.5 Data.exe”: run both to install) is available at OAQPS’s Shared Drive at G:\SHARE\NEXUS\NEXUS 1.5\ or at EPA’s new FTP site ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
(Note: Require software installation privilege to install “NEXUS tool” at EPA’s PCs)
5

## Slide 6: NEXUS Tool: Three Key Modules
Data Viewer module
View and create interactive Map/Data/Chart/Table
Provide flexible selections & mapping of “Ambient” and/or “Risk” levels of PM2.5, O3 and air toxics
Provide regional analysis for “EPA region”, “States”. CBSA”, and “County”
Link and display major emission sources locations & emitted pollutants info.
6

## Slide 7: NEXUS Tool: Three Key Modules
Currently, there are 10 input data files used (publicly available)
Allow users to update/preview/filter Input data files
Run and Save to a new project after loading new input data files
Data Input module
Allow to update & change input data files
Provide data preview and filter functions
Extend to use 10 input data files now (publicly available, ~4 GB)
Quick turnaround to run & save to a new “project” using new input data files
7

## Slide 8
Data Input Module: Input Files & Attributes
Data Input File Names | Data Format | Data Description | Data Source | Data Period
“2014 O3 & PM2.5 fused Ambient & Risk” | Geodataset | O3/PM2.5 ambient & risk data at county/census tract level | from OAQPS MP team | 2014
“2014 NATA Risk” | Geodataset | Air toxics ambient & risk data at county/census tract level | from OAQPS MP team | 2014
“O3_DV_2009_2018” | Excel | O3 design values at county level | From EPA public website: https://www.epa.gov/air-trends/air-quality-design-values | 2009 to 2018
“PM_DV_2009_2018” | Excel | PM2.5 design values at county level | From EPA public website: https://www.epa.gov/air-trends/air-quality-design-values | 2009 to 2018
“Advance areas O3_PM” | Geodataset | O3 & PM2.5 Advance Areas | from OAQPS MP team | 2018
“Index of Poverty_ Disadvantage” | Excel | Index of poverty/disadvantage at county level | from Univ. of Michigan website: https://poverty.umich.edu/projects/understanding-communities-of-deep-disadvantage/ | 2017
“NEI_County_CAPs” “NEI_Facility_HAPs_ CAPs” | Geodataset | Major emission sources and facility info. of CAPs & HAPs at county level | From OAQPS public website: ftp://newftp.epa.gov/EPADataCommons/OAR/OAQPS/NEI/NEI_Facility_HAPs_CAPs.zip ftp://newftp.epa.gov/EPADataCommons/OAR/OAQPS/NEI/NEI_County_CAP.zip | 2008, 2011, 2014
“2014 NEI_NATA Emissions” | Access Database (*. accdb) | NATA emissions data from 2014 NEI database, including various source groups | From EPA public website: https://www.epa.gov/national-air-toxics-assessment/2014-nata-assessment-results#emissions | 2014
“Class1_FederalAreas” | Geodataset | Mandatory Class 1 Federal Areas | From Mandatory Class 1 Federal Areas Web Service: https://edg.epa.gov/data/public/OAR/OAQPS/Class1/Class1Areas.zip | —
8

## Slide 9: NEXUS Tool: Three Key Modules
Data Query module
Expand data field selections and flexibility for exploratory/advanced users
Provide overlaying map and summary table for data query results
Current data query based on selected data fields: “Ambient/Risk, Advance area, Socio-demographic (EJ) area, NA Area, Class I area”
9

## Slide 10: What Types of Questions May AQPD Ask?
How can NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics?
  Example 1 for Region 4  Miami
How can NEXUS be used to identify the nature of multi-pollutant risks within nonattainment areas?
  Example 2 for Region 4  Atlanta
How can NEXUS be used to identify the nature of multi-pollutant risks within Advance areas?
  Example 3 for Region 4  Louisville
10

## Slide 11: NEXUS Tool: Example 1
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. Example map above is for Region 4
11

## Slide 12: NEXUS Tool: Example 1
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. Example table above was generated in Data Query for Region 4. Table Generator Module is planned for future development. Currently, data can be exported to Excel.
12

## Slide 13: NEXUS Tool: Example 1
NEXUS can be used to identify highest risk areas across O3, PM2.5, and Air Toxics. Information above was generated in Data Query for Region 4 and exported into excel where rankings were applied.
Top 5 CBSAs (using this approach) – Miami, Tampa, Atlanta, Birmingham, Louisville
13

## Slide 14: NEXUS Tool: Example 1
NEXUS can be used to identify top emission sources. Information above was generated in Data Query for the Miami CBSA. This can help identify the potential co-benefits of controls.
14

## Slide 15: NEXUS Tool: Example 1
NEXUS can be used to identify top emission sources. Information above was generated in Data Query for the Miami CBSA.
What is this and where is it located?
15

## Slide 16: NEXUS Tool: Example 2
The maps above were generated for the Atlanta CBSA (2014 O3 NAA), using the data query module. The top 10 Gas & VOC HAPS emission sources are plotted.
16

## Slide 17: NEXUS Tool: Example 2
NEXUS can be used to identify top emission sources. Information above was generated in Data Query for the Atlanta CBSA. This can help identify the potential co-benefits of controls.
17

## Slide 18: NEXUS Tool: Example 3
The map above was generated for the Louisville/Jefferson County - Elizabethtown - Madison, KY-IN CBSA (2014 O3 NAA), using the data query module. The top 10 Gas & VOC HAPS emission sources are identified.
18

## Slide 19: NEXUS Tool: Example 3
2 of the top 4 NOx emission sources outside Jefferson County, KY (Jefferson County, IN & Tremble, KY)
19

## Slide 20: NEXUS Tool: Example 3
Top 2 VOC emission sources are in Nelson County, KY
20

## Slide 21: NEXUS Tool: Example 3
2 of the top 4 gas & VOC HAPs emission sources in Indiana (Harrison & Clark County)
21

## Slide 22
Live Demo
Carey Jang
22

## Slide 23: Discussion and Next Steps (1)
    Short-term:
    GOAL: Develop a functional version that reflects latest data and information available for internal testing and use
    Currently expect limited FY21 funding to support NEXUS —perhaps $50k from AQAD?
      Update NEXUS data to 2017
        2017 data for O3, PM2.5, Air Toxics risk, concentrations, & emissions
        Tribal boundaries & socioeconomic data for EJ
      Add O3, PM2.5, and Air Toxics monitoring data
      Update metrics/indicators (e.g., risk metrics, EJ indicators)
    Engage across Office to determine how this tool may best inform or be used for OAQPS’s Air Toxic Strategy programs
      Consider addition of screening-level analysis & assessment capabilities (e.g., proximity EJ analysis)
23

## Slide 24: Discussion and Next Steps (2)
    Long-term:
    Upgrade and prepare NEXUS for Beta test with EPA Regions followed by public release & training
    Based on Office wide engagements, use updated NEXUS tool with 2017 data to inform Multi-pollutant, Air Toxics, Advance, and EJ efforts as appropriate
    Develop plan for routine updates and maintenance of the NEXUS tool to best support OAR/OAQPS programs and determine appropriate extensions as need and resources provide.
24

## Slide 25
Additional Information
25

## Slide 26: NEXUS Tool Demo: 2014 NEXUS Case
26
Launching Page
Roadmap for Demo:
(Use example cases)
National View: Use “NEXUS” across pollutants to provide an initial “SCREEN” at the national level by providing an indicator where there may be a common set of sources contributing to Multi-pollutant issues.
Regional View: Dial into a region or area of interest to understand the pollutant/source connections, and potential for more effective and efficient multi-pollutant solution.
2008

## Slide 27: RoadMap for NEXUS Tool Demo (1)
National Screening (2014 Data)
Replicate 2008 NEXUS map with O3/PM2.5 concentrations above NAAQS and NATA risk estimates above selected percentile of top 10%
  What happens to areas at lower O3/PM2.5 NAAQS levels?
  What happens to areas current over O3/PM2.5 NAAQS if change HAP risk percentile?
Provide NEXUS map on risk basis: O3/PM2.5 BenMAP mortality risk based on fused surfaces and NATA risk estimates above selected percentile of top 10% for all pollutants
  What happens to MP areas as one changes percentile to top 20% or others?
  What is relationship between Heavy Metal HAPs risk (top 10%) and PM2.5 risk to identify potential co-pollutant issues?
  What is relationship between Gas/VOC HAPs risk (top 10%) and O3 risk to identify potential co-pollutant issues?
27

## Slide 28: RoadMap for NEXUS Tool Demo (2)
Regional/State/CBSA/County Screening
EPA Region 4 Example
  Areas with MP risk in top 10% across O3, PM2.5 and HAPs
  Louisville CBSA: General view and then dial into “Jefferson County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
28

## Slide 29: RoadMap for NEXUS Tool Demo (3)
Data Query: State/CBSA/County Views
Advance Areas
  Initial view of national level information using the Advance Area definition to show overlay with MP areas
  Region 5 => Minneapolis Example: General view and then dial into “Dakota County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
29

## Slide 30: RoadMap for NEXUS Tool Demo (4)
Data Query: State/CBSA/County Views
Socio-Economic/Demographic (EJ) Areas
  Initial view of national level information using the Poverty/Disadvantaged indicator to show overlay with MP areas
  Region 5 => Detroit Example: General view and then dial into “Wayne County” with transparent map color
    What are the top 10 emissions sources in county by pollutant?
    What specific sources are common across pollutants that may indicate co-control potential?
    Can view these sources on the map with summary data available.
30

## Slide 31: “NEXUS 1.5”: Quick Tutorial
Carey Jang, 12/10/2020
Download “NEXUS” tool: The “NEXUS 1.5” package (“NEXUS v1.5 setup.exe” & “NEXUS 1.5 Data.exe”: run both to install) is available at OAQPS’s Shared Drive at: G:\SHARE\NEXUS\NEXUS 1.5\
or at EPA’s new FTP site:
ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.5/
(Note: Require software installation privilege to install “NEXUS tool” at EPA’s; Older EPA PCs may be less efficient in running “NEXUS tool”) PCs
31

## Slide 32: NEXUS Tool: On-line User’s Manual
Hot link to User’s manual’s “Data Viewer” chapter (same for “Data Input” & “Data Query”
Click “book” icon to launch “User’s manual”
32

## Slide 33: NEXUS Tool: Data Viewer Module
Select & adjust “Ambient” & “Risk” levels
“Advanced Option”: provide HAPs & species selections
Click “File” to open or save a project
Switch between 3 key modules
Loaded NEXUS project file name
33

## Slide 34: Data Viewer Module: Selections & Map Display
Select & adjust “Ambient” & “Risk” threshold levels for color map display
“Apply” new selections to “Radio button” panel
34

## Slide 35: Data Viewer: “Apply” New Selections
New selections will appear on-the-fly in “radio button” panel and map display
“Apply” new selections
“Check” new selections
35

## Slide 36: Data Viewer Module: Base Map & Color
Click to change color & transparency
“Base Map”: Change boundary lines and background map
“Right-click” map to save image
36

## Slide 37: Data Viewer: “Region Selection”
Allow to select “EPA regions”, “States”, or “CBSA”
37

## Slide 38: Data Viewer: Select EPA Region/State/CBSA
Examples:
EPA Region 4
NC
Louisville CBSA
38

## Slide 39: Data Viewer: Major Emission Sources
Click “Emission Sources” tab to display emission sources (green dots) and launch new window
Click any “facility” to link & display source location and emission information
39

## Slide 40: Data Viewer: Major Emission Sources
Allow to scroll down to county-level (e.g., Wake County, NC)
Wake county, NC
40

## Slide 41: Data Viewer: Top “x” Emission Sources
Durham county, NC
Provide selection of CAPs precursors & HAPs species
41

## Slide 42: Data Viewer: EPA Region Table Generator
“EPA Region Table Generator” is still under development, but a preview of example “EPA Region 4” tables can be provided
42

## Slide 43: Data Viewer: Data Search & Filter
Click “+” to add filters; Click “x” to remove current filter;
Click “Output data…” to output current page records or all records
Show specified records per page.
43

## Slide 44: Data Query Module: Main Page
Region Selection
Data Query qualifier selection
Map Overlaying selection
Detachable “Attribute Table”
11111111
Data Query Configuration
44

## Slide 45: Data Query Module: Configure Data Query
45
“Data Query Filter” allows to select “qualifiers” for query
“Data Query Preview” displays the selected “qualifiers” at the same time

## Slide 46: Data Query Module: Overlaying Map
46
Overlaying Map selection
46

## Slide 47: Data Query Module: Attribute Table
Detachable “Attribute Table”
Filter/link/export functions (to be completed)
47

## Slide 48: Data Query Module: Attribute Table
Click a “record” to link and display its location & info.
48

## Slide 49: Data Input Module: Data Preview
Click to change input data file
Click to view data
Click to run & save project
Click to view data
Select a table to view if there are multiple tables in the selected data source file
Check to use filter to query data
49

## Slide 50
End
50