## Slide 1: “NEXUS” Multi-Pollutant Analysis Tool: Recent Upgrades and Improvements
MP Team Briefing
May 24, 2021
Carey Jang, Beth Landis and Matt Woody
Data Viewer Module
Data Input Module
Data Query Module
“NEXUS 1.8.5” available on OAQPS’s Shared Drive at: “G:\SHARE\NEXUS\NEXUS 1.8.5\”
or EPA’s new FTP site: ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.8.5/

## Slide 2: Outline
Feedback from OAQPS/SMT Briefings and MP Team
NEXUS Upgrades & Improvements (NEXUS “1.5”  “1.8.5”)
  New/revised Metrics (Air Toxics, PM2.5, O3 & EJ)
  New/updated data inputs and functions:
    EJ/Demographic data (from EJSCREEN)
    Tribal areas & Advance areas
    2017 emissions data (including GHG & sector mapping) (updated from 2014)
  “Source & Sector” emissions summary to support “Sector prioritization” effort (Appendix B)
  “Source Category” emissions analysis (point, non-point, road, non-road, event)
  Complete EPA region “Table Generator”
  Upgrade “Data Query” module & “Data Input” module
Demo of NEXUS Updates (v.1.8.5) (w/ “Quick tutorial” attached)
Next Steps and Work Plan
  2017 fused PM2.5 & O3 and risk data (July) and 2017 fused air toxic and risk data (TBD)
  Include & display Monitoring sites/data (PM2.5 & O3 first, then AT) (August)
  Developing screening capabilities for “Proximity analysis of MP risks and EJ” (TBD) (Appendix A)
2

## Slide 3: Main Feedback from OAQPS/SMT and MP Team
Improve the national screening metrics for air toxics to reduce possible “false-negatives”
Update to recent emissions, AQ and health risk data and include EJ/demographic indicators, tribal areas, and monitoring data
Enhance current “region” focus of tool to provide “national” (zoom-out) and “area-specific” (zoom-in) screening capabilities for “sources/sector groups” in multi-pollutant context
Within high-risk areas, provide proximity screening capabilities for selected source, monitoring site, or community of interest to conduct analyses for both MP and EJ issues of concern
3

## Slide 4: NEXUS: 2021 Development Plan
Near-term Priorities for 2021 NEXUS development:
Upgrade NEXUS (metrics/EJ indicators) for EPA beta testing
  Revising national air toxic (AT) metrics based on AT team’s suggestions
  Include EJ/demographic index from EJSCREEN and Tribal areas
Update to 2017 emissions data and develop “source/sector emissions summary” and “source category emissions” function
Update to 2017 AQ fused data (PM2.5, O3, AT) and health risk data (Note: need approval from SMT on updating AT risk work)
Include & display AQ monitoring sites/data (PM2.5, O3, AT)
Develop screening capabilities for “Proximity analysis for MP risk and EJ” at census tract-level and/or block group-level
Ongoing
Planned
4

## Slide 5: NEXUS Updates: New Metrics and EJ Data

## Slide 6: NEXUS Updates: New Air Toxics Metrics
Previous
Updated
6

## Slide 7: NEXUS Updates: EPA Region “Table Generator”
7
“EPA Region Table Generator” provides attainment status of O3 and PM2.5 and their DVs; also allows to select any EPA region based on data updated to 2018

## Slide 8: NEXUS Update: “Source/Sector” Emissions Summary
8
“Source/Sector Emissions Summary” function allows to select major CBSAs and provides source and sector emissions summary to support OAQPS’s “Sector Prioritization” project effort

## Slide 9: Sectors Most Prevalent in Highest Risk Areas
“Sector group” emissions combined for all 50 Highest Risk Ranked CBSAs Total Population: 134,940,816 |  |  |  |  |  |  |  | 
Sector Group | SO2 (TON) | NOx (TON) | PM2.5 (TON) | Gas_VOC_HAPs (LB) | Heavy_Metal_HAPs (LB) | CO2e (TON) | SO2 Score (freq. & rank) | 
Electric Utilities | 276526 | 195865 | 25828 | 6432707 | 127030 | 485754073 | 2014 | 
Petroleum Refining | 52943 | 40169 | 12438 | 10295621 | 99736 | 95097998 | 574 | 
Coke Ovens | 22405 | 15473 | 5158 | 1787622 | 29716 | 14570119 | 132 | 
Pesticides and Agricultural Chemical Manufacturing | 17644 | 5861 | 1292 | 1627958 | 1788 | 18233480 | 153 | 
Inorganic Chemical Manufacturing | 14522 | 7273 | 1405 | 1073205 | 48966 | 5231826 | 190 | 
Mineral Processing | 13714 | 12628 | 1659 | 886251 | 33740 | 8364046 | 256 | 
Iron and Steel Production | 10679 | 13345 | 5691 | 858984 | 110757 | 33030868 | 375 | 
Cement Manufacturing | 10566 | 44083 | 5007 | 1472498 | 25010 | 27859268 | 444 | 
Air Transportation | 8127 | 63035 | 2685 | 10417526 | 122777 | 18485627 | 1380 | 
Pulp and Paper Industry | 7413 | 9791 | 2779 | 7227413 | 23704 | 10517197 | 251 | 
Organic Chemical Manufacturing | 6240 | 38070 | 6254 | 10280694 | 20059 | 82521408 | 299 | 
Landfills | 2952 | 9872 | 2356 | 2799470 | 1880 | 28651639 | 563 | 
Consumer Products (Cleaning, Photographic, etc.) | 2815 | 1980 | 486 | 1363144 | 1724 | 1389978 | 66 | 
Oil and Gas Production and Distribution | 2717 | 28271 | 2259 | 4467061 | 1804 | 12342771 | 466 | 
Food Products Manufacturing | 2705 | 6197 | 3085 | 4110212 | 2496 | 3408089 | 327 | 
Non-Ferrous Metals Production | 2694 | 3511 | 1695 | 3663067 | 91643 | 2165692 | 212 | 
Glass Manufacturing | 2355 | 5832 | 953 | 92289 | 9990 | 1174855 | 210 | 
Clay Products Manufacturing | 1349 | 685 | 602 | 650323 | 1631 | 200293 | 311 | 
Waste Incineration | 1024 | 11872 | 483 | 679918 | 1801 | 9825913 | 189 | 
Method: Highest emitting sectors within top ranked 50 CBSAs (Note: Facilities are grouped based on “Sector definition” spreadsheet created by Marc H. & SPPD)*
9
*Appendix B contains example graphic with sector ranking by pollutants

## Slide 10: NEXUS Updates: Data Input Module
O3 & PM2.5 DVs data updated to 2018 (to 2020 as planned in June)
Advance areas updated to 2020 (to 2021 in June)
10
“Transparency” & “Open-Source”:
All NEXUS input/output data files are available under:
“This PC\Documents\My NEXUS files\Data (\Result)”
EJSCREEN data (updated to 2020) are used for EJ/Demographic data
Emissions data (county & facility) are updated to 2017 from 2014
Tribal boundaries & areas data are inlcuded

## Slide 11: NEXUS Upgrades: Data Query Module
11
Overlaying Map selection
Data Query qualifier selection
Data Query Configuration

## Slide 12: Data Query Module Upgrades: Configure Data Query
12
“Data Query Filter” allows to select “qualifiers” for query
“Data Query Preview” displays the selected “qualifiers” at the same time

## Slide 13: Data Query Module Upgrades: Attribute Table
13
Detachable “Attribute Table”
“Data Filter” functions to search/sort/export data of interest
Click “+” to add filters; Click “x” to remove current filter;
Click “Output data…” to output current page records or all records

## Slide 14: “NEXUS 1.8.5”Demo
14
NEXUS 1.8.5 “Quick Tutorial” slides attached

## Slide 15: “NEXUS 1.8.5”: Quick Tutorial
Carey Jang
Download “NEXUS” tool: The “NEXUS 1.8.5” package (“NEXUS 1.8.5 Setup.exe” & “NEXUS 1.8.5 Data.exe”: run both “*.exe” files to install) can be downloaded at OAQPS’s Shared Drive: G:\SHARE\NEXUS\NEXUS 1.8.5\*
or at EPA’s new FTP site:
ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.8.5/*
Note: Require software installation privilege or “Power Broker” (limited elevated privilege) to install “NEXUS tool” at EPA’s PC;
Check “This PC\Documents\My NEXUS files\data\* (\tool\*, \result\*)” to see if NEXUS program & input dataset installations are successful
15

## Slide 16
NEXUS 1.8.5 Demo: Upgrades/Improvements
    Data Input module:
    Data transparency: My Nexus files location
    PM & O3 DVs (update to 2020 in June)
    Advanced area (will update to 2021)
    EJSCREEN data
    2017 Emissions
    Tribal areas
    Data Query Module:
    Add new fields/flexibility: Exploratory users
    Configure DQ” window: Select EJ, Tribal areas, 2017 NA & DVs => Apply map
    Overlaying Map
    Detachable table to allow data filter/search/sort/export
    CBSA: Houston -> Harris Co. (EJ off)
16
    Data Viewer:
    Air Toxics: new Metric (max tract-level risk value)
    AT: species (updated list of H.M. & G.V.)
    PM2.5 & O3: new Risk Metric (max/avg/#)
    Slider bars: >90 %tile (from top 10%tile) w/ EJSCREEN
    New EJ metrics
    Chart & Table :
    EPA Region “Table Generator” (Region 4 & 9)
    EPA Region/State/CBSA View:
    “Zoom-in” for regional (all risk: 10%)
    EPA Regions -> CBSA: Louisville
    “right-click” -> Major Emis. Sources
    Change color transparency/Google Map
    Major Emission Sources:
    CBSA: Louisville -> Jefferson Co. -> Facility (Louisville G&E)
    CO2e & Diesel PM
    Source/Sector Emissions Summary
    Source Category Emissions
Notes: 1. Thank Cen/Gao/Luo/Chen; 2. HZ more visits; 3. AP on HZ

## Slide 17: Next Steps and Development Plan
Main Feedback from OAQPS/SMT Briefings and MP Team
NEXUS Upgrades & Improvements
  Metrics (Air Toxics, PM2.5, O3 & EJ)
  New/updated data inputs:
    2017 emissions data (source/sector & GHG)
    EJ data (from EJSCREEN),
    Tribal areas & Advance areas
  EPA region “Table Generator”
  “Source & Sector” emissions summary
  “Source category” emissions (point, non-point, road, non-road, event)
NEXUS (v.1.8.5) Demo
Next Steps and Work Plan
  2017 fused PM2.5 & O3 data and health risk data (July)
  2017 fused air toxic data and health risk data (TBD)
  Include & display monitoring sites/data (PM2.5 & O3 first, then AT) (August)
  Developing screening capabilities for “Proximity analysis of MP risks and EJ” (TBD)
    Close proximity analysis of MP risks & EJ/demographics to community of concern or monitoring site
    Select a source/facility or site within a flexible “Radius of influence” (e.g., 5 km)
    High spatial resolution: Census tract-level and/or block group-level
    Compare MP risks & EJ/demographics of interested community to CBSA/State/Nation
17

## Slide 18: Appendix A
Developing Screening Capabilities for “Proximity Analysis of MP Risks & EJ”
18

## Slide 19: Developing Screening Capabilities for “Proximity Analysis of MP Risks & EJ”
19
Facility: American Synthesis Rubber Co., KY Sector group: Polymers and Resins Production
[ x Display national map for Sector group
Create Table
Create Plot
Proximity and Spatial Analysis for MP Risks and EJ
Proximity Analysis
5
50km
Radius of Influence
Spatial Analysis
Proximity and Spatial Analysis for MP Risk and EJ
Proximity Analysis
EJ Indicator
MP Risk
Minority
Air Toxics
Spatial Analysis
Climate Risks
Air Quality
PM2.5 risk
O3 risk
Air Toxics risk
Cancer risk
Non-Cancer risk
Flood
Fire
Sea Level Rise
Heat
Disease
Climate Risks
EJ Indicators
Population
Minority
Income
Education
Language
Flood
Fire
Sea Level Rise
Heat
Disease
Chart: MP Risk and EJ Analysis for Selected Facility/Sector Group
| Within Radius of Facility | County Avg. | State Avg. | EPA Region Avg. | Nation Avg. | Sector Group (within radius) National avg.
PM Risk | 0.85 | 0.75 | 0.7 | 0.6 | 0.5 | 0.75
Air Toxic Risk | 0.95 | 0.85 | 0.77 | 0.65 | 0.55 | 0.81
EJ Index | 0.92 | 0.82 | 0.73 | 0.72 | 0.5 | 0.78
Proximity Analysis
(Selected Facility or Monitoring Site)
Spatial
Analysis
Graphical
& Tabular
Analysis
NEXUS now can be used to quickly identify top emitters of NOx, SO2, PM2.5, and heavy-metal & VOCs HAPs near EJ areas of concern; plan to develop proximity & spatial analysis capabilities
Facility: American Synthesis Rubber Co., Louisville, KY Sector Group: Polymers and Resins Production Top Risk Drivers: ETO, Formaldehyde (examples) |  |  |  |  | Selected Options: Radius of Impact: 10km Number of CBSAs: 25 (top MP risk ranking) Air Toxics Risk threshold: 10 (“x”-in-a million) |  |  | 
 | Within Radius of Facility | County Avg. | State Avg. | EPA Region Avg. |  | Nation Avg. | Sector Group (within radius) National avg. | Sector Group (within radius) Top 25 CBSAs
Population total | x,xxx | xx,xxx | xxx,xxx | xxx,xxx |  | 317,xxx,xxx | xxx,xxx | xxx,xxx
PM2.5 risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Ozone risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Air Toxics risk: Cancer risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Cancer risk value (“x”-in-a million)) | x.x | x.x | x.x | x.x |  | x.x | x.x | x.x
Cancer risk value above selected threshold (population %tile) | x% | x% | x% | x% |  | x% | x% | x%
Non-cancer risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Non-cancer risk (Hazard Index) | x.x | x.x | x.x | x.x |  | x.x | x.x | x.x
Climate risks: Flood (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Sea level rise (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Fire (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Disease (%tile) | x% | x% | x% | x% |  | x% | x% | x%
EJ/Demographics: Minority group (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Low-income group (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Demographic Index (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Linguistic Isolation (%tile) | x% | x% | x% | x% |  | x% |  | x%

## Slide 20
20
Facility: American Synthesis Rubber Co., KY Sector group: Polymers and Resins Production
[ x Display national map for Sector group
Create Table
Create Plot
Proximity and Spatial Analysis for MP Risks and EJ
Proximity Analysis
5
50km
Radius of Influence
NEXUS now can quickly identify top emitters of CAPs & HAPs; Plan to develop proximity screening capabilities to include EJ/demographic indicators
Spatial Analysis
Developing Capabilities for Proximity and Spatial Analysis
Proximity analysis will allow to set a flexible “Radius of Influence” for a selected facility or monitoring site (based on census tract- and/or block group-level)

## Slide 21: Developing Capabilities for Proximity and Spatial Analysis
21
Proximity and Spatial Analysis for MP Risk and EJ
Proximity Analysis
EJ Indicator
MP Risk
Minority
Air Toxics
Spatial Analysis
Climate Risks
Air Quality
PM2.5 risk
O3 risk
Air Toxics risk
Cancer risk
Non-Cancer risk
Flood
Fire
Sea Level Rise
Heat
Disease
Climate Risks
EJ Indicators
Population
Minority
Income
Education
Language
Flood
Fire
Sea Level Rise
Heat
Disease

## Slide 22: Screening Proximity Analysis in NEXUS: Example Tabular Data Summary
Facility: American Synthesis Rubber Co., Louisville, KY Sector Group: Polymers and Resins Production Top Risk Drivers: ETO, Formaldehyde (examples) |  |  |  |  | Selected Options: Radius of Impact: 10km Number of CBSAs: 25 (top MP risk ranking) Air Toxics Risk threshold: 10 (“x”-in-a million) |  |  | 
 | Within Radius of Facility | County Avg. | State Avg. | EPA Region Avg. |  | Nation Avg. | Sector Group (within radius) National avg. | Sector Group (within radius) Top 25 CBSAs
Population total | x,xxx | xx,xxx | xxx,xxx | xxx,xxx |  | 317,xxx,xxx | xxx,xxx | xxx,xxx
PM2.5 risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Ozone risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Air Toxics risk: Cancer risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Cancer risk value (“x”-in-a million)) | x.x | x.x | x.x | x.x |  | x.x | x.x | x.x
Cancer risk value above selected threshold (population %tile) | x% | x% | x% | x% |  | x% | x% | x%
Non-cancer risk (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Non-cancer risk (Hazard Index) | x.x | x.x | x.x | x.x |  | x.x | x.x | x.x
Climate risks: Flood (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Sea level rise (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Fire (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Disease (%tile) | x% | x% | x% | x% |  | x% | x% | x%
EJ/Demographics: Minority group (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Low-income group (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Demographic Index (%tile) | x% | x% | x% | x% |  | x% | x% | x%
Linguistic Isolation (%tile) | x% | x% | x% | x% |  | x% |  | x%
22

## Slide 23
Proximity Analysis for Selected Facility/Sector or Monitoring Site: Example Chart
Climate Risks
Air Quality
PM2.5 risk
O3 risk
Air Toxics risk
Cancer risk
Non-Cancer risk
Flood
Fire
Sea Level Rise
Heat
Disease
Climate Risks
EJ Indicators
Population
Minority
Income
Education
Language
Flood
Fire
Sea Level Rise
Heat
Disease
Chart: MP Risk and EJ Analysis for Selected Facility and its Sector Group
| Within Radius of Facility | County Avg. | State Avg. | EPA Region Avg. | Nation Avg. | Sector Group (within radius) National avg.
PM Risk | 0.85 | 0.75 | 0.7 | 0.6 | 0.5 | 0.75
Air Toxic Risk | 0.95 | 0.85 | 0.77 | 0.65 | 0.55 | 0.81
EJ Index | 0.92 | 0.82 | 0.73 | 0.72 | 0.5 | 0.78
(%tile)

## Slide 24: Proximity & Spatial Analysis: Allow to “Zoom-out” & “Zoom-in” Nationally for all Facilities under same “Sector Group”
24
Facility: American Synthesis Rubber Co., KY Sector group: Polymers and Resins Production
[ x Display national map for Sector group
Create Table
Create Plot
Proximity and Spatial Analysis for MP Risks and EJ
Proximity Analysis
5
50km
Radius of Influence
Spatial Analysis
Zoom-out
Zoom-in
Display all facilities within same “Sector group”
Allow to “zoom out” nationally and “zoom-in” back to facility level
Provide color scale for selected MP risk value (e.g., red w/ high MP risk)
Proximity Analysis for Source/Sector

## Slide 25: Appendix B
Source & Sector Emissions Summary for High MP Risk Ranking CBSAs
(Support “Sector Prioritization” Effort)
25

## Slide 26: MP Ranking: CBSAs w/ Top-Ranked MP Risks
Method: Identify CBSAs with top MP risk ranking: Major CBSAs are selected.
26
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
1 | EPA Region 5 | IL-IN-WI | Chicago-Joliet-Naperville, IL-IN-WI | 1
2 | EPA Region 3 | PA | Pittsburgh, PA | 1
3 | EPA Region 6 | TX | Houston-Sugar Land-Baytown, TX | 1
4 | EPA Region 9 | CA | Los Angeles-Long Beach-Santa Ana, CA | 2
5 | EPA Region 6 | TX | Dallas-Fort Worth-Arlington, TX | 2
6 | EPA Region 4 | GA | Atlanta-Sandy Springs-Marietta, GA | 3
7 | EPA Region 4 | FL | Tampa-St. Petersburg-Clearwater, FL | 3
8 | EPA Region 4 | AL | Birmingham-Hoover, AL | 3
9 | EPA Region 9 | AZ | Phoenix-Mesa-Glendale, AZ | 3
10 | EPA Region 9 | CA | Fresno, CA | 3
11 | EPA Region 2 | NY-NJ-PA | New York-Northern New Jersey-Long Island, NY-NJ-PA | 3
12 | EPA Region 5 | OH | Cleveland-Elyria-Mentor, OH | 3
13 | EPA Region 9 | CA | Sacramento--Arden-Arcade--Roseville, CA | 4
14 | EPA Region 9 | NV | Las Vegas-Paradise, NV | 4
15 | EPA Region 4 | NC-SC | Charlotte-Gastonia-Rock Hill, NC-SC | 5
16 | EPA Region 9 | CA | San Diego-Carlsbad-San Marcos, CA | 5
17 | EPA Region 5 | MI | Detroit-Warren-Livonia, MI | 5
18 | EPA Regions 5 & 7 | MO-IL | St. Louis, MO-IL | 5
19 | EPA Region 5 | MI | Grand Rapids-Wyoming, MI | 6
20 | EPA Region 4 | TN | Nashville-Davidson--Murfreesboro--Franklin, TN | 6
21 | EPA Region 9 | CA | Bakersfield-Delano, CA | 6
22 | EPA Regions 2 & 3 | PA-NJ-DE-MD | Philadelphia-Camden-Wilmington, PA-NJ-DE-MD | 6
23 | EPA Region 9 | CA | Riverside-San Bernardino-Ontario, CA | 6
24 | EPA Region 4 | FL | Miami-Fort Lauderdale-Pompano Beach, FL | 6
25 | EPA Region 6 | LA | Baton Rouge, LA | 7
26 | EPA Region 6 | TX | El Paso, TX | 7
27 | EPA Region 10 | WA | Seattle-Tacoma-Bellevue, WA | 7
28 | EPA Region 4 & 5 | KY-IN | Louisville-Jefferson County, KY-IN | 7
 | EPA_REGION | STATE | CBSA_NAME | Overall Rank
29 | EPA Region 8 | CO | Denver-Aurora-Broomfield, CO | 8
30 | EPA Region 3 | PA | Reading, PA | 8
31 | EPA Region 9 | CA | Visalia-Porterville, CA | 8
32 | EPA Region 1 | CT | Bridgeport-Stamford-Norwalk, CT | 8
33 | EPA Region 4 & 6 | TN-MS-AR | Memphis, TN-MS-AR | 8
34 | EPA Regions 2 & 3 | PA-NJ | Allentown-Bethlehem-Easton, PA-NJ | 9
35 | EPA Region 6 | LA | New Orleans-Metairie-Kenner, LA | 9
36 | EPA Region 4 | NC | Greensboro-High Point, NC | 10
37 | EPA Region 4 | AL | Mobile, AL | 10
38 | EPA Region 4 | TN-GA | Chattanooga, TN-GA | 11
39 | EPA Region 4 | TN | Knoxville, TN | 11
40 | EPA Region 3 | DC-VA-MD-WV | Washington-Arlington-Alexandria, DC-VA-MD-WV | 11
41 | EPA Region 6 | OK | Tulsa, OK | 11
42 | EPA Region 9 | AZ | Tucson, AZ | 11
43 | EPA Region 4 | SC | Charleston-North Charleston-Summerville, SC | 12
44 | EPA Region 4 | SC | Greenville-Mauldin-Easley, SC | 12
45 | EPA Region 3 | WV | Charleston, WV | 13
46 | EPA Region 4 | SC | Spartanburg, SC | 13
47 | EPA Region 4 | NC | Winston-Salem, NC | 13
48 | EPA Region 4 | FL | Lakeland-Winter Haven, FL | 13
49 | EPA Region 5 | OH | Akron, OH | 13
50 | EPA Region 6 | TX | Beaumont-Port Arthur, TX | 14
51 | EPA Region 5 | MI | Lansing-East Lansing, MI | 14
52 | EPA Region 4 | FL | Orlando-Kissimmee-Sanford, FL | 14
53 | EPA Region 10 | OR | Eugene-Springfield, OR | 14
54 | EPA Region 9 | NV | Reno-Sparks, NV | 14
55 | EPA Regions 4 & 5 | OH-KY-IN | Cincinnati-Middletown, OH-KY-IN | 14
56 | EPA Region 3 | PA | Lancaster, PA | 14

## Slide 27: NEXUS Update: “Source/Sector” Emissions Summary
27
“Source/Sector Emission Summary” function allow to select major CBSAs and provides source and sector emissions summary to support OAQPS’s “Sector Prioritization” project effort

## Slide 28: Sectors Most Prevalent in Highest Risk Areas
“Sector group” emissions combined for all 50 Highest Risk Ranked CBSAs Total Population: 134,940,816 |  |  |  |  |  |  |  | 
Sector Group | SO2 (TON) | NOx (TON) | PM2.5 (TON) | Gas_VOC_HAPs (LB) | Heavy_Metal_HAPs (LB) | CO2e (TON) | SO2 Score (freq. & rank) | 
Electric Utilities | 276526 | 195865 | 25828 | 6432707 | 127030 | 485754073 | 2014 | 
Petroleum Refining | 52943 | 40169 | 12438 | 10295621 | 99736 | 95097998 | 574 | 
Coke Ovens | 22405 | 15473 | 5158 | 1787622 | 29716 | 14570119 | 132 | 
Pesticides and Agricultural Chemical Manufacturing | 17644 | 5861 | 1292 | 1627958 | 1788 | 18233480 | 153 | 
Inorganic Chemical Manufacturing | 14522 | 7273 | 1405 | 1073205 | 48966 | 5231826 | 190 | 
Mineral Processing | 13714 | 12628 | 1659 | 886251 | 33740 | 8364046 | 256 | 
Iron and Steel Production | 10679 | 13345 | 5691 | 858984 | 110757 | 33030868 | 375 | 
Cement Manufacturing | 10566 | 44083 | 5007 | 1472498 | 25010 | 27859268 | 444 | 
Air Transportation | 8127 | 63035 | 2685 | 10417526 | 122777 | 18485627 | 1380 | 
Pulp and Paper Industry | 7413 | 9791 | 2779 | 7227413 | 23704 | 10517197 | 251 | 
Organic Chemical Manufacturing | 6240 | 38070 | 6254 | 10280694 | 20059 | 82521408 | 299 | 
Landfills | 2952 | 9872 | 2356 | 2799470 | 1880 | 28651639 | 563 | 
Consumer Products (Cleaning, Photographic, etc.) | 2815 | 1980 | 486 | 1363144 | 1724 | 1389978 | 66 | 
Oil and Gas Production and Distribution | 2717 | 28271 | 2259 | 4467061 | 1804 | 12342771 | 466 | 
Food Products Manufacturing | 2705 | 6197 | 3085 | 4110212 | 2496 | 3408089 | 327 | 
Non-Ferrous Metals Production | 2694 | 3511 | 1695 | 3663067 | 91643 | 2165692 | 212 | 
Glass Manufacturing | 2355 | 5832 | 953 | 92289 | 9990 | 1174855 | 210 | 
Clay Products Manufacturing | 1349 | 685 | 602 | 650323 | 1631 | 200293 | 311 | 
Waste Incineration | 1024 | 11872 | 483 | 679918 | 1801 | 9825913 | 189 | 
Method: Highest emitting sectors within top ranked 50 CBSAs (Note: Facilities are grouped based on “Sector definition” spreadsheet created by Marc H. & SPPD)*
28
*Appendix contains graphics with sector ranking by pollutants

## Slide 29: SO2 & NOx: Sector Group emissions Summed up top 20 facility emissions over 50 major CBSAs
Chart: Total SO2 & NOx emissions (tpy) from top Sector groups
| Electric Utilities | Petroleum Refining | Coke Ovens | Pesticides and Agricultural Chemical Manufacturing | Inorganic Chemical Manufacturing | Mineral Processing | Iron and Steel Production | Cement Manufacturing | Air Transportation | Pulp and Paper Industry | Organic Chemical Manufacturing | Landfills | Consumer Products (Cleaning, Photographic, etc.) | Oil and Gas Production and Distribution | Food Products Manufacturing | Non-Ferrous Metals Production | Glass Manufacturing | Clay Products Manufacturing | Waste Incineration | Asphalt Products Manufacturing | Mining Activities
SO2 | 276526.3062 | 52943.1734 | 22404.8065 | 17644.0804 | 14521.6033 | 13714.4318 | 10678.7031 | 10566.429 | 8126.8388 | 7412.9793 | 6239.8283 | 2952.1673 | 2814.5235 | 2716.7565 | 2704.9001 | 2693.8076 | 2354.6044 | 1348.7497 | 1024.3245 | 917.4123 | 860.1116
NOx | 195864.5328 | 40168.8675 | 15472.6338 | 5861.2174 | 7272.8804 | 12628.2753 | 13345.4622 | 44083.4072 | 63034.7835 | 9790.7401 | 38070.4692 | 9872.4188 | 1980.2363 | 28271.167 | 6197.3419 | 3510.7028 | 5832.2555 | 684.7521 | 11871.941 | 1211.0917 | 3246.8551
over
29

## Slide 30: Questions?
30

## Slide 31: “NEXUS 1.8.5”: Quick Tutorial
Carey Jang
Download “NEXUS” tool: The “NEXUS 1.8.5” package (“NEXUS 1.8.5 Setup.exe” & “NEXUS 1.8.5 Data.exe”: run both “*.exe” files to install) can be downloaded at OAQPS’s Shared Drive: G:\SHARE\NEXUS\NEXUS 1.8.5\*
or at EPA’s new FTP site:
ftp://newftp.epa.gov/aqmg/cjang/NEXUS/NEXUS 1.8.5/*
Note: Require software installation privilege or Power Broker (limited elevated privilege) to install “NEXUS tool” at EPA’s PC;
Check “This PC\Documents\My NEXUS files\data\* (\tool\*, \result\*)” to see if NEXUS program & input dataset installations are successful
31

## Slide 32: NEXUS Tool: On-line User’s Manual
32
Hot link to User’s manual’s “Data Viewer” chapter (same for “Data Input” module & “Data Query” model)
Click “book” icon to launch “User’s manual”

## Slide 33: NEXUS Tool: Data Viewer Module
Select & adjust “Ambient” or “Risk” levels
“Advanced Option”: provide HAPs & species selections
33
Click “File” to open or save a project
Switch between 3 key modules
NEXUS project file name

## Slide 34: Data Viewer: “Apply” New Selections
New selections will appear in “Slider bars” panel and map display
“Apply” new selections
34
“Check” boxes to change/add selections
“Slider bars” allow to select & adjust “Ambient” and/or “Risk” threshold levels and displaying color map

## Slide 35: NEXUS Update: New EJ Metric and Data

## Slide 36: Data Viewer Module: Base Map & Color
36
Click to change color & transparency
“Base Map”: Change boundary lines and background map
“Right-click” map to save image

## Slide 37: Data Viewer: “Region Selection”
Allow to select “EPA regions”, “States”, or “CBSA”
37

## Slide 38: Data Viewer: Select EPA Region/State/CBSA
38
Examples:
EPA Region 4
NC State
Louisville CBSA

## Slide 39: Data Viewer: Major Emission Sources
39
Click “Emission Sources” tab to display emission sources (green dots) and launch new window
Click any “facility” to link & display source location and emission information

## Slide 40: Data Viewer: Major Emission Sources
40
Allow to scroll down to county-level (e.g., Wake County, NC)
Wake county, NC

## Slide 41: Data Viewer: Top “x” Emission Sources
41
Durham county, NC
Provide selection of CAPs precursors & HAPs species

## Slide 42: NEXUS Update: “Source/Sector” Emissions Summary
42
“Source/Sector Emission Summary” function allow to select major CBSAs and provides source and sector emissions summary to support OAQPS’s “Sector Prioritization” project effort

## Slide 43: Data Viewer: EPA Region Table Generator
43
“EPA Region Table Generator” provides attainment status of O3 and PM2.5 and their DVs; also allows to select any EPA region based on data updated to 2018.

## Slide 44: Data Viewer: Data Search & Filter
Click “+” to add filters; Click “x” to remove current filter;
Click “Output data…” to output current page records or all records
Show specified records per page.

## Slide 45: Data Query Module: Overlaying Map
45
Overlaying Map selection
Region Selection
Data Query qualifier selection
Data Query Configuration

## Slide 46: Data Query Module: Configure Data Query
46
“Data Query Filter” allows to select “qualifiers” for query
“Data Query Preview” displays the selected “qualifiers” at the same time

## Slide 47: Data Query Module: Attribute Table
47
Detachable “Attribute Table”
Filter/search/export functions

## Slide 48: Data Query Module: Attribute Table
48
Click a “record” to link and display its location & info.

## Slide 49: Data Input Module: Data Preview
Click to change input data file
Click to view data
Click to run & save project
Click to view data
Select a table to view if there are multiple tables in the selected data source file
Check to use filter to query data
“Transparency” & “Open-Source”:
All NEXUS input/output data files are available under:
“This PC\Documents\My NEXUS files\Data (\Result)”

## Slide 50: End
50