## Slide 1: Water Quality Indicators (WQI) Tool Version 2.0 View, Focus, and Screen Ambient Monitoring Data
April 2018
https://echo.epa.gov/maps/wqimap

## Slide 2: Agenda
Tool Background
Using Tool/Live Demo
WQI Derivative Projects
Future Plans

## Slide 3: Issues Focusing Solely on Impaired Waters
303(d) Listed As Impaired Waters Indexed to NHDPlus Version 2.1, EPA OW

## Slide 4: Project Approach
Derive and use available total nitrogen and total phosphorus measurements in Water Quality Portals data (2009-Present).
Calculate relevant statistics (percentiles, counts) with data and compare to CWA 304(a) ANE Criteria, Harmful Algal Bloom (HAB) Criteria, user supplied criteria.
When total nitrogen is not reported, derive it by combining subspecies of nitrogen present in the NWIS and STORET.
Only measurements reported as total phosphorus are used.
Other important steps:
  identifying and considering non-detects – currently substituting ½ detection limit
  identifying and averaging duplicate samples
  identifying and validating ambiguously reported data
  identifying and rejecting poorly reported data (e.g. missing units)
Normalize Monitoring Data
QA/QC data
Visualize Data
Compared to WQ Criteria
With additional data layers
Gather Monitoring Data
Calculate representative statistic
US Water Quality Portals 2009-Present

## Slide 5
Scope
Nutrients Monitoring Records 2009-Present
Data Sources
National Water Quality Monitoring Council – Water Quality Portal
  EPA’s STOrage and RETrieval Data Warehouse (STORET)
  USGS National Water Information System (NWIS)
  USDA Sustaining The Earth’s Watersheds – Agricultural Research Database System (STEWARDS)
ECHO Facilities Map Service
CWA 304(a) National Criteria
  Aggregate Nutrient Ecoregional (ANE) Criteria
Yuan, L. L., & Pollard, A. I. (2015). Deriving nutrient targets to prevent excessive cyanobacterial densities in US lakes and reservoirs. Freshwater Biology, 60(9), 1901-1916.
CWA 303(d) impaired waters and CWA 305(b) assessed waters map services (NHDPlus Version 2.1)
National Land Cover Data Set (2011)
Chesapeake Bay Land Cover

## Slide 6: NPDES Permitting Use Case
What are the recent nutrient concentration trends of the receiving water body?
Locate nitrogen or phosphorus hotspot and facilities upstream from hotspot.
Do upstream facilities discharge nitrogen or phosphorus?
Do upstream facilities have nitrogen or phosphorus limits?
This is a screening tool!

## Slide 7: Water Monitoring Use Cases
Finding potentially impaired water bodies
  A water body has not been designated impaired for nutrient pollution
Helping to determine a water body is no longer impaired for nutrients
Finding facilities that discharge into a water body impaired for nutrient pollution
This is a screening tool!

## Slide 8: Prioritizing Inspection Resources Use Cases
Identifying inspection priorities on unassessed waters or assessed waters that are not impaired for nutrients
Identify potential non-compliance
Identify un-permitted facilities
This is a screening tool!

## Slide 9: Live Demo
https://echo.epa.gov/maps/wqimap
ECHO Gov log in required (lan ID and password)

## Slide 10: Future Plans
Pollutant Expansion
  Pathogens – e. coli, enterococci, possibly fecal coliforms
  Suggested new pollutants/parameters
New Map Layers
  Updated County Level CAFO Counts
Enhanced Searching
  Between monitoring locations – ‘Upstream Downstream’ Analysis
  Between NPDES facilities
Modernize treatment of detection limits

## Slide 11: Accessing the Tool
Go to: https://echo.epa.gov/maps/wqimap
  You will be asked to log into ECHO Gov with your Lan ID and password.
Resources and Technical Documentation
  https://echo.epa.gov/files/echodownloads/Data-Analytics/
You must have an ECHO Gov account to access.
  Register here: https://echo.epa.gov/user/register
Download the dataset (publicly available):
  https://echo.epa.gov/tools/data-downloads/wqi-data-review

## Slide 12: Questions, Comments & Feedback?
Rusty Wasem
(202) 564-7096
wasem.russell@epa.gov
Bob Greenspun
(202) 564-2506
greenspun.robert@epa.gov
A 508 compliant version of this presentation will be made available upon request.

## Slide 13
The following slides to be used if live demo is not possible.

## Slide 14: Using the Tool: The Legend
No Samples
  n = 0
Only Rejected Samples
  All samples were rejected
No Concern
  Threshold Statistic < 1.00 of criteria
Possible Concern
  Threshold Statistic 1.00 < 5.00 of criteria
Concern
  Threshold Statistic 5.00 < 10.00 of criteria
High Concern
  Threshold Statistic >= 10.00 of criteria

## Slide 15: Using the Tool: Default View

## Slide 16: Using the Tool: Viewing Symbol Pop Up Window

## Slide 17: Using the Tool: Search for Upstream Facilities
Feature searches 15 km upstream/ downstream (tributaries and main stem)
Maps up/downstream NPDES facilities
  ECHO Symbol pop ups include compliance summary and links more reports
Download facility list as a .csv file
Click here to search Pollutant Upstream up/downstream
Select 15 km upstream, downstream, or upstream pollutant point source
Download facility list as a .csv file

## Slide 18: Using the Tool: Symbology Tab Options
Timeframe
Pollutant
Class-break threshold statistic
CWA 304(a) Criteria
HAB Criteria
User Defined Criteria
Top 50-500 Sites

## Slide 19: Using the Tool: User Defined Criteria and Break Points
Set criteria and breakpoints either globally or by Ecoregion

## Slide 20: Using the Tool: Layers Tab Options
Check Box(s) & Zoom to View Layer(s)
  NPDES Permitted Facilities
  CWA 303(d) Impaired Waters*
  CWA 305(b) Assessed Waters*
  HUC 8, 10 and 12*
  NHD+ Flow Lines*
  CAFO Density
Click the to view a layer’s legend
*To view these layers, you must be zoomed in

## Slide 21: Using the Tool: Filter Tab Options
Filter by:
  Ecoregion: I-XIV
  Water Body Type: River/Stream or Lake/Reservoir
Category:
  Station category (eg. High Concern only)
Number of Samples
EPA Region
State/County
HUC-8 Subbasin

## Slide 22: Using the Tool: Adding a Map Layer
Import your own map or map layer, by adding the service URL in the Add Layer Tab

## Slide 23: Prioritizing Inspection Resources Use Cases
Filter Minimum Number of Samples = 40
Select Top 50 Sites National
Zoom to Charlotte NC Area
Change Minimum Number of Samples = 0
Select HAB Criteria
Upstream locations below threshold
Downstream location 10x above threshold
Who is discharging in between?